## Slide 1: Little´s law basics-1st part

## Slide 2: Běžná situace, kterou je potřeba řešit
30 zákazníků/hodina – (max kapacita provozovny)
8 zákazníků čeká ve frontě (nárazník)
5 minut trvá doba obsluhy jednoho zákazníka
Potřeba odstranit všechny časy, které nepřinášejí hodnotu
1 obslužné místo=12 zákazníků za hodinu, takže pro 30 zákazníků /hodinu je potřeba kapacita 2,5 obslužného místa
8 zákazníků
čeká ve frontě
5 minut/obsluha 1 zákazníka

## Slide 3: Otázky
Jak dlouho průměrně čeká zákazník ve frontě ?
Kolik průměrně lidí může být naráz obslouženo ?
Kolik zákazníků je v provozovně v jenom okamžiku (jak čekající, tak ti, které personál obsluhuje) ?
Jaká je průměrná doba „průstupu“ (průtoku) zákazníka provozovnou (čekání i obsluha)
Zjednodušující podmínky
  „Vstupní tok“ (průměr) =„Výstupní tok“ (průměr)
  Díky průměrování neuvažujeme fluktuace (viz hody mincí)

## Slide 4: Klíčová měřítka (proměnné)
Lead Time =LT (jak dlouho trvá celý proces)
Inventory = WIP (kolik jednotek je v procesu= nedokončená výroba-Work In Progress)
Throughput Rate =T (počet zákazníků/jednotka času) – někdy Flow Time nebo Flow Rate – např. 30/hod
Cycle Time = čas/jednotka = počet minut /zákazník nebo počet hodin/výrobek = CT = (někdy se tomu říká TAKT TIME) - např- 5 minut/1 zákazník
CT= 1/T=1/ FT, kde FT = Flow Time
Tyto měřítka jsou propojena Littlovým zákonem WIP=T x CT =T/FT (někdy je T označováno jako TH)
Příklad 1 : T= 30 výrobků/hod, výroba jednoho výrobku trvá 0,5 hodiny (0,5 hod/výrobek=CT).
Otázka : kolik je WIP ?
Odpovědˇ : WIP =30*0,5=15 výrobků
Příklad 2 : T=30 zákazníků/hod, obsluha jednoho je 5 minut, WIP=(30/60) *(5/1)=30/12=2,5
WIP
Lead Time
T

## Slide 5: Řešení |(home study)
Proces | WIP | T (Zák/hod) | LT
Buffer | 8 | 30 | 
Obsluha |  | 30 | 5
Celkem |  | 30 | 
Proces | WIP | T (Zák/hod) | CT (min/Zák) | LT
Buffer | 8 | 30 | 0,5 | 
Obsluha |  | 30 | 0,5 | 5
Celkem |  | 30 | 0,5 | 
Proces | WIP | T (Zák/hod) | CT(min/Zák) | Lead Time
Buffer | 8 | 30 | 0,5 | 
Obsluha | 2,5 | 30 | 0,5 | 5
Celkem | 10,5 | 30 | 0,5 | 
WIP =T x LT(třetí sloupec je kvůli jednotkám)
Proces | WIP | T (Zák/hod) | CT (/min/Zák) | Lead Time
Buffer | 8 | 30 | 0,5 | 16
Obsluha | 2,5 | 30 | 0,5 | 5
Celkem | 10,5 | 30 | 0,5 | 21
LT= WIP /T (třetí sloupec je kvůli jednotkám)
Zadání (z předchozích snímků)
30 zákazníků/hodina – (max kapacita provozovny) = Throughput Rate = T
8 zákazníků čeká ve frontě (nárazník) = WIP
5 minut trvá doba obsluhy jednoho zákazníka = CT (Cycle Time)
2,5=TxLT=((30/60)*5)=(3*5)/6 , 10,5=8,0+2,5 a dále pak
LT=16=WIP/T=8/(3/6)= (8*6)/3=58/3=16 a 5=(2,5*(3/6))=2,5*6/3=15/3

## Slide 6: Otázky
Jak dlouho průměrně čeká zákazník ve frontě ?
Odpověď =16
Kolik průměrně lidí může být naráz obslouženo ?
Odpověď = 2,5
Kolik zákazníků je v provozovně v jenom okamžiku (jak čekající tak ty, které personál obsluhuje) ?
Odpověď = 10,5
Jaká je průměrná doba „průstupu“ zákazníka provozovnou (čekání i obsluha) ?
Odpověď = 21 minut

## Slide 7: Takt time (process capacity)= Cycle Time
Throughput Rate: kolik jednotek (výrobků) může linka vyrobit za určitý časový úsek
Takt Time : inverzní hodnota k Flow Time (což je jiný název pro T)
nebo také čas výroby jednoho ks výrobku na stroji – viz žluté Obdélníčky, který je úzkým místem bottleneck) – v našem případě stroj s časem 30, protože to trvá nejdéle !!!!
30 15 -> Takt Time=TT= Cycle Time = 30 minut
Takt Time = celkový dostupný čas, který je k dispozici/ zákaznický požadavek
Příklad : Požadavek 100 výrobků, 1 směna denně, 8 hodin směna, 5 dní v týdnů
Dostupný čas : 1 x 8 x 5=40 hod a požadavek je 100 , takže TT=0,4 hod =40/100
=24 minut a Thoughput Rate = 1/Takt Time = 1/0,4 =2,5 výrobku/hod

## Slide 8: Little´s law-2nd part
Skorkovský ,KPH,ESF.MU
Based on resource : Factory Physics (Hopp and Spearman)

## Slide 9: Little´s law - definition (formula)
Fundamental relationships among :
  WIP (Work In Process)
  Cycle Time (CT)
  Throughput (T or sometimes TH)
Formula
Can be applied to :
  Single machine station
  Complex production line
  Entire plant
WIP=TH x CT
Relationships among these variables will serve to se clearly precise (quantitative) description of behaviour of the single production line . It helps user to use a given scale to benchmark actual production systems

## Slide 10: Definition of basic parameters
Throughput (Throughput rate, TH) : production per unit time that is sold (see TOC definition)
If TH is measured in cost dollars rather 1than in prices, it is typically called :
Cost of good sold (COGS)
Upper limit of TH in production process is capacity
If you release more raw material above capacity of the line (machine), system become unstable –> WIP goes up !!

## Slide 11: Definition of basic parameters
WIP (Work In Process) : inventory between start and end points of the product routing
WIP can be used as one parameter to calculate (measure) an efficiency
Efficiency can be defined as Turnover Ratio = TH/FGI for warehouses or TH/(FGI+WIP) for production plants where FGI=Finished goods inventory
WIP : inventory still in line
FGI : inventory waiting for dispatch (shipping)

## Slide 12: Definition of basic parameters
CT (Cycle Time or so called Throughput Rate) : average time from release of the job of the beginning of the routing until it reaches an inventory point at the end of the routing or time that part spends as a WIP.
LT (Lead Time) : managerial constant used for planning of production
Service Level (especially for MTO lines, where plant have to satisfy orders with specific due dates) :
Service level P{Cycle time=<Lead Time}

## Slide 13: Definition of basic parameters
Where
  Arrival Rate =r = amount of parts arriving to workstation per time unit
  Effective production time is maximum average rate at which the workstation can process parts (considering effects of failures, setup times and so on)
Bottleneck rate (see TOC)
  rb = rate (parts per unit time or jobs per unit time) of workstation having the highest long term utilization
Utilization U(x) = Arrival rate / Effective production rate

## Slide 14: Definition of basic parameters
T₀ =Row process time of the line is the sum of the long –term average process time of each workstation in the line (single job entering empty line from staring point to the ending one)
7, 8, 9, 7, 6, 10
7,83
5,3, 4, 5, 6, 8
5,16
9, 8, 4, 5, 5, 6
6,1
19,16=7,83+5,16+6,1

## Slide 15: Definition of basic parameters
Critical WIP (W₀) of the line is the WIP level for which a line with given values of rb (bottleneck rate) and T₀ achieves maximum throughput ( rb ) with minimum cycle time (which is in this case T₀ )
W₀ = rb xT₀
WIP=TH x CT
Poznámka vyučujícího : problém s reprezentací algoritmu je např. ten, že v různé literatuře
se využívá jiné označení proměnných. Principy jsou samozřejmě identické.

## Slide 16: Use of defined parameters (home study)
Simple production line that makes giant one-cent pieces
It is as a model very with unrealistic assumption because process times are deterministic (no waiting times after every operation and no queue times before any other operation, 24 hours /day an unlimited market) balanced line
Any machine can be regarded as the bottleneck (one half part per hour=0,5 )
Head stamping
Tail stamping
Rimming
Deburring
2 h
2 h
2 h
2 h
  rb = bottleneck rate (parts per unit time or jobs per unit time) of workstation having the highest long term utilization =0.5 penny per hour, which means 24 hour x 0.5=12 pennies /day
T₀ =Row process time of the line is the sum of the long –term average process time of each workstation in the line = 8 hours=2+2+2+2=8
Critical WIP (W₀) of the line is the WIP level for which a line with given values of rb and T₀ achieves maximum throughput ( rb ) with minimum cycle time (which is in this case T₀ ) = rb x T₀ = 0.5 x 8 = 4 pennies
1
2
3
4

## Slide 17: Use of defined parameters (home study)
Head stamping
Tail stamping
Deburring
2 h
5 h
10 h
3 h
Tail stamping
Rimming
Rimming
Rimming
Rimming
Rimming
Rimming
Deburring
Station number | Number of machines | Process time (hours) | Station capacity (jobs per hour)
1 | 1 | 2 | 0.5=(1/2)*1
2 | 2 | 5 | 0.4=(1/5)*2
3 | 6 | 10 | 0.6=(1/10)*6
4 | 2 | 3 | 0.67=(1/3)*2
Bottleneck= rb =0,4
It is neither the station that contains the slowest
machines nor the one with fewest machines !!!
T₀ =Row process time of the line =2+5+10+3 =20 and
Critical WIP(W₀) =rb x T₀ = 0.4 x20 = 8 pennies <number of machines (11). This is because system is not balanced.
Not balanced line is the line where some stations are not fully utilized !!!
1
2
3
4

## Slide 18: Best case performance I (home study)
WIP=1, Total cycle time= T ₀=8=CT,
Throughput=1/8=part/hour= rb/4=0,125,
Bottleneck rate = rb=0,5=4*0,125
WIP=3
WIP=4
t=0
t=2
t=4
t=6
t=1
t=2
t=4
t=6
WIP=2, Total cycle t ime= T ₀=8=CT
Throughput=WIP/CT=WIP/T ₀= 2/8=part/hour= rb/2=0,250, což je
50 % of rb where bottleneck rate = rb=0,5
WIP=3, Total cycle time= T ₀=8=CT,
Throughput=WIP/CT=WIP/T ₀= 3/8=part/hour
= 0,375, což je 75 % of rb where bottleneck rate = rb=0,5
t=8
Text on the next slide
time
time

## Slide 19: Best case performance II (home study)
t=1
t=2
t=4
t=6
t=8
WIP=4
All stations stay busy all the time. Because no waiting so T ₀=8 h., rb=0,5 .
So minimum value of T ₀ an maximum value of rb (throughput) is achieved only if
WIP is set to critical value !
Critical WIP (W₀) of the line is the WIP level, for which a line with given values of rb and T₀ achieves maximum throughput ( rb ) with minimum cycle time (which is in this case T₀ ), so WIP (W₀) = rb x T₀ = 0.5 x 8 = 4 pennies- on the next slide se red line
T₀ =Row process time of the line is the sum of the
long –term average process time of each workstation
in the line (single job entering empty line from staring point
to the ending one)

## Slide 20: Best case performance III (home study)
20 hours = 12 hours waiting before line and 8 hours processing
All machines remains busy so rb=0,5 (2 hours per processing one penny)
% T₀ =(CT/ T₀) *100, so e.g. 250=(20/8)*100
% rb =((WIP/ T₀)/0,5)*100, where rb=0,5
Explanation : Max rb=0,5 so if WIP=5, then T₀ =5/0,5=10,
If WIP=6, then T₀=6/0,5=6/(5/10)=12 and so on
Parameters : | 100 % rb=0,5 |  |  | 
WIP | CT=T₀ | % T₀ | TH=Throughput | % rb
1 | 8 | 100 | 0,125=1/8 | 25
2 | 8 | 100 | 0,25=2/8 | 50
3 | 8 | 100 | 0,375=3/8 | 75
4 | 8 | 100 | 0,5=4/8 | 100
5 | 10 | 125 | 0,5=5/10 | 100
6 | 12 | 150 | 0,5=6/12 | 100
7 | 14 | 175 | 0,5=7/14 | 100
8 | 16 | 200 | 0,5=8/16 | 100
9 | 18 | 225 | 0,5=9/18 | 100
10 | 20 | 250 | 0,5=10/20 | 100
Table 1.

## Slide 21: Best case performance IV

## Slide 22: Conclusion
Close examination of Table 1 reveals fundamental relationship among WIP, CT and TH (throughput)
At every WIP level WIP is equal to the product of TH and CT (cycle time)
This relation is known as Little´s law.
WIP=TH * CT
Source : Factory Physiscs, Wallace J Hopp and Mark L. Spearman ; ISBN 13: 978-1-57766-739-1 or ISBN 10 :1-57766-739-5
http://www.factoryphysics.com/principle/littleslaw.htm

## Slide 23: Example 1
Estimating Waiting Times: If are in a grocery queue behind 10 persons and estimate that the clerk is taking around 5 minutes/per customer, we can calculate that it will take us 50 minutes (10 persons x 5 minutes/person) to start service.
This is essentially Little's law. We take the number of persons in the queue (10) as the "inventory".
The inverse of the average time per customer (1/5 customers/minute) provides us the rate of service or the throughput.
Finally, we obtain the waiting time as equal to number of persons in the queue divided by the processing rate 10/(1/5) = 50 minutes).
(home study

## Slide 24: Example 2
Planned Inventory Time: Suppose a product is scheduled so that we expect it to wait for 2 days in finished goods inventory before shipping to the customer. This two days is called planned inventory time and is sometimes used as protection against system variability to ensure high delivery service. Using Little's law the total amount of inventory in finished goods can be computed as :
FGI = throughput × planned inventory time
(home study)

## Slide 25: Youtube examples (6 minutes)
http://www.youtube.com/watch?v=VU8TUSnQ-vw
http://www.youtube.com/watch?v=rtGihR-bm-U