## Slide 1: Littlův zákon-základy
Ing. J.Skorkovský,CSc.
KPH-ESF-MU BRNO

## Slide 2: Používané vstupní veličiny I.
Lead time (LT) – průběžný čas-většinou konstantní . Jeho hodnota představuje kvalifikovaný odhad

## Slide 3: Používané vstupní veličiny II.
Flow time: Časový interval vymezující určující začátek a konec dílčího procesu (např. operace obrábění hřídele nebo oholení zákazníka) .
Někdy se tento čas nazývá procesní čas.
Pokud můžete procesem projít po různých cestách, pak flow time je čas strávený na nejdelší cestě ze všech možných variant.

## Slide 4: Používané vstupní veličiny III.
Cycle time = průměrný čas od zahájení „jobu“, (projektu, operace na strojním centru) do doby, než součástka, (obsloužený zákazník, úkol-task projektu-jobu) operaci opustí
V různých zdrojích věnujících se Littlovu zákonu někdy dochází k tomu, že CT=FT

## Slide 5: Konstatování
Je velice podstatné, aby všechny tři používané veličiny Littlova zákona byly přesně definovány, což umožní jeho lepší pochopení.
LZ je součástí teorie front

## Slide 6: Different times used in Little´s law
Lead time (LT)
Flow time (FT)
Cycle time (CT)
It is absolutely essential to define precisely above mentioned times in order to better understand principles of Little´s law
WIP=TH x CT

## Slide 7: Další dvě veličiny
WIP= Work in Process (Work in Progress)- nedokončená výroba
TH=Throughput=Throughput Rate = Průtok= =kolik dílců (zákazníků) zpracuje jednotka (stroj, holič, obsluha bankovní přepážky, obslužné místo,....) za definovanou jednotku času (minuta, hodina, atd.)

## Slide 8: Littlův zákon (teorém)
WIP=TH x CT
Zákon je součástí teorie front. .

## Slide 9: Definitions (anglická varianta definic)
CT=average time from when the job is released into station (machine) or line to when it exits
LT=management constant indicating the time allotted for production of a part on a given routing
CT =FT (in different publications they use FT instead of CT)
CT=Throughput Time (in different publications they use Throughput Time instead of CT)

## Slide 10: Běžná situace, kterou je potřeba řešit
30 zákazníků/hodina – (maximální kapacita provozovny) =Průtok
8 zákazníků čeká ve frontě (nárazník=buffer) = WIP=NV
5 minut trvá doba obsluhy jednoho zákazníka=CYCLE Time
Je potřeba odstranit všechny časy, které nepřinášejí hodnotu
1 obslužné místo=12 zákazníků za hodinu (60/5=12), takže pro 30 zákazníků/hodinu je potřeba kapacita 2,5 =30/12 obslužného místa, tedy 2,5 obslužných míst
8 zákazníků
čeká ve frontě
5 minut/obsluha 1 zákazníka
na jednom obslužném místě

## Slide 11: Otázky
Jak dlouho průměrně čeká zákazník ve frontě ?
Kolik průměrně lidí může být naráz obslouženo ?
Kolik zákazníků je v provozovně v jenom okamžiku (jak čekající, tak ti, které personál obsluhuje) ?
Jaká je průměrná doba „průstupu“ (průtoku) zákazníka provozovnou (čekání i obsluha)
Zjednodušující podmínky
  „Vstupní tok“ (průměr) =„Výstupní tok“ (průměr)
  Díky průměrování neuvažujeme fluktuaci (viz hody mincí)

## Slide 12: Klíčová měřítka a proměnné (doplnění definic)
CT =Cycle Time (jak dlouho trvá celý proces) =5
Work in Process = WIP (kolik jednotek je v procesu= nedokončená výroba=Work In Progress)
Throughput =TH (počet zákazníků/jednotka času) – např. 30/hod (naše zadání)
Tyto měřítka jsou propojena Littlovým zákonem WIP=TH x CT
Náš příklad : TH=30 zákazníků/hod, obsluha jednoho je 5 minut, WIP=(30/60) *(5/1)=(1/2)*5 =2,5 –kapacita obslužného místa
WIP
Cycle Time

## Slide 13: Řešení (home study)
Proces | WIP | TH (Zák/hod) | CT
Buffer | 8 | 30 | 
Obsluha |  | 30 | 5
Celkem |  | 30 | 
Proces | WIP | TH (Zák/hod) | CT (min/Zák) | Time
Buffer | 8 | 30 | 5 | 
Obsluha |  | 30 | 5 | 5
Celkem |  | 30 | 5 | 
Proces | WIP | TH (Zák/hod) | CT(min/Zák) | Time
Buffer | 8 | 30 | 5 | 
Obsluha | 2,5 | 30 | 5 | 5
Celkem | 10,5 | 30 | 5 | 
WIP =TH x CT
Proces | WIP | TH(Zák/hod) | CT (/min/Zák) | Time
Buffer | 8 | 30 | 5 | 16
Obsluha | 2,5 | 30 | 5 | 5
Celkem | 10,5 | 30 | 5 | 21
CT= WIP /TH (třetí sloupec je kvůli jednotkám)
Zadání (z předchozích snímků)
30 zákazníků/hodina – (max kapacita provozovny) = Throughput = TH
8 zákazníků čeká ve frontě (nárazník) = WIP =buffer- nárazník
5 minut trvá doba obsluhy jednoho zákazníka = CT
WIP = TH x CT=((30/60)*5)=(3*5)/6 = 2,5 , tedy kolik zákazníků naráz může být obslouženo a celkem jich je v provozovně 10,5=8,0+2,5 a dále pak :
CT= WIP /TH=8/(3/6)= (8*6)/3=48/3=16 (tak dlouho čeká zákazník ve frontě ) a nakonec pro kontrolu CT=5=(2,5/(3/6))=2,5*6/3=15/3=5 je doba obsluhy (už to bylo zadáno)

## Slide 14: Otázky
Jak dlouho průměrně čeká zákazník ve frontě ?
Odpověď =16
Kolik průměrně lidí může být naráz obslouženo ?
Odpověď = 2,5
Kolik zákazníků je v provozovně v jenom okamžiku (jak čekající tak ty, které personál obsluhuje) ?
Odpověď = 10,5
Jaká je průměrná doba „průstupu“ zákazníka provozovnou (čekání i obsluha) ?
Odpověď = 21 minut

## Slide 15: Little´s law-2nd part
Skorkovský ,KPH,ESF.MU
Based on resource : Factory Physics (Hopp and Spearman)

## Slide 16: Little´s law - definition (formula)
Fundamental relationships among :
  WIP (Work In Process)
  Cycle Time (CT)
  Throughput (T or sometimes TH)
Formula
Can be applied to :
  Single machine station
  Complex production line
  Entire plant
WIP=TH x CT
Relationships among these variables will serve to se clearly precise (quantitative) description of behaviour of the single production line . It helps user to use a given scale to benchmark actual production systems

## Slide 17: I finally figured it out !!!!
Avg.Lead Time =Cycle Time !!

## Slide 18: Daily application of the law….

## Slide 19: Definition of basic parameters (supplements) – home study
Throughput (Throughput rate, TH) : production per unit time that is sold (see TOC definition)
If TH is measured in cost dollars rather than in prices, it is typically called :
Cost of good sold (COGS)
Upper limit of TH in production process is capacity
If you release more raw material above capacity of the line (machine), system become unstable –> WIP goes up !! See later …

## Slide 20: Definition of basic parameters (supplements)
WIP (Work In Process) : inventory between start and end points of the product routing
WIP can be used as one parameter to calculate (measure) an efficiency
Efficiency can be defined as Turnover Ratio = TH/FGI for warehouses or TH/(FGI+WIP) for production plants where FGI=Finished goods inventory
WIP : inventory still in line
FGI : inventory waiting for dispatch (shipping)

## Slide 21: Definition of basic parameters (supplements)
CT (Cycle Time) or so called Throughput Rate) : average time from release of the job of the beginning of the routing until it reaches an inventory point at the end of the routing or time that part spends as a WIP.
LT (Lead Time) : managerial constant used for planning of production
Service Level (especially for M-T-O lines, where plant have to satisfy orders with specific due dates) :
Service level P{Cycle time=<Lead Time}

## Slide 22: Best case performance

## Slide 23: Resources
WIP=TH * CT
Source : Factory Physiscs, Wallace J Hopp and Mark L. Spearman ; ISBN 13: 978-1-57766-739-1 or ISBN 10 :1-57766-739-5
http://www.factoryphysics.com/principle/littleslaw.htm

## Slide 24: Example 1
Estimating Waiting Times: If are in a grocery queue behind 10 persons and estimate that the clerk is taking around 5 minutes/per customer, we can calculate that it will take us 50 minutes (10 persons x 5 minutes/person) to start service.
This is essentially Little's law. We take the number of persons in the queue (10) as the "inventory".
The inverse of the average time per customer (1/5 customers/minute) provides us the rate of service or the Throughput.
Finally, we obtain the waiting time as equal to number of persons in the queue divided by the processing rate 10/(1/5) = 50 minutes).
(home study)

## Slide 25: Example 2
Planned Inventory Time: Suppose a product is scheduled so that we expect it to wait for 2 days in finished goods inventory before shipping to the customer. This two days is called planned inventory time and is sometimes used as protection against system variability to ensure high delivery service. Using Little's law the total amount of inventory in finished goods can be computed as :
FGI = throughput × planned inventory time
(home study)

## Slide 26: Youtube examples (6 minutes)
http://www.youtube.com/watch?v=VU8TUSnQ-vw
http://www.youtube.com/watch?v=rtGihR-bm-U