## Slide 1: Basics of Statistical Process Control
Statistical Process Control (SPC)
  monitoring production process to detect and prevent poor quality
Sample
  subset of items produced to use for inspection
Control Charts
  process is within statistical control limits
UCL
LCL

## Slide 2: Variability
Random
  common causes
  inherent in a process
  can be eliminated only through improvements in the system
Non-Random
  special causes
  due to identifiable factors
  can be modified through operator or management action

## Slide 3: Quality Measures
Attribute
  a product characteristic that can be evaluated with a discrete response
  good – bad; yes - no
Variable
  a product characteristic that is continuous and can be measured
  weight - length

## Slide 4: Applying SPC to Service
Nature of defect is different in services
Service defect is a failure to meet customer requirements
Monitor times, customer satisfaction

## Slide 5: Applying SPC to Service
Hospitals
  timeliness and quickness of care, staff responses to requests, accuracy of lab tests, cleanliness, courtesy, accuracy of paperwork, speed of admittance and checkouts
Grocery stores
  waiting time to check out, frequency of out-of-stock items, quality of food items, cleanliness, customer complaints, checkout register errors
Airlines
  flight delays, lost luggage and luggage handling, waiting time at ticket counters and check-in, agent and flight attendant courtesy, accurate flight information, passenger cabin cleanliness and maintenance
Fast-food restaurants
  waiting time for service, customer complaints, cleanliness, food quality, order accuracy, employee courtesy
Catalogue-order companies
  order accuracy, operator knowledge and courtesy, packaging, delivery time, phone order waiting time
Insurance companies
  billing accuracy, timeliness of claims processing, agent availability and response time

## Slide 6: Where to Use Control Charts
Process has a tendency to go out of control
Process is particularly harmful and costly if it goes out of control
Examples
  at the beginning of a process because it is a waste of time and money to begin production process with bad supplies
  before a costly or irreversible point, after which product is difficult to rework or correct
  before and after assembly or painting operations that might cover defects
  before the outgoing final product or service is delivered

## Slide 7: Control Charts
A graph that establishes control limits of a process
Control limits
  upper and lower bands of a control chart
Types of charts
  Attributes
    p-chart
    c-chart
  Variables
    range (R-chart)
    mean (x bar – chart)

## Slide 8: Process Control Chart
1
2
3
4
5
6
7
8
9
10
Sample number
Upper
control
limit
Process
average
Lower
control
limit
Out of control

## Slide 9: Normal Distribution
=0
1
2
3
-1
-2
-3
95%
99.74%

## Slide 10: A Process Is in Control If …
… no sample points outside limits
… most points near process average
… about equal number of points above and below centerline
… points appear randomly distributed

## Slide 11: Control Charts for Attributes
p-charts
  uses portion defective in a sample
c-charts
  uses number of defects in an item

## Slide 12: p-Chart
UCL = p + zp
LCL = p - zp
z = number of standard deviations from process average
p = sample proportion defective; an estimate of process average
p = standard deviation of sample proportion
p =
p(1 - p)
n

## Slide 13: p-Chart Example
20 samples of 100 pairs of jeans
NUMBER OF PROPORTION
SAMPLE DEFECTIVES DEFECTIVE
1 6 .06
2 0 .00
3 4 .04
: : :
: : :
20 18 .18
200

## Slide 14: p-Chart Example (cont.)
UCL = p + z = 0.10 + 3
p(1 - p)
n
0.10(1 - 0.10)
100
UCL = 0.190
LCL = 0.010
LCL = p - z = 0.10 - 3
p(1 - p)
n
0.10(1 - 0.10)
100
= 200 / 20(100) = 0.10
total defectives
total sample observations
p =

## Slide 15: p-Chart Example (cont.)
0.02
0.04
0.06
0.08
0.10
0.12
0.14
0.16
0.18
0.20
Proportion defective
Sample number
2
4
6
8
10
12
14
16
18
20
UCL = 0.190
LCL = 0.010
p = 0.10

## Slide 16: c-Chart
UCL = c + zc
LCL = c - zc
where
c = number of defects per sample
c = c

## Slide 17: c-Chart (cont.)
Number of defects in 15 sample rooms
1 12
2 8
3 16
: :
: :
15 15
190
SAMPLE
c = = 12.67
190
15
UCL = c + zc
= 12.67 + 3 12.67
= 23.35
LCL = c + zc
= 12.67 - 3 12.67
= 1.99
NUMBER
OF
DEFECTS

## Slide 18: c-Chart (cont.)
3
6
9
12
15
18
21
24
Number of defects
Sample number
2
4
6
8
10
12
14
16
UCL = 23.35
LCL = 1.99
c = 12.67

## Slide 19: Control Charts for Variables
Mean chart ( x -Chart )
  uses average of a sample
Range chart ( R-Chart )
  uses amount of dispersion in a sample

## Slide 20: x-bar Chart
x =
x1 + x2 + ... xk
k
=
UCL = x + A2R LCL = x - A2R
=
=
where
x = average of sample means
=

## Slide 21: x-bar Chart Example
Example 15.4
OBSERVATIONS (SLIP- RING DIAMETER, CM)
SAMPLE k 1 2 3 4 5 x R
1 5.02 5.01 4.94 4.99 4.96 4.98 0.08
2 5.01 5.03 5.07 4.95 4.96 5.00 0.12
3 4.99 5.00 4.93 4.92 4.99 4.97 0.08
4 5.03 4.91 5.01 4.98 4.89 4.96 0.14
5 4.95 4.92 5.03 5.05 5.01 4.99 0.13
6 4.97 5.06 5.06 4.96 5.03 5.01 0.10
7 5.05 5.01 5.10 4.96 4.99 5.02 0.14
8 5.09 5.10 5.00 4.99 5.08 5.05 0.11
9 5.14 5.10 4.99 5.08 5.09 5.08 0.15
10 5.01 4.98 5.08 5.07 4.99 5.03 0.10
50.09 1.15

## Slide 22: x- bar Chart Example (cont.)
UCL = x + A2R = 5.01 + (0.58)(0.115) = 5.08
LCL = x - A2R = 5.01 - (0.58)(0.115) = 4.94
=
=
x = = = 5.01 cm
=
x
k
50.09
10
Retrieve Factor Value A2

## Slide 23: x- bar Chart Example (cont.)
UCL = 5.08
LCL = 4.94
Mean
Sample number
|
1
|
2
|
3
|
4
|
5
|
6
|
7
|
8
|
9
|
10
5.10 –
5.08 –
5.06 –
5.04 –
5.02 –
5.00 –
4.98 –
4.96 –
4.94 –
4.92 –
x = 5.01
=

## Slide 24: R- Chart
UCL = D4R LCL = D3R
R =
R
k
where
R = range of each sample
k = number of samples

## Slide 25: R-Chart Example
OBSERVATIONS ()
SAMPLE k 1 2 3 4 5 x R
1 5.02 5.01 4.94 4.99 4.96 4.98 0.08
2 5.01 5.03 5.07 4.95 4.96 5.00 0.12
3 4.99 5.00 4.93 4.92 4.99 4.97 0.08
4 5.03 4.91 5.01 4.98 4.89 4.96 0.14
5 4.95 4.92 5.03 5.05 5.01 4.99 0.13
6 4.97 5.06 5.06 4.96 5.03 5.01 0.10
7 5.05 5.01 5.10 4.96 4.99 5.02 0.14
8 5.09 5.10 5.00 4.99 5.08 5.05 0.11
9 5.14 5.10 4.99 5.08 5.09 5.08 0.15
10 5.01 4.98 5.08 5.07 4.99 5.03 0.10
50.09 1.15
Example 15.3

## Slide 26: R-Chart Example (cont.)
Example 15.3
R
k
R = = = 0.115
1.15
10
UCL = D4R = 2.11(0.115) = 0.243
LCL = D3R = 0(0.115) = 0
Retrieve Factor Values D3 and D4

## Slide 27: R-Chart Example (cont.)
UCL = 0.243
LCL = 0
Range
Sample number
R = 0.115
|
1
|
2
|
3
|
4
|
5
|
6
|
7
|
8
|
9
|
10
0.28 –
0.24 –
0.20 –
0.16 –
0.12 –
0.08 –
0.04 –
0 –

## Slide 28: Using x- bar and R-Charts Together
Process average and process variability must be in control
It is possible for samples to have very narrow ranges, but their averages is beyond control limits
It is possible for sample averages to be in control, but ranges might be very large

## Slide 30: Control Chart Patterns
UCL
LCL
Sample observations
consistently above the
center line
LCL
UCL
Sample observations
consistently below the
center line

## Slide 31: Control Chart Patterns (cont.)
LCL
UCL
Sample observations
consistently increasing
UCL
LCL
Sample observations
consistently decreasing

## Slide 32: Process Capability
Tolerances
  design specifications reflecting product requirements
Process capability
  range of natural variability in a process what we measure with control charts

## Slide 33: Process Capability
(b) Design specifications and natural variation the same; process is capable of meeting specifications most of the time.
Design Specifications
Process
(a) Natural variation exceeds design specifications; process is not capable of meeting specifications all the time.
Design Specifications
Process

## Slide 34: Process Capability (cont.)
(c) Design specifications greater than natural variation; process is capable of always conforming to specifications.
Design Specifications
Process
(d) Specifications greater than natural variation, but process off center; capable but some output will not meet upper specification.
Design Specifications
Process