## Slide 1: Basic production algorithms and its main concepts- first part Příklad na výrobu – druhá část
Ing.J.Skorkovský,CSc.
Department of Corporate Economy
Slides 2-28 –basic production theory in English and 29-48 practical NAV example (Czech)
Comment : without basic production theory it is useless to model production in ERP
První sekce slouží k teoretické přípravě. Druhá je klasický výrobní příklad,
který navazuje na materiál ve Wordu : 22_Příklad na výrobu_20201024

## Slide 2: Main concepts
MRP=Material Requirements Planning (push)
MRP_II=Manufacturing Resource Planning (push)
APS = Advanced Planning and Scheduling
JIT = Just In Time (pull)
TOC (Drum Buffer Rope) (push-pull->combined)
Bylo prezentováno v letním semestru BPH_PIS1)
Work Order=Production order in MS Dynamics NAV
Výrobní zakázka

## Slide 3: BOM=Bill Of Material (structure of the product)
A
100
300
400
200
B
500
300
600
100
300
400
Component
Product|Semiproduct
0
1
2
3
Independent demand (nezávislý požadavek) for products and semi-products and dependent for components
Planning backwards from production schedule (independent) to dependent- demand components – (závislé požadavky) without statistically calculated Reorder Point (ROP)– (Reorder Point =Bod přiobjednání) see next lesson and next slide as well
IF ROP is not taken into consideration – MRP is PUSH system -> it computes schedule of what should be started (pushed) into system, that authorize production as inventory is consumed (ROP will be explained later in this session)
0,1,2,,..Low Level Codes
BOM-Kusovník

## Slide 4: Push system
Supplier1
Supplier 2
MRP|ERP
Operation 1
Operation 2
Operation 3
Operation 4
Customer 1
Customer 2
FG warehouse
Component
warehouse
Forecast
Purchase orders
ROUTING
WIP
WIP
Take it !
WIP

## Slide 5: PUSH and PULL
PUSH : production jobs (production orders) are scheduled: MRP and MRP_II= Manufacturing Resource Planning
  often not feasible plans are generated and problems are often detected too late (rejects=neshody=zmetky), lack of components)
  used fixed lead times=LT (see next slide) do not depend on capacity utilization (LT=Průběžný čas)
  Having in mind , that production is random process, Lead Time is very pessimistic constant (invariable).
PULL : production jobs (production orders) starts are triggered by completion of another job (JIT-see later in this session)
Black box
t=start of the job
t+LT=end time of the job (where LT=constant)

## Slide 6: Determination of the Reorder Point (ROP)
ROP=expected demand during lead time + safety stock
20
50=ROP
50-20=30
LT =Lead time – Průběžný čas
Expected demand=30
Bod přiobjednání
(home study)

## Slide 7: Determination of the Reorder Point (ROP) (home study)
ROP = expected demand during lead time + z* σdLT
where z = number of standard deviations and
σdLT = the standard deviation of lead time demand and z* σdLT =Safety Stock
aan

## Slide 8: Example (home study- also Pareto analysis and ABC model simplified- PWP will be shown later)
The manager of a construction supply house determined knows that demand for sand during lead time averages is 50 tons.
The manager knows, that demand during lead time could be described by a normal distribution that has a mean of 50 tons and a Standard Deviation of 5 tons (σdLT )
The manager is willing to accept a stock out risk of no more than 3 percent

## Slide 9: Example-data (home study)
Expected lead time averages = 50 tons.
σdLT = 5 tons
Risk = 3 % max
Questions :
  What value of z (number of standard deviations) is appropriate?
  How much safety stock should be held?
  What reorder point should be used?

## Slide 10: Example-solution (home study)
Service level =1,00-0,03 (risk) =0,97 and from probability tables you will get z= +1,88
See next slide with probability table

## Slide 11: Probability table
(home study)

## Slide 12: Example-solution (home study)
Service level =1,00-0,03 =0,97 and from probability tables we have got : z= +1,88
Safety stock = z * σdLT = 1,88 * 5 =9,40 tons
ROP = expected lead time demand + safety stock = 50 + 9.40 = 59.40 tons
For z=1 service level =84,13 %
For z=2 service level= 97,72 %
For z=3 service level = 99,87% (see six sigma)

## Slide 13: Schematic of MRP
BOM
On-hand inventory
Scheduled receipts
MPS
MPS=Master Production Schedule
Netting – Lot Sizing –Time Phasing –BOM Exploding
Production
Orders (jobs)
Purchase
orders
Exception and change notices
Net requirement =Gross requirement – Stock in hand – Purchases + Sales + Safety Stock
Čistý požadavek= Hrubý požadavek- Množství na skladě – Nákupy + Prodeje + Bezpečnostní zásoba
Lot sizing= divide netted demand into appropriate lot sizes to form jobs (see LLC) and EOQ PWP show (later)
Time Phasing = offset the due dates of the jobs with lead times to determine start times
(Due Date-Lead time = Start of the job)

## Slide 14: MRP matrix calculation (see related xls file in study material)
Parameters
  Gross requirements (hrubý požadavek)
    Derivied from Master Production Scheduled or Planned order releases of the parent BOM (finished good)
  Scheduled receipts (vytvořené a dodavatelům zaslané objednávky)
    On order (issued) and scheduled to be received
  Projected on hand = Stock in Hand (stav na skladě)
    Anticipated quantity on hand at the end of the period
  Net requirement (čistý požadavek)
    Net requirement =Gross requirement – Stock in hand – Purchases + Sales + Safety Stock
  Planned order receipts (naplánované příjmy – např. ty v sešitu požadavků)
  When order need to be received (documents are not issued)
  Planned order releases
    When order need to be placed to be received on time
(home study)

## Slide 15: MRP matrix example 1
MRP basic calculations |  | Lot-for lot - ordering exact quntity needed |  |  |  |  |  |  |  |  |  | 
 |  | Lead Time =1 - time to get item from the moment the purchase order is issued or to make it |  |  |  |  |  |  |  |  |  | 
Master Production Schedule |  |  |  |  |  |  |  |  |  |  |  | 
Part A | Projected on hand | 1 | 2 | 3 | 4 | 5 |  |  |  |  |  | 
Gross Requirements |  | 85 | 95 | 120 | 100 | 100 |  |  |  |  |  | 
MRP |  |  |  |  |  |  |  |  |  |  |  | 
Part A |  | 1 | 2 | 3 | 4 | 5 |  |  |  |  |  | 
Gross Requirements |  | 85 | 95 | 120 | 100 | 100 |  |  |  |  |  | 
Scheduled Receipts | Is already issued | 175 |  |  |  |  |  |  |  |  |  | 
Projected on hand (POH) | 25 | 115 | 20 | 0 | 0 | 0 |  |  |  |  |  | 
Net requirements |  | 0 | 0 | 100 | 100 | 100 |  |  |  |  |  | 
Planned order receipts |  |  |  | 100 | 100 | 100 |  |  |  |  |  | 
Planned order releases |  |  | 100 | 100 | 100 |  |  |  |  |  |  | 
 |  | Period | Action |  |  |  |  |  |  |  |  | 
 |  | 1 | 25+175-85=115=POH |  |  |  |  |  |  |  |  | 
 |  | 2 | POH=115-95=20 |  |  |  |  |  |  |  |  | 
 |  | 3 | Cannot cover GR, so we have to release one PO for 100 one period earlier in order to get it in period 3 |  |  |  |  |  |  |  |  | 
 |  | 3 | Net req=120-20 =100, POH in period 3=120-20-100=0 |  |  |  |  |  |  |  |  | 
 |  | 4 | Net req =100-0=100-POH=100, so we heave to release one PO one period earlier in order to cover demand in period 4 |  |  |  |  |  |  |  |  | 
 |  | 5 | Similar to period 4 |  |  |  |  |  |  |  |  | 
(home study)
period
period

## Slide 16: MRP matrix example 2
MRP |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Part A |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |  |  |  | 
Gross Requirements |  | 20 | 30 | 50 | 50 | 60 | 90 | 40 | 60 |  |  |  |  | 
Scheduled Receipts | Is already issued |  | 50 |  |  |  |  |  |  |  |  |  |  | 
Projected on hand (POH) | 40 | 20 | 40 | 40 | 40 | 30 | 0 | 10 | 0 |  |  |  |  | 
Net requirements |  |  |  | 10 | 10 | 20 | 60 | 40 | 50 |  |  |  |  | 
Planned order receipts |  |  |  | 50 | 50 | 50 | 60 | 50 | 50 |  |  |  |  | 
Planned order releases |  | 50 | 50 | 50 | 60 | 50 | 50 |  |  |  |  |  |  | 
 |  | Period | Action |  |  |  |  |  |  |  |  |  |  | 
 |  | 1 | Can be covered from POH and new POH=40-20=POH-GR=20 |  |  |  |  |  |  |  |  |  |  | 
 |  | 2 | In period 2 GR can be covered by POH and SR, but next period where GR=50 will be not covered, so POR must be released in per 1 (LT=2) |  |  |  |  |  |  |  |  |  |  | 
 |  | 3 | We have got 50, POH=40, so altogether we have 90 nad after demand is covered only 90-50=40=POH |  |  |  |  |  |  |  |  |  |  | 
 |  | 3 | Net req=50-40=10 in order to cover demand in period 4, but we can released only 50 or more, so in period 2 another 50 is released |  |  |  |  |  |  |  |  |  |  | 
 |  | 4 | Demand is covered by receipt 50 and POH =10 but for the next period net req=60-40=20 |  |  |  |  |  |  |  |  |  |  | 
 |  | 5 | Net req= 60-40=20, so demand in period 5 can be covered by POH=40+ quantity X, which have to be ordered 2 period earlier |  |  |  |  |  |  |  |  |  |  | 
 |  | 5 | Quantity X can 50 or more. So take it 50 as sufficient quantity, and POH =30=40+50-60 |  |  |  |  |  |  |  |  |  |  | 
 |  | 6 | To cover demand in period 6 we need at least 90 and we have only 30 in POH, so 90-POH=90-30=60 have to ordered 2 period earlier |  |  |  |  |  |  |  |  |  |  | 
 |  | 6 | POH-90-60-30=0; Ner req=90-30=GR-POH=60 , which is reason why we have ordered 60 two period earlier |  |  |  |  |  |  |  |  |  |  | 
 |  | 7 | Net req= 40 because 40-0=GR-POH=40. To cover it we have to order two period earlier 50 |  |  |  |  |  |  |  |  |  |  | 
 |  | 8 | and so on |  |  |  |  |  |  |  |  |  |  | 
(home study)

## Slide 17: Benefits of MRP
Low levels of in process inventories - Optimalizace stavu skladů- nižší skladové úrovně)
The Ability to keep track of material requirements
Schopnost lépe sledovat důvody doplňování
A means of allocating production time
Nástroj jak lépe alokovat komponenty v závislosti na výrobních časech
The ability to easily determine inventory usage by Back flushing (see explanation below) Process of determining the number of parts that must be subtracted from inventory records. This number is computed by referring to the number of parts withdrawn from the inventory (and delivered to the shop-floor) and the number of parts assumed (according to the BOM) to have been consumed in a manufacturing line at one or more deduct points- HOME STUDY Proces umožňující vypočítat množství komponent, které musí být odepsány ze skladu. Tento výpočet stojí na vzorci, který obsahuje jako proměnné množství komponent odepsaných ze skladu, komponent dodaných ze skladu do dílen a množství předpokládané spotřeby komponent na výrobní lince v jednom nebo více místech, kde je spotřeba zpětně registrována a to vždy v závislosti na konstrukci kusovník.- DOMÁCÍ STUDIUM

## Slide 18: MRP_II =MRP + resource capacity planning
Intermediate-range
planning
Short term
control
(Shop floor)
MPS
Demand
management
Rough-cut capacity planning
BOM
MRP
Scheduled
receipts
Job
Pool (planned)
Capacity requirement planning
Job Release
Routings
(operations)
Job
Dispatch
Dispatch=rozvrhování (na který stroj se dá která operace při dílenském řízení)
MPS= Master Production Schedule= Hlavní rozvrh výroby = Prognóza

## Slide 19: MPS –Hlavní rozvrh výroby

## Slide 20: MPS –Hlavní rozvrh výroby

## Slide 21: Kusovník (aplikace MPS)

## Slide 22: Karta výrobku (aplikace MPS)

## Slide 23: Sešit plánování výroba

## Slide 24: Sešit plánování výroba
Panel požadavků

## Slide 25: Sešit plánování výroba
Vytvoření výrobních
zakázek

## Slide 26: BOM in MS Dynamics NAV 2018
BOM-Bill of Material=Kusovník

## Slide 27: Routings in MS Dynamics NAV
Routing= TNG postup- Pracovní postup=Rozpis operací

## Slide 28: Calendar of machine center

## Slide 29: Zatížení strojního centra (Load)
Viz další snímek

## Slide 30: Capacity of resources in MS Dynamics NAV
Kapacity výrobních zdrojů (Pracovní centra a Strojní centra).
Pracovní centrum je seskupení jednoho nebo více strojních center.
Strojní centra jsou stroje nebo také dělníci.

## Slide 31: JIT=Just In Time
Toyota Motors and Taiichi Ohno
Production based only on demand
Lower inventory costs
The concept behind it is that a company can save money on parts and components---by not have having to store them--- if they are delivered to the assembly line just in time to be installed on the car as it is being built.

## Slide 32
Operation (Job1)
Authorization
to start Job 2
Controlling parameter
DOWNSTREAM
UPSTREAM
Operation (Job2)
Operation (JobN)
Components for Job N needed…
1 (kanban = card=signal)
2
Components for Job N produced and
Supplied (pulled)
1
Production
=kanban
The number of kanban cards in the system determines the WIP levels in the plant
WIP= Work in Progress
JIT=Just In Time
Demand
Home study

## Slide 33: JIT (manufacturing philosophy)
Kanban is not JIT !!!
JIT encompasses (zahrnuje):
  kanban cards (kan=card, ban=signal)
  total quality control (TQM) – e.g. scrap loss not tolerated….( žádné zmetky)
  setup reduction (snížení nastavovacích časů)
  worker participation (větší zapojení dělníků)
  lean production (low level of waste) (nízká úroveň zmetků)
Advantages of JIT philosophy :
  reduced WIP (Work in Progress)->Higher Throughput (see Little´s law- will be presented later (BPH-PIS2 viz letní kurz BPH_PIS1 2020)
  shorter production times (zkrácení výrobních časů)
  lower production costs (nižší výrobní náklady)
  greater customer responsiveness (větší spokojenost zákazníků)
Home study

## Slide 34: Kanban principle
Resource :
(home study)

## Slide 35: Some time units (home study)
Will be presented later in sections such as :
  Little´s law (LT=WIP*CT=WIP/Throughput)
  Theory of Constraint
  Cycle Time (CT)– time to complete task (time/unit)
Takt Time (TT) – rhythm in which we have to produce in order to satisfy customer demand (demand is 240 toaster ovens and we can produce these in 480 minutes ->TT= 480/240=2
Lead Time (LT) – Number of minutes, hours, or days that must be allowed for the completion of an operation or process, or must elapse before a desired action takes place –see next slide
Comment : CT<>LT !!

## Slide 36: Lead time – průběžný čas (home study)
The lead time is the time and not the effort. You may have a lead time of 100 days and only have to work 1 hour to fix the bug. Sometimes you start working on the bug. The cycle time is the time from the start of the work until the bugfix is fixed.
Cycle time
Lead time
Request
(bug reported)
Priority of the task
is set
Start work
Bug fixed
IDLE TIME

## Slide 37: Orders Tracking
Sales Order
Customer
Purchase Order
Sales Order Line
Demand
Požadavek
Planning production (MRP-II )
Tracking
Production Order
Bill of Material
Routing (OP1-OP4)
Technologický postup
Tracking
Requisition Worksheet (MRP)
Tracking
Supply
Supply
Doplnění zásob)
Tracking- Sledování
Stock
Vendor
Tracking
Sledování zakázky
Sešit požadavků
Sešit plánování výroby
(Navrhuje i nákupy-doplnění)

## Slide 38: Požadavek
Požadavek (Prodejní objednávka) bude na prodej Předního náboje 1150 (na skladě 200),
jehož kusovník se skládá ze dvou komponent 1151 (200 na skladě)
a 1155 (200 na skladě).
Příprava dat pro příklad : Změňte u obou komponent (1151 a 1155)
Způsob přiobjednání na Dávka-pro- dávku. Dále s pomocí deníku zboží prodejte 200 ks
výrobku 1150 a jeho komponent 1151 a 1155. Pozor : komponenty i výrobek
nejsou uloženy na žádné lokaci. Dále změňte na záložkách Doplnění
u obou komponent dodavatel na 10000.
Výsledkem požadavku bude naplánování Výrobní zakázky a její následné odhlášení
(komponenty do spotřeby a výrobek na sklad)

## Slide 39: Prodejní objednávka na 100 ks 1150
Dostaneme upozornění, že podsestava kola 1150 není na skladě !! Reakce->ANO
Dále změňte Plánované datum dodávky na datum 25.5. , tedy dostatečně daleko od pracovního data – Důvod : aby plánovací algoritmus nenaplánoval počátek výroby na datum před pracovním datem.
Prodejní řádek

## Slide 40: Plánovací sešit
Plánované datum dodávky (viz prodejní řádek)
je pro tuto databázi 4.5.2017. Do Čísla zboží zavedeme ručně Jak číslo výrobku tak i čísla komponent ->1150|1151|1155

## Slide 41: Naplánovaný řádek (výrobní zakázka)
Viz karta zboží,
záložka Doplnění
a pole Zmetky %

## Slide 42: Naplánovaný řádek (nákupní objednávka)

## Slide 43: Vytvoření VZ (pevně plánované-bude vysvětleno)

## Slide 44: Řádky nákupní objednávky

## Slide 45: Výrobní zakázka (VZ)
Podívejte se na Sledování zakázky : vazby mezi výrobou, nákupem a prodejem
Najdete to na ikoně Funkce v řádcích VZ

## Slide 46: Sledování zakázky
VZ<->PO
NO<->PO

## Slide 47: Zaúčtujte příjem komponent na NO

## Slide 48: Výrobní zakázka-komponenty a TNG postup
(TNG= Technologický)
Řádek VZ->Komponenty
Řádek VZ->TNG postup

## Slide 49: Statistika VZ (s pomocí F7)

## Slide 50: Převedení do stavy VZ Vydaná (od plánovače do dílny)

## Slide 51: Odhlášení spotřeby a zdrojů
V řádku VZ vydané, kde je ikona Řádek najdete Deník výroby
Zadejte odhadnutou dobu seřízení a zpracování včetně spotřeby materiálu.
Zadané hodnoty by se neměly lišit od TNG postupu uvedeného pře několika snímky.
Na dalším obrázku to zobrazíme ještě jednou pro ulehčení zadávání hodnot do
Výrobního deníku. Zde se často používají dotykové obrazovky a BAR čtečky

## Slide 52: Deník výroby po vyplnění
Záměrně byly některé časy změněny- reálné časy nemusí přesně odpovídat plánu.

## Slide 53: Statistika VZ po zaúčtování deníku

## Slide 54: Položky VZ po zaúčtování (VZ->Ctrl-F7)

## Slide 55: Věcné položky po změně stavu VZ- >Dokončená
Spotřeba a účtování NV (nedokončená výroba)

## Slide 56: Věcné položky po změně stavu VZ- >Dokončená
Naskladnění výrobku a deaktivace NV

## Slide 57: Karta výrobku

## Slide 58
Konec sekce
Děkuji za pozornost !!