## Slide 1: Product mix and TOC

## Slide 2
P (50)
Q (50)
R (55)
S (52)
Machine A (6)
Machine A (8)
Machine A (10)
Machine B (10)
Machine A (5)
Machine A (5)
Machine B (20)
RM=5
RM=10
RM=10
RM=10
RM=5
RM=5
RM=5
8 hours /day=480 min, cost/hour/resource=10 USD
To produce P or Q->20 minutes of B (bottleneck)
To produce R or S->30 minutes of B (bottleneck)
Product | Price | Material | Work (min USD) | Profit
P | 50 | 20 | 36 min (6 USD) | 50-20-6=24
Q | 50 | 25 | 38 min (6,33 USD) | 50-25-6,33=18,67
R | 55 | 25 | 35 min (5,83 USD) | 55-25-5,83=24,17
S | 52 | 20 | 35 min (5,83 USD) | 52-20-5,83=26,17
Based on Prof. James R. Holt, Washington State University
Two workers are always needed
to produce each of the four products

## Slide 3: Four different approaches how to solve the product mix

## Slide 4: Classic approach – highest margin (accountant) – S product
52*16 pcs - 20*16 pcs - 2 workers*8 hours*10 USD/hour = 352 USD/day
Where 16= 480/30=16 = 480/(20+10)
20+ 10 is capacity of machine B to produce S
Machine B (10)
Machine B (20)
Product | Price | Material | Work (min USD) | Profit
P | 50 | 20 | 36 min (6 USD) | 50-20-6=24
Q | 50 | 25 | 38 min (6,33 USD) | 50-25-6,33=18,67
R | 55 | 25 | 35 min (5,83 USD) | 55-25-5,83=24,17
S | 52 | 20 | 35 min (5,83 USD) | 52-20-5,83=26,17

## Slide 5: Marketing approach – highest selling price R product
55*16 pcs - 25*16 pcs - 2 workers*8 hours*10 USD/hour = 320 USD/day
Where 16= 480/30=16 = 480/(20+10)
20+ 10 is capacity of machine B to produce R
Product | Price | Material | Work (min USD) | Profit
P | 50 | 20 | 36 min (6 USD) | 50-20-6=24
Q | 50 | 25 | 38 min (6,33 USD) | 50-25-6,33=18,67
R | 55 | 25 | 35 min (5,83 USD) | 55-25-5,83=24,17
S | 52 | 20 | 35 min (5,83 USD) | 52-20-5,83=26,17

## Slide 6: Production approach – highest machine efficiency Q product
50*24 pcs - 25*24 pcs - 2 workers*8 hours*10 USD/hour = 440 USD/day
Where 24= 480/ 20 (the quantity of the product)
20 is capacity of machine B to produce Q
Machine B (20)
Product | Price | Material | Work (min USD) | Profit
P | 50 | 20 | 36 min (6 USD) | 50-20-6=24
Q | 50 | 25 | 38 min (6,33 USD) | 50-25-6,33=18,67
R | 55 | 25 | 35 min (5,83 USD) | 55-25-5,83=24,17
S | 52 | 20 | 35 min (5,83 USD) | 52-20-5,83=26,17

## Slide 7: TOC approach – highest use of bottleneck P product
50*24 pcs - 20*24 pcs - 2 workers*8 hours*10 USD/hour = 560 USD/day
Where 24= 480/ 20
20 is capacity of machine B to produce P product
Product | Price | Material | Work (min USD) | Profit
P | 50 | 20 | 36 min (6 USD) | 50-20-6=24
Q | 50 | 25 | 38 min (6,33 USD) | 50-25-6,33=18,67
R | 55 | 25 | 35 min (5,83 USD) | 55-25-5,83=24,17
S | 52 | 20 | 35 min (5,83 USD) | 52-20-5,83=26,17

## Slide 8: Results
Accounting approach S $352 100%
Sales-Higher Sales Price R $320 90%
Production-Efficiency Q $440 125%
TOC approach P $560 159%