## Slide 1: Appraisal of transport projects – the British approach
Chris Nash

## Slide 2: Outline
Development of appraisal methods
Current approach
Key issues
- Appraisal optimism
-Value of time
-Value of environmental impacts
-Wider Economic Benefits
-Scarcity of investment funds

## Slide 3: Transport Appraisal in the 1960s
Pioneering studies of the Victoria Line (London Underground) and the M1 Motorway
By the end of the 1960s, cost benefit analysis routinely applied to main road schemes (financial appraisal the norm on rail, although the Cambrian Coast study was a pioneering study of a rail closure)

## Slide 4: Transport Appraisal in the early 1970s
Solely concerned with economic efficiency – simply presented an NPV
Nothing about who gained and who lost
Concentrated on construction and maintenance costs, time and accident savings: neglect of environment, planning and wider economic impact
10% discount rate and 30 year horizon so emphasis on the short run
Much criticised as narrow and mechanistic

## Slide 5: The Leitch report (1977)
Framework approach
Nested CBA in a broader multi criterion approach in which much material (e.g. environmental impacts) was presented in physical rather than in money terms
Problem of volume of information; no formal way of trading off costs and benefits expressed in different units

## Slide 6: New Approach to Transport Appraisal (NATA) 1998
Revised the framework
To be applied to all decisions:
Road investment
Public transport investment
Subsidies
Move to 3.5% discount rate and 60 year time horizon

## Slide 7: NATA objectives
Environment
Economy
Safety
Accessibility
Integration
Now replaced by a simple grouping of impacts into
Economic, Environmental, Social and Government Finance

## Slide 8: Current approach in WebTAG (Web based transport analysis guidance)
Based on Treasury Green Book (2020)
5 cases approach to appraisal
- Strategic case
Economic case
Commercial case
Financial case
Management case.

## Slide 9: The Treasury Green Book: Appraisal and Evaluation in Central Government
The purpose of the Green Book is to ensure that no policy, programme or project is adopted without first having the answer to these questions:
❑ Are there better ways to achieve this objective?
❑ Are there better uses for these resources?
Thus a shortlist of alternatives must be appraised.
The shortlist must always include the ‘do minimum’ option
(note – this may be problematic for instance if traffic is growing fast)

## Slide 10: British transport appraisal guidelines (www.dft.gov.uk/webtag)
- All projects should be compared with a do minimum base case
Forecasts need to be made of costs and benefits throughout the life of the project (assumed to be 60 years in the case of major transport infrastructure but DfT caps benefits after 20 years)
As far as possible all costs and benefits should be valued in money terms
All costs and benefits should be discounted back to the present using a discount rate of 3.5% for the first 30 years and then 3% after that
A benefit cost ratio is then calculated as the ratio of benefits minus costs to all excluding the government over net government transport funding

## Slide 11: WebTAG and appraisal systems worldwide
  International context:
  many other countries have similar appraisal practice and guidance
      e.g. Netherlands, Sweden, Germany, USA, NZ, Australia (NSW), France, Denmark, Canada, Japan ...
      international comparisons: see ITS (2013)
  international level:
      EU: DG REGIO CBA guide (2014) ; DG Mobility & Transport ‘HEATCO’ guidelines (2006); Handbook on External Costs (CE Delft, 2019)
      The World Bank (2005) http://go.worldbank.org/09MMD2C490

## Slide 12: Transport Economic Efficiency Table
User Benefits
(time, operating costs, user charges, delays during construction)
Private Sector Provider Impact
(revenues, costs, grants and subsidies)
Other Impacts
Net Business Impact
Total

## Slide 13: Notes
-Generated trips valued using ‘rule of a half’ i.e. given half the benefit figure of trips that would take place anyway.
-Users perceive costs and benefits in market prices (i.e. including tax). Government and firms perceive them at factor cost.
Need to use a common unit of account – conversion factor 1.19

## Slide 14: Public Accounts Table
Local Government Funding
Central Government Funding
(inc. impact on tax revenues)
Total

## Slide 15: Analysis of Monetarised Costs and Benefits Table (other monetised effects)
Noise
Local Air Quality
Greenhouse Gases
Journey Quality
Physical Activity
Accidents
NB Common values applied regardless of incomes
(equivalent of applying weights except for money costs – can have perverse impacts)
But values assumed to rise in proportion to GDP/head

## Slide 16: Appraisal summary table
Economy
Business users
Transport providers
Regeneration
Wider Impacts
Environmental
Noise
Air Quality Greenhouse gases
Landscape Townscape Historic Environment
Biodiversity
Water Environment

## Slide 17: Appraisal Summary Table CTD
Social
Commuting and Other users Time and Reliability
Accidents
Affordability
Option and non-use values
Public accounts
Cost to Broad Transport Budget
Indirect Tax Revenues

## Slide 18: Valuation of costs and benefits – key issues
Optimism bias
Value of time (esp business travel and small time savings)
Value of environmental impacts
Wider Economic Benefits
Scarcity of investment funds

## Slide 19: Optimism Bias
Recommended optimism bias uplifts for different projects at different stages of the life of a transport project
Stage 1 Stage 2 Stage 3
Roads 44% 15% 3%
Light rail, Metro 66% 40% 6%
Conventional rail 64% 18% 4%
Stage 1 Strategic appraisal
Stage 2 Outline business case
Stage 3 Full business case

## Slide 20: Values of Time for rail travellers per hour (2010 prices) DfT 2015
 |  |  | Previous | New | 
commuting |  |  | 6.81 | 10.01 | 
other leisure |  |  | 6.04 | 4.57 | 
Business |  |  | 31.96 | 36.19 | 
(>100km) |  |  |  |  | 

## Slide 21: Why do businesses value time savings so highly?
Ability to work effectively on the train should reduce value
But:
Ability to fit more meetings into a day
Reduced travel in unsocial hours
Better productivity at destination

## Slide 22: Values of Time for rail travellers per hour (£2010 market prices)
Commuting 9.95
Other non business 4.54
Business <50km 10.02
50-100km 16.21
100-200km 28.23
>200km 40.72

## Slide 23: Major changes
For working time, previously used the cost savings approach (wage rate plus overheads)
This was much criticised (people work whilst travelling; but they get other benefits from time savings – can do more work on a single visit, avoid an overnight stay etc)
Switched to valuing business time savings using willingness to pay studies
Values depend on length of trip – much higher for long distance trips

## Slide 24: Multipliers for waiting, walking and late time
Walking and waiting revised from 2.5 to 2
Late time revised from 3 to 2.4

## Slide 25: WHAT ELSE HAVE THE RAILWAYS VALUED?
Walking time (to and from station and at interchange)
Waiting time (at departure and at interchange)
Interchange penalties
Headway and Displacement Time
Reliability (Late arrivals and large delays)
Crowding (Standing time and crowded while seated)
Rolling stock improvements (new trains and specific attributes)
Station improvements, staffing and security
Information provision, purchasing and fare simplification
On-board facilities (e.g. catering, wi-fi, toilets, cleanliness)
Seating layout
See the Passenger Demand Forecasting Handbook

## Slide 26: Externalities
what are externalities?
  not part of user cost (GC) or producer costs
  externalities are effects for which no money compensation is paid
  occur where markets are absent (e.g. no market for clean air, so when an HGV pollutes the air no compensation is paid)
The challenge:
methods are needed to measure the value to people of these impacts so that they can be included in the CBA.

## Slide 27: Safety
Typical costs imposed by transport accidents:
  material damage†
  police and fire service costs†
  insurance administration†
  legal and court costs†
  medical and healthcare costs*
  lost economic output*
  pain, grief and suffering*
Cost per fatality, serious or slight injury

## Slide 28: Safety: Overall Casualty Values
Source: TAG Data Book (DfT, July 2017)

## Slide 29: Environment: Noise
UK Noise values:
benefit transfer from Birmingham study, 1997, gives UK values at 2002 prices
Source: Nellthorp, Bristow and Day, 2005/7

## Slide 30: Environment - air pollution damage and abatement costs (2010)
PM10 damage costs (£/household/1μg/m³) 92.7
NOx damage costs (£/tonne) 955
NOx abatement costs (£/tonne) 29000

## Slide 31: Values of carbon (£ per tonne of CO2e; 2010 prices)
2010 52.3
2020 60.7
2030 70.8
2040 136.6
2050 202.3

## Slide 32: How to value impact of diverting passengers from other modes?
Ideally use a multimodal model
If that is not possible, use diversion factors

## Slide 33: Diversion Factors (change in passenger km as a percentage of change in rail km) typical inter city values
Walk | -0.47
Cycle | -0.46
Car Driver | -26
Car Passenger | -20
Bus | -7.4
Total km travelled | 46
Source: WEBTAG

## Slide 34: Marginal external costs and indirect taxation (2010) (weighted mean for all roads and times of day)
 |  | cars | heavy goods vehicles |  | 
Congestion |  | 10.1 |  | 52.4 | 
Infrastructure |  | 0.1 |  | 9 | 
Accidents |  | 1.6 |  | 2.8 | 
Local Air Quality |  | 0.1 |  | 2.5 | 
Noise |  | 0.1 |  | 7 | 
Greenhouse gases |  | 0.9 |  | 3.8 | 
Other |  | 0 |  | 6.4 | 
Indirect taxation |  | -4.7 |  | -34.1 | 
Total |  | 8.2 |  | 49.7 | 

## Slide 35: Sources for previous table
Source:
Cars: Department for Transport (2017 TAG databook
Heavy Goods Vehicles Department for Transport (2009) Mode Shift Benefit Values: Technical Report
Note: values for heavy goods vehicles are estimated 2015 values in 2010 prices
Note: dominance of relief of congestion over environmental factors controversial

## Slide 36: Wider economic impacts
It is usually assumed that when a transport scheme attracts new economic activity to an area it is simply shifting it from somewhere else. But some additional benefits are now recognised.
1. Agglomeration externalities
  Productivity depends on effective density (i.e. accessibility to population) esp for business services
  (size of labour market
  Economies of scale in supply of services
  Speed of technological change)

## Slide 37: Wider economic benefits CTD
  2. Imperfect competition in output markets
  10% uplift in benefits (based on studies of price cost
  margins)
  3. Labour supply
Reduced commuting costs generate increased labour supply (people entering the market or longer hours)
Benefits of extra trips already estimated (but value to user depends on post tax income)
But government benefits from extra tax revenue
  (‘tax wedge’)

## Slide 38: Wider economic benefits CTD
4. Move to more productive jobs due to land use changes
If project attracts jobs to where productivity is higher.
Again net benefit is increased tax revenue.

## Slide 39: Two ways of dealing with scarcity of investment funds
Shadow price public funds
Compute the BCR (benefits per pound of government funds) and require a value significantly above 1
Britain currently does the latter

## Slide 40: Value for Money (VfM) and BCR Categories
For most projects, which impose a net cost on the Broad Transport Budget:
DfT (2017), Value for Money Framework

## Slide 41: Conclusions
British transport appraisal nests CBA within a wider assessment of impacts
It is state of the art on many issues e.g.
Value of time and environmental impacts
Wider economic impacts
But still much uncertainty on some issues
No formal method to combine quantitative and qualitative elements

## Slide 42: Questions for discussion
Are there important impacts still omitted from the British approach?
Is it possible to value safety and environmental effects in money terms?

## Slide 43: References
The general approach to appraisal of the British government is outlined in:
The Green Book (2020) - GOV.UK (www.gov.uk)
The current British DfT guidance on appraisal can be accessed via the TAG website Transport analysis guidance - GOV.UK (www.gov.uk)
Estimation of the new values of time is described at DepartmentforTransport(2015)Understanding_and_Valuing_Impacts_of_Transport_Investment
https://www.gov.uk/government/uploads/system/uploads/attachment_data/file/470998/Understanding_and_Valuing_Impacts_of_Transport_Investment.pdf

## Slide 44: References continued
Department of Business, Energy and Industrial Strategy (2021) Valuation of greenhouse gases: for policy appraisal and evaluation tps://www.gov.uk/government/publications/valuing-greenhouse-gas-emissions-in-policy-appraisal/valuation-of-greenhouse-gas-emissions-for-policy-appraisal-and-evaluation
Department for Transport (2016) Understanding and valuing the impacts of transport investment: wider impacts transport appraisal guidance (WebTAG) htts://www.gov.uk/government/consultations/transport-investment-understanding-and-valuing-impacts
Graham D J (2007) Agglomeration, productivity and transport investment, Journal of Transport economics and Policy, 41 (3) ,317-343
Nellthorp,J;Bristow,AL;Day,B (2007) Introducing Willingness-to-pay for Noise Changes into Transport Appraisal: An Application of Benefit Transfer Transport Reviews 27, 327-353

## Slide 45: References continued
Venables, A.J. (2007), ‘Evaluating urban transport improvements. Cost–benefit analysis in the presence of agglomeration and income taxation’, Journal of Transport Economics and Policy, 41 (2), 173–188.
Wardman M (2001) A review of British evidence on Time and Service Quality. Transportation Research E, Vol 37, No 2 pp 107-128.