## Slide 1: VLANs (Virtual LANs)

## Slide 2: VLAN introduction
VLANs provide segmentation based on broadcast domains.
Typically VLAN = Subnet
VLANs can logically segment switched networks based on:
  Physical location (Example: Building)
  Organization (Example: Marketing)
  Function (Example: Staff)
vlan 10
Default vlan 1
Default vlan 1

## Slide 3: VLAN introduction
VLANs are created to provide segmentation services traditionally provided by physical routers in LAN configurations.
VLANs address scalability, security, and network management.
Without VLANs
10.3.0.0/16
10.2.0.0/16
10.1.0.0/16
One link per VLAN or a single VLAN Trunk (later)
With VLANs
10.1.0.0/16
10.2.0.0/16
10.3.0.0/16

## Slide 4: Two Subnets, One Switch, No VLANs
Layer 2 Broadcasts
  What happens when 10.1.0.10 sends an ARP Request for 10.1.0.30?
10.1.0.10/16 DG: 10.1.0.1
10.2.0.20/16 DG: 10.2.0.1
10.1.0.30/16 DG: 10.1.0.1
10.2.0.40/16 DG: 10.2.0.1

## Slide 5: Two Subnets, One Switch, No VLANs
Layer 2 Broadcasts and unknown Unicasts
  Switch floods it out all ports.
  All hosts receive it, even those on a different subnet.
  Layer 2 broadcast should be isolated to only that network.
  Note: If the switch supports VLANs, by default all ports belong to the same VLAN and it floods it out all ports that belong to the same VLAN as the incoming port (coming).
10.1.0.10/16 DG: 10.1.0.1
10.2.0.20/16 DG: 10.2.0.1
10.1.0.30/16 DG: 10.1.0.1
10.2.0.40/16 DG: 10.2.0.1

## Slide 6: Traditional Solution: Multiple Switches
The traditional solution is have devices on the same subnet connected to the same switch.
This provides broadcast and unknown unicast segmentation, but is also less scalable.
10.1.0.10/16 DG: 10.1.0.1
10.2.0.20/16 DG: 10.2.0.1
10.1.0.30/16 DG: 10.1.0.1
10.2.0.40/16 DG: 10.2.0.1
Fa 0/0
Fa 0/1
10.1.0.1/16
10.2.0.1/16
ARP Request

## Slide 7: Two Subnets, One Switch, No VLANs
Even though hosts are connected to the same switch (or even hub), devices on different subnets must communicate via a router.
Remember a switch is a layer 2 device, it forwards by examining Destination MAC addresses, not IP addresses.
10.1.0.10/16 DG: 10.1.0.1
10.2.0.20/16 DG: 10.2.0.1
10.1.0.30/16 DG: 10.1.0.1
10.2.0.40/16 DG: 10.2.0.1
Fa 0/0
Fa 0/1
10.1.0.1/16
10.2.0.1/16

## Slide 8: Broadcast domains with VLANs and routers
A VLAN is a broadcast domain created by one or more switches.
VLANs are assigned on the switch and correspond with the host IP address.
Each switch port can be assigned to a different VLAN.
10.1.0.10/16 DG: 10.1.0.1
10.2.0.20/16 DG: 10.2.0.1
10.1.0.30/16 DG: 10.1.0.1
10.2.0.40/16 DG: 10.2.0.1
Port 1 VLAN 10
Port 9 VLAN 10
Port 12 VLAN 20
Port 4 VLAN 20

## Slide 9: Broadcast domains with VLANs and routers
Ports assigned to the same VLAN share the same broadcast domain.
Ports in different VLANs do not share the same broadcast domain.
10.1.0.10/16 DG: 10.1.0.1
10.2.0.20/16 DG: 10.2.0.1
10.1.0.30/16 DG: 10.1.0.1
10.2.0.40/16 DG: 10.2.0.1
Port 1 VLAN 10
Port 9 VLAN 10
Port 12 VLAN 20
Port 4 VLAN 20
ARP Request

## Slide 10: VLAN operation

## Slide 11: Static VLANS
Static membership VLANs are called port-based and port-centric membership VLANs.
This is the most common method of assigning ports to VLANs.
As a device enters the network, it automatically assumes the VLAN membership of the port to which it is attached.
There is a default VLAN, on Cisco switches that is VLAN 1.
Switch(config)#interface fastethernet 0/9
Switch(config-if)#switchport access vlan 10
vlan 10
Default vlan 1
Default vlan 1

## Slide 12: Dynamic VLANs
Dynamic membership VLANs are created through network management software. (Not as common as static VLANs)
CiscoWorks 2000 or CiscoWorks for Switched Internetworks is used to create Dynamic VLANs.
Dynamic VLANs allow for membership based on the MAC address of the device connected to the switch port.
As a device enters the network, it queries a database within the switch for a VLAN membership.

## Slide 13: VLAN Trunking/Tagging
VLAN Tagging is used when a link needs to carry traffic for more than one VLAN.
Trunk link: As frames are received by the switch from any attached end-station device, a unique frame identifier is added within each header.
This header information designates the VLAN membership of each frame.

## Slide 14: VLAN Trunking/Tagging
The frame is then forwarded to the appropriate switches or routers based on the VLAN identifier and MAC address.
Upon reaching the destination node (Switch) the VLAN ID is removed from the frame by the adjacent switch and forwarded to the attached device.
Frame tagging provides a mechanism for controlling the flow of broadcasts and applications while not interfering with the network and applications.
This is known as a trunk link or VLAN trunking.

## Slide 15: VLAN Trunking/Tagging
No VLAN Tagging
VLAN Tagging

## Slide 16: VLAN Trunking/Tagging
There are two major methods of frame tagging, Cisco proprietary Inter-Switch Link (ISL) and IEEE 802.1Q.
ISL used to be the most common, but is now being replaced by 802.1Q frame tagging.
Cisco recommends using 802.1Q.

## Slide 17: Trunk - ISL vs. 802.1q Frame Format
Data

## Slide 18: 802.1q Tagging details
Dest
Src
T/L
Data
FCS
Original frame
Dest
Src
T/L
Data
New FCS
Tag
Ethertype (0x8100)
PRI
Canonical Format Identifier
Tag Protocol ID
Tag Control Information
VLAN ID
Tagged Frame
CFI

## Slide 19: IEEE 802.1Q
Tag
A 4-byte header field containing a tag protocol identifier (TPID) and tag control information (TCI) with the following elements:
Type/Lenghts field - TPID
A 2-byte TPID with a fixed value of 0x8100.
This value indicates that the frame carries the 802.1Q/802.1p tag information.
TCI
A TCI containing the following elements:
  Three-bit user priority (8 priority levels, 0 thru 7)
  One-bit canonical format (CFI indicator), 0 = canonical, 1 = noncanonical, to signal bit order in the encapsulated frame
  Twelve-bit VLAN identifier - uniquely identifies the VLAN to which the frame belongs, defining 4,096 VLANs

## Slide 20: VLAN numbering
VLAN ID ranges
0 and 4095 reserved for system use
Some switches (2960) supports only 255 VLANs together
Normal-range IDs
1 – 1005
1002 – 1005 Reserved for Token Ring and FDDI VLANs
Stored in vlan.dat file in flash memory
Extended-range IDs
1006 – 4094
Designed for service providers
Fewer options than normal range VLANs
Stored in running configuration file

## Slide 21: Configuring VLANs
vlan 10
Default vlan 1
Default vlan 1
The following guidelines must be followed:
  The maximum number of VLANs is switch dependent.
  VLAN 1 is one of the factory-default VLANs.
  VLAN 1 is the default Ethernet VLAN.
  Cisco Discovery Protocol (CDP) and VLAN Trunking Protocol (VTP) advertisements are sent on VLAN 1 (later).
  The switch IP address is in the VLAN 1 broadcast domain by default.

## Slide 22: Creating VLANs
Creating VLAN and assigning access ports (non-trunk ports) to it. Notice informing about VLAN non-existence.
  Switch(config)#interface fastethernet 0/9
  Switch(config-if)#switchport access vlan vlan_number
  Switch(config-if)#switchport mode access
Create the VLAN on older switches such as the 2900 Series XL.
  Switch#vlan database
  Switch(vlan)#vlan vlan_number
  Switch(vlan)#exit

## Slide 23: Creating VLANs
Assign ports to the VLAN
  Switch(config)#interface fastethernet 0/9
  Switch(config-if)#switchport access vlan 10
  Switch(config-if)#switchport mode access
switchport mode access – denotes this port as an access port and not a trunk link
  should be configured on all ports that the network administrator never does want to become a trunk port
vlan 10
Default vlan 1
Default vlan 1

## Slide 24: Configuring Ranges of VLANs
This command does not work on all switches, such as the 2900 Series XL.
It does work on the 2950.
vlan 3
Switch(config)#interface range fastethernet 0/8 - 12
Switch(config-if-range)#switchport access vlan 3
Switch(config-if-range)#switchport mode access
Switch(config-if-range)#exit

## Slide 25: Creating VLANs
Default: dynamic desirable
By default, all ports are configured as switchport mode dynamic desirable,
if the port is connected to another switch with an port configured with the same default mode (or desirable or auto), this link will become a trunking link.
This link will become a trunking link unless one of the ports is configured with as an access link, i.e. switchport mode access

## Slide 26: Switch port trunking – trunk modes
Switch port trunking – trunk modes
switchport mode trunk
  Unconditional trunking state (always on)
switchport mode access
  Attempts to persuade peer to become acces port
switchport mode dynamic desirable
  Actively attempts to create trunk (default)
switchport mode dynamic auto
  According peer wish can become trunk or access
  If no explicit wish, both remain access
switchport nonegotiate
  access or trunk, no negotiation
Notes: Graphic 3.2.3.1

## Slide 27: Configuring Trunk setting
If SwitchA can only be a 802.1.Q trunk and SwitchB can be either ISL or 8021.Q trunk, configure SwitchB to be 802.1Q.
On switches that support both 802.1Q and ISL, the switchport trunk encapsulation command must be done BEFORE the switchport mode trunk command.
SwitchA(config-if)switchport mode trunk
SwitchB(config-if)switchport trunk encapsulation dot1q
SwitchB(config-if)switchport mode trunk
Trunk
802.1Q only
Both ISL and 802.1Q

## Slide 28: Native VLAN
Native VLAN
Native VLAN frames are untagged on Cisco trunk
  Tagged frame with native VLAN ID are dropped
  Untagged frames are forwarded to the native VLAN
Configuration
  sw(config)#int fa0/20
  sw(config-if)#switchport trunk native vlan 2
Native VLAN mismatch – different native VLAN ID on both ends of trunk
  %CDP-4-NATIVE_VLAN_MISMATCH: Native VLAN mismatch discovered on FastEthernet0/13 (1), with sw1 FastEthernet0/13 (10)
Default native VLAN is VLAN 1
Notes: <number>
Graphics 3.1.2.1 & 3.1.2.2

## Slide 29: Verifying VLANs – show vlan
vlan 3
vlan 2
vlan 1 default

## Slide 30: Verifying VLANs – show vlan brief
vlan 3
vlan 2
vlan 1 default

## Slide 31: Deleting VLANs
Switch(config-if)#no switchport access vlan vlan_number
This command will reset the interface to VLAN 1.
VLAN 1 cannot be removed from the switch.
Create VLAN
Delete VLAN

## Slide 32: Accessing/Managing the Switch
The IP Address, Subnet Mask, and Default Gateway on a switch is for the same purposes as when you configure it for a host.
This address is for management purposes only and does not affect the Layer 2 switching operations of the switch.
The switch must be configured with a vty login/password and a privileged password for telnet access.
By default, VLAN 1 is the “management VLAN”.
Real management VLAN should be different
Switch(config)#interface vlan 1
Switch(config-if)#ip address 10.1.0.5. 255.255.0.0
Switch(config-if)#no shutdown
Switch(config-if)#exit
Switch(config)#ip default-gateway 10.1.0.1

## Slide 33: Accessing/Managing the Switch
Switch(config)# enable secret class
Switch(config)#line vty 0 4
Switch(config-line)#password cisco
Switch(config-line)#login
Switch(config)#interface vlan 99
Switch(config-if)#ip add 10.1.0.5. 255.255.0.0
Switch(config-if)#no shut
Switch(config)#ip default-gateway 10.1.0.1

## Slide 34: Accessing/Managing the Switch
Host 10.1.0.10
C:\>telnet 10.1.0.5
username:cisco
password:class
Switch>show vlan
Switch>ping 10.2.0.20
Switch>telnet 10.1.0.1
Router>exit
Switch>
10.1.0.10/16 DG: 10.1.0.1
10.2.0.20/16 DG: 10.2.0.1
10.1.0.30/16 DG: 10.1.0.1
10.2.0.40/16 DG: 10.2.0.1
Fa 0/0
Fa 0/1
10.1.0.1/16
10.2.0.1/16
10.1.0.5/16 DG: 10.1.0.1

## Slide 35: Erasing VLAN information
Switch communication with its neighbors should be blocked.
VLAN information is kept in the vlan.dat file.
The file is not erased when erasing the startup-config.
To remove all VLAN information, use the command above and reload the switch.
Switch(config)#interface range fastethernet 0/1 - 12
Switch(config-if)#shutdown
Switch#delete flash:vlan.dat
Delete filename [vlan.dat]?
Delete flash:vlan.dat? [confirm]
Switch#erase startup-config
Switch#reload