## Slide 1: Implementing IP Addressing Services
Accessing the WAN – Chapter 7

## Slide 2: Objectives
Configure DHCP in an enterprise branch network
Configure NAT on a Cisco router
Configure new generation RIP (RIPng) to use IPv6

## Slide 3: Configure DHCP in an Enterprise Branch Network
Function of DHCP in a network
Notes: Graphic 7.1.1.1

## Slide 4: Configure DHCP in an Enterprise Branch Network
Describe the differences between BOOTP and DHCP (oldest ancestor - RARP)
Notes: Graphic 7.1.3.1

## Slide 5: Configure DHCP in an Enterprise Branch Network
How DHCP dynamically assigns an IP address to a client
Can be multiple
RARP
boot
Notes: Graphic 7.1.2.1

## Slide 6: History – bootp (Internet Bootstrap Protocol)
Files
  /etc/bootpd (bootp daemon)
  /etc/bootptab (bootp cofiguration file)
  (/etc/hosts)
# @(#)bootptab,v 6.4 1995/01/27 12:54:50 neil Exp - STREAMware TCP/IP source
# SCCS IDENTIFICATION
# /etc/bootptab: database for bootp server (/etc/bootpd)
# Legend: (see bootptab.5)
# first field -- hostname (not indented)
# bf -- bootfile
# bs -- bootfile size in 512-octet blocks
# cs -- cookie servers
# df -- dump file name
# dn -- domain name
# ds -- domain name servers
# ef -- extension file
# gw -- gateways
# ha -- hardware address
# hd -- home directory for bootfiles
# hn -- host name set for client
# ht -- hardware type
# im -- impress servers
# ip -- host IP address
# lg -- log servers
# lp -- LPR servers
# ns -- IEN-116 name servers
# ra -- reply address
# rl -- resource location protocol servers
# rp -- root path
# sa -- boot server address
# sm -- subnet mask
# sw -- swap server
# tc -- template host (points to similar host entry)
# td -- TFTP directory
# to -- time offset (seconds)
# ts -- time servers
# vm -- vendor magic number
# Tn -- generic option tag n
Notes: Graphic 7.1.2.1

## Slide 7: History – bootp (Internet Bootstrap Protocol)
An example /etc/bootptab file follows:
# Sample bootptab file
xterm-1:\
:bf=bootimage:\
:ds=160.216.1.1 160.216.1.3 147.251.6.10:\
:gw=160.216.1.10:\
:hd=/usr/boot\
:bf=null:\
:ha=7FF8100000AF:\
:ht=6:\
:ip=160.216.1.11:\
:sm=255.255.255.0:\
:ts=160.216.1.1:
Notes: Graphic 7.1.2.1

## Slide 8: Configure DHCP in an Enterprise Branch Network
DHCP server on router
ip dhcp excluded-address 10.0.0.1 10.0.0.9
ip dhcp excluded-address 10.0.0.250 10.0.0.254
…
ip dhcp pool INTERNALNET-1
network 10.0.0.0 255.255.255.0
default-router 10.0.0.254
dns-server 147.251.6.10 160.216.40.10
domain-name unob.cz
lease 5
ip dhcp pool INTERNALNET-2
network 10.0.1.0 255.255.255.0
default-router 10.0.1.254
dns-server 147.251.6.10 160.216.40.10
domain-name unob.cz
lease 5
Notes: Graphic 7.1.4.1

## Slide 9: Configure DHCP in an Enterprise Branch Network - RFC 2131
7 | 15 | 23 | 31
OP Code (1) | Hardware Type (1) | Hardware Address Length (1) | Hops (1)
Transaction Identifier (4) |  |  | 
Seconds (2) – since acquisition begin |  | Flags (2) | 
Client IP address (4) – only in BOUND, RENEW or REBINDING state |  |  | 
'Your' (client) IP address (4) |  |  | 
IP address of next server (4) - bootstrap; in DHCPOFFER, DHCPACK by server |  |  | 
Relay agent IP address (4), used in booting via a relay agent |  |  | 
Client Hardware Address (16) |  |  | 
Optional server host name (64) |  |  | 
Boot file name (128) |  |  | 
Optional parameters field (var) |  |  | 

## Slide 10: Configure DHCP in an Enterprise Branch Network
Windows, Linux; Linksys home router as a DHCP client
Notes: Graphic 7.1.5.1

## Slide 11: Configure DHCP in an Enterprise Branch Network
Relay DHCP messages when the server and the client are not on the same segment
Notes: Graphic 7.1.6.1

## Slide 12: Configure DHCP in an Enterprise Branch Network
Troubleshooting a DHCP configuration
show ip dhcp binding
show ip dhcp server statistics
show ip dhcp pool
debug ip packet …
Notes: Graphic 7.1.8.1

## Slide 13: Configure NAT on a Cisco Router
Operation and benefits of using private and public IP addressing
Notes: Graphic 7.2.1.1

## Slide 14: Configure NAT on a Cisco Router
Key features of NAT and NAT overload
Notes: Graphics 7.2.2.1, 7.2.2.2 & 7.2.2.3

## Slide 15: Configure NAT on a Cisco Router
Inside/Outside, Local/Global
Inside is about the source
  Inside Local is the source real address (typically private one) before translation.
  Inside Global is the source address as it can be seen by the destination host.
Outside is about the destination
  Outside Local is the IP address of an outside host as it appears to the inside network. The address is typically allocated from address space that is routable inside.
  Outside Global is the destination address on the outside network assigned by its owner. That address is globally unique.
Notes: Graphics 7.2.2.1, 7.2.2.2 & 7.2.2.3

## Slide 16: Configure NAT on a Cisco Router
Key features of NAT and NAT overload
Notes: Graphics 7.2.2.1, 7.2.2.2 & 7.2.2.3

## Slide 17: Configure NAT on a Cisco Router
Key features of NAT and NAT overload
209.165.200.226
Notes: Graphics 7.2.2.1, 7.2.2.2 & 7.2.2.3

## Slide 18: Configure NAT on a Cisco Router
Advantages and disadvantages of NAT
Notes: Graphic 7.2.3.1

## Slide 19: Configure NAT on a Cisco Router
Configure static NAT
Notes: Graphic 7.2.4.1

## Slide 20: Configure NAT on a Cisco Router
Configure dynamic NAT
Notes: Graphic 7.2.5.1

## Slide 21: Configure NAT on a Cisco Router
Configure NAT Overload
Overload
Notes: Graphics 7.2.6.1 & 7.2.6.2

## Slide 22: Configure NAT on a Cisco Router
interface Ethernet0
ip address 10.0.0.254 255.255.255.0
ip nat inside
!
interface Ethernet1
ip address 160.216.1.137 255.255.255.0
ip nat outside
!
ip nat inside source list 10 interface Ethernet1 overload
ip route 0.0.0.0 0.0.0.0 160.216.1.10
!
access-list 10 permit any
Notes: Graphic 7.2.7.1

## Slide 23: Configure NAT on a Cisco Home Router
Configure port forwarding
Notes: Graphic 7.2.7.1

## Slide 24: Configure NAT on a Cisco Router
Verifying and troubleshooting NAT and NAT overload configurations
# show ip nat translations
(display active NAT translations)
Notes: Graphic 7.2.8.1 & 7.2.8.2

## Slide 25: Configure New Generation RIP (RIPng) to use IPv6
IPv6 addresses and the appropriate methods for abbreviating them
Notes: Graphic 7.3.2.1

## Slide 26: Configure New Generation RIP (RIPng) to use IPv6
Various methods of assigning IPv6 addresses
EUI-64
  64-bit interface identifier is most commonly derived from its 48-bit MAC address.
    A MAC address 00:1D:BA:06:37:64 is turned into a 64-bit EUI-64 by inserting FF:FE in the middle: 00:1D:BA:FF:FE:06:37:64.
Notes: Graphic 7.3.2.3

## Slide 27: Configure New Generation RIP (RIPng) to use IPv6
Transition strategies for implementing IPv6
Notes: Graphic 7.3.3.1

## Slide 28: Configure New Generation RIP (RIPng) to use IPv6
Dual stack enables IPv6 to run concurrently with IPv4 in a network
Notes: Graphic 7.3.4.1

## Slide 29: Configure New Generation RIP (RIPng) to use IPv6
Concept of IPv6-over-IPv4 tunneling
Notes: Graphic 7.3.5.1 & 7.3.5.2

## Slide 30: Configure New Generation RIP (RIPng) to use IPv6
Describe how IPv6 affects common routing protocols, and how these protocols are modified to support IPv6
Notes: Graphic 7.3.6.2

## Slide 31: Configure New Generation RIP (RIPng) to use IPv6
Explain how to configure a router to use IPv6
Notes: Graphics 7.3.7.1, 7.3.7.2 & 7.3.7.3

## Slide 32: Configure New Generation RIP (RIPng) to use IPv6
Explain how to configure a router to use IPv6
Notes: Graphics 7.3.7.1, 7.3.7.2 & 7.3.7.3

## Slide 33: Configure New Generation RIP (RIPng) to use IPv6
Explain how to configure and verify RIPng for IPv6
Notes: Graphics 7.3.8.1 & 7.3.9.2

## Slide 34: Configure New Generation RIP (RIPng) to use IPv6
Explain how to verify and troubleshoot IPv6
Notes: Graphic 7.3.9.1

## Slide 35: Summary
Dynamic Host Control Protocol (DHCP)
  This is a means of assigning IP address and other configuration information automatically.
DHCP operation
  3 different allocation methods
    Manual
    Automatic
    Dynamic
  Steps to configure DHCP
    Define range of addresses
    Create DHCP pool
    Configure DHCP pool specifics

## Slide 36: Summary
DHCP Relay
  Concept of using a router configured to listen for DHCP messages from DHCP clients and then forwards those messages to servers on different subnets
Troubleshooting DHCP
  Most problems arise due to configuration errors
  Commands to aid troubleshooting
    Show ip dhcp
    Show run
    debug

## Slide 37: Summary
Private IP addresses
  Class A = 10.x.x.x
  Class B = 172.16.x.x – 172.31.x.x
  Class C = 192.168.x.x
Network Address Translation (NAT)
  A means of translating private IP addresses to public IP addresses
  Type s of NAT
    Static
    Dynamic
  Some commands used for troubleshooting
    Show ip nat translations
    Show ip nat statistics
    Debug ip nat

## Slide 38: Summary
IPv6
  A 128 bit address that uses colons to separate entries
  Normally written as 8 groups of 4 hexadecimal digits
Cisco IOS Dual Stack
  A way of permitting a node to have connectivity to an IPv4 & IP v6 network simultaneously
IPv6 Tunneling
  An IPV6 packet is encapsulated within another protocol

## Slide 39: Summary
Configuring RIPng with IPv6
  1st globally enable IPv6
  2nd enable IPv6 on interfaces on which IPv6 is to be enabled
  3rd enable RIPng using either
  ipv6 rotuer rip name
  ipv6 router name enable