## Slide 1: Implement Spanning Tree Protocols
LAN Switching and Wireless – Chapter 5
Notes: <number>

## Slide 2: Role of Redundancy in a Converged Switched Network
How redundancy can disable a hierarchical network
Notes: <number>
Graphics 5.1.3.1 & 5.1.3.2

## Slide 3: Link layer Loops
Bridge loops can occur any time there is a redundant path or loop in the bridge network.
The switches will flip flop the bridging table entry for Station A (creating extremely high CPU utilization).
Bridge Loops can cause:
  Broadcast storms
  Multiple copies of Ethernet frames
  MAC address table instability in switches

## Slide 4: Role of Redundancy in a Converged Switched Network
How Layer 2 loops can be solved
Radia Perlman
Notes: <number>
Graphic 5.2.1.1

## Slide 5: Two key concepts
STP calculations make extensive use of two key concepts in creating a loop-free topology:
  Bridge ID
  Path Cost
Link Speed | Cost (First IEEE Spec) | Cost (Revised 802.1D-1998) | Cost (Revised 802.1t-2001)
10 Gbps | 1 | 2 | 2 000
1 Gbps | 1 | 4 | 20 000
100 Mbps | 10 | 19 | 200 000
10 Mbps | 100 | 100 | 2 000 000

## Slide 6: Port roles and operation of STP
Notes: <number>
Graphic 5.2.4.1

## Slide 7
A Spanning Tree

## Slide 8: Spanning-Tree Operation
One root bridge per network.
One root port per nonroot bridge.
One designated port per segment.
Nondesignated ports are unused.

## Slide 9: STP - Bridge Protocol Data Unit
Bridge protocol data unit (BPDU)

## Slide 10: STP – BPDU Details
Destination MAC address 01-80-C2-00-00-00
Notes: <number>
Graphic 5.2.2.1

## Slide 11: Extended BID and its Role
Notes: <number>
Graphic 5.2.3.1

## Slide 12: STP port states and BPDU timers
Notes: <number>
Graphic 5.2.5.2

## Slide 13: STP port states
Spanning tree transitions each port through several different states.
From Blocking to Forwarding:
20 sec + 15 sec + 15 sec = 50 seconds
Notes: <number>

## Slide 14: Three-Step STP Decision Sequence 
Convergence for a switched network and summarize the 3 step process STP uses to create a loop free topology
Notes: <number>
Objective for the slide: Define convergence for a switched network and summarize the 3 step process STP uses to create a loop free topology
Graphic 5.3.1.1

## Slide 15: Three-Step STP Decision Sequence 
Notes: <number>
Objective for the slide: Define convergence for a switched network and summarize the 3 step process STP uses to create a loop free topology
Graphic 5.3.1.1

## Slide 16: Three-Step STP Decision Sequence 
Notes: <number>
Objective for the slide: Define convergence for a switched network and summarize the 3 step process STP uses to create a loop free topology
Graphic 5.3.1.1

## Slide 17: Three-Step STP Decision Sequence 
Notes: <number>
Objective for the slide: Define convergence for a switched network and summarize the 3 step process STP uses to create a loop free topology
Graphic 5.3.1.1

## Slide 18: Three-Step STP Decision Sequence 
Notes: <number>
Objective for the slide: Define convergence for a switched network and summarize the 3 step process STP uses to create a loop free topology
Graphic 5.3.1.1

## Slide 19: Three-Step STP Decision Sequence 
Notes: <number>
Objective for the slide: Define convergence for a switched network and summarize the 3 step process STP uses to create a loop free topology
Graphic 5.3.1.1

## Slide 20: Three-Step STP Decision Sequence 
Notes: <number>
Objective for the slide: Define convergence for a switched network and summarize the 3 step process STP uses to create a loop free topology
Graphic 5.3.1.1

## Slide 21: How the STP Algorithm Uses Three Steps to Converge on a Loop-Free Topology
Electing a root bridge
Notes: <number>
Graphic 5.3.2.1

## Slide 22: How the STP Algorithm Uses Three Steps to Converge on a Loop-Free Topology
Electing a root port
Notes: <number>
Graphic 5.3.3.1

## Slide 23: How the STP Algorithm Uses Three Steps to Converge on a Loop-Free Topology
Electing designated ports and non-designated ports
Notes: <number>
Graphic 5.3.4.1 – try to put in as many of the steps as you can

## Slide 24: Five-Step STP Decision Sequence 
When creating a loop-free topology, STP always uses the same five-step decision sequence (or three-step?):
Five-Step decision Sequence
Step 1 – Lowest BID => Root Bridge
Step 2 – Lowest Cumulated Path Cost to Root Bridge
Step 3 – Lowest Sender BID
Step 4 – (Lowest Port Priority)
Step 5 – Lowest Port ID

## Slide 25: show spanning-tree
Distribution1#show spanning-tree
VLAN0001
Spanning tree enabled protocol ieee
Root ID Priority 32769
Address 0009.7c0b.e7c0
Cost 19
Port 3 (FastEthernet0/3)
Hello Time 2 sec Max Age 20 sec Forward Delay 15 sec
Bridge ID Priority 32769 (priority 32768 sys-id-ext 1)
Address 000b.fd13.9080
Hello Time 2 sec Max Age 20 sec Forward Delay 15 sec
Aging Time 300
Interface Port ID Designated Port ID
Name Prio.Nbr Cost Sts Cost Bridge ID Prio.Nbr
---------------- -------- --------- --- --------- -------------------- --------
Fa0/1 128.1 19 BLK 19 32769 000b.befa.eec0 128.1
Fa0/2 128.2 19 BLK 19 32769 000b.befa.eec0 128.2
Fa0/3 128.3 19 FWD 0 32769 0009.7c0b.e7c0 128.1
Fa0/4 128.4 19 BLK 0 32769 0009.7c0b.e7c0 128.2
Fa0/5 128.5 19 FWD 19 32769 000b.fd13.9080 128.5
Gi0/1 128.25 4 FWD 19 32769 000b.fd13.9080 128.25
Interface Port ID Designated Port ID
Name Prio.Nbr Cost Sts Cost Bridge ID Prio.Nbr
---------------- -------- --------- --- --------- -------------------- --------
Gi0/2 128.26 4 BLK 19 32769 000b.befa.eec0 128.26

## Slide 26: show spanning-tree detail
Distribution1#show spanning-tree detail
VLAN0001 is executing the ieee compatible Spanning Tree protocol
Bridge Identifier has priority 32768, sysid 1, address 000b.fd13.9080
Configured hello time 2, max age 20, forward delay 15
Current root has priority 32769, address 0009.7c0b.e7c0
Root port is 3 (FastEthernet0/3), cost of root path is 19
Topology change flag not set, detected flag not set
Number of topology changes 7 last change occurred 00:14:34 ago
from GigabitEthernet0/1
Times: hold 1, topology change 35, notification 2
hello 2, max age 20, forward delay 15
Timers: hello 0, topology change 0, notification 0, aging 300

## Slide 27: Different types of STP
Cisco Proprietary | PVST Uses the Cisco proprietary ISL trunking protocol Each VLAN has an instance of spanning tree Ability to load balance traffic at layer-2 Includes extensions BackboneFast. UplinkFast, and PortFast
 | PVST+ Supports I5L and IEEE 802.10 rocking Supports Cisco proprietary 5Th extensions Adds BPDU guard and Root guard enhancements
 | Rapid-PVST+ Based on IEEE 802.1w standard Has faster convergence than 802.1D
IEEE Standard | RSTP (originally IEEE 802.1w, every VLAN has separate STP instance) Introduced in 1982 provides faster convergence than 802.1D Implements versions of the Cisco proprietary STP extensions IEEE has incorporated RSTP into 802.1D as IEEE 802.1D-2004
 | MSTP (originally IEEE 802.1s) Multiple VLANs can be served by the same spanning-tree instance Inspired by the Cisco Multiple Instances Spanning Tree Protocol (MISTP) IEEE 802.1Q-2003 now includes MSTP

## Slide 28: Rapid per VLAN Spanning Tree (Rapid PVST+) in a LAN
Notes: <number>
Graphic 5.4.2.1 & 5.4.2.2

## Slide 29: Rapid per VLAN Spanning Tree (Rapid PVST+) in a LAN
Characteristics:
• Is the preferred protocol for preventing Layer 2 loops in a switched network
• Transparently integrates Cisco-proprietary enhancements
• Performs better than the Cisco-proprietary enhancements
• Defines different port states and port roles
• Is backward compatible with 802.1D
• Has kept most configuration parameters unchanged
• Has the same BPDU format as the IEEE 802.1D BPDU
• Does not need 802.1D timers
Notes: <number>
Graphic 5.4.3.1 (characteristics)

## Slide 30: Rapid per VLAN Spanning Tree (Rapid PVST+) in a LAN
RSTP edge and non-edge ports
Non-edge ports
Notes: <number>
Graphic 5.4.4.1

## Slide 31: Rapid per VLAN Spanning Tree (Rapid PVST+) in a LAN
RSTP link/port types
  Root port
  Designated port
  Alternative port
  (redundant root)
  Backup port
  (redundant designated)
Notes: <number>
Graphic 5.4.5.1

## Slide 32: Rapid per VLAN Spanning Tree (rapid PVST+) in a LAN
Port states and port roles
Notes: <number>
Graphic 5.4.6.1 try to use all 3 but if you can’t then use the description graphic

## Slide 33: Rapid per VLAN Spanning Tree (rapid PVST+) in a LAN
How to configure rapid PVST+
Notes: <number>
Graphic 5.4.7.1 try to use both the configuration commands and the example configuration. If you can’t then use the example.

## Slide 34: Spanning Tree Troubleshooting
How to identify and solve the key STP configuration issues?
To troubleshoot a bridging loop, you need to know:
  The topology of the bridge network
  The location of the root bridge
  The location of the blocked ports and the redundant links
Notes: <number>
Graphic 5.4.9.2

## Slide 35: Summary
Spanning Tree Protocol (STP) is used to prevent loops from being formed on redundant networks
STP uses different port states & timers to logically prevent loops
There is at least one switch in a network that serves as the root bridge
  Root bridge is elected using information found in BPDU frames
Root ports are determined by the spanning tree algorithm and are closest to the root bridge
Notes: <number>

## Slide 36: Summary
STP lengthy convergence time (50 seconds) facilitated the development of:
  RSTP
    convergence time is slightly over 6 seconds (or better)
  Rapid PVST+
    adds VLAN support to RSTP
    is the preferred spanning-tree protocol on a Cisco switch network
Tips:
a)
switch(config-if)# switchport mode access
switch(config-if)# spanning-tree portfast
b)
switch(config)# spanning-tree portfast default

## Slide 37
Notes: <number>