## Slide 1: VLANs
LAN Switching and Wireless – Chapter 3
Notes: <number>

## Slide 2: Role of VLANs
Traditional LANs
Notes: <number>
Graphic 3.1.1.2

## Slide 3: 3 Broadcast Domains, 3 Switches, 3 LANs, 1 Router
Classical configuration without VLAN
Each department has its own switch which serves all its nodes as one broadcast domain
Each department has its own IP subnet
Particular networks are separated/connected by router with as many interfaces as number of departments is.
Notes: <number>
<number>

## Slide 4: VLAN introduction
VLANs provide segmentation based on broadcast domains.
Typically VLAN = Subnet
VLANs can logically segment switched networks based on:
  Physical location (Example: Building)
  Organization (Example: Marketing)
  Function (Example: Staff)
vlan 10
Default vlan 1
Default vlan 1

## Slide 5: 3 Broadcast Domains, 1 Switch, 3 VLANs, 1 Router
The same need solved by VLANs
All share one common switch, but it it divided into VLANs
Communication among VLANs provides router.
Notes: <number>
<number>

## Slide 6: VLAN numbering (Cisco)
VLAN ID ranges
0 and 4095 reserved for system use
Normal-range IDs
1 – 1005
1002 – 1005 Reserved for Token Ring and FDDI VLANs
Stored in vlan.dat file in flash memory
Extended-range IDs
1006 – 4094
Designed for service providers
Fewer options than normal range VLANs
Stored in running configuration file
Some switches (2960) supports only 255 VLANs together

## Slide 7: VLAN port membership
VLAN port membership assignment modes
Default is VLAN 1 – initially consists all ports
Database
MAC ↔ VLAN
Notes: <number>
Graphic 3.1.3.1

## Slide 8: Role of VLANs
Controlling Broadcast Domains with Switches and Routers – Intra/Inter VLAN Communication
Notes: <number>
Graphic 3.1.4.3

## Slide 9: Role of VLANs
Controlling Broadcast Domains with VLANs and Layer 3 Forwarding - Intra/Inter VLAN Communication (more details: see CCNP SWITCH )
SVI
logical interface
configured for a specific VLAN.
Notes: <number>
The objective listed above doesn’t make much sense to me. I’m not sure what is wanted….I think that the objective should read something like the following “ explain the role of a trunk when using multiple VLANs in a converged network.”

## Slide 10: Configure VLANs
Cisco IOS commands used to create a VLAN on a Cisco Catalyst switch
Notes: <number>
Graphic 3.3.2.1 ( if space is an issue use the example)
Graphic 3.3.2.2 (use example graphic)

## Slide 11: Configure VLANs
Assign port to the VLAN (repeat for all needed ports or see next )
  Switch(config)#interface fastethernet 0/9
  Switch(config-if)#switchport access vlan 10
  Switch(config-if)#switchport mode access
switchport mode access – denotes this port as an access port and not a trunk link
  should be configured on all ports that the network administrator never does want to become a trunk port
vlan 10
Default vlan 1
Default vlan 1

## Slide 12: Configure ranges of VLANs
This command does not work on all switches, such as the 2900 Series XL.
It does work on the 2950.
vlan 3
Switch(config)#interface range fastethernet 0/8 - 12
Switch(config-if-range)#switchport access vlan 3
Switch(config-if-range)#switchport mode access
Switch(config-if-range)#exit

## Slide 13: VLAN Trunking
Traditional LANs
New students in ground floor = we need to connect both student LANs
“Student“ LAN II
Notes: <number>
Graphic 3.1.1.2

## Slide 14: VLAN Trunking
Multiple VLANs without trunk
Notes: <number>

## Slide 15: VLAN Trunking
Multiple VLANs with trunk
Notes: <number>

## Slide 16: Role of Trunking VLANs
How a trunk works
Notes: <number>
Use graphic 3.2.2.1

## Slide 17: VLANs remarks
Special meaning of VLAN1
VLAN1 plays roles after start (out-of-the-box) of
  data VLAN
  default VLAN
  management VLAN
All ports are primarily VLAN1 members
Cannot be deleted
Cannot be renamed
Serves for L2 management traffic - CDP, old STP, etc.
Notes: <number>
<number>
Graphics 3.1.2.1 & 3.1.2.2

## Slide 18: VLANs remarks
Native VLAN
Native VLAN frames are untagged on Cisco trunk
  Tagged frame with native VLAN ID are dropped
  Untagged frames are forwarded to the native VLAN
Default native VLAN is VLAN 1
Notes: <number>
<number>
Graphics 3.1.2.1 & 3.1.2.2

## Slide 19: Trunk as Inter-Switch Link
Tagging | Method | Media
Inter-Switch Link (ISL) | Fast Ethernet | ISL header encapsulates the LAN frame and there is a VLAN ID field in the ISL header
802.1Q | Fast Ethernet | IEEE defined Ethernet VLAN protocol

## Slide 20: ISL vs. 802.1q Frame Format
Data

## Slide 21: 802.1q Tagging details
Dest
Src
T/L
Data
FCS
Original frame
Dest
Src
T/L
Data
New FCS
Tag
Ethertype (0x8100)
PRI
Canonical Format Identifier
Tag Protocol ID
Tag Control Information
VLAN ID
Tagged Frame
CFI

## Slide 22: IEEE 802.1Q
A 4-byte tag header containing a tag protocol identifier (TPID) and tag control information (TCI) with the following elements:
Type/Lenghts field
A 2-byte TPID with a fixed value of 0x8100.
This value indicates that the frame carries the 802.1Q/802.1p tag information.
TCI
A TCI containing the following elements:
  - Three-bit user priority (8 priority levels, 0 thru 7)
  - One-bit canonical format (CFI indicator), 0 = canonical, 1 = noncanonical, to signal bit order in the encapsulated frame
  - Twelve-bit VLAN identifier - Uniquely identifies the VLAN to which the frame belongs, defining 4,096 VLANs, with 0 and 4095 reserved.

## Slide 23: Configuring Trunking 1
If SwitchA can only be a 802.1.Q trunk and SwitchB can be either ISL or 8021.Q trunk, configure SwitchB to be 802.1Q.
On switches that support both 802.1Q and ISL, the switchport trunk encapsulation command must be done BEFORE the switchport mode trunk command.
SwitchA(config-if)switchport mode trunk
SwitchB(config-if)switchport trunk encapsulation dot1q
SwitchB(config-if)switchport mode trunk
Trunk
802.1Q only
Both ISL and 802.1Q

## Slide 24: Switch port trunking modes
Switch port trunking modes
switchport mode trunk
  Unconditional trunking state (always on)
switchport mode access
  Attempts to persuade peer to become acces port
switchport mode dynamic desirable
  Actively attempts to create trunk (default)
switchport mode dynamic auto
  According peer wish can become trunk or access
  If no explicit wish, both remain access
switchport nonegotiate
  access or trunk, no negotiation
Notes: <number>
Graphic 3.2.3.1

## Slide 25: Native VLAN
Native VLAN
Native VLAN frames are untagged on Cisco trunk
  Tagged frame with native VLAN ID are dropped
  Untagged frames are forwarded to the native VLAN
Configuration
  sw(config)#int fa0/13
  sw(config-if)#switchport trunk native vlan 20
Native VLAN mismatch – different native VLAN ID on both ends of trunk
  %CDP-4-NATIVE_VLAN_MISMATCH: Native VLAN mismatch discovered on FastEthernet0/13 (20), with sw1 FastEthernet0/13 (1)
Default native VLAN is VLAN 1
Notes: <number>
<number>
Graphics 3.1.2.1 & 3.1.2.2

## Slide 26: Verifying VLANs – show vlan
vlan 3
vlan 2
vlan 1 default

## Slide 27: Verifying VLANs – show vlan brief
vlan 3
vlan 2
vlan 1 default

## Slide 28: Deleting VLANs
Switch(config-if)#no switchport access vlan vlan_number
This command will reset the interface to VLAN 1.
VLAN 1 cannot be removed from the switch.
Create VLAN
Delete VLAN

## Slide 29: Accessing/Managing the Switch
The IP Address, Subnet Mask, and Default Gateway on a switch is for the same purposes as when you configure it for a host.
This address is for management purposes only and does not affect the Layer 2 switching operations of the switch.
The switch must be configured with a vty login/password and a privileged password for telnet access.
By default, VLAN 1 is the “management VLAN”.
Real management VLAN should be different
Switch(config)#interface vlan 1
Switch(config-if)#ip address 10.1.0.5. 255.255.0.0
Switch(config-if)#no shutdown
Switch(config-if)#exit
Switch(config)#ip default-gateway 10.1.0.1

## Slide 30: Access to the Switch
Switch(config)# enable secret class
Switch(config)#line vty 0 4
Switch(config-line)#password cisco
Switch(config-line)#login
Switch(config)#interface vlan 99
Switch(config-if)#ip add 10.1.0.5. 255.255.0.0
Switch(config-if)#no shutdown
Switch(config)#ip default-gateway 10.1.0.1

## Slide 31: Troubleshoot Common Software or Hardware Misconfigurations Associated with VLANs
Notes: <number>
Graphic 3.4.1.1

## Slide 32: Erasing VLAN information
Switch communication with its neighbors should be blocked.
VLAN information is kept in the vlan.dat file.
The file is not erased when erasing the startup-config.
To remove all VLAN information, use the command above and reload the switch.
Switch(config)#interface range fastethernet 0/1 - 12
Switch(config-if)#shutdown
Switch#delete flash:vlan.dat
Delete filename [vlan.dat]?
Delete flash:vlan.dat? [confirm]
Switch#erase startup-config
Switch#reload

## Slide 33
Notes: <number>