## Slide 1: Frame Relay
Accessing the WAN – Chapter 3
Notes: <number>

## Slide 2: Fundamental Concepts of Frame Relay Technology
Frame Relay is used to provide WAN services to the Enterprise
DS0 = 64 kbps
Notes: <number>
Graphic 3.1.1.1 (frame relay)

## Slide 3: Fundamental Concepts of Frame Relay Technology
Frame Relay competitors
  Ethernet over fiber optics
  MPLS
  VPN
  Cable modem
  DSL
Frame Relay today’s usage
  Rural sites with low bandwidth demand (local stores to into their corporate WAN)
  Sensors
  Surveillance cameras
Frame Relay as part/complement ISDN, X.25 (original ideas)
  FR optimized for throughput, other services guaranteed by others
Notes: <number>
Graphic 3.1.1.1 (frame relay)

## Slide 4: Fundamental Concepts of Frame Relay Technology
Notes: <number>
Graphic 3.1.1.1 (frame relay)

## Slide 5: Fundamental Concepts of Frame Relay Technology
Frame Relay is used to provide WAN services to the Enterprise
  Frame Relay typical speeds are 56 kbps to 44.7 Mbps.
Notes: <number>
Graphic 3.1.1.1 (frame relay)

## Slide 6: Concepts of Frame Relay Technology
Frame Relay uses virtual circuits to carry packets from one DTE to another DTE
Multiple VCs on the same line are distinguishable by the Data-link Connection Identifier (DLCI)
Notes: <number>
Graphic 3.1.2.1
Graphic 3.1.2.2

## Slide 7: Fundamental Concepts of Frame Relay Technology
Frame Relay – frame encapsulation
Notes: <number>
Graphic 3.1.3.1

## Slide 8: Fundamental Concepts of Frame Relay Technology
Frame Relay – frame format
01111110
01111110
DLCI 10 bits together (6 + 4)
C/R Not used in FR (Command/Response)
EA Extended Address
FECN Forward Explicit Congestion Notification
BECN Backward Explicit Congestion Notification
DE Discard Eligible
(max 8 kB)
Notes: <number>
Graphic 3.1.3.1

## Slide 9: Fundamental Concepts of Frame Relay Technology
FECN - BECN
Device A is sending data to device B accross a Frame Relay intrastructure
One of the intermediate Frame Relay switches encounters congestion; it will set:
  BECN bit on packets being returned to the sending device
    It tells the sending router to back off and apply flow control like traffic Shaping
  FECN bit on the packets being sent to the receiving device.
    It informs the receiving device that the flow is congested and that it should inform upper layer protocols, if possible, that it should close down windowing etc. to inform the sending application to slow down.
Notes: <number>
Graphic 3.1.3.1

## Slide 10: Fundamental Concepts of Frame Relay Technology
Types of topologies that are used for implementing Frame Relay in different environments
Notes: <number>
Graphic 3.1.4.1
Graphic 3.1.4.2

## Slide 11: Fundamental Concepts of Frame Relay Technology
Types of topologies that are used for implementing Frame Relay in different environments
Notes: <number>
Graphic 3.1.4.1
Graphic 3.1.4.2

## Slide 12: Fundamental Concepts of Frame Relay Technology
Local Management Interface (LMI).
  Keepalive mechanism
  Provides status information about Frame Relay connections between the router (DTE) and the Frame Relay switch (DCE)
LMI Extensions
  VC status messages
  Multicasting
  Global addressing
  Simple flow control (XON/XOFF – 0x11/0x13 – DC1/DC3)
Notes: <number>
Graphic 3.1.5.4

## Slide 13: Fundamental Concepts of Frame Relay Technology
Router attached to a Frame Relay network uses LMI status messages and inverse ARP queries to map VCs to layer 3 network IP Addresses
Notes: <number>
Graphic 3.1.5.4

## Slide 14: Fundamental Concepts of Frame Relay Technology
Inverse ARP
Once the interface is enabled, the router will send Inverse-Arp requests out all DLCIs learned via LMI for all protocols configured on the interface.
Notes: <number>
Graphic 3.1.5.4

## Slide 15: Configure a Basic Frame Relay PVC
Configure a basic Frame Relay PVC on a router serial interface
Notes: <number>
Graphic 3.2.1.1 & 3.2.1.2

## Slide 16: Configure a Basic Frame Relay PVC
Configure a static Frame Relay map
broadcast – in effect turns the broadcast into a unicast to send it out so that the other side gets the routing updates.
R1
interface s0/0/1
ip address 10.1.1.1 255.255.255.252
encapsulation frame relay
bandwidth 64
frame relay map ip 10.1.1.2 102 broadcast
Notes: <number>
Graphic 3.2.2.1

## Slide 17: Configure a Basic Frame Relay PVC
Router as a Frame Relay Switch
!
frame-relay switching
interface Serial0
no ip address
encapsulation frame-relay
clockrate 56000
frame-relay intf-type dce
frame-relay route 102 interface Serial1 201
!
interface Serial1
no ip address
encapsulation frame-relay
clockrate 56000
frame-relay intf-type dce
frame-relay route 201 interface Serial0 102
Notes: <number>
Graphic 3.2.2.1

## Slide 18: Advanced Concepts of Frame Relay Technology
Bandwidth control
  Committed Information Rate (CIR)
  Committed Burst Information Rate (CBIR)
  Excess Burst (BE)
Notes: <number>
Graphic 3.3.2.1 & 3.3.2.2

## Slide 19: Advanced Concepts of Frame Relay Technology
Flow control in Frame Relay technology
Notes: <number>
Graphic 3.3.3.1

## Slide 20: Configure an Advanced Frame Relay PVC
Point-to-point subinterfaces on a physical interface
Notes: <number>
Graphic 3.4.1.2

## Slide 21: Configure an Advanced Frame Relay PVC
Commands used for verifying Frame Relay operation
Notes: <number>
Graphic 3.4.2.1

## Slide 22: Configure an Advanced Frame Relay PVC
Steps for troubleshooting a Frame Relay configuration
Notes: <number>
Graphic 3.4.3.1

## Slide 23: Summary
Frame relay is the most widely used WAN technology because it:
  Provides greater bandwidth than leased line
  Reduces cost because it uses less equipment
  Easy to implement
Frame relay is associated with layer 2 of the OSI model and encapsulates data packets in a frame relay frame
Frame relay is configured on virtual circuits
  These virtual circuits may be identified by a DLCI
Frame relay uses inverse ARP to map DLCI to IP addresses
Notes: <number>

## Slide 24: Summary
Configuring frame relay requires
  Enable frame relay encapsulation
  Configuring either static or dynamic mapping
  Considering split horizon problems that develop when multiple VCs are placed on a single physical interface
Factor affecting frame relay configuration
  How service provider has their charging scheme set up
Frame relay flow control
  DE
  FECN
  BECN

## Slide 25: Summary
The following commands can be used to help verify frame relay configuration
  show interfaces
  show frame-relay lmi
  show frame-relay pvc ###
  show frame-relay map
use the following command to help troubleshoot a frame relay configuration
  debug frame-relay lmi

## Slide 26
Notes: <number>