## Slide 1: PA197 Secure Network Design
Cryptography aspects in Wireless Sensor Networks
Petr Švenda svenda@fi.muni.cz
Faculty of Informatics, Masaryk University

## Slide 2: Lecture overview
Cryptography and key management in WSNs
  Approaches and typical issues
Partial compromise and what can be done
  Dealing with partially compromised network
Case study: WSNProtectLayer

## Slide 3: Network lifetime
key pre-distribution
time
key update
message routing …
physical deployment
neighbors discovery
link key setup
nodes authentication
message routing …
nodes re-deployment
new to old nodes
authentication
link key setup
Network operation
Initial deployment

## Slide 4: Cryptographic aspects
Wireless Sensor Networks – Crypto

## Slide 5: Do we have need for on-node crypto?
Data for base-station (end-to-end)
Data for neighbors (hop-by-hop encryption)
Nodes authentication
Authenticated broadcast
Group/cluster-keys (aggregation)
Traffic analysis resistance (phantom routing…)
No-keys, symmetric crypto, asymmetric crypto
Random number generation (IV, padding, keys…)

## Slide 6: Recall: WSN specifics
Limited computation power and memory
Limited energy
  Consumed by communication, computation, storage…
Limited connectivity
No direct central synchronization
  Low-range radio
  No or loosely synchronized clocks
Limited or no tamper resistance

## Slide 7: Native vs. software-only cryptography
Native support inside radio module
Software execution on main processor
Additional cryptographic co-processor
I. Native support by radio module
II. Software execution on main processor
III. Additional cryptographic co-processor

## Slide 8: I. Crypto in radio module

## Slide 9: Native cryptographic support by radio
Cryptographic functionality provided by radio module
  Supported algorithms depend on used standard, only very few
  Usually easy to use and transparent to developer/user
  Energy efficient (ASIC)
Usually focus only on link-level security
  Encryption, integrity (MAC), node authentication, key establishment
Performance matched to radio’s transmission rate
Allows for better parallelization => lower latency
  Main processor not occupied with cryptographic operation
Customized crypto protocols usually not possible

## Slide 10: Native cryptographic support - examples
IEEE 802.15.4 (ZigBee, AES-128b)
  AES-CBC-MAC-32/64 (no encryption, 4/8B MAC)
  AES-CTR (CTR mode for encryption, no MAC)
  AES-CCM-32/64 (encryption + MAC)
Bluetooth LE/Smart (AES-128b, ECDH P-256)
  AES-CCM (encryption + MAC)
  ECDH (key establishment)
…

## Slide 11: Crypto on main processor

## Slide 12: Crypto on main processor
Cryptographic functionality executed on main processor
  Performance highly depends on main processor
  Usually less energy efficient and possibly slower than other options
High flexibility: customized algorithms and protocols
  Anything that can be compiled, fit and executed on MCU
  Important parameters: code size (EEPROM), state (RAM), speed
Introduces additional latency
  Main processor occupied with crypto operation, serialization
Possibility to update implementation in the field
  Over-the-air (OTA) updates
Keys can be extracted after node capture
  no tamper resistance

## Slide 13: Available implementations
Security Frameworks for Wireless Sensor Networks-Review
Gaurav Sharma, Suman Bala, Anil K. Verma DOI: 10.1016/j.protcy.2012.10.119
Standalone algorithms (e.g., AES)
General-purpose libraries (mostly C)
Platform specific libraries (TinySec…)
Kernel modules (part of embedded OS)

## Slide 14
Security Frameworks for Wireless Sensor Networks-Review: G. Sharma, S. Bala, A. Verma DOI: 10.1016/j.protcy.2012.10.119

## Slide 15: Modes for encryption / integrity
CBC used often in software libraries (simple)
  Need for initialization vector update and synchronization
CTR mode
  possibility for precomputation => lower latency when packet arrives
  No message length extension
  (used also in Bluetooth LE / IEEE 802.15.4 ZigBee)
CBC-MAC - same underlying code reused

## Slide 16: Initialization vector management
IV is send with every packet
  Shorter than normally (e.g., 2 bytes only), ~10% overhead
    Relatively low number of messages (65k) before key update
  Advantage in high packet loss environments
  Example: TinySec, ZigBee
IV is kept synchronized (counter), no IV send
  Resynchronization on packet loss required
  Example: SPINS
Only part of IV send (last few bits)
  Balance between overhead and expected number of lost packets
  Example: MiniSec-U

## Slide 17: SPINS/SNEP (Perrig et al., 2002)
Suite of lightweight protocols
  Based on symmetric cryptography only, RC5 (stream c.)
SNEP: Sensor Network Encryption Protocol
  Semantic security, Data authentication
  Replay protection – synchronized counters
  Freshness – weak (counter), strong (challenge)
  Low communication overhead
De-facto benchmark for protocols proposed later
Notes: http://users.ece.cmu.edu/~adrian/projects/mc2001/mc2001.pdf

## Slide 18: SPINS – energy consumption
http://users.ece.cmu.edu/~adrian/projects/mc2001/mc2001.pdf

## Slide 19: Asymmetric crypto – energy consumption
Significantly different ratio w.r.t. symmetric crypto
  Most energy consumed by computation of operation (MCU)
  Transmission accounts only to about 1% of energy use
  Even when significantly longer signature is transmitted
    128B RSA signature vs. 4-8B MAC
Overall impact on network lifetime is still very small
  Relevant only to networks with high number of signed messages
More important factors are code size, state and increased probability of collision during transmission
https://www.ics.uci.edu/~steffenp/files/SASN_piotrowski.pdf

## Slide 20: Authenticated Broadcast
Authenticated message to be delivered to “all” nodes
Solution1: Asymmetric crypto
  Potentially high computation and transmission overhead
Solution2: Single network-wide key for MAC verification
  Single compromised node => attacker can forge BS’s messages
Solution3: Unique key between every node and BS
  Compromised node => only messages to this node can be forged
  But separate message (or at least MAC) for every node needs to be computed and delivered (overhead)
Can we use symmetric crypto and have only single key?

## Slide 21: μTesla: Authenticated Broadcast
Message broadcasted from base station with MAC
  Node stores received message, but cannot verify yet
Base station later broadcasts key used for MAC (“epoch”)
  Once broadcasted, nodes can verify messages from given epoch
  New messages from previous epoch are not accepted any more
    As MAC key for that epoch is now public
Message authentication keys form hash key chain
  No need to store keys for older epochs
  Validity of MAC keys can be verified against pre-distributed root

## Slide 22: Hash chains (as used in µTesla)
root = H1(H2(…HX(seed)…))
Knowledge of root will not allow to compute any Hi
  Inversion of hash function H is hard
Hi can be quickly verified against Hi-1
  Unlimited length of chain (if root is not required)
  Length X chosen in advance (if root is pre-distributed)
Knowledge of seed allows to compute any chain value
  Used by base station for MAC key computation
root used for verification of μTesla MAC keys

## Slide 23: μTesla properties
Very low overhead (MAC/message + key/epoch)
Requires loosely synchronized clock (”epochs”)
Robust against packet loss
Overhead independent from number of nodes

## Slide 24: crypto co-processor
Tamper Resistant Hardware and Asymmetric crypto on WSN node

## Slide 25: Cryptographic co-processor
Additional dedicated co-processor for crypto ops
  Only cryptographic speedup (no tamper protection)
  Also tamper protection of cryptographic secrets
Possibility to parallelize (MCU/Crypto/Radio)
Small to medium flexibility (fixed set of algorithms)
Energy efficient
E.g., cryptographic smart card provides:
  Strong tamper resistance, RSA-1024/2048, ECC…
  Strong protection also for keys for symmetric crypto
  Relatively cheap ($2, Feitian A40 Infineon SLE78)

## Slide 26: Smart card to sensor node connection
Direct connection via serial interface (UART)
  Communication speed 9600 baud, APDU commands
Keys and crypto operation executed only on-card
Hanáček, Nagy, Pecho: Power Consumption of Hardware Cryptography Platform for Wireless Sensor, IEEE CS, 2009, s. 6, ISBN 978-0-7695-3914-0

## Slide 27: Performance with cryptographic smartcard
Total time = T(dataIn) + T(operation) + T(dataOut)
Experiment: MICAz (ATmega128L), GemXpresso R4
Performance for RSA-1024b
  30x faster (750ms), 27x more energy efficient (27mW)
Performance for RSA-2048b
  88x faster (1900ms), 70x more energy efficient (79mW)
Hanáček, Nagy, Pecho: Power Consumption of Hardware Cryptography Platform for Wireless Sensor, IEEE CS, 2009, s. 6, ISBN 978-0-7695-3914-0

## Slide 28: Performance with newer cards
Even faster with current cards and faster UART
  9600 baud  128000 baud => 12x faster data I/O
$2 Feitian A40 smart card (Infineon SLE78)
  25ms per single RSA-1024b operation
  150ms per single RSA-2048b operation
Expected performance
  below 50ms (440x faster) for RSA-1024
  below 200ms (900x faster) for RSA-2048
Even cheaper and efficient ASICs available…

## Slide 29: Multiple keys / engines can be stored
https://www.fi.muni.cz/~xsvenda/jcalgtest

## Slide 30: Key Distribution
Wireless Sensor Networks – Key Distribution

## Slide 31: Problem: wide range of assumptions
Different works assume different types of WSNs
  network architecture and topology
  network nodes hardware and required lifetime
  degree of (de)centralism, level of nodes mobility
  communication medium used, quality of links
  computational power, memory limitations, energy source
  routing and data collection algorithms
  assumptions about attacker capabilities
  …
One security approach doesn’t fit all scenarios

## Slide 32: Level of keys pre-distribution (I.)
No pre-distribution
  all keys established after nodes are deployed
  e.g., Key Infection (exchange keys in plaintext)
  problem: usually assumes period of limited attacker
Fixed network wide “master” key(s)
  pre-distributed keys allowing key establishment with all others
  problem: very low node capture resilience

## Slide 33: Fixed network wide “master” key(s)
Single master key shared by whole network
All transmission encrypted/MAC by master key
  What are possible attacks?
  Reuse of key for long time, no origin authentication…
  Compromise of master key (node capture)
Link keys derived from master key
  linkKey = KDF(nodeID1 | nodeID2 | random)
What attacks are possible?

## Slide 34: Why “Master key” pre-distribution fails
Perfect in terms of memory storage
Completely fails with single node

## Slide 35: Level of keys pre-distribution (II.)
No pre-distribution
  all keys established after nodes are deployed
  e.g., Key Infection (exchange keys in plaintext)
  problem: usually assumes period of limited attacker
Fixed network wide “master” key(s)
  pre-distributed keys allowing key establishment with all others
  problem: very low node capture resilience
Partial pre-distribution
  not all nodes can establish key directly
  e.g., probabilistic pre-distribution [EG02]
  problem: node capture resiliency

## Slide 36: Probabilistic key pre-distribution
Key pool
K7
K23
K53
K3
K11
K21
K23
K1
K16
K11
K27
K75
K8
Eschenauer & Gligor 2002
Elegant idea with low memory requirements
  based on birthday paradox
  large pool of cryptographic keys with unique IDs used
For every node prior deployment:
  randomly select keys from large key pool
  return selected keys back to pool
  proceed with next node
K7
K23
K75
K3
K23
K11

## Slide 37: Probabilistic key pre-distribution (2)
During neighbour discovery:
  neighbours establish radio communication
  nodes iterate over their keyrings for shared key(s)
  if shared (by chance) key(s) are found, secure link is established
  e.g., 100 keys from 10000 => 60% probability at least one key shared
Not all nodes can establish secure link
  but sufficient connectivity probability can be set
Node capture resilience (NCR) is a problem
K7
K23
K75
K3
K23
K11

## Slide 38: How probabilistic pre-distribution fails
Keys from uncaptured nodes compromised as well

## Slide 39: Level of keys pre-distribution (III.)
Pairwise keys (node2BS, node2node)
  all nodes can establish keys if necessary
  Every node to BS, every node to every node

## Slide 40: Pairwise keys – every node to BS
Predistributed unique key(s) between BS and every node
  BS holds database of all keys, node holds just single key to BS
End-to-end encryption/MAC
  Intermediate nodes just forward towards BS
  Low latency, memory and computation overhead (no processing on intermediate nodes)
Possibility for periodic key update
  newKey = KDF(oldKey, “Periodi”), erase previous oldKey
  Better than newKey=KDF(masterKey,“Periodi”) – why?
Disadvantages of scheme?
  No data aggregation, insertion of corrupted packets…

## Slide 41: Pairwise keys – every node to every node
Predistributed unique key(s) between every two nodes
  Every node holds keys to all other potential neighbours
  (1MB flash storage => 65k of 16B keys)
  Proper key is found and used when needed
Unused keys may be erased after neighbour discovery
  When unused keys will not be necessary
  No need for a priory knowledge of network layout
Keys to not yet deployed nodes can be also included
  Later redeployment of fresh nodes
  Authentication between old and new nodes possible
Node capture resiliency
  no keys except for compromised node are revealed

## Slide 42: How “Pairwise keys” pre-distribution fails?
Node1
K12
K13
K14
Only links to captured node are compromised
Key from captured node can be used everywhere
Node2
K12
K23
K24
Node4
K14
K24
K34
Node3
K13
K23
K34
Node1
K12
K13
K14

## Slide 43: Level of keys pre-distribution (2)
Pairwise keys (node2BS, node2node)
  all nodes can establish keys if necessary
Asymmetric cryptography
  all nodes can establish keys if necessary
  e.g., ECC, pairing-based crypto
  shown to be feasible (2.5 sec verification, 20KB ROM)
  problem: revocation of compromised keys/nodes

## Slide 44: Why asymmetric cryptography may fail?
Only links to captured node are compromised
High computational/transmission overhead (> 128B)
Private key from captured node can be used everywhere
Revocation is hard

## Slide 45: Level of keys pre-distribution (2)
Pairwise keys
  all nodes can establish keys if necessary
Asymmetric cryptography
  all nodes can establish keys if necessary
  e.g., ECC, pairing-based crypto
  shown to be feasible (2.5 sec verification, 20KB ROM)
  problem: revocation of compromised keys/nodes
Central key distribution (via Base Station)
  BS acts as trusted third party, centralized solution (SPINS)
  problem: multi-hop communication to BS

## Slide 46: How TTP distribution fails?
Every key is established via base station (good control)
Communication is multi-hop and energy expensive
Network may be temporarily disconnected
Base station

## Slide 47: Partial compromise
All approaches vulnerable to some extend.
What should we do with partial compromise?

## Slide 48: Secrecy amplification protocols

## Slide 49: Secrecy amplification protocols
Additional protocol executed atop of distributed keys
  network partially compromised after some attack
  some link keys known to attacker (eavesdropped, captured)
Secrecy amplification is able to secure previously compromised link(s)
  transport of fresh link key over secure path
  success depends on compromise pattern
Protocol can be executed even when information about compromise is not available
  old and new key is combined
PUSH
PULL

## Slide 50: Comparison: total success rate
Avg 7.5 neighbours
before SA: 60 % secure
after SA: 97 % secure
Depending on network density, up to 30 %  95 %
Avg 20.3 neighbours
Notes: Great improvement, but for what price? And what is important currency in battery-powered networks? Number of messages -> Energy

## Slide 51: Main advantages of secrecy amplification
Is preventive measure (no detection/reaction)
Can work in (partially) compromised environment
Work with different underlying (pre)distributions
Are introducing secrets (keys) usable only locally
Can be (automatically) parameterized/optimized
Can run continuously – attacker must maintain its presence
Survey: http://www.crcs.cz/papers/wistp2015

## Slide 52: Hybrid SA - prototype implementation
TelosB hardware platform with the TinyOS 2.1.2 operating system
Three different roles:
  master: being node NC
  slave: being node NP
  forwarder: being intermediate node
Six phases executed in parallel
  discovery of radio distance to neighbors
  measured distances broadcast
  computation of mapping to real nodes
  execution of hybrid protocol
  verification of shared sub-keys transmitted
  combination of all sub-keys with existing link key

## Slide 53: Practical implementation – results
Scenario: 10 neighbours on average
Hybrid secrecy amplification protocol
TinyOS 2.1.2 implementation
  < 500B RAM (peak usage, reusable later), ~3KB code
  Seconds to minutes to reliably map radio propagation
    highly depends on surrounding noise, etc.
  ~1 KB of payload is transmitted during whole secrecy amplification phase (by every node)
  1 second worth local computation
  1-10 seconds to transmit all amplification messages

## Slide 54: Case study: wsnProtectLayer
https://github.com/crocs-muni/WSNProtectLayer

## Slide 55: Scenario 1 - Warehouse
Monitored devices with RFID-based radio tags
Tracking of person movement
Static routes
Long-living network

## Slide 56: Scenario 2 – Police unit
Defense of central point (base station)
Detection of moving attacker
Reporting of moving policeman
Jamming detection
Dynamic routes
Short-living network

## Slide 57: Scenario 3 – Building monitoring
Tracking of selected person movement
Multiple levels of privacy protection
Static routes
Long-living network

## Slide 58: Attacker models assumed
Local / global passive eavesdropping
  Packet capture, traffic analysis
Active attacker manipulating traffic
  Packet dropping, injection, jamming
Active attacker capturing nodes
  And extracting cryptographic keys

## Slide 59: Core architecture components
Intrusion detection component
  Distributed packet dropper and jamming detection
  Local neighbour reputation metric
  Base station notified when misbehaving node is detected
Privacy protection component
  4 levels of protection, controlled by authenticated broadcast
  Open communication
  Message integrity and authentication
  Packet encryption
  Traffic analysis-resistant phantom routing
Key management component
  Cryptographic key distribution and establishment (node, base stations)
  Cryptographic services for other components

## Slide 61: Architecture
ProtectLayer middleware
Node persistent state
Server control
AM Radio module
Original user application

## Slide 63: Hardware used, testbed
Laboratory testbed
Crossbow TelosB
Crossbow MICAz
Zilog ePIR
RFID reader 125kHz

## Slide 64
configuration BlinkToRadioAppC {
}
implementation {
components MainC;
components LedsC;
components BlinkToRadioC as App;
components new TimerMilliC() as Timer0;
components new TimerMilliC() as InitTimer;
---> Original Components
components ActiveMessageC;
components new AMSenderC(AM_BLINKTORADIO);
components new AMReceiverC(AM_BLINKTORADIO);
---> Replaced by new ProtectLayerC
// Basic components wiring
App.Boot -> MainC;
App.Leds -> LedsC;
App.Timer0 -> Timer0;
App.InitTimer -> InitTimer;
---> Original wirings
App.Packet -> AMSenderC;
App.AMPacket -> AMSenderC;
App.AMControl -> ActiveMessageC;
App.AMSend -> AMSenderC;
App.Receive -> AMReceiverC;
---> Replaced by new one to ProtectLayerC
}
configuration BlinkToRadioAppC {
}
implementation {
components MainC;
components LedsC;
components BlinkToRadioC as App;
components new TimerMilliC() as Timer0;
components new TimerMilliC() as InitTimer;
components ProtectLayerC;
// Basic components wiring
App.Boot -> MainC;
App.Leds -> LedsC;
App.Timer0 -> Timer0;
App.InitTimer -> InitTimer;
App.Packet -> ProtectLayerC.Packet;
App.AMControl -> ProtectLayerC.AMControl;
App.AMSend -> ProtectLayerC.AMSend;
App.Receive -> ProtectLayerC.Receive;
}
Wiring Blink2Radio @ ProtectLayer…

## Slide 65
Police scenario

## Slide 66: Try it!
TinyOS 2.x-based (TelosB nodes used)
Václav MATYÁŠ, Petr ŠVENDA, Andriy STETSKO, Dušan KLINEC, Filip JURNEČKA a Martin STEHLÍK. WSNProtectLayer – security middleware for wireless sensor networks. Securing Cyber-Physical Systems. USA: CRC Press, 2015. s. 119-162, 44 s. CRC Press. ISBN 978-1-4987-0098-6.
https://github.com/crocs-muni/WSNProtectLayer

## Slide 67: Summary
Common security protocols often cannot be used
  Preference for symmetric crypto-only solutions
  Low transmission overhead important due to energy
Key distribution is (as usual) critical factor
Partial compromise should be anticipated
  And protocols designed to be able to cope with it
Mandatory reading
  A. Perrig et al: SPINS: Security Protocols for Sensor Networks
  https://users.ece.cmu.edu/~adrian/projects/mc2001/mc2001.pdf