## Slide 1: PB173 - Tématický vývoj aplikací v C/C++ (jaro 2016)
Skupina: Aplikovaná kryptografie a bezpečné programování
Petr Švenda svenda@fi.muni.cz
Konzultace: A.406, Pondělí 15-15:50

## Slide 2: Smartcards in wider system

## Slide 3: Big picture – terminal/reader and card
What principles and standards are used?
Merchant payment
Digital signature

## Slide 4: Big picture - components
User application
  Merchant terminal GUI
  Banking transfer GUI
  Browser TLS
  …
Card application
  EMV applet for payments
  SIM applet for GSM
  OpenPGP applet for PGP
  …
User application
Card OS
Card application
Card I/O manager
contact(less)
transmission
OS smart card API
smart card reader

## Slide 5
Libraries
PKCS#11, OpenSC, JMRTD
Smartcard control language API
C/C# WinSCard.h, Java java.smartcardio.*, Python pyscard
System smartcard interface: Windows’s PC/SC, Linux’s PC/SC-lite
Manage readers and cards, Transmit ISO7816-4’s APDU
Custom app with
direct control
PC application via library:
browser TLS, PDF sign…
PC application
with direct control:
GnuPG, GPShell
API: EMV, GSM, PIV, OpenPGP, ICAO 9303 (BAC/EAC/SAC)
OpenPlatform, ISO7816-4 cmds, custom APDU
SC app programming:
JavaCard, MultOS, .NET, MPCOS
Readers
Contact: ISO7816-2,3 (T=0/1)
Contactless: ISO 14443 (T=CL)
Card application 3
Card application 2
Card application 1
APDU packet

## Slide 6: Main standards
User application
Card OS
Card application
Card I/O manager
contact(less)
transmission
OS smart card API
smart card reader
ISO7816 1-4
  Card physical properties ISO7816-1
  Physical layer communication protocol ISO7816-2-3
  Data packet format (APDU)
PC/SC, PC/SCLite (host side)
  Readers/cards management
  Transmission of logical APDU packets
  C/C# WinSCard.h, Java java.smartcardio.*, Python pyscard
PKCS#11
  standardized interface on host side
  card can be proprietary
GlobalPlatform
  remote card management interface
  secure installation of applications

## Slide 7: Card’s programming platforms
User application
Card OS
Card application
Card I/O manager
contact(less)
transmission
OS smart card API
smart card reader
MultOS
  Multiple supported languages, native compilation
  Often bank cards
JavaCard
  open programming platform from Sun
  applets portable between cards
Microsoft .NET for smartcards
  Similar to JavaCard, but C#
  Applications portable between cards
  Limited market penetration

## Slide 8: What is the typical performance?
Hardware differ significantly
  Clock multiplier, memory speed, crypto coprocessor…
Typical speed of operation is:
  Milliseconds (RNG, symmetric crypto, hash)
  Tens of milliseconds (transfer data in/out)
  Hundreds of millisecond (asymmetric crypto)
  Seconds (RSA keypair generation)
Operation may consists from multiple steps
  Transmit data, prepare key, prepare engine, encrypt
   additional performance penalty

## Slide 9: Performance tables for common cards
Visit http://www.fi.muni.cz/~xsvenda/jcalgtest/
http://www.fi.muni.cz/~xsvenda/jcalgtest/

## Slide 10: Practical assignment (from last week)
Client to client network communication
Speed-up encryption of data packets between two clients with CTR mode
  Divide packet into multiple parts
  Use parallel threads to protect parts of data packet
    number of available cores is parameter for function
    (at least one thread required ;))
Document performance gains
  speed before and after the optimization (can you increase speed linearly?)
  What is length of packet for which multiple threads brings speedup benefit? (overhead with running threads)

## Slide 11: Submissions, deadlines
Upload application source codes as single zip file into IS Homework vault (Crypto - 8. homework (Threads))
DEADLINE 2.5. 12:00
  0-10 points assigned