## Slide 1: PA197 Secure network design
Basic wireless networking
Petr Švenda svenda@fi.muni.cz
Lukáš Němec Lukas.nemec@mail.muni.cz
Faculty of Informatics, Masaryk University

## Slide 2: Laboratory
Start of implementing ad-hoc networks based on Arduino with RF module
  Basic Arduino programming model
  RF library – send packet between two nodes
  Neighbours discovery (logical communication group)

## Slide 3: Laboratory
Download and run Arduino IDE
  https://www.arduino.cc/en/Main/Software
Plug in JeeNode
Select COM port
  Can be assigned to different values
  Try other ports if selected does not work
Board: Arduino Mini
Processor: ATMega328

## Slide 4: FileExamples01.BasicsBlink
Basic application, should blink the LED
During upload, Rx and Tx small leds are blinking
After upload, blue LED should blink (1 second)
You should now be able to compile and upload app
  If LED is not blinking, check PIN value
  Should be 9 for JeeNode => 13->9

## Slide 5: Blink.ino
// the setup function runs once when you press reset or power the board
void setup() {
// initialize digital pin as an output.
pinMode(13, OUTPUT);
}
// the loop function runs over and over again forever
void loop() {
digitalWrite(13, HIGH); // turn the LED on (HIGH is the voltage level)
delay(1000); // wait for a second
digitalWrite(13, LOW); // turn the LED off by making the voltage LOW
delay(1000); // wait for a second
}
(Note that PIN used for LED can be different on different boards, 9 on JeeNode)

## Slide 6: Troubleshooting
Check if you have proper board and processor
  Arduino Mini, ATMega328
Don’t have serial monitor running if going to upload new app
Try to re-plug jeenode
Try to plug into different USB port
Try to restart Arduino IDE
Check if you have same serial port speed on arduino and port monitor
  Try different speeds, otherwise you will see garbled data
Try again (anything )

## Slide 7: FileExamples … DigitalReadSerial
Original code prints state of button to serial port
Run Serial monitor
  Will automatically restart Arduino board
  Observe data as print out
Modify to print out loop counter (instead of button)
  Small red LED should blink during data transfer
You should now be able to upload application and see data via serial port
You may use any other application to capture data
  https://github.com/gskielian/Arduino-DataLogging/tree/master/PySerial

## Slide 8: RF networking with Jeelib

## Slide 9: JeeLib library
Provides support for JeeNode radio module
Download Jeelib-master.lib
  https://github.com/jcw/jeelib/archive/master.zip
Documentation: http://jeelabs.org/pub/docs/jeelib/index.html
Add library into Arduino IDE
  Sketch  Include library  Add .ZIP library
  Examples are now available: Examples  jeelib-master

## Slide 10: RF12 packet structure
C = CTL, D = DST, A = ACK, 5-bit node ID
  A bit (ACK) – indicates if sender wants to get ACK back
  D bit (DST) – indicates if node ID bits specify destination or source node
  C bit (CTL) – 1 if packet is ACK (and A must be 0)
To send packet only to node with nodeID
  rf12_sendNow(RF12_HDR_DST | nodeID, &data, dataLen);
Warning: radio is always broadcast in nature, filtering only in driver!
http://jeelabs.org/2011/06/09/rf12-packet-format-and-design/index.html
http://jeelabs.org/2011/06/10/rf12-broadcasts-and-acks/index.html
Values set/visible via (rf12_send, rf12_recv)

## Slide 11
#include <JeeLib.h>
const byte LED = 9;
byte counter;
// turn the on-board LED on or off
static void led (bool on) {
pinMode(LED, OUTPUT);
digitalWrite(LED, on ? 0 : 1); // inverted logic
}
void setup () {
// this is node 1 in net group 100 on the 868 MHz band
rf12_initialize(1, RF12_868MHZ, 100);
}
void loop () {
led(true);
// actual packet send: broadcast to all, current counter, 1 byte long
rf12_sendNow(0, &counter, 1);
rf12_sendWait(1);
led(false);
// increment the counter (it'll wrap from 255 to 0)
++counter;
// let one second pass before sending out another packet
delay(1000);
}
test1.ino
rf12_sendNow(RF12_HDR_DST | nodeID, …);
rf12_sendNow(RF12_HDR_DST | nodeID | RF12_HDR_ACK|, …);
FileExamplesjeelib-masterDINJ  test1

## Slide 12: Basic beacon application
Select FileExamplesjeelib-masterDINJ test1
  Compile, upload
  Application sends packet with counter every second
Try to change your node ID (1..31 possible)
  rf12_initialize(1, RF12_868MHZ, 100);
  31 is special ID for promiscuous mode (receives everything)
Try to change your group
  rf12_initialize(1, RF12_868MHZ, 100);
  You will hear only messages within your group

## Slide 13: Basic beacon application – send packet
rf12_sendNow(T, &counter, 1);
  T = 0 is broadcast
  T = 1..31 concrete target node ID
  sendNow takes pointer to data and its length (&counter, 1B)
    Busy waiting until send can be done (free channel check)
rf12_sendWait(1);
  Waits until a packet send is done
Maximum length of payload data RF12_MAXDATA
  66 bytes, but don’t push it too close (unreliable)
  Stay below 60

## Slide 14
#include <Ports.h>
#include <RF12.h>
byte saveHdr, saveLen, saveData[RF12_MAXDATA];
word saveCrc;
void setup () {
Serial.begin(57600);
Serial.println("\n[sniffer] 868 MHz group 100");
rf12_initialize(31, RF12_868MHZ, 100);
}
void printPacket(byte saveHdr, byte saveLen, byte saveData[RF12_MAXDATA]){
// … nice print of packet via Serial port, see full code at IS
}
void loop () {
if (rf12_recvDone()) {
// quickly save a copy of all volatile data
saveLen = rf12_len;
saveCrc = rf12_crc;
saveHdr = rf12_hdr;
if (saveLen <= sizeof(saveData)) { memcpy(saveData, (const void*) rf12_data, saveLen); }
else { memset(saveData, 0xff, sizeof(saveData));}
rf12_recvDone(); // release lock on info for next reception
if (saveCrc != 0) {
Serial.print("CRC error #");
Serial.println(saveLen, DEC);
} else { printPacket(saveHdr, saveLen, saveData);}
}
}
Sniffer.ino

## Slide 15: Sniffer application
Download sniffer code from IS (sniffer.ino)
  FileNew, Paste sniffer code
  Compile and upload
App listens for RF12 packets and prints it via Serial port
  rf12_initialize(31, RF12_868MHZ, 100);
  rf12_recvDone() – true if packet received
  rf12_recvDone()
  rf12_len, rf12_crc, rf12_hdr, rf12_data
    Global variables set by radio module
  Local copy of global variables (rf12_len  saveLen) made to:
    Prevent overwrite by another packet
    Enable radio module to start receiving next packet

## Slide 16: Test1 + sniffer
Collaborate two together
  First node runs test1
  Second node runs sniffer
Make sure that same group is used
Data transferred by first node should be captured sniffer

## Slide 17: Basic transmission: one hop
Pair together with one other colleague
  Write app that will blink LED X-times based on value inside received packet
First node is beacon sending counter
  Send is unicast to particular second node (not broadcast)
  Use also different group
Second node – receiver blinking counter % 5
  Use sniffer application
  rf12_initialize(17, RF12_868MHZ, groupID);
  Don’t forget to set LED output pin
How far you can transmit? (try hall space)

## Slide 18: Packet acknowledgements
Send packets can frequrntly get lost (noise, collision) or missed by sender (performing other task)
  How can be sender sure that the packet was delivered?
  Sometimes does not care (broadcast or “UDP”-like transmission)
If care, thank special message back from receiver can be expected/required (ACK)
  Create packet for target node with bit flag that (A)CK = 1
  Receiver reply with special ACK packet upon successful reception
    Same header as received packet, but with (A)CK bit = 0 and (C)TL=1
byte createHeader(boolean requireACK, byte destID){
byte header = requireACK ? RF12_HDR_ACK : 0;
header |= RF12_HDR_DST | destID;
return header;
}
if(RF12_WANTS_ACK){
rf12_sendStart(RF12_ACK_REPLY,0,0);
}
http://jeelabs.org/2010/12/11/rf12-acknowledgements/

## Slide 19: Homework 11 – Network sniffing
Identify radio group which is being used
  Automatic or manual trials
  Possible range 1 – 200
Create sniffer node that will capture as many packets as possible from single network run
  Modify sniffer code from study materials
  10 minutes transmission, 5 minutes silence (then repeat)
  Try to capture packets from multiple runs and compare
Submit before: 10.5. 23:59 (full number of points)
  Every additional started day (24h) means 1.5 points penalization

## Slide 20: Homework 11 – Network sniffing
Submit 3 files:
Modified sniffer application
Description of solution (1xA4)
  How network properties were found
  How was traffic logged
  How were packets analyzed
Plain .txt file with captured traffic (example next slide)
  Will be evaluated automatically, the structure MUST match exactly
  Capture as many unique messages as possible

## Slide 21: Example .txt file you should submit
#440#time year
#458#random person
#464#secret break