## Slide 1: PV204 Security technologies
Hardware Security Modules (HSM), PKCS#11
Petr Švenda svenda@fi.muni.cz
Faculty of Informatics, Masaryk University

## Slide 2: Overview
Usage scenarios for HSMs
Available hardware, security certifications
Available security APIs (PKCS#11…)
Known API-level attacks

## Slide 3: Motivation usage scenarios
Protection against trusted insiders
  bank PIN processor
Device with high impact of compromise
  Private key of root certification authority
Device in untrusted environment (ATM, PoS)
DRM application (paid satellite TV)
Smart grids (privacy of users)
Intelligent transport systems…

## Slide 4: Hardware Security Module
Hardware Security Module

## Slide 5: Hardware Security Module - definition
HSM is trusted hardware element
  Contains own physical and logical protection
  May provide increased performance (compared to CPU)
Attached to or put inside PC/server/network box
Provides in-device:
  Secure generation (and entry)
  Secure storage (and backup)
  Secure use (cryptographic algorithms)
Should never export sensitive data in plaintext
  Especially keys = Critical Security Parameters (CSP)

## Slide 6: Many HSM forms possible
Stand-alone Ethernet boxes (1U/2U)
PCI cards
Serial/USB tokens
SmartCards, TPMs…
Note: we will focus on more powerful devices (smart cards already covered)
https://www.thales-esecurity.com/products-and-services/products-and-services/hardware-security-modules

## Slide 7: Hardware Security Module - specification
Common functions
  Generate functions (generate new key)
  Load functions (import key, plain/wrapped by other key)
  Use key functions (various cryptographic algorithms)
  Export key functions (wrapping)
  Access control functions (public, login user, login admin)
  Destroy secrets functions
Possibility to write custom “plugins”
  Custom code running inside HSM
  (usually invalidates certification)

## Slide 8: Hardware Security Module - protection
Protections against physical attacks (tamper)
  Invasive, semi-invasive and non-invasive attacks
Protection against logical attacks
  API-level attacks, Fuzzing…
Preventive measures
  Statistical testing of random number generator
  Self-testing of cryptographic engines (encrypt twice, KAT)
  Firmware integrity checks
  Periodic reset of device (e.g., every 24 hour)
  …

## Slide 9: HSM – tamper security
Protection epoxy
Wiring mesh
Temperature sensors
Light sensors
Variations in power supply
Erasure of memory (write 0/random)
  After tamper detection to mitigate data remanence
…
Which one is tamper resistance,
evidence, detection and/or reaction?
www.techbriefs.com

## Slide 10: HSM – logical security
Access control with limited/delayed tries
  < 1:1000 000 probability of random guess of password
  < 1:100 000 probability of unauthorized access in one minute
Integrity and authentication of firmware update
  Signed updates
Logical separation of multiple users (memory)
  Additional protection logic for separate memory regions
Audit trails
…

## Slide 11: Certifications

## Slide 12: Certifications: NIST FIPS 140-2
Requirements on hardware and software components of security modules to be used by US government
  Verified under Cryptographic Module Validation Program (CMVP)
  Testing against a defined cryptographic module, provides a suite of conformance tests to required security level
  List of validated devices http://csrc.nist.gov/groups/STM/cmvp/validation.html
Common levels for HSMs
  NIST FIPS 140-2 Level 1+2 – basic levels, tamper evidence (broken shell, epoxy), role-based authentication (user/admin))
  NIST FIPS 140-2 Level 3 – addition of physical tamper-resistance, identity-based authentication, separation of interfaces with different sensitivity

## Slide 13: Certifications: NIST FIPS 140-2 (cont.)
Common levels for HSMs (cont.)
  NIST FIPS 140-2 Level 4 + additional physical security requirements, environmental attacks
  http://csrc.nist.gov/publications/fips/fips140-2/fips1402.pdf
  Only very few devices certified to FIPS 140-2 Level 4
NIST FIPS 140-3 (2013, but still draft)
  Additional focus on software security and non-invasive attacks

## Slide 14: NIST FIPS 140-2 and RNG
Truly random number generators (TRNG)
  No approved FIPS 140-2 TRNG
Pseudorandom number generators
  ANSI X9.31 Appendix A.2.4, 3DES/AES-based
FIPS 140-2 requires testing of RNG
  Known-answer-tests (KAT), Diehard battery

## Slide 15: “Random” FIPS 140-2 example
EXP9000 Hardware Security Module (07/2011)
  http://csrc.nist.gov/groups/STM/cmvp/documents/140-1/140sp/140sp1577.pdf
  FIPS140-2, security level 3
  Approved algorithms
  Non approved algorithms
  Roles and authentication
  Critical Security Parameters (CSP)
  Physical security mechanisms
  …

## Slide 16: Certifications: Common Criteria EAL 4-5+
CC does not directly measure the security of the system/device itself
  only states level on which the system/device was tested
  and against what Security Target
To achieve particular level, system must meet assurance requirements
  Documentation, design analysis, functional/penetration testing
CC certifies that system followed certain rules when implementing target goals
  Broader than FIPS 140-2

## Slide 17: Certifications: Common Criteria (cont.)
Common levels for HSMs
  EAL4: Methodically Designed, Tested and Reviewed
  EAL5: Semi-formally Designed and Tested
Protection profiles
  Specifies generic security evaluation criteria to substantiate vendors' claims (more technical)
  Crypto Module Protection Profile
  https://www.bsi.bund.de/cae/servlet/contentblob/480256/publicationFile/29291/pp0045b_pdf.pdf
+ means “augmented” version (current version + additional requirements, e.g., EAL4+)

## Slide 18: Certifications: PCI HSM version 1,2
PCI HSM v1 (2009), v2 (2012)
  https://www.pcisecuritystandards.org/security_standards/documents.php
Focused on area of payment transactions
  Payment terminals, backend HSMs…
  Payment transaction processing
  Cardholder authentication
  Card issues procedure
Set of logical and physical requirements relevant to payment industry
  Closer to NIST FIPS 140-2 then to CC (more concrete requirements)

## Slide 19: Cost of certification
Certification is usually done by commercial “independent” laboratories
  Laboratories are certified by governing body
  Quality and price differ
  Usually payed for by device manufacturer
Certification pre-study
  Verify if product is ready for certification
Full certification
  Checklist if all required procedures were followed

## Slide 20: Cost of CC EAL (US GAO, 2006)

## Slide 21: Be aware what is actually certified
Certified != secure
  Satisfies defined criteria, producer claims are verified to be valid
Usually certified bundle of hardware and software
  Concrete underlying hardware
  Concrete version of firmware, OS and pre-loaded application
Certification usually invalidated when:
  New hardware revision used (less common)
  New version of firmware, OS, application (common)
  Any customization, e.g., user firmware module (very common)
Pragmatic result
  “I’m using product that was certified at some point in time”

## Slide 22: How is certified product used?
Trade-off between security functionality and required data centre operations
Certification FIPS 140-2
  users usually turn FIPS mode off (want use additional functionality)
“Almost” FIPS 140-2 mode
  Everything FIPS except what user added (custom module)

## Slide 23: HSM performance

## Slide 24: HSM – performance I.
Limited independent public information available
  Claim: “up to 9000 RSA-1024b operations / second”
But…
  Real operations are not just raw crypto (formatting of messages…)
  Longer key length may be needed (RSA-2048b)
  Internal vs. external speed (data in/out excluded)
  Measurements in “optimal” situations (single pre-prepared key, large data blocks…)
  …

## Slide 25: HSM – performance II.
F. Demaertelaere (2010)
  https://handouts.secappdev.org/handouts/2010/Filip%20Demaertelaere/HSM.pdf
RSA 1024 bit private key operation: 100 – 7000 ops/sec
ECC 160 bit ECDSA signatures: 250 – 2500 ops/sec
3DES: 2 - 8 Mbytes/sec
AES: 6 - 40 Mbytes/sec (256 bit key)
No significant breakthrough in technology since 2010
Higher throughput achieved by multiple HSMs

## Slide 26: HSM - load balancing, failover
HSMs often used in business critical scenarios
  Authorization of payment transaction
  TLS accelerator for internet banking
  …
Redundancy and load-balancing required
Single HSM is not enough
  At least two in production for failover
  At least one or two for development and test

## Slide 27: Steps of crypto operation
Hardware Security Module

## Slide 28: Steps of cryptographic operation
Transfer input data
Transfer wrapped key in
Initialize unwrap engine
Unwrap data/key (decrypt/verify)
Initialize key object with key value
Initialize cryptographic engine with key
Start, execute and finalize crypto operation
Initialize wrap engine
Wrap data/key (encrypt/sign)
Erase key(s)/engine(s)
Transfer output data
Transfer wrapped key out

## Slide 29: S1: One user, few keys
No sharing, all engines fully prepared

## Slide 30: S2: One user, many keys
No sharing, frequent crypto context change

## Slide 31: S3: Few users, few keys
Device is shared  isolation of users

## Slide 32: S4:Few users, many keys
Limited sharing, frequent crypto context change

## Slide 33: S5: Many users, many keys
High sharing, frequent crypto context change

## Slide 34: HSM in cloud

## Slide 35: Security topics in cloud environment
Move of legacy application into cloud
  Previously used locally connected HSMs
Protection of messages exchanged between multiple cloud-based applications
  Key exchange of used key without pre-distribution?
Volume encryption in cloud
  Encrypted block mounted after application request (e.g., Amazon’s Elastic Block Storage)
Encrypted databases
  Block encryption of database storage, encryption of rows/cells
Cryptography as a Service
  Not only key management, also other cryptographic functionality

## Slide 36: Use case: Microsoft Azure KeyVault
REST API to generate keys, export pub, use keys…
  https://docs.microsoft.com/en-us/rest/api/keyvault/
Language bindings (language specific wrappers)
  JS, PowerShell, C#…

## Slide 37: Microsoft Azure KeyVault
https://channel9.msdn.com/Events/Ignite/2015/BRK2706

## Slide 38: Use case: AWS Key Management Service
AWS Key Management Service Cryptographic Details, M. Campagna (2015)
  https://d0.awsstatic.com/whitepapers/KMS-Cryptographic-Details.pdf
Centralized key management
  Used by cloud-based applications
  Used by any client application
  Replication of wrapping keys into HSMs in different datacenters

## Slide 39: Usage scenario: envelope encryption
Protected message exchange between multiple (cloud-based) application
  Random key generated in one application
  Key protected (wrap) using trusted element (HSM)
  Wrapped key appended to message
  Key unwrapped in second application (via HSM)
https://d0.awsstatic.com/whitepapers/KMS-Cryptographic-Details.pdf

## Slide 40
https://d0.awsstatic.com/whitepapers/KMS-Cryptographic-Details.pdf
What is difference to
PGP/S-MIME?

## Slide 41: Who is trusted?
KMS Service to wrap envelope keys properly
KMS Service not to leak wrapping key
Cloud operator not to read unwrapped keys from memory

## Slide 42: Use case: Amazon AWS CloudHSM
Amazon’s AWS CloudHSM
  Based on SafeNet’s Luna HSM
  Only few users can share one HSM (probably no sharing)
  => High initial cost (~$5000 + $1.88 per hour)
Note: significantly different service from AWS KMS
  “Whole” HSM is available to single user/application, not only key (un)wrapping functionality
  Suitable for legacy apps, compliancy requirements

## Slide 43: Use case: Amazon AWS CloudHSM

## Slide 44: Cryptography as a service

## Slide 45: Offloading security operations…
WS API: JSON

## Slide 46: … into secured environment
How to import key(s) securely?
Which hardware platform to use?
High number of clients?

## Slide 47: Cryptography as a Service (CaaS)
HSM
Notes: Focus on device technology behind CaaS
  (not business considerations)

## Slide 48: Different levels of trust
CaaS with trusted server
  Software operation only, HTTPS for in/out
  Trust to server, CaaS platform is target, insider attack
CaaS with semi-trusted server
  HTTPS for in/out, decrypted by server
  Operation send into trusted hardware
  CaaS platform still target
CaaS with untrusted server
  HTTPS for in/out, but inner protection
  Data decrypted/processed/encrypted inside device

## Slide 49: Requirements – client view
Untrusted CaaS provider (handling secrets)
Secure import of app’s secrets - enrollment
Client<->CaaS communication security
  Confidentiality/integrity of input and output data
  Authentication of input/output requests
Key use control
  Use constraints – e.g., number of allowed ops
Easy recovery from client-side compromise

## Slide 50: Requirements – CaaS provider view
Massive scalability
  W.r.t. users, keys, transactions…
Low latency of responses
Robust audit trail of key usage
Tolerance and recovery from failures
  hardware/software failures
Easy to use API
  also easy to use securely

## Slide 51: CaaS - implementation issues
Software-only CaaS more vulnerable to attacks
Classic HSMs are not build for high-level of sharing
  Performance degradation due to frequent context exchange
  Logical separation only to few entities (16-32)
  Physical separation on device-level
If interested, read more at
  Architecture Considerations for Massively Parallel Hardware Security Platform, D. Cvrcek, P. Svenda (2015) http://crcs.cz/papers/space2015

## Slide 52: HSM Security API
Hardware Security Module

## Slide 53: Application Programming Interfaces (API)
Proprietary API (legacy or custom functions)
Standardized API - but proprietary library required (PKCS#11)
Cryptographic service providers – plugin into standardized API (CNG, CSP…)
Standardized API - no proprietary component (PIV, EMV CAP…)
Proprietary (service-specific), but public API (MS KeyVault, AWS..)

## Slide 54: PKCS#11, (PKCS#15), ISO/IEC 7816-15
Standards for API of cryptographic tokens
PKCS#11
  http://www.rsa.com/rsalabs/node.asp?id=2133
  software library on PC, rather low level functions
  widely used, TrueCrypt, Mozilla FF/TB, OpenSSL, OpenVPN…
PKCS#15
  http://www.rsa.com/rsalabs/node.asp?id=2141
  both hardware and software-only tokens, identity cards…
  superseded by ISO/IEC 7816-15 standard

## Slide 55: PKCS#15 (https://github.com/OpenSC)
pkcs15-init
pkcs15-tool --dump
pkcs15-tool --list-keys
#!/bin/bash
sleep 5
pkcs15-init --create-pkcs15 --pin 12345678 --no-so-pin
sleep 5
pkcs15-init --store-pin --auth-id 01 --pin 12345678
--puk 12345678 --label “PV204 Tutorial"

## Slide 56: PKCS#11
Standardized interface of security-related functions
  vendor-specific library in OS, often paid
  communication library->card proprietary interface
Functionality cover
  slot and token management
  session management
  management of objects in smartcard memory
  encryption/decryption functions
  message digest
  creation/verification of digital signature
  random number generation
  PIN management
Secure channel not possible!
  developer can control only AppPKCS#11 lib
User Application
Vendor library
Smartcard
PKCS#11 interface
proprietary interface

## Slide 57: PKCS#11 library
API defined in PKCS#11 specification
  http://www.rsa.com/rsalabs/node.asp?id=2133
  functions with prefix ‘C_’ (e.g., C_EncryptFinal())
  header files pkcs11.h and pkcs11_ft.h
Usually in the form of dynamically linked library
  cryptoki.dll, opensc-pkcs11.dll, dkck232.dll…
  different filenames, same API functions (PKCS#11)
Virtual token with storage in file possible
  suitable for easy testing (no need for hardware reader)
  Mozilla NSS, SoftHSM…

## Slide 58: PKCS#11: role model
Functions for token initialization
  outside scope of the specification
  usually implemented (proprietary function call), but erase all data on token
Public part of token
  data accessible without login by PIN
Private part of token
  data visible/accessible only when PIN is entered

## Slide 59: PKCS#11: Cryptographic functionality
C_GetMechanismList to obtain supported cryptographic mechanisms (algorithms)
Many possible mechanisms defined (pkcs11t.h)
  CK_MECHANISM_TYPE, not all supported
  (compare to JavaCard API)
C_Encrypt, C_Decrypt, C_Digest, C_Sign, C_Verify, C_VerifyRecover, C_GenerateKey, C_GenerateKeyPair, C_WrapKey, C_UnwrapKey, C_DeriveKey, C_SeedRandom, C_GenerateRandom…

## Slide 60: PKCS#11 - conclusions
Wide support in existing applications
Low-level API
Difficult to start with
Requires proprietary library by token manufacturer
Complex standard with vague specification => security problems
  Hard to implement properly

## Slide 61: Play with HSM (without HSM )
SoftHSM
  Software-only HSM
  Open-source implementation of cryptographic store
  Botan library for cryptographic operations
  https://www.opendnssec.org/softhsm/
  https://github.com/disig/SoftHSM2-for-Windows
Utimaco HSM simulator
  https://hsm.utimaco.com/download/
  Simulator of physical HSM (with PKCS#11 and other interfaces)

## Slide 62: Microsoft CNG
Cryptography API: Next Generation (CNG API)
Long-term replacement for CryptoAPI
CNG API
  Cryptographic Primitives
  Key Storage and Retrieval
  Key Import and Export
  Data Protection API: Next Generation (CNG DPAPI)
http://msdn.microsoft.com/en-us/library/windows/desktop/aa376210%28v=vs.85%29.aspx

## Slide 63: Cryptographic Service Providers (CSP)
Generic framework with API for providers of cryptographic functionality
  E.g., implementation of RSA
  Different underlying storage (software vs. hardware-based)
Allows for runtime selection
  Connect to target provider (usually identification string)
  E.g., “Microsoft Base Cryptographic Provider v1.0”
Microsoft CSPs
  http://msdn.microsoft.com/en-us/library/windows/desktop/aa386983%28v=vs.85%29.aspx
Java CSPs (JCE)…

## Slide 64: Chip Authentication Program (CAP)
Usage of chip-based banking card for additional operations
Designed for backward compatibility
  existing cards can be used
  Separate on-card applet is preferred, but not required
Designed by MasterCard as EMV-CAP
  https://en.wikipedia.org/wiki/Chip_Authentication_Program
  Adopted by Visa as Dynamic Passcode Authentication (DPA)
Hardware CAP readers available
Python software implementation
  http://sites.uclouvain.be/EMV-CAP/Application/

## Slide 65: CAP – supported commands
Supported operations
  Code/identify
  Response
  Sign
Variants:
  Mode 1: amount included in computed cryptogram
  Mode 2: no amount, used for logging into system
  Mode 2 + TDS
    With transaction data signing
    Multiple data fields of the transaction

## Slide 66: Custom API pro/cons
Is design of own API better idea?
Pros:
  derive api in line with use
  focused api, no overhead
  highly efficient implementation
Cons:
  security holes by design
  high effort
  lost certification

## Slide 67: Attacks against API

## Slide 68: Attacks against PKCS#11
Lack of policy for function calls
  functions are too “low-level”
  sensitive objects can be manipulated directly
Key binding attack (C_WrapKey)
  target key with double length is exported from SC
  encrypted by unknown master key
  attacker divide key into two parts and import them as wrapped key for ECB mode
  perform brute-force search on each half separately
Missing authentication of wrapped key
  attacker can create its own wrapping key
  and ask for export of unknown key under his own wrapping key
Export of longer keys under shorter, …

## Slide 69: RSA padding oracle attack
Allows to recover content of encrypted message even when key is unknown
Based on 1 bit leakage from correct/incorrect padding
  Error status returned by device
(cycle) mess with encrypted message, send to card, inspect error
30 minutes with HSM, hours/days with smart card
See more at
  http://secgroup.dais.unive.it/wp-content/uploads/2012/11/Practical-Padding-Oracle-Attacks-on-RSA.html

## Slide 70: Tookan tool
Formal verification with real device model
  probe PKCS#11 token with multiple function calls
  automatically create formal model for token
  run model checker and find attack
  try to execute attack against real token
http://secgroup.dais.unive.it/projects/tookan/

## Slide 71: Conclusions
Hardware Security Module is device build for security and performance of cryptographic operations
Security certifications (but be aware of limits)
Initially mostly for banking sector
  Now more widespread (TLS, key management..)
Diverse APIs, potential logical attacks

## Slide 73: PKCS#11 details

## Slide 74: PKCS#11: Function prototypes
GetProcAddress() returns untyped function pointer
We need to cast this function pointer to known function type
Function types for PKCS#11 are in pkcs11_ft.h
typedef CK_RV CK_ENTRY (*FT_C_Encrypt)(
CK_SESSION_HANDLE hSession,
CK_BYTE_PTR pData,
CK_ULONG ulDataLen,
CK_BYTE_PTR pEncryptedData,
CK_ULONG_PTR pulEncryptedDataLen
);

## Slide 75: PKCS#11: Load and init library
int LoadAndInitLibrary(const char* path, HINSTANCE* phLib) {
CK_RV status = CKR_OK;
FT_C_Initialize fInitialize = NULL;
if (phLib) {
if ((*phLib = LoadLibrary(path)) != NULL) {
// INITIALIZE LIBRARY
fInitialize = NULL;
if ((fInitialize = (FT_C_Initialize) GetProcAddress(*phLib, "C_Initialize")) != NULL) {
(fInitialize)(NULL);
}
else status = GetLastError();
}
else status = GetLastError();
}
else status = -1;
return status;
}

## Slide 76: PKCS#11: Finalize and unload library
int FinalizeAndCloseLibrary(HINSTANCE hLib) {
CK_RV status = CKR_OK;
FT_C_Finalize fFinalize;
if (hLib != NULL) {
// UNINITIALIZE LIBRARY
fFinalize = NULL;
if ((fFinalize = (FT_C_Finalize) GetProcAddress(hLib, "C_Finalize")) != NULL) {
(fFinalize)(NULL);
}
FreeLibrary(hLib);
}
else status = -1;
return status;
}

## Slide 77: PKCS#11: List tokens in system
Slots in system are equivalent to readers
  C_GetSlotList
  C_GetSlotInfo
Slot can be empty or with inserted token
  C_GetTokenInfo

## Slide 78: PKCS#11: Connect to token
When slot with token is found
  C_OpenSession
  public session is opened
Switch to private session by inserting PIN
  C_Login
  C_Logout
C_CloseAllSessions

## Slide 79: PKCS#11: arguments lists
Most of the PKCS#11 functions accept parameters as CK_ATTRIBUTE[] array
Every value is encoded in single CK_ATTRIBUTE
  CK_ATTRIBUTE_TYPE type
  CK_VOID_PTR pValue
  CK_ULONG ulValueLen
CK_CHAR label_public[] = {"Test1_public"}; //label of data object
CK_CHAR data_public[] = {“PV204 Public"};
CK_ATTRIBUTE dataTemplate_public[] = {
{CKA_CLASS, &dataClass, sizeof(dataClass)},
{CKA_TOKEN, &ptrue, sizeof(ptrue)},
{CKA_LABEL, label_public, sizeof(label_public)},
{CKA_VALUE, (CK_VOID_PTR) data_public, sizeof(data_public)},
{CKA_PRIVATE, &pfalse, sizeof(pfalse)} // is NOT private object
};
BYTE numAttributes_public = 5;
C_CreateObject(hSession, dataTemplate_public, numAttributes_public, &hObject);

## Slide 80: PKCS#11: Store/search/get data
Data created in public/private part of the token
  CKA_PRIVATE attribute
  C_CreateObject()
User must be logged when creating/read private objects
You must find target object
  attribute template, must be logged when searching private objects
  C_FindObjectsInit()
  C_FindObjects()
  C_FindObjectsFinal()
Read data from object
  C_GetAttributeValue()