## Slide 1: High Availability
CCNP SWITCH: Implementing Cisco IP Switched Networks

## Slide 2: Chapter 9 Objectives
This chapter covers the following Cisco Catalyst switch features:
The need and basic idea behind switch stacking and VSS
StackWise
The benefits of StackWise
Verifying StackWise
VSS
VSS benefits
Verifying VSS
Supervisor redundancy
Supervisor redundancy modes

## Slide 3: The Need for Logical Switching Architectures

## Slide 4: The Need for Logical Switching Architectures
Access switchs needs its own uplink to each of the distribution switches to satisfy the redundancy requirements, but one of the uplinks has to be blocked by the Spanning Tree Protocol (STP) to prevent a loop, thus cutting the bandwidth in half.
To overcome some of these limitations, Cisco proposes the following virtualization solutions.
  StackWise: Focused on the access layer module
  VSS: Focused on the aggregation layer module

## Slide 5
What Is StackWise?

## Slide 6: What Is StackWise?
Cisco StackWise technology provides a method for collectively utilizing the capabilities of a stack of switches.
Configuration and routing information is shared by every switch in the stack, creating a single switching unit.
Switches can be added to and deleted from a working stack without affecting performance.
The stack is managed as a single unit by a master switch, which is elected from one of the stack member switches.
Notes: The switches are united into a single logical unit, using special stack interconnect cables that create a bidirectional closed-loop path.
Network topology and routing information is updated continuously through the stack interconnect.
All stack members have full access to the stack interconnect bandwidth
Up to nine separate switches can be joined.

## Slide 7: StackWise Details
Each stack of switches has a single IP address and is managed as a single object.
This allows each switch in the stack to share the same network topology, MAC address, and routing information.
Catalyst 3750-E, 3750-X, and 3850 series switches support StackWise and StackWise Plus.
StackWise Plus is an evolution of StackWise. StackWise Plus supports local switching, so locally destined packets need not traverse the stack ring.
Catalyst 3850 series supports StackWise-480 with improved 480-Gbps stacking. Catalyst 2960-S series supports FlexStack, aStackWise-based feature tailored for Layer 2 switches. FlexStack is limited to four stacked switches.
Notes: In addition, it allows for any member to become the master if the master ever fails.

## Slide 8: StackWise Benefits
Notes: Multiple switches are used to provide enough access ports. The stack, up to nine switches, is managed as a single unit, reducing the number of units that you have to manage in your network
Switches can be added to and removed from a working stack without affecting stack performance. When a new switch is added, the master switch automatically configures the unit with the currently running IOS image and the configuration of the stack.
You do not have to do anything to bring up the switch before it is ready to operate.

## Slide 9: Verifying StackWise
Notes: show switch command without additional parameters returns the shared stack MAC address and lists all the switches in a stack with their stack number, stack role, MAC address, hardware priority, hardware version, and current state.
Hardware priority is used in stack master election and can be configured. Hardware version number is associated with the switch model. Different switch models can have the same hardware version if they support the same system-level features. Hardware version number is not used in the stack master election.

## Slide 10
What Is VSS?

## Slide 11: What Is VSS?
Virtual Switching System (VSS) is a network system virtualization technology that combines a pair of Catalyst 4500 or 6500 series switches into one virtual switch, increasing the operational efficiency, boosting nonstop communications, and scaling the system bandwidth capacity.
The VSS simplifies network configuration and operation by reducing the number of Layer 3 routing neighbors and by providing a loop-free Layer 2 topology.

## Slide 12: What Is VSS?
The VSL is made of up to eight 10 Gigabit Ethernet connections bundled into an EtherChannel.
VSL carries the control plane communication between the two VSS members, in addition to regular data traffic.
Once the VSS is formed, only the control plane of one of the members is active. The data plane and switch fabric of both members are active.
Both chassis are kept in sync with the interchassis SSO mechanism, along with NSF to provide nonstop communication even in the event of failure of one of the member supervisor engines or chassis.

## Slide 13: VSS Benefits
VSS increases operational efficiency by reducing switch management overhead and simplifying the network.
It provides a single point of management, IP address, and routing instance.
Neighbors see the VSS as a single Layer 2 switching or Layer 3 routing node, thus reducing the control protocol traffic.
VSS provides a single VLAN gateway IP address, removing the need for the first-hop redundancy protocol (HSRP, VRRP, GLBP),
Multichannel EtherChannel (MEC) allows you to bundle links to two physical switches in VSS, creating a loop-free redundant topology without the need for STP.
Interchassis stateful failover results in no disruption to applications that rely on network state information.
VSS eliminates Layer 2 / Layer 3 protocol reconvergence if a virtual switch member fails, resulting in deterministic subsecond virtual switch recovery.

## Slide 14: VSS Benefits

## Slide 15: Verifying VSS
To verify the status of VSS configuration, use the following commands:
show switch virtual
show switch virtual link
show switch virtual role
show switch virtual link port-channel

## Slide 16: Verifying VSL
Notes: Use the show switch virtual link command to display virtual switch link status. More information, such as EtherChannel used for VSL, can be obtained by adding the portchannel keyword

## Slide 17: Redundant Switch Supervisors

## Slide 18: Redundant Switch Supervisors
The Cisco supervisor engine module is the heart of the Cisco modular switch platforms.
The supervisor provides centralized forwarding information and processing.
All software processes of a modular switch are run on a supervisor.
Redundant supervisors are highly recommended for the aggregation and core layer so that they might help provide faster convergence in case of the primary supervisor failure. Platforms such as the Catalyst 4500, 6500, and 6800 series can accept two supervisor modules that are installed in a single chassis, thus removing a single point of failure.
The first supervisor module to successfully boot becomes the active supervisor for the chassis.
The other supervisor remains in a standby role, waiting for the active supervisor to fail.
The active supervisor provides all switching functions. The standby supervisor, however, is allowed to boot and initialize only to a certain level.
When the active module fails, the standby module can proceed to initialize any remaining functions and take over the active role.

## Slide 19: Supervisor Redundancy Modes
Redundant supervisor modules can be configured in several modes.
Redundancy mode limits the standby supervisor’s state of readiness.
SSO allows for NSF.

## Slide 20: Supervisor Redundancy Modes
Route processor redundancy (RPR)
  The redundant supervisor is only partially booted and initialized. When the active module fails, the standby module must reload every other module in the switch and then initialize all the supervisor functions.
Route processor redundancy plus (RPR+)
  The redundant supervisor is booted, allowing the supervisor and route engine to initialize. No Layer 2 or Layer 3 functions are started. When the active module fails, the standby module finishes initializing without reloading other switch modules. This allows switch ports to retain their state.
Stateful switchover (SSO)
  The redundant supervisor is fully booted and initialized. Both the startup and running configuration contents are synchronized between the supervisor modules. Layer 2 information is maintained on both supervisors so that hardware switching can continue during a failover. The state of the switch interfaces is also maintained on both supervisors so that links do not flap during a failover.

## Slide 21: Stateful Switchover
The redundant supervisor engine starts up in a fully initialized state and synchronizes with the startup configuration and the running configuration of the active supervisor engine.
The standby supervisor in SSO mode also keeps in sync with the active supervisor engine for all changes in hardware and software states for features that are supported via SSO.
Any supported feature interrupted by failure of the active supervisor engine is continued seamlessly on the redundant supervisor engine.
Notes: On the Catalyst 6500 family of switches, the time it takes for the Layer 2 traffic to be fully operational following a supervisor failure is between 0 and 3 seconds.
On the Catalyst 4500, subsecond switchover can be achieved for Layer 2 traffic. Layer 3 information, however, needs to be relearned after a supervisor engine failover with just the SSO mode of redundancy, but the newly active supervisor engine continues to use existing Layer 2 switching information to continue forwarding traffic until Layer 3 information is relearned. This relearning involves rebuilding Address Resolution Protocol (ARP) tables and Layer 3 Cisco Express Forwarding (CEF) and adjacency tables. Until the routing converges and CEF and adjacency tables are rebuilt, packets that need to be routed are dropped.

## Slide 22: Nonstop Forwarding
NSF is an interactive method that focuses on quickly rebuilding the Routing Information Base (RIB) table after a supervisor switchover.
The RIB is used to generate the Forwarding Information Base (FIB) table for CEF, which is downloaded to any switch modules that can perform CEF.
NSF with SSO redundancy includes the standard SSO for Layer 2 switching; however, it also minimizes the amount of time that a Layer 3 network is unavailable following a supervisor engine switchover by continuing to forward IP packets using CEF entries built from the old active supervisor.
Notes: Both the Catalyst 4500 and 6500 family supports this feature

## Slide 23: Chapter 9 Summary
The need and basic idea behind switch stacking and VSS
StackWise
The benefits of StackWise
Verifying StackWise
VSS
VSS benefits
Verifying VSS
Supervisor redundancy
Supervisor redundancy modes

## Slide 24: Chapter 9 Labs
None

## Slide 26: Acknowledgment
Some of the images and texts are from Implementing Cisco IP Switched Networks (SWITCH) Foundation Learning Guide: (CCNP SWITCH 300-115) by Richard Froom and Erum Frahim (1587206641)
Copyright © 2015 – 2016 Cisco Systems, Inc.
Special Thanks to Bruno Silva