## Slide 1: Chapter 5: Inter-VLAN Routing
CCNP SWITCH: Implementing Cisco IP Switched Networks
Notes: Cisco Networking Academy Program
CCNP ROUTE: Implementing IP Routing
Chapter 1: Routing Services

## Slide 2: Chapter 5 Objectives
Given an enterprise network, design, implement, and verify inter-VLAN routing using an external router or a multilayer switch, using either switch virtual interfaces or routed interfaces
Understand Layer 3 EtherChannel and its configuration
Understand DHCP operation and its implementation and verification in a given enterprise network
Notes: Chapter 1 Objectives

## Slide 3: Describing Inter-VLAN Routing

## Slide 4: Describing Inter-VLAN Routing
Introduction to inter-VLAN routing
Inter-VLAN routing using an external router
Inter-VLAN routing with switch virtual interfaces
Routing with routed ports
Configuring inter-VLAN routing using SVI and routed ports
Troubleshooting inter-VLAN routing

## Slide 5: Introduction to Inter-VLAN Routing
Because VLANs isolate traffic to a defined broadcast domain and subnet, network devices in different VLANs cannot communicate with each other natively.
The devices in each VLAN can communicate to the network devices in another VLAN only through a Layer 3 routing device
The following devices can provide inter-VLAN routing:
  Any Layer 3 multilayer Catalyst switch
  Any external router with an interface that supports trunking (router-on-a-stick)
  Any external router or group of routers with a separate interface in each VLAN

## Slide 6: Introduction to Inter-VLAN Routing

## Slide 7: Router vs MLS for IVR
Router-on-a-stick is simple to implement because routers are usually available in every network, but most enterprise networks use multilayer switches to achieve high packet processing rates using hardware switching.
Layer 3 switches usually have packet-switching throughputs in the millions of packets per second (pps), whereas traditional general-purpose routers provide packet switching in the range of 100,000 pps to more than 1 million pps.
All the Catalyst multilayer switches support three different types of Layer 3 interfaces:
  Routed port: A pure Layer 3 interface similar to a routed port on a Cisco IOS router.
  Switch virtual interface (SVI): A virtual VLAN interface for inter-VLAN routing. In other words, switch virtual interfaces (SVIs) are the virtual routed VLAN interfaces.
  Bridge virtual interface (BVI): A Layer 3 virtual bridging interface.
Notes: Note As mentioned in previous chapters, the default configurations do not appear in the running or startup config. For some Cisco switches, the switchport command is the default configuration, and for others the no switchport command is the default configuration.

## Slide 8: Inter-VLAN Routing Using an External Router
Configure subinterfaces so that R1 that will route between PC1 (VLAN10) and PC2 (VLAN20).
Configure a trunk so that R1 will receive the traffic that needs to be routed.

## Slide 9: Routing with an External Router Configuration
Configure router subinterface for routing of VLAN 10 / VLAN 20 traffic.
R1(config)# interface ethernet 0/0.10
R1(config-subif)# encapsulation dot1q 10
R1(config-subif)# ip address 10.0.10.1 255.255.255.0
R1(config)# interface ethernet 0/0.20
R1(config-subif)# encapsulation dot1q 20
R1(config-subif)# ip address 10.0.20.1 255.255.255.0
Configure a subinterface for native VLAN traffic.
R1(config)# interface ethernet 0/0.1
R1(config-subif)# encapsulation dot1q 1 native
R1(config-subif)# ip address 10.0.1.1 255.255.255.0

## Slide 10: Verify configuration

## Slide 11: Routing with an External Router Configuration
Configure switch trunk port. Allow only VLAN 1, 10, and 20 traffic.
SW1(config)# interface ethernet 0/0
SW1(config-if)# switchport trunk encapsulation dot1q
SW1(config-if)# switchport mode trunk
SW1(config-if)# switchport trunk allowed vlan 1,10,20

## Slide 12: External Routers: Advantages Disadvantages
The following are advantages of external router usage:
An external router works with any switch because Layer 3 services are not required on the switch. Many switches do not contain Layer 3 forwarding capability, especially switches that are used at the access layer of a hierarchical network.
The implementation is simple. Only one switch port and one router interface require configuration.
If the network design includes only Layer 2 switches, the design and also the process for troubleshooting traffic flow become very simple because there is only one place in the network where VLANs interconnect.

## Slide 13: External Routers: Advantages Disadvantages
The following are disadvantages of external router usage:
The router is a single point of failure.
A single traffic path may become congested. With a router-on-a-stick model, the trunk link is limited by the speed of the router interface being shared across all trunked VLANs
Latency may be introduced as frames leave and reenter the switch chassis multiple times and as the router makes software-based routing decisions.

## Slide 14: Inter-VLAN Routing Using Switch Virtual Interfaces
An SVI is a virtual interface configured within a multilayer switch, as compared to external router configuration
An SVI can be created for any VLAN that exists on the switch. Only one VLAN associates with one SVI.

## Slide 15: Switch Virtual Interfaces
An SVI is “virtual” in that there is no physical port dedicated to the interface, yet it can perform the same functions for the VLAN as a router interface would
Can be configured in much the same way as a router interface (IP address, inbound/outbound access control lists [ACLs], and so on).
The SVI for the VLAN provides Layer 3 processing for packets to or from all switch ports associated with that VLAN.
By default, an SVI is created for the default VLAN (VLAN1) to permit remote switch administration.
Additional SVIs must be explicitly created and the number used corresponds to the VLAN tag associated.

## Slide 16: Reasons to configure SVI
To provide a gateway for a VLAN so that traffic can be routed into or out of that VLAN
To provide fallback bridging if it is required for nonroutable protocols
To provide Layer 3 IP connectivity to the switch
To support routing protocol and bridging configurations

## Slide 17: SVI: Advantages and Disadvantages
The following are some of the advantages of SVI:
It is much faster than router-on-a-stick because everything is hardware switched and routed.
No need for external links from the switch to the router for routing.
Not limited to one link. Layer 2 EtherChannels can be used between the switches to get more bandwidth.
Latency is much lower because it does not need to leave the switch.
The following are some of the disadvantages:
It needs a Layer 3 switch to perform inter-VLAN routing, which is more expensive

## Slide 18: Routing with Routed Ports
A routed port is a physical port that acts similarly to a port on a traditional router with Layer 3 addresses configured.
Unlike an access port, a routed port is not associated with a particular VLAN. A routed port behaves like a regular router interface.
Also, because Layer 2 functionality has been removed, Layer 2 protocols.
Link Aggregation Control Protocol (LACP), which can be used to build either Layer 2 or Layer 3 EtherChannel bundles, would still function at Layer 3.
Routed ports are used for point-to-point links
Routed interfaces do not support subinterfaces as with Cisco IOS routers.
To configure routed ports, make sure to configure the respective interface as a Layer 3 interface using the no switchport interface command

## Slide 19: Routed Ports: Advantages
Following are some of the advantages of routed ports:
A multilayer switch can have SVI and routed ports in a single switch. How is this an advantage of a routed port?
Multilayer switches forward either Layer 2 or Layer 3 traffic in hardware, so it helps to do routing faster.

## Slide 20: Configuring Inter-VLAN Routing Using SVI and Routed Ports

## Slide 21: Configuring Routing on a Multilayer Switch
Step 1. Create VLANs 10 and 20:
DSW1(config)# vlan 10
DSW1(config-vlan)# vlan 20
Step 2. On DSW1, enable IPv4 routing:
DSW1(config)# ip routing
Step 3. Configure SVI for VLANs with IP address
DSW1(config)# interface vlan 10
DSW1(config-if)# ip address 10.0.10.1 255.255.255.0
DSW1(config-if)# no shutdown
DSW1(config)# interface vlan 20
DSW1(config-if)# ip address 10.0.20.1 255.255.255.0
DSW1(config-if)# no shutdown

## Slide 22: Configuring Routing on a Multilayer Switch
Step 4. Turn the interface that connects to R1 (Ethernet 0/0) into a routed interface and configure it with IP address.
DSW1(config)# interface ethernet 0/2
DSW1(config-if)# no switchport
*Nov 28 15:03:55.138: %LINK-3-UPDOWN: Interface Ethernet0/2, changed state to up
*Nov 28 15:03:56.142: %LINEPROTO-5-UPDOWN: Line protocol on Interface Ethernet0/2, changed state to up
DSW1(config-if)# ip address 10.0.99.1 255.255.255.0
Step 5. Configure a Routing Protocol
DSW1(config)# router eigrp 1
DSW1(config-router)# network 10.0.0.0
*Nov 28 15:12:22.448: %DUAL-5-NBRCHANGE: EIGRP-IPv4 1: Neighbor 10.0.99.2 (Ethernet0/2) is up: new adjacency

## Slide 23: Using the SVI autostate exclude Command
The SVI interface is brought up when one Layer 2 port in the VLAN has had time to converge (transition from STP listening-learning state to forwarding state).
The default action when a VLAN has multiple ports is that the SVI goes down when all ports in the VLAN go down.
This action prevents features such as routing protocols from using the VLAN interface as if it were fully operational and minimizes other problems, such as routing black holes.
You can use the SVI autostate exclude command to configure a port so that it is not included in the SVI line-state up-and-down calculation.

## Slide 24: Configuring autostate exclude
Switch(config)# interface interface slot/number
Switch(config-if)# switchport autostate exclude
This disables the SVI autostate and makes the SVI interface permanently active.

## Slide 25: SVI Configuration Checklist
Identify which VLANs require a Layer 3 gateway.
Create a VLAN on a multilayer switch if it does not already exist.
Create an SVI interface for each VLAN.
Configure the SVI interface with an IP address.
Enable the SVI interface.
Enable IP routing on the multilayer switch.
Determine whether a dynamic routing protocol is needed.
Configure a dynamic routing protocol if needed.
Identify any switch ports that require autostate exclude.
Configure autostate exclude on identified switch ports.

## Slide 26: Common Inter-VLAN Routing Problems

## Slide 27: Troubleshooting Inter-VLAN Problems
Correct VLANs on all switches and trunks.
Correct routes.
Correct primary and secondary root bridges.
Correct IP address and subnet masks.

## Slide 28
Layer 2 Versus Layer 3 EtherChannel

## Slide 29: Layer 2 Versus Layer 3 EtherChannel
On a multilayer switch, you can configure Layer 2 or Layer 3 EtherChannels, depending on what type of devices that will be connected, and depending on their position in the network.

## Slide 30: Layer 3 EtherChannel Configuration
Step 1. Create a virtual Layer 2 interface:
Switch(config)# interface port-channel 1
Step 2. Change interface to Layer 3 and enable the use of the ip address command:
Switch(config-if)# no switchport
Step 3. Assign an IP address to the port channel interface because this will now be a Layer 3 interface:
Switch(config-if)# ip address 172.32.52.10 255.255.255.0
Step 4. Navigate to the interface that is to be associated with the EtherChannel bundle.
Switch(config)# interface range fastethernet 5/4 - 5

## Slide 31: Layer 3 EtherChannel Configuration
Step 5. Remove the independent Layer 2 and Layer 3 functionality of the port so that the port can function as part of a group:
Switch(config-if-range)# no switchport
Switch(config-if-range)# channel-protocol pagp
Step 6. Assign all of the physical interfaces in the range to the EtherChannel group:
Switch(config-if-range)# channel-group 1 mode desirable

## Slide 32: L3 EtherChannel Configuration Guidelines
The following are the guidelines for configuration for EtherChannel:
Speed and duplex: Configure all interfaces in an EtherChannel to operate at the same speed and in the same duplex mode.
Interface mode: Because the port channel interface is a routed port, the no switchport the same command must also be applied to the physical ports
Verifying the EtherChannel configuration: After EtherChannel is configured, use the following commands to verify and troubleshoot EtherChannel:
show interface port-channel channel-group-number
show etherChannel channel-group-number summary
show spanning-tree vlan vlan-number detail

## Slide 33
Implementing DHCP

## Slide 34: Implementing DHCP
Explain the idea behind DHCP
Configure a DHCP server
Configure manual DHCP bindings
Configure a DHCP relay
Configure DHCP options

## Slide 35: DHCP Overview
DHCP provides configuration parameters to Internet hosts. DHCP consists of two components: a protocol for delivering host-specific configuration parameters from a DHCP server to a host, and a mechanism for allocating network addresses to hosts.
DHCP is built on a client/server model in which designated DHCP server hosts allocate network addresses and deliver configuration parameters to dynamically configured hosts.
Clients in access VLANs need DHCP services, and not only external servers but also routers can be used for DHCP services.

## Slide 36: DHCP on MLS
Cisco multilayer switches running Cisco IOS Software include DHCP server and relay agent software.
Distribution multilayer switches often act as Layer 3 gateways for clients connecting to the access switches on various VLANs.
Therefore, the DHCP service can be provided directly by the distribution switches.
Alternatively, DHCP services can be concentrated in an external, dedicated DHCP server.
In that case, distribution switches need to redirect the incoming clients’ DHCP requests to the external DHCP server.

## Slide 37: Configuring DHCP in Multilayer Switched Network

## Slide 38: Configuring DHCP in Multilayer Switched Network
DHCP Server
DSW1(config)# ip dhcp excluded-address 10.0.10.1
DSW1(config)# ip dhcp pool VLAN10POOL
DSW1(config-dhcp)# network 10.0.10.0 255.255.255.0
DSW1(config-dhcp)# default-router 10.0.10.1
DSW1(config-dhcp)# lease 2
Assign ip address to client
DSW1(dhcp-config)# host 10.0.10.200 255.255.255.0
DSW1(dhcp-config)# client-identifier 0063.6973.636f.2d61.6162.622e.6363.3030.2e30.3630.302d.4574.302f.30
Or
DSW1(dhcp-config)# hardware-address MAC-address
Notes: O cliente identifier é conseguido depois de ser atribuído a primeira vez por dhcp com o comando show ip dhcp binding

## Slide 39: Configuring DHCP in Multilayer Switched Network

## Slide 40: DHCP Discovery Process
In addition to these four messages, the following DHCP messages are displayed with debug output:
DHCPDECLINE: Message sent from the client to the server that the address is already in use.
DHCPNAK: The server sends a refusal to the client for request for configuration.
DHCPRELEASE: Client tells a server that it is giving up a lease.
DHCPINFORM: A client already has an IP address but is requesting other configuration parameters that the DHCP server is configured to deliver such as DNS address.

## Slide 41: Configuring a DHCP Relay
A client that resides in VLAN 55 needs to have the following two configurations to forward the DHCP broadcast to the centralized server 192.168.1.244:
The multilayer switch must have a Layer 3 IP address that will receive the client DHCP request that is 10.0.55.1/24. This address may be a routed port or an SVI.
The ip helper-address command must be configured on the multilayer switch Layer 3 interface. With the DHCP relay address, when the switch receives a DHCP request in the form of a broadcast message from a client, the switch forwards this request, as a unicast message, to the IP address that is specified in the ip helper-address command.
The ip helper-address command not only forwards DHCP UDP packets but also forwards TFTP, DNS, time, NetBIOS, name server, and BOOTP packets by default.

## Slide 42: Configuring DHCP Options
Use DHCP options to “expand” the basic DHCP commands.
The following are some of the commonly used options.
  Option 43: Vendor-encapsulated option that enables vendors to have their own list of options on the server. For example, you can use it to tell a lightweight access point where the Wireless LAN Controller (WLC) is.
  Option 69: SMTP server, if you want to specify available SMTP servers to the client.
  Option 70: POP3 server, if you want to specify available POP3 servers to the client.
  Option 150: TFTP server that enables your phones to access a list of TFTP servers.

## Slide 43: Chapter 5 Summary
Inter-VLAN routing provides communication between the devices in different VLANs. Recall that a VLAN is a single broadcast domain, and the devices within a VLAN cannot communicate beyond VLAN boundaries unless through a Layer 3 device. Multilayer switches support two types of Layer 3 interfaces: routed ports and SVIs (VLAN interfaces).
Routed ports are point-to-point connections such as those that interconnect the building distribution submodules and the campus backbone submodules when using Layer 3 in the distribution layer.
SVIs are VLAN interfaces that route traffic between VLANs and VLAN group ports. In multilayer switched networks with Layer 3 in the distribution layer and Layer 2 in the access layer, SVIs can route traffic from VLANs on the access layer switches.

## Slide 44: Chapter 5 Summary
Using router-on-a-stick is an alternative and legacy method of implementing inter- VLAN routing for low-throughput and latency-tolerant applications.
On multilayer switches, Layer 3 links can be aggregated using Layer 3 EtherChannels.
When a Layer 3 interface is configured, routing can be enabled.
DHCP server function can be configured on the Cisco switches and routers.
If the network uses a centralized DHCP server, a DHCP relay agent feature can be configured on the switches by using the ip helper-address command.

## Slide 45: Chapter 5 Labs
CCNPv7.1 SWITCH Lab5.1 IVL-ROUTING
CCNPv7.1 SWITCH Lab5.2 DHCP4/6

## Slide 47: Acknowledgment
Some of the images and texts are from Implementing Cisco IP Switched Networks (SWITCH) Foundation Learning Guide: (CCNP SWITCH 300-115) by Richard Froom and Erum Frahim (1587206641)
Copyright © 2015 – 2016 Cisco Systems, Inc.
Special Thanks to Bruno Silva