## Slide 1: Campus Network Security
CCNP SWITCH: Implementing Cisco IP Switched Networks

## Slide 2: Chapter 10 Objectives
This chapter covers the following topics:
Overview of switch security issues
Required best practices for basic security protection on Catalyst switches
Campus network vulnerabilities
Port security
Storm control
Mitigating spoofing attacks
DHCP snooping, IP Source Guard, and dynamic ARP inspection
Securing VLAN trunks
Private VLANs

## Slide 3: Overview of Switch Security Issues

## Slide 4: Overview of Switch Security Issues
Most of the industry attention focuses on security attacks from outside the walls of an organization and at the upper OSI layers.
The default state of networking equipment highlights this focus on external protection and internal open communication.
Many security features are available for switches and routers, but they must be enabled to be effective

## Slide 5: Overview of Switch Security Issues
Reasons exist for strong protection of the enterprise campus infrastructure
Relying on the security that has been established at the enterprise edge fails as soon as security there is compromised. Having several layers of security increases the protection of the enterprise campus, where the most strategic assets usually reside.
If the enterprise allows visitors into its buildings, an attacker can potentially gain physical access to devices in the enterprise campus. Relying on physical security is not enough.
Very often, external access does not stop at the enterprise edge. Applications require at least an indirect access to the enterprise campus resources, which means that strong campus network security is also necessary.
Public and hybrid cloud architectures pose new risks. Even if the cloud is secure, attacks from the inside can ultimately compromise the cloud.

## Slide 6
Cisco Switch Security Configuration Best Practices

## Slide 7: Cisco Switch Security Configuration Best Practices
Secure passwords
  The enable password command employs weak encryption.
  Use enable secret whenever possible.
  Use the service password-encryption global configuration command to encrypt all passwords that cannot be encrypted using strong authentication.
  Having external AAA.
Leverage system banners
  The goal is to warn unauthorized users that their activities could be grounds for persecution.
  Use the banner login command.
Secure console access
  Even though switches usually reside in locked cabinets and access-controlled data centers, it is a best practice to configure authentication on any console.

## Slide 8: Cisco Switch Security Configuration Best Practices
Secure vty access
  Always secure all vty lines on a device.
  Configure access lists to limit access from source IP addresses of potential administrative users who try to access the device remotely.
  access-list 1 permit 10.0.0.234
  access-list 1 permit 10.0.0.235
  line vty 0 15
  access-class 1 in
Secure the embedded web interface
  If you are not using web interface to manage a switch, disable its web interface using no ip http server command.
  If you do decide to use the switch’s web interface, use HTTPS. To enable HTTPS, use the ip http secure server global configuration command.
  If you do decide to use the switch’s web interface, use access lists to limit source addresses that can access the HTTPS interface.
  access-list 1 permit 10.100.50.0 0.0.0.255
  ip http secure server
  ip http access-class 1

## Slide 9: Cisco Switch Security Configuration Best Practices
Always leverage Secure Shell (SSH) and ensure that the Telnet server is disabled
  Telnet is easy to use but not secure. All text that is sent through a Telnet session is passed in clear text.
  SSH uses strong encryption to secure session data. You should use the highest SSH version available on the device.
Secure SNMP access
  If you do not need the write access through SNMP, disable it.
  It is always recommended to exclusively use SNMPv3, which leverages secure authentication.

## Slide 10: Cisco Switch Security Configuration Best Practices
Secure STP operation
  You should always enable the BPDU Guard feature on any access switch ports.
  Do not ever configure BPDU Guard and BPDU Filter on the same port. If you do, only BPDU Filter will take effect.
Secure Cisco Discovery Protocol (CDP)
  As a rule, all Cisco devices have CDP enabled on all ports by default. Disable CDP on ports that connect to outside networks.
  In addition, always disable CDP on end-user access ports.
  CDP advertisements are sent in clear text, and you cannot configure authentication.
Notes: You should always enable the BPDU Guard feature on any access switch ports. This way, if an unexpected BPDU is received, the port will be automatically disabled.
Do not ever configure BPDU Guard and BPDU Filter on the same port. If you do, only BPDU Filter will take effect. BPDU Filter ignores BPDUs when enabled on an interface; and if you enable it on access ports, this can be a great opportunity for a Layer 2 loop to occurs

## Slide 11: Cisco Switch Security Configuration Best Practices
Secure unused switch ports
  All unused switch ports should be shut down to prevent unauthorized users from connecting to your network.
  All user ports should be configured with switchport mode access command.
  Place all unused ports into an isolated or bogus VLAN.
Notes: You should always enable the BPDU Guard feature on any access switch ports. This way, if an unexpected BPDU is received, the port will be automatically disabled.
Do not ever configure BPDU Guard and BPDU Filter on the same port. If you do, only BPDU Filter will take effect. BPDU Filter ignores BPDUs when enabled on an interface; and if you enable it on access ports, this can be a great opportunity for a Layer 2 loop to occurs

## Slide 12
Campus Network Vulnerabilities

## Slide 13: Rogue Access
Rogue access comes in several forms.
These rogue devices can be a serious breach of network security because they can be plugged into a network port behind the corporate firewall.
Because employees generally do not enable any security settings on the rogue AP, it is easy for unauthorized users to use the AP to intercept network traffic and hijack client sessions.

## Slide 14: Switch Vulnerabilities
Attacks that are launched against switches and at Layer 2 can be grouped as follows:
MAC layer attacks
VLAN attacks
Spoofing attacks
Attacks on switch devices

## Slide 15: MAC Layer Attacks
MAC Address Flooding
  Frames with unique, invalid source MAC addresses flood the switch, exhausting the content-addressable memory (CAM) table space, disallowing new entries from valid hosts.
  Traffic to valid hosts is then flooded out all ports.
Mitigation
  Port security.
  MAC address VLAN access maps.

## Slide 16: VLAN Attacks
VLAN Hopping
  By altering the VLAN ID on packets that are encapsulated for trunking, an attacking device can send packets on various VLANs, bypassing Layer 3 security measures.
Mitigation
  Tighten up trunk configurations and the negotiation state of unused ports. Shut down unused ports. Place unused ports in a common VLAN.
Attacks Between Devices on a Common VLAN
  Devices may need protection from one another, even though they are on a common VLAN. This is especially true o service provider segments that support devices from multiple customers.
Mitigation
  Implement private VLANs (PVLANs).

## Slide 17: Spoofing Attacks
DHCP Starvation and DHCP Spoofing
  An attacking device can exhaust the address space available to the DHCP servers for a time period or establish itself as a DHCP server in man-in-the-middle attacks.
Mitigation
  Use DHCP snooping.
Spanning-tree Compromises
  Attacking device spoofs the root bridge in the Spanning Tree Protocol (STP) topology. If successful, the network attacker can see various frames.
Mitigation
  Proactively configure the primary and backup root devices.
  Enable Root Guard.

## Slide 18: Spoofing Attacks
MAC Spoofing
  Attacking device spoofs the MAC address of a valid host currently in the CAM table. The switch then forwards to the attacking device any frames that are destined for the valid host.
Mitigation
  Use DHCP snooping, port security.
Address Resolution Protocol (ARP) spoofing
  Attacking device crafts Address Resolution Protocol (ARP) replies intended for valid hosts. The MAC address of the attacking device then becomes the destination address that is found in the Layer 2 frames that were sent by the valid network device.
Mitigation
  Use DAI.
  Use DHCP snooping, port security.

## Slide 19: Switch Device Attacks
Cisco Discovery Protocol (CDP manipulation)
  Information sent through CDP is transmitted in clear text and unauthenticated, allowing it to be captured and to divulge network topology information.
Mitigation
  Disable Cisco Discovery Protocol on all ports where it is not intentionally used.
SSH Protocol and Telnet Attacks
  Telnet packets can be read in clear text. SSH is an option, but it has security issues in Version 1.
Mitigation
  Use SSH Version 2.
  Use Telnet with vty ACLs.

## Slide 20: Introducing Port Security

## Slide 21: Introducing Port Security
Port security restricts a switch port to a specific set or number of MAC addresses.
Those addresses can be learned dynamically or configured statically.
The port will then provide access to frames from only those addresses.

## Slide 22: Port Security Process
1. Configure port security.
  Configure port security to allow only the desired number of connections on the port.
  Configure an entry for each of these allowed MAC addresses.
  This configuration, in effect, populates the MAC address table with new entries for that port and allows no additional entries to be learned dynamically.
2. Allowed frames are processed.
  When frames arrive on the switch port, their source MAC address is checked against the MAC address table. If the frame source MAC address matches an entry in the table for that port, the frames are forwarded to the switch to be processed like any other frames on the switch.

## Slide 23: Port Security Process (cont)
3. New addresses are not allowed to create new MAC address table entries.
  When frames with a nonallowed MAC address arrive on the port, the switch determines that the address is not in the current MAC address table and does not create a dynamic entry for that new MAC address, because the number of allowed addresses has been limited.
4. Switch takes action in response to nonallowed frames.
  The switch will disallow access to the port and take one of these configuration-dependent actions: the entire switch port can be disabled, access can be denied for that MAC address only and a log error can be generated, or access can be denied for that MAC address but without generating a log message.

## Slide 24: Port Security Configuration
switchport port-security maximum value
  Optionally sets the maximum number of secure MAC addresses for the interface. The range is 1 to 3072; the default is 1.
switchport port-security violation { restrict | shutdown }
  Optionally sets the violation mode, the action to be taken when a security violation is detected, as one of these:
    restrict A port security violation restricts data and causes the SecurityViolation counter to increment and send an SNMP trap notification.
    shutdown The interface is err-disabled when a portsecurity violation occurs.
switchport port-security limit rate invalid-source-mac
  Sets the rate limit for bad packets.

## Slide 25: Port Security Configuration (cont)
switchport port-security mac-address mac-address
  Optionally enters a secure MAC address for the interface.
  You can use this command to enter the maximum number of secure MAC addresses. If you configure fewer secure MAC addresses than the maximum, the remaining MAC addresses are dynamically learned.
switchport port-security mac-address sticky
  Optionally enables sticky learning on the interface.

## Slide 26: Port Security Example

## Slide 27: Port Security Example II

## Slide 28: Port Error Conditions
The following list highlights the most common situations where a port will go into the err-disabled state:
Port security violation
  When an invalid MAC address is learned on a port or too many MAC addresses, the switch can optionally place the port into the err-disabled state.
Spanning-tree BPDU guard violation
  When you have PortFast configured in combination with BPDU Guard
EtherChannel misconfiguration
  All parameters have to be the same for all ports on both sides of the bundle
Duplex mismatch
  Duplex mode has to be the same on both sides of the link;

## Slide 29: Port Error Conditions (cont)
UDLD condition
  Unidirectional Link Detection (UDLD) ensures that the link is bidirectional at all times; so when it detects a unidirectional link, it places the port into the err-disabled state.
Spanning-tree Root Guard
  If a Root Guard-enabled port receives a superior BPDU from those sent by the current root bridge
Link flapping
  When link state is flapping between the up and down states, the port is placed into the err-disabled state.
Other reasons
  Other reasons include late collision detection, Layer 2 Tunneling Protocol Guard, DHCP snooping rate-limit, incorrect gigabit interface convert (GBIC), and ARP inspection.

## Slide 30: Err-Disable Ports
Err-disabled detection is enabled for all of these causes by default.
You can configure other reasons to trigger the port being disabled.
Use the following command to specify the causes:
Switch(config)# errdisable detect cause [ all | cause-name ]

## Slide 31: Err-Disabled Automatic Recovery
Once the root cause of the err-disabled state is removed, an err-disabled port can become operational after a shut / no shut.
Because the error condition is no longer present, the trigger for err-disable will not occur.
Therefore, to reduce the administrative overhead, the switch port can be configured to be automatically reenabled after a specified time.
Of course, if the error condition is still present, the port will immediately go back to the err-disabled state.

## Slide 32: Port Access Lists
Port access lists (PACLs) are yet another way to apply security in the campus network.
Standard access control lists (ACLs) are applied to traffic passing through the Layer 3 interface.
The PACL feature provides the ability to perform access control on a specific Layer 2 port.
A Layer 2 port is a physical access or trunk port that belongs to a VLAN.
The port ACL feature is supported only in hardware. (Port ACLs are not applied to any packets routed in software.)
The PACL feature does not affect Layer 2 control packets, such as CDP, VTP, DTP, and STP, received on the port.

## Slide 33: Port Access Lists
There are two types of PACL:
IP access list
  Filters IPv4 and IPv6 packets on a Layer 2 port.
MAC access list
  Filters packets that are of an unsupported type (not IP, ARP, or MPLS) based on the fields of the Ethernet frame.
  A MAC access list is not applied to IP, MPLS, or ARP messages.
  You can define only named MAC access lists.

## Slide 34: Port Access Lists
PACLs interaction with other types of ACLs depends on the configured mode:
  In prefer port mode , the PACL takes effect and overrides the effect of other ACLs. This mode is the only mode that is allowed when applying PACL on a trunk.
  In merge mode , PACLs, VACLs, and standard ACLs are merged in the ingress direction. This is the default mode.
IP and MAC ACLs can be applied to Layer 2 physical interfaces. Standard (numbered, named) and extended (numbered, named) IP ACLs and extended named MAC ACLs are supported.

## Slide 35: Port Access Lists
Commands to configure a MAC ACL and apply it to a Layer 2 interface:
SW(config)# mac access-list extended acl-name
SW(config-ext-macl)# permit host [ source-mac | any ] [ destination-mac | any ]
SW(config-ext-macl)# interface interface-slot/number
SW(config-if)# mac access-group acl-name in
Commands to configure an IP ACL and apply it to a Layer 2 interface:
SW(config)# ip access-list acl-type acl-name
SW(config-ext-nacl)# permit protocol [ source-address | any ] [ destination-address | any ]
SW(config-ext-nacl)# interface interface-slot/number
SW(config-if)# ip access-group acl-name in

## Slide 36: PACL’s Group Mode
Configure the access group mode on a Layer 2 interface:
SW(config)# interface interface-slot/number
SW(config-if)# access-group mode [ prefer port | merge ]
Note:
  Access mode command is not supported on all platforms.

## Slide 37
Storm Control

## Slide 38: Storm Control
Describe what a traffic storm is and how to control it
Configure and verify storm control

## Slide 39: Introduction to Storm Control
A traffic storm occurs when packets flood the LAN, creating excessive traffic and degrading network performance.
The storm control feature prevents LAN ports from being disrupted by a broadcast, multicast, or unicast traffic storm on physical interfaces.

## Slide 40: Storm Control Behavior
During the interval, it compares the traffic level with the traffic storm threshold level that you configure.
The traffic storm control level is either an absolute number of bits or packets per second or a percentage of the total available bandwidth of the port.
Two thresholds can be configured.
When traffic exceeds the rising threshold level, storm control blocks the port.
Once the traffic falls under the falling threshold, storm control removes the block.
Configuration of a falling threshold is optional.

## Slide 41: Storm Control Behavior
Optionally, an interface can be shut down if a threshold level is breached or an SNMP trap is sent.
In addition, storm control is configured per interface for each traffic type (unicast, multicast, broadcast) separately.

## Slide 42: Configuring and Verifying Storm Control on an Interface
Switch(config)# interface interface-slot/int
Switch(config-if)# storm-control [ broadcast | multicast | unicast ] level { risingpercent | bps rising-bps | pps rising-pps } [falling-percent|falling-bps|falling-pps]
Switch(config)# interface interface-slot/int
Switch(config-if)# storm-control action { shutdown|trap }
Notes: Another noted caveat is that although storm control can be configured on the port channel interface of an EtherChannel, do not configure it on ports that are members of an EtherChannel because it is an unsupported configuration.

## Slide 43: Verify Storm Control Configurations
Notes: Note Traffic generation tools such as iPerf are useful in testing storm control in a lab environment.

## Slide 44
Mitigating Spoofing Attacks

## Slide 45: Mitigating Spoofing Attacks
How can a rogue DHCP server harm your network
DHCP spoofing
Configuring and verifying DHCP snooping
What IP Source Guard is and why you need it
Configuring IP Source Guard
ARP spoofing
How DAI works
Configure DAI

## Slide 46: DHCP Spoofing Attacks
The most common example of a rogue DHCP server is when a PC is configured as a DHCP server in the campus network.
If the rogue DHCP server’s reply arrives at the DHCP client first, the client will use this response.
Because this first response from the rogue server is bogus, the client will not be able to gain the correct network connectivity and may have its traffic redirected to a bogus default gateway

## Slide 47: Rogue DHCP Server Process
Attacker hosts a rogue DHCP server off a switch port to the same subnet as the clients.
Client broadcasts a request for DHCP configuration information.
The rogue DHCP server responds before the legitimate DHCP server, assigning attacker-defined IP configuration information.
Host packets are redirected to the attacker’s address because it emulates a default gateway for the erroneous IP address that is provided to the client via DHCP.

## Slide 48: DHCP Snooping
DHCP Snooping feature configures two types of port:
Trusted ports
  Host a DHCP server or can be an uplink toward the DHCP server.
Untrusted ports
  Are those that are not explicitly configured as trusted.
  From a DHCP snooping perspective, untrusted access ports should not send any DHCP server responses, such as DHCPOFFER, DHCPACK, or DHCPNAK.
  If a rogue device on an untrusted port attempts to send a DHCP response packet into the network, the port is shut down.
  This feature can be coupled with DHCP option 82, in which switch information, such as the port ID of the DHCP request, can be inserted into the DHCP request packet.
Notes: DHCP Option 82
As mentioned in the previous section, DHCP option 82 provides additional security when DHCP is used to allocate network addresses. This feature enables the DHCP relay agent, to include information about itself and the attached client in the DHCP request frames when forwarding DHCP requests from a DHCP client to a DHCP server.
The DHCP server can then use this information to assign IP addresses, perform access control, and set quality of service (QoS) and security policies (or other parameterassignment policies) for each subscriber of a service provider network. Some cable providers use DHCP option 82 with cable modems to ensure access control and quality of server for business class users among residential users. Alternatively, if the information is not present or incorrect, the DHCP server could choose to ignore the request. DHCP option 82 along with DHCP snooping are both best practices for campus networks as an additional security measure.

## Slide 49: DHCP Snooping

## Slide 50: DHCP Snooping Example Configuration

## Slide 51: DHCP Snooping Example Configuration
Steps to enable DHCP snooping for VLAN 10 with a DHCP server on Ethernet 0/0:
Step 1. Enable DHCP snooping globally.
Step 2. Enable DHCP snooping on selected VLANs.
Step 3. Configure trusted interfaces, since untrusted is default.
Step 4. Configure rate-limit of DHCP requests on untrusted ports.
Step 5. Configure information option using DHCP option 82.
Notes: If you want to provide more information about the actual client that generated the DHCP request, configure DHCP option 82 with the ip dhcp snooping information option command.

## Slide 52: Verifying DHCP Snooping Configuration

## Slide 53: Verifying DHCP Snooping Configuration

## Slide 54: DHCP Snooping Command Review
ip dhcp snooping
  Enables DHCP snooping globally. By default, the feature is not enabled.
ip dhcp snooping information option
  Enables DHCP option 82. This is optional for the forwarded DHCP request packet to contain information on the switch port where it originated. The option is enabled by default.
ip dhcp snooping vlan vlan-id [ vlan-id ]
  Identifies VLANs that will be subject to DHCP snooping.
ip dhcp snooping trust
  Configures trusted port. Use the no keyword to revert to untrusted. Use this command in the interface configuration mode.
ip dhcp snooping limit rate rate
  Configures the number of DHCP packets per second that an interface can receive. This ensures that DHCP traffic will not overwhelm the DHCP servers. Normally, the rate limit applies to untrusted interfaces. Use this command in the interface configuration mode.
show ip dhcp snooping
  Verifies the configuration.

## Slide 55: IP Source Guard
IPSG operates by dynamically maintaining per-port VLAN ACLs based on learned IP-to-MAC-to-switch-port bindings.
When IPSG is enabled, the switch blocks all IP traffic into the port except for DHCP packets captured by the DHCP snooping process.
After the DHCP process is complete and the client receives a valid IP address from the DHCP server (or when a static IP source binding is configured by the user), a per-port and VLAN access control list (PVACL) is installed on the port dynamically.
This process restricts the client IP traffic ingress on the respective port to the source IP address that is configured in the binding.
Any IP traffic with a source IP address other than that in the IP source binding will be filtered out.
Notes: Note If IPSG is enabled on a trunk port with a large number of VLANs that have DHCP snooping enabled, the switch might not have enough ACL hardware resources to accommodate this configuration. Consult Cisco.com for ACL limitations before enabling IPSG on trunk ports.
Nevertheless, the best practice is to enable IPSG on access ports.

## Slide 56: IPSG Topology Layout

## Slide 57: IPSG Filters
For each untrusted port, there are two possible levels of IP traffic security filtering:
Source IP address filter
  IP traffic is filtered based on its source IP address. Only IP traffic with a source IP address that matches the IP source binding entry is permitted. An IP source address filter is changed when a new IP source entry binding is created or deleted on the port.
Source IP and MAC address filter
  IP traffic is filtered based on its source IP address in addition to its MAC address; only IP traffic with source IP and MAC addresses that match the IP source binding entry are permitted.

## Slide 58: IPSG Configuration

## Slide 59: IPSG Configuration
To enable IPSG on the port use the ip verify source interface command for enabling IP address filters.
To enable MAC address filtering and IP filters, add the ip verify source port-security interface command.

## Slide 60: IPSG Configuration and State Verification

## Slide 61: ARP Spoofing

## Slide 62: ARP Spoofing
Step 1. PCA sends an ARP request for MAC address of R1.
Step 2. R1 replies with its MAC and IP address. It also updates its ARP cache.
Step 3. PCA binds MAC address of R1 to R1’s IP address in its ARP cache.
Step 4. Attacker sends its ARP reply to PCA, binding its MAC address to the IP of R1.
Step 5. PCA updates ARP cache with MAC address of attacker bound to IP address of R1.
Step 6. Attacker sends its ARP reply to R1, binding its MAC address to the IP of PCA.
Step 7. R1 updates ARP cache with MAC address of attacker bound to IP address of PCA.
Step 8. Packets are diverted through attacker.

## Slide 63: Dynamic ARP Inspection
Dynamic ARP inspection (DAI) helps prevent such attacks by not relaying invalid or gratuitous ARP replies out to other ports in the same VLAN.
DAI intercepts all ARP requests and all replies on the untrusted ports.
Each intercepted packet is verified for valid IP-to-MAC binding similar to IPSG.
ARP replies coming from invalid devices are either dropped or logged by the switch for auditing so that ARP poisoning attacks are prevented.
You can also use DAI to rate-limit the ARP packets and then err-disable the interface if the rate is exceeded.
DAI determines the validity of an ARP packet based on a valid MAC-address-to-Ip address bindings database that is built by DHCP snooping.
In addition, to handle hosts that use statically configured IP addresses, DAI can validate ARP packets against user configured ARP ACLs.

## Slide 64: DAI Configuration Steps
Step 1. Implement protection against DHCP spoofing:
  a. Enable DHCP snooping globally.
  b. Enable DHCP snooping on selected VLANs.
Step 2. Enable DAI: Enable ARP inspection on selected VLANs.
Step 3. Configure trusted interfaces for DHCP snooping and ARP inspection (untrusted is default).
Notes: ■ Forwards ARP packets that are received on a trusted interface without any checks
■ Intercepts all ARP packets on untrusted ports
■ Verifies that each intercepted packet has a valid IP-to-MAC address binding before forwarding packets that can update the local ARP cache
■ Drops, logs, or drops and logs ARP packets with invalid IP-to-MAC address bindings

## Slide 65: DAI Configuration

## Slide 66: DAI Commands
ip arp inspection vlan vlan-id [ , vlan-id ]
  Enables DAI on a VLAN or range of VLANs
ip arp inspection trust
  Sets the interface as a trusted interface
ip arp inspection validate {[ src-mac ] [ dst-mac ] [ ip ]}
  Configures DAI to drop ARP packets when the IP addresses are invalid, or when the MAC addresses in the body of the ARP packets do not match the addresses that are specified in the Ethernet header

## Slide 67
Securing VLAN Trunks

## Slide 68: Securing VLAN Trunks
Describe the switch spoofing attack associated with VLAN trunks
Protect your network against switch spoofing
Describe the VLAN hopping attack
Protect your network against the VLAN hopping attack
Describe the need for VLAN access lists
Describe how VLAN access lists interact with standard and port access lists
Configure the VLAN access lists

## Slide 69: Switch Spoofing
There are several mechanisms or best practices to minimize authorized access to trunk ports and switch spoofing, including the following
  Manually configure access and trunk ports
  Shut down unused interfaces
  Restrict VLANs on trunk ports

## Slide 70: Switch Spoofing

## Slide 71: VLAN Hopping
The IP-enabled device the attacker is using must be connected to an access port.
The IP-enabled device must send a double-tagged frame.
The first-hop switch must be configured to accept 802.1Q frames.
The first-hop switch must be connected to another switch with an 802.1Q truck, and its native VLAN must match the attackers outer VLAN tag.

## Slide 72: Protecting Against VLAN Hopping
Because an attacker’s port VLAN must match the native VLAN of a trunk, the simple solution is to configure the native VLAN of all trunk ports to an unused VLAN.
SW(config)# interface interface-slot/number
SW(config-if)# switchport trunk native vlan vlan-id
SW(config-if)# switchport trunk allowed vlan remove vlan-id
Yet another option is to tag all frames on trunk ports by default. The command to configure this option is as follows:
SW(config)# vlan dot1q tag native
Notes: Note, maintenance protocols, such as CDP and DTP, are normally carried over the native VLAN. Native VLAN pruning will not affect the functionality of these protocols because they will use the native VLAN regardless of configuration.

## Slide 73: VLAN Access Lists
VACLs can provide access control for all packets that are bridged within a VLAN or packets that are routed into or out of a VLAN or a WAN interface.
VACLs can configured for IP or MAC layer traffic with some limitations depending on platform and software version.
VLAN access lists (VACLs) on Catalyst switches serve the following two distinct purposes:
  With certain limitations, filter traffic at Layer 2
  Overcome VLAN Switch Port Analyzer (SPAN) limitations via use of the Capture Port feature

## Slide 74: VACLs Process
Each VLAN access map can consist of one or more map sequences; each sequence has a match clause and an action clause.
The match clause specifies IP or MAC ACLs for traffic filtering, and the action clause specifies the action to be taken when a match occurs.
When a flow matches a permit ACL entry, the associated action is taken, and the flow is not checked against the remaining sequences.
When a flow matches a deny ACL entry, it will be checked against the next ACL in the same sequence or the next sequence.
If a flow does not match any ACL entry and at least one ACL is configured for that packet type, the packet is denied.

## Slide 75: Advantage of VACL Capture Port usage over VSPAN
Granular traffic analysis
  VACLs can match based on source IP address, destination IP address, Layer 4 protocol type, source and destination Layer 4 ports, and other information.
The number of sessions
  VACLs are enforced in hardware..
Destination port oversubscription
  Granular traffic identification reduces the number of frames to be forwarded to the destination port and thereby minimizes the probability of their oversubscription.
VACLs are enforced in hardware
Notes: EXAMPLE
interface GigabitEthernet1/1 description PRI-CAPTURE-PORT switchport switchport access vlan 999 switchport mode access switchport capture switchport capture allowed vlan 110 no ip address spanning-tree portfast

## Slide 76: VACL Interaction with ACLs and PACLs

## Slide 77: Configuring VACLs
SW(config)# mac access-list extended acl-name
SW(config-ext-macl)# permit host [ source-mac | any ] [ destination-mac | any ]
SW(config)# ip access-list acl-type acl-name
SW(config-ext-nacl)# permit protocol [ source-address | any ] [ destination-address | any ]
SW(config)# vlan access-map map-name
SW(config-access-map)# match [ mac | ip ] address acl-name
SW(config-access-map)# action [drop|forward|redirect][log]
SW(config)# vlan filter map-name vlan-list [ vlan-list | all ]

## Slide 78: VACL examples

## Slide 79: Private VLANs

## Slide 80: Private VLANs
Introduction to private VLANs
Describe the private VLAN feature
Describe the private VLAN port types
Configure private VLANs
Verify private VLAN configuration
Describe private VLANs across multiple switches
Describe the protected port feature

## Slide 81: Introduction to PVLANs
PVLANs restrict enduser devices such as PCs and mobile devices from communicating with each other, but still allow communication to router ports and network services.
The end-user devices will behave as normal but cannot communicate to other devices in the same Layer 2 domain.
This mechanism provides a level of security.
Assigning every single end device its own VLAN would accomplish the same security method as PVLANs; however, switches have a limit on the number of VLANs supported, and a large number of VLANs creates scalability issues.

## Slide 82: Introduction to PVLANs
PVLANs are essentially VLANs inside a VLAN.
A Layer 3 device is needed to route packets between different PVLANs.
When a VLAN is partitioned into PVLANs, devices in different PVLANs still belong to the same IP subnet, but are unable to communicate with each other on Layer 2.
PVLANs are an elegant solution when you need to keep multiple devices in the same IP subnet yet provide port isolation on Layer 2.

## Slide 83: Introduction to PVLANs

## Slide 84: PVLAN Port Types
A PVLAN domain has one primary VLAN.
Each port in a private VLAN domain is a member of the primary VLAN; the primary VLAN is the entire private VLAN domain.
Secondary VLANs are subdomains that provide isolation between ports within the same private VLAN domain.
There are two types of secondary VLANs: isolated VLANs and community VLANs.
  Isolated VLANs contain isolated ports, which cannot communicate between each other in the isolated VLAN.
  Community VLANs contain community ports that can communicate between each other in the community VLAN.

## Slide 85: PVLAN Port Types
Notes: A PVLAN domain has one primary VLAN. Each port in a private VLAN domain is a member of the primary VLAN; the primary VLAN is the entire private VLAN domain.
Secondary VLANs are subdomains that provide isolation between ports within the same private VLAN domain. There are two types of secondary VLANs: isolated VLANs and community VLANs. Isolated VLANs contain isolated ports, which cannot communicate between each other in the isolated VLAN. Community VLANs contain community ports that can communicate between each other in the community VLAN.

## Slide 86: PVLAN Port Types
Promiscuous
  A promiscuous port belongs to the primary VLAN and can communicate with all mapped ports in the primary VLAN, including community and isolated ports.
  There can be multiple promiscuous ports in a primary VLAN.
Isolated
  An isolated port is a host port that belongs to an isolated secondary VLAN.
  An isolated port has complete isolation from other ports, except with associated promiscuous ports.
  You can have more than one isolated port in a specified isolated VLAN.
Community
  A community port is a host port that belongs to a community secondary VLAN.
  Community ports communicate with other ports in the same community VLAN and with associated promiscuous ports.
  They are isolated from all ports in other community VLANs and all isolated ports.

## Slide 87: PVLAN Configuration
VTP must be set to transparent or off.
Configure the primary VLAN.
Configure the secondary VLANs and apply the configuration of these PVLANs as isolated or community.
Associate the primary VLAN with the secondary VLANs

## Slide 88: Assign Ports
Promiscuous Ports
SW(config)# interface interface-slot/number
SW(config-if)# switchport mode private-vlan promiscuous
SW(config-if)# switchport private-vlan mapping primary-vlan-id add secondary-vlanid {, secondary-vlan-id }
Community or Isolated Ports
SW(config)# interface range interface-range
SW(config-if-range)# switchport mode private-vlan host
SW(config-if-range)# switchport private-vlan host-association primary-vlan-id secondary-vlan-id

## Slide 89: Assign Ports

## Slide 90: Using the Protected Port Feature
The PVLAN feature is not available on all switches.
Protected port, also known as the PVLAN edge, is a feature that (unlike PVLANs) has only local significance to the switch.
Protected ports do not forward any traffic to protected ports on the same switch.
SW(config)# interface interface-slot/number
SW(config-if)# switchport protected

## Slide 91: Chapter 10 Summary
Configure port security to limit and filter MAC addresses on ports; port security supports features that reduce the overhead of assigning MAC addresses per port.
Use PVLANs to restrict traffic within a VLAN with simple configuration.
Leverage DHCP snooping, DAI, and IPSG to prevent spoofing attacks.
Consider VACLs when appropriate to block unnecessary traffic and known traffic attacks.
Always adhere to basic security configurations such as AAA on all Cisco devices.
Stay current on all vulnerabilities and security notices from Cisco.
Keep current on Cisco Catalyst software versions because new software versions address known vulnerabilities.

## Slide 92: Chapter 10 Labs
CCNPv7.1 SWITCH Lab 10.1 Securing Layer2
CCNPv7.1 SWITCH Lab 10.2 Securing VLANs

## Slide 94: Acknowledgment
Some of the images and texts are from Implementing Cisco IP Switched Networks (SWITCH) Foundation Learning Guide: (CCNP SWITCH 300-115) by Richard Froom and Erum Frahim (1587206641)
Copyright © 2015 – 2016 Cisco Systems, Inc.
Special Thanks to Bruno Silva