## Slide 1: Software-defined networks (SDN) PA160: Net-Centric Computing II.
Tomáš Rebok
Institute of Computer Science Masaryk University
rebok@ics.muni.cz

## Slide 2
Motivation

## Slide 3: Traditional Computing vs Modern Computing

## Slide 4: Traditional vs Modern Computing Provisioning Methods
Source: Adopted from Transforming the Network With Open SDN by Big Switch Network

## Slide 5: Modern Networking Complexity
Ref: Javvin

## Slide 6: The Ossified Network
Million of lines of source code
6000+ RFCs
Barrier to entry
Billions of gates
Bloated
Power Hungry
Many complex functions baked into the infrastructure
    OSPF, BGP, multicast, differentiated services, Traffic Engineering, NAT, firewalls, MPLS, redundant layers, …
An industry with a “mainframe-mentality”, reluctant to change
Specialized Packet Forwarding Hardware
Operating
System
Feature
Feature
Routing, management, mobility management, access control, VPNs, …
6
Notes: 6

## Slide 7: Traditional vs Modern Networking Provisioning Methods
Source: Adopted from Transforming the Network With Open SDN by Big Switch Network

## Slide 8: Computing vs Networking
Source: Adopted from Transforming the Network With Open SDN by Big Switch Network

## Slide 14: Software-Defined Networking (SDN)
The answer to necessary networking evolution
      making them able to better (i.e. more flexibly, faster, …) react to current requirements
The basic idea: Management of network services through abstraction of lower-level functionality
      decoupling the system that makes decisions about where traffic is sent (the control plane) from the underlying systems that forward traffic to the selected destination (the data plane)
      centralized management

## Slide 15
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
Operating
System
Operating
System
Operating
System
Operating
System
Operating
System
App
App
App
15
Current Internet
Closed to Innovations in the Infrastructure
Closed
Notes: The next 3 slides are a set of animation to show how we enable innovation:
- Infrastructure is closed to innovation and only driven by vendors. Consumers have little say
- Business model makes it hard for new features to be added

## Slide 16: “Software Defined Networking” approach to open it
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
Operating
System
Operating
System
Operating
System
Operating
System
Operating
System
App
App
App
Network Operating System
App
App
App
Notes: How do we redefine the architecture to open up networking infrastructure and the industry!
By bring to the networking industry what we did to the computing world

## Slide 17: The “Software-defined Network”
App
Simple Packet Forwarding Hardware
Simple Packet Forwarding Hardware
Simple Packet Forwarding Hardware
App
App
Simple Packet Forwarding Hardware
Simple Packet Forwarding Hardware
Network Operating System
1. Open interface to hardware
3. Well-defined open API
2. At least one good operating system
Extensible, possibly open-source
Notes: Switches, routers and other middleboxes are dumbed down
The key is to have a standardized control interface that speaks directly to hardware

## Slide 18
Software-defined network (SDN)

## Slide 19: SDN – Basic Concepts
Software-Defined Networking = a modern buzzword 
      like Software-Defined Anything…
Several SDN concepts have been proposed
      all of them follow the basic ideas
        centralized control, programmability, flexibility, …
      could be based on:
        uniform configuration of (more or less) traditional devices
          RESTconf, NETconf, specialized protocols, …
        novel networking paradigm (requiring novel devices)
          OpenFlow

## Slide 20
Notes: Switches, routers and other middleboxes are dumbed down
The key is to have a standardized control interface that speaks directly to hardware

## Slide 27: SDN – benefits summary
Reducing overhead costs (easier management)
      centralized management
Easier and faster deployment of new services
      from weeks/months to days/hours/minutes
Higher flexibility
      allowing to support applications with specific needs
Higher usage efficiency
      lowering over-provisioning
Support of new features and applications
      including e.g. virtualization/slicing of the network
etc. etc.
Notes: Ondro, jen pro Tebe: overprovisioning je volna kapacita site, kterou musis ponechat, aby sit fungovala (v SDN si muzes diky vysoke flexibilite ty toky planovat efektivneji)

## Slide 28
OpenFlow protocol

## Slide 29: SDN/OpenFlow - introduction
A novel networking paradigm
      first standard communication interface between the control and forwarding layers
        vendor-independent
          forwarding HW has to comply with the OpenFlow specification
      allows direct access to and manipulation of the forwarding plane of network devices
          besides basic OpenFlow SW client, the devices contain packet forwarding tables (flow tables)
            define packet matching rules and packet actions

## Slide 30
Notes: Switches, routers and other middleboxes are dumbed down
The key is to have a standardized control interface that speaks directly to hardware

## Slide 31
Notes: Switches, routers and other middleboxes are dumbed down
The key is to have a standardized control interface that speaks directly to hardware

## Slide 32
Notes: Switches, routers and other middleboxes are dumbed down
The key is to have a standardized control interface that speaks directly to hardware

## Slide 33: Components of OpenFlow Network
Controller
OpenFlow Switch
Flow
Table
Secure
Channel
PC
OpenFlow
Protocol
TCP / TLS
hw
sw
OpenFlow Switch specification
* Figure From OpenFlow Switch Specification

## Slide 34: How does OpenFlow work?
34

## Slide 35
Controller
PC
Hardware
Layer
Software
Layer
Flow Table
MAC
src
MAC
dst
IP
Src
IP
Dst
TCP
sport
TCP
dport
Action
OpenFlow Client
*
*
5.6.7.8
*
*
*
port 1
port 4
port 3
port 2
port 1
1.2.3.4
5.6.7.8
OpenFlow Example

## Slide 36: OpenFlow usage
Controller
PC
OpenFlow Switch
OpenFlow Switch
OpenFlow Switch
Alice’s code
Decision?
OpenFlow
Protocol
Alice’s Rule
Alice’s Rule
Alice’s Rule
OpenFlow offloads control intelligence to a remote software
Notes: 36
36
How the actual protocol works

## Slide 37: OpenFlow Basics Flow Table Entries
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
L4
sport
L4
dport
Rule
Action
Stats
Forward packet to zero or more ports
Encapsulate and forward to controller
Send to normal processing pipeline
Modify Fields
Any extensions you add!
+ mask what fields to match
Packet + byte counters
VLAN
pcp
IP
ToS
Notes: Now I’ll describe the API that tries to meet these goals.

## Slide 38: Examples
Switching
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
00:1f:..
*
*
*
*
*
*
*
port6
Flow Switching
port3
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
00:20..
00:1f..
0800
vlan1
1.2.3.4
5.6.7.8
4
17264
80
port6
Firewall
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
*
*
*
22
drop

## Slide 40: Scalability & Robustness
40

## Slide 41: Centralized vs Distributed Control Both models are possible with OpenFlow
Centralized Control
OpenFlow
Switch
OpenFlow
Switch
OpenFlow
Switch
Controller
Distributed Control
OpenFlow
Switch
OpenFlow
Switch
OpenFlow
Switch
Controller
Controller
Controller

## Slide 42: Flow Routing vs. Aggregation Both models are possible with OpenFlow
Flow-Based
Every flow is individually set up by controller
Exact-match flow entries
Flow table contains one entry per flow
Good for fine grain control, e.g. campus networks
Aggregated
One flow entry covers large groups of flows
Wildcard flow entries
Flow table contains one entry per category of flows
Good for large number of flows, e.g. backbone

## Slide 43: Reactive vs. Proactive (pre-populated) Both models are possible with OpenFlow
Reactive
First packet of flow triggers controller to insert flow entries
Efficient use of flow table
Every flow incurs small additional flow setup time
If control connection lost, switch has limited utility
Proactive
Controller pre-populates flow table in switch
Zero additional flow setup time
Loss of control connection does not disrupt traffic
Essentially requires aggregated (wildcard) rules

## Slide 44: Basic SDN/OpenFlow principles

## Slide 45: Basic SDN/OpenFlow principles
Basic networking concepts remain unchanged
      including all the packet headers & communication protocols
        however, some configuration protocols and functions (like VRF) are not needed any more
      the only change is performed in packet handling and its configuration
Major benefits in network management
      centralized control & easier management
      network segmentation on multiple levels
        physical and virtual network separation
      dynamic response

## Slide 46: Real-life deployment Traditional approach
Let’s illustrate a few basic real-life concepts on MUNI network (simplified description)
      interconnects several sites (faculties) using MPLS core
        employes further complex technologies (like VRF, BGP, …)
      on each site, several separate networks exist
        separated using VLANs (isolation of different-purpose network – Windows/Linux hosts, printers, specific segments etc.)
      very complex ecosystem with limited flexibility
        and very hard to maintain
          many technologies used

## Slide 47: Real-life deployment SDN/OpenFlow approach
The SDN/OF network consists of several “dumb” network devices (forwarding elements)
      the logical network view dynamically configured by the controller
Several layers of network separation
      Virtual Tenant Networks (VTNs)
        for networks separation based on e.g. the purpose
      Virtual network representations
        simplified configuration of L2/L3 networks
      Physical separation
        allows multiple network instances, controlled by different controllers
          each of them further separated into VTNs, L2/L3 network, etc.

## Slide 48: Real-life deployment SDN/OpenFlow approach
Virtual networks in SDNs – Virtual Tenant Networks
Separate VTNs for (MUNI examples):
production network
technology network
sensitive-data network
infected nodes or nodes under attack
experimental network
commercial network
… all of them fully isolated (may run same IPs)
Link redundancy is welcomed!
Notes: Nad tim obrazkem se prosim dukladneji zamysli; tady se da ohledne VTNs okomentovat hodne veci…

## Slide 49: Real-life deployment SDN/OpenFlow approach
Virtual networks in SDN – Virtual Tenant Networks
Notes: Zduraznit, ze VTNs jsou logickou konfiguraci site, kazda muze slouzit pro jiny ucel…

## Slide 50: Real-life deployment SDN/OpenFlow approach
Virtual network representation / topology (in each VTN may differ)
just end ports (statically/dynamically) configured
internal configuration of all OFSs computed by the controller
Notes: OFS = OpenFlow Switch

## Slide 51: Real-life deployment SDN/OpenFlow approach
Physical network separation
      allows to divide OpenFlow HW switches into separate (SDN) worlds
          controller by own SDN controllers
          e.g. production, experimental controller and control network
In case of hybrid switches, part of the HW may serve as control network (traditional approach)
Notes: Zde jeste dodam obrazek fyzickeho rozdeleni (vcetne moznosti vyuziti pro ridici sit)…

## Slide 52: SDN/OpenFlow Demo
  FTP client and FTP server
  Two physical paths through the network exist
        one path is congested (allows for a lower speed)
          emulated using increased packet drop & delay
        the other one is free (thus faster)
  Two users: ondra & sven
        user “sven” is privileged
          his transmission speed is monitored and – if too low – the FTP server contacts SDN controller, which forces his flows to use the free/faster link
            (monitoring in 2sec. interval)
          all the other users remain on the congested link

## Slide 53: SDN/OpenFlow Demo – VTN representation
  VTN representation:

## Slide 54: SDN/OpenFlow Demo
Video running…

## Slide 55: Further examples of real-life use-cases

## Slide 56: Further examples of real-life use-cases
Notes: Zde se da zminit, ze neco podobneho lze pouzit pro bezpecnost – definovane toky smerovat na Intrusion Detection System, a tam je analyzovat…

## Slide 57: Further examples of real-life use-cases
Notes: Napriklad ochrana prenosu citlivych dat…

## Slide 58: Further examples of real-life use-cases
Further use-case examples related to university usage
      prioritize traffic / enforce lower priority (backups)
      security applications
        centralized monitoring probes (monitoring just specific traffic)
          e.g. HTTP traffic through DPI, FTP through common probes
        isolation of infected nodes and monitoring the attacker
        distribution of filtering rules
          in cooperation with stateful firewall
      connection redundancy, high-capacity links deployment, …
      etc. etc.

## Slide 59
Network Function Virtualization (NFV)

## Slide 60: Today’s network infrastructure
Diverse network functions (NF).
Providing desired overall functionality or service.
Adding new services
  New service instances take weeks to activate
  New service types may take months up to years
  New service types require either new equipment or upgrading of existing equipment
We have to simplify network design, increase agility, speed up deployment of new services.

## Slide 61: What is NFV ?
NFV – Network Functions Virtualization
Likewise VM
Virtualization – NF and part of the infrastructure is implemented as a software.
Result – from dedicated proprietary appliance to COTS hardware

## Slide 62: NFV in nutshell

## Slide 63
SDN controllers

## Slide 64: SDN controllers
Common objectives:
      multiple Southbound interface protocol support
      well-defined Northbound API support
      programmability
      high availability & performance
      security
Open-source vs. commercial

## Slide 67
OpenDaylight architecture illustration
Service Abstraction Layer/Core
Base Network Functions
- Lithium
OpenFlow Enabled Devices
DLUX
VTN Coordinator
OpenStack Neutron
SDNI Wrapper
Network Applications
Orchestrations & Services
Open vSwitches
Additional Virtual & Physical Devices
Data Plane Elements
(Virtual Switches, Physical Device Interfaces)
Controller Platform Services/Applications
OpenFlow Stats Manager
OVSDB
NETCONF
PCMM/COPS
SNBI
LISP
BGP
PCEP
SNMP
SXP
Southbound Interfaces &
Protocol Plugins
OpenFlow
OpenFlow Switch Manager
USC
CAPWAP
OPFLEX
CoAP
HTTP
OpenFlow Forwarding Rules Mgr
L2 Switch
Host Tracker
Topology Processing
AAA AuthN Filter
OpenDaylight APIs REST/RESTCONF/NETCONF
Data Store (Config & Operational)
Messaging (Notifications / RPCs)
LACP
Network Services
Service Function Chaining
Reservation
Virtual Private Network
Virtual Tenant Network Mgr.
Unified Secure Channel Mgr
OVSDB Neutron
Device Discovery, Identification & Driver Management
LISP Service
DOCSIS Abstraction
SNMP4SDN
Network Abstractions (Policy/Intent)
ALTO Protocol Manager
Network Intent Composition
Group Based Policy Service
Platform Services
Authentication, Authorization & Accounting
Neutron Northbound
Persistence
SDN Integration Aggregator
Time Series Data Repository
Link Aggregation Ctl Protocol
Module 3: OpenDaylight
3-03

## Slide 68
NETCONF & YANG
different SDN view…

## Slide 69: NETCONF and YANG in Context
NETCONF
Manager
NETCONF
Yang
Models
YANG Models
YANG Models
YANG Models
YANG Models
Management
Applications

## Slide 70: What is a Data-Model? What is a Network Management Protocol?
Data-Model
  A data-model explicitly and precisely determines the structure, syntax and semantics of the data…
  …that is externally visible
  Consistent and complete
Protocol
  Remote primitives to view and manipulate the data
  Encoding of the data as defined by the data-model
Data-Model
Protocol

## Slide 71: Standards background, motivation and history RFC 3535: Operators’ problems and requirements on network management (results of IETF’s meeting with network operators)

## Slide 72: Informational RFC 3535
SNMP had failed
  For configuration, that is
  Extensive use in fault handling and monitoring
CLI scripting
  “Market share” 70%+
Abstract
This document provides an overview of a workshop held by the Internet Architecture Board (IAB) on Network Management. The workshop was hosted by CNRI in Reston, VA, USA on June 4 thru June 6, 2002. The goal of the workshop was to continue the important dialog started between network operators and protocol developers, and to guide the IETFs focus on future work regarding network management.
configuration

## Slide 73: Operator Requirement #1/14
1. Ease of use is a key requirement for any network management technology from the operators point of view.
Maybe not assume integrators and
software developers for any addition
or change
Manage

## Slide 74: Operator Requirement #2-3/14
Clearly separating configuration
Ability to compare across devices
2. It is necessary to make a clear distinction between configuration data, data that describes operational state and statistics.
3. It is required to be able to fetch separately configuration data, operational state data, and statistics from devices, and to be able to compare these between devices.
$show running-config

## Slide 75: Operator Requirement #4-5/14
Service and Network management, not only device management
Network wide transactions
4. It is necessary to enable operators to concentrate on the configuration of the network as a whole rather than individual devices.
5. Support for configuration transactions across a number of devices would significantly simplify network configuration management.
VPN Configuration
All or nothing

## Slide 76: Operator Requirement #6-7/14
Devices figure out ordering
No unnecessary changes
Finally: backup/restore of configuration
6. Given configuration A and configuration B, it should be possible to generate the operations necessary to get from A to B with minimal state changes and effects on network and systems. It is important to minimize the impact caused by configuration changes.
7. A mechanism to dump and restore configurations is a primitive operation needed by operators. Standards for pulling and pushing configurations from/to devices are desirable.
The litmus-test of a management interface
configuration

## Slide 77: Operator Requirement #8, 10/14
8. It must be easy to do consistency checks of configurations over time and between the ends of a link in order to determine the changes between two configurations and whether those configurations are consistent.
10. It is highly desirable that text processing tools such as diff, and version management tools such as RCS or CVS, can be used to process configurations, which implies that devices should not arbitrarily reorder data such as access control lists.
Validation of configuration
Validation at network level
Text based configuration
VPN Configuration
Valid?
Text

## Slide 78: Operator Requirement #9/14
Standardized data models
9. Network wide configurations are typically stored in central master databases and transformed into formats that can be pushed to devices, either by generating sequences of CLI commands or complete configuration files that are pushed to devices. There is no common database schema …, although the models used by various operators are probably very similar.
It is desirable to extract, document, and standardize the common parts of these network wide configuration database schemas.
Interfaces Data-Model

## Slide 79: Operator Requirement #13/14
Support for multiple configuration sets
Delayed, orchestrated activation
13. It is important to distinguish between the distribution of configurations and the activation of a certain configuration.
Devices should be able to hold multiple configurations.
Config, Config, Commit

## Slide 80: Operator Requirement #11,12,14/14
11. … Typical requirements are a role-based access control model and the principle of least privilege, where a user can be given only the minimum access necessary to perform a required task.
12. It must be possible to do consistency checks of access control lists across devices.
14. SNMP access control is data-oriented, while CLI access control is usually command (task) oriented. … As such, it is a requirement to support both data-oriented and task-oriented access control
Role-Based Access Control (RBAC)
  Data oriented
  Task oriented

## Slide 81
NETCONF was designed to conform to RFC 3535.
Today many operators require NETCONF and YANG in devices.
NETCONF makes a difference on the bottom line.

## Slide 82: What makes NETCONF/YANG different?
 | SNMP | NETCONF | SOAP | REST
Standard | IETF | IETF | W3C | -
Resources | OIDs | Paths |  | URLs
Data models | Defined in MIBs | YANG Core Models |  | 
Data Modeling Language | SMI | YANG | (WSDL, not data) | Undefined, (WSDL), WADL, text…
Management Operations | SNMP | NETCONF | In the XML Schema, not standardized | HTTP operations
Encoding | BER | XML | XML | XML, JSON,…
Transport Stack | UDP | SSH TCP | SSL HTTP TCP | SSL HTTP TCP
“RESTConf”

## Slide 83: What makes NETCONF/YANG different?
SNMP
GET
GET-NEXT
SET
TRAP
…
… so what?
NETCONF
<get-config>
<edit-config>
<copy-config>
<delete-config>
<get>
<lock>
…
… same same?
Data-Model
MIB Modules
YANG Modules
Protocol
The SNMP Protocol
NETCONF

## Slide 84: What makes NETCONF/YANG different?
Use Case | SNMP | NETCONF
Get collection of status fields | Yes | Yes. Bulk xfer up to 10x faster. Really.
Set collection of configuration fields | Yes, up to 64kB | Yes
Set configuration fields in transaction | No | Yes
Transactions across multiple network elements | No | Yes
Invoke administrative actions | Well… | Yes
Send event notifications | Yes | Yes, connected
Backup and restore configuration | Usually not | Yes
Secure protocol | v3 is fair | Yes
Test configuration before final commit | No | Yes
This is where the difference is: In the supported use cases!

## Slide 85: YANG ?
Data modeling language
  Configuration data
  State data
Tree structure
Data and Types
acme-box module
properties container
interfaces container
name: string, config
name: string, config
interface: list, index = name
oper-state: enum, config

## Slide 86: YANG Header

## Slide 87
Thank you for your attention!