## Slide 1: PV204 Security technologies
Trusted element, side channels attacks
Petr Švenda
svenda@fi.muni.cz @rngsec
https://crocs.fi.muni.cz/people/svenda
Faculty of Informatics, Masaryk University, Czech Republic

## Slide 2: Trusted element and side channels
Lecture:
  Introduction (30min), course content, formal requirements
  Secure anchor in a system – trusted element
  Usage scenario for secure hardware as trusted point
  Attacks against trusted element
  Timing attacks against software implementations
  Power and fault analysis
  How to write robust code as a mitigation
Lab:
  Correction of flawed implementation (timing analysis)

## Slide 3: Course trivia

## Slide 4: Introduction
    See PV204_CourseOverview_2018.ppt

## Slide 5: Trusted element

## Slide 6: What is “Trusted” system (plain language)
Many different notions
System trusted by someone
System that you can’t verify and therefore must trust not to betray you
  If a trusted component fails, security can be violated
System build according to rigorous criteria so you are willing to trust it
…
Why Trust is Bad for Security, D. Gollman, 2006
  http://www.sciencedirect.com/science/journal/15710661/157/3
We need more precise specification of Trust

## Slide 7: Untrusted VS. Trusted vs. Trustworthy

## Slide 8: Untrusted system
System explicitly unable to fulfill specified security policy
Additional layer of protection must be employed
  E.g., Encryption of data before storage
  E.g., Digital signature of email before send over network

## Slide 9: Trusted system
“…system that is relied upon to a specified extent to enforce a specified security policy. As such, a trusted system is one whose failure may break a specified security policy.” (TCSEC, Orange Book)
Trusted subjects are those excepted from mandatory security policies (Bell LaPadula model)
User must trust (if wants to use the system)
  E.g., you and your bank

## Slide 10: Trustworthy system (computer)
“Computer system where software, hardware, and procedures are secure, available and functional and adhere to security practices” (Black's Law Dict.)
User have reasons to trust reasonably
Trustworthiness is subjective
  Limited interface and hardware protections can increase trustworthiness (e.g., append-only log server)
Example: Payment card - Trusted? Trustworthy?
Trusted does not mean automatically Trustworthy

## Slide 11: Trusted computing base (TCB)
The set of all hardware, firmware, and/or software components that are critical to its security
The vulnerabilities inside TCB might breach the security properties of the entire system
  E.g., server hardware + virtualization (VM) software
The boundary of TCB is relevant to usage scenario
  TCB for datacentre admin is around hw + VM (to protect against compromise of underlying hardware and services)
  TCB for web server client also contains Apache web server
Very important factor is size and attack surface of TCB
  Bigger size implies more space for bugs and vulnerabilities
https://en.wikipedia.org/wiki/Trusted_computing_base

## Slide 12: Cryptography on client
Which parts are trusted?
What are threats?
What are attacker models?
What is trusted computing base?

## Slide 13: On client, but with secure hardware
Which parts are trusted?
What are threats?
What are attacker models?
What is trusted computing base?
Notes: Problem: how to get key where is necessary?
- generate on device
- import into device (securely)

## Slide 14: Cryptography in cloud
WS API: JSON
Which parts are trusted?
What are threats?
What are attacker models?
What is trusted computing base?

## Slide 15: Cryptography in cloud in secure hardware
Which parts are now trusted?
Are also trustworthy?

## Slide 16: Example: different levels of trust
CaaS with trusted CaaS provider
  Software operation only, HTTPS for in/out
  Trusted provider => insider attack, also valid target itself…
CaaS with semi-trusted CaaS provider
  HTTPS for in/out, decrypted by server
  Data processed inside trusted hardware
  CaaS platform still target (data visible)
CaaS with untrusted provider
  HTTPS for in/out + inner protection
  Data decrypted/processed/encrypted inside device

## Slide 17: Trusted element

## Slide 18: What exactly can be trusted element (TE)?
Recall: Anything user entity of TE is willing to trust 
  Depends on definition of “trust” and definition of “element”
  We will use narrower definition
Trusted element is element (hardware, software or both) in the system intended to increase security level w.r.t. situation without the presence of such element
  By storage of sensitive information (keys, measured values)
  By enforcing integrity of execution of operation (firmware update)
  By performing computation with confidential data (DRM)
  By providing unforged reporting from untrusted environment
  …

## Slide 19: Typical examples
Payment smart card
  TE for issuing bank
SIM card
  TE for phone carriers
Trusted Platform Module (TPM)
  TE for user as storage of Bitlocker keys, TE for remote entity during attestation
Trusted Execution Environment in mobile/set-top box
  TE for issuer for confidentiality and integrity of code
Hardware Security Module for TLS keys
  TE for web admin
Energy meter
  TE for utility company
Server under control of service provider
  TE for user – private data, TE for provider – business operation
For whom is TE trusted?

## Slide 20: Risk management
No system is completely secure ( risk is present)
Risk management allows to evaluate and eventually take additional protection measures
Example: payment transaction limit
  “My account/card will never be compromised” vs. “Even if compromised, then loss is bounded”
Example: medical database
  central governmental DB vs. doctor’s local DB
Good design practice is to allow for risk management

## Slide 21: Trusted element Modes of usage

## Slide 22: Trusted element - modes of usage
Element carries fixed information
Element as a secure carrier
Element as encryption/signing device
Element as computational device
Element as root of trust (TPM)

## Slide 23: Element carries fixed information
Fixed information ID transmitted, no secure channel
Low cost solution (nothing “smart” needed)
Problem: Attacker can eavesdrop and clone chip
Element is trusted with ID carriage
But is it trustworthy?

## Slide 24: Element as a secure carrier
Key(s) stored on a card, loaded to a PC before encryption/signing/authentication, then erased
High speed usage of key possible (>>MB/sec)
Attacker with an access to PC during operation will obtain the key
  key protected for transport, but not during the usage
Element is trusted as confidential key storage,
but cannot perform (or not trusted with) operation

## Slide 25: Element as root of trust (TPM)
Secure boot process, remote attestation
Element provides robust storage with integrity
Application can verify before pass control (measured boot)
Computer can authenticate with remote entity…
Element is trusted with integrity of stored values

## Slide 26: Element as encryption/signing device
PC just sends data for encryption/signing…
Key never leaves element
  personalized in secure environment
  protected during transport and usage
Attacker must attack the element
  or wait until card is inserted and PIN entered!
Potentially low speed encryption (~kB/sec)
  low communication speed / limited element performance

## Slide 27: Element as computational device
PC just sends input for application on smart card
Application code & keys never leave the element
  Element can do complicated programmable actions
  Can open secure channels to other entity
    secure server, trusted time service…
    PC act as a transparent relay only (no access to data)
Attacker must attack the element or input

## Slide 28: Attacks against TRUSTED ELEMENT

## Slide 29: Trusted hardware (TE) is not panacea!
Can be physically attacked
  Christopher Tarnovsky, BlackHat 2010
  Infineon SLE 66 CL PE TPM chip, bus read by tiny probes
  9 months to carry attack, $200k
  https://youtu.be/w7PT0nrK2BE (great video with details)
Attacked via vulnerable API implementation
  IBM 4758 HSM (Export long key under short DES one)
Provides trusted anchor != trustworthy system
  weakness can be introduced later
  E.g., bug in securely updated firmware

## Slide 30: How to reason about attack and countermeasures?
Where does an attack come from (principle)?
  Understand the principles
Different hypothesis for the attack to be practical
  More ways how to exploit the same weakness
Attack’s countermeasures by cancel of hypothesis
  For every way you are aware of
Costs and benefits of the countermeasures
  Cost of the assets protected
  Cost for an attacker to perform attack
  Cost of a countermeasure
Important: Consider Break Once, Run Everywhere (BORE)

## Slide 31: Motivation: Bell’s Model 131-B2 / Sigaba
Encryption device intended for US army, 1943
  Oscilloscope patterns detected during usage
  75 % of plaintexts intercepted from 80 feets
  Protection devised (security perimeter), but later forgot
CIA in 1951 – recovery over ¼ mile of power lines
Other countries also discovered the issue
  Russia, Japan…
More research in use of (eavesdropping) and defense against (shielding)  TEMPEST

## Slide 32: Common and realizable attacks on TE
Non-invasive attacks
  API-level attacks
    Incorrectly designed and implemented application
    Malfunctioning application (code bug, faulty generator)
  Communication-level attacks
    Observation and manipulation of communication channel
  Side-channel attacks
    Timing/power/EM/acoustic/cache-usage/error… analysis attacks
Semi-invasive attacks
  Fault induction attacks (power/light/clock glitches…)
Invasive attacks
  Dismantle chip, microprobes…

## Slide 33: Where are frequent problems with crypto nowadays?
Security mathematical algorithms
  OK, we have very strong ones (AES, SHA-3, RSA…)
Implementation of algorithm
  Problems  implementation attacks
Randomness for keys
  Problems  achievable brute-force attacks
Key distribution
  Problems  old keys, untrusted keys, key leakage
Operation security
  Problems  where we are using crypto, key leakage

## Slide 34: Non-invasive attacks
Non-invasive side-channel attacks

## Slide 35: TRNG  Key: What if faulty TRNGs?
Good source of randomness is critical
  TRNG can be weak or malfunctioning
How to inspect TRNG correctness?
  Analysis of TRNG implementation (but usually blackbox)
  Output data can be statistically tested (100MB-1GB stream, NIST STS, Dieharder, TestU01 batteries) http://www.phy.duke.edu/~rgb/General/dieharder.php
  Behaviour in extreme condition (+70/-50° C, radiation…)
    Analyse data stream gathered during extreme conditions
  Simple power analysis of TRNG generation
    Is hidden/unknown operation present?

## Slide 36: Serial test: Histogram of 16bits patterns
Normal distribution (expected)
Biased distribution (lower entropy)

## Slide 37: Algorithmic flaw in Infineon’s RSALib (CVE-2017-15361)
All keys generated by Infineon library are affected
Practical factorization of common lengths 512/1024/2048b
All public keys have unique “fingerprint” (easy to scan for)
  Tool for detection (public since 16th October, try it!)
  https://keychest.net/roca, https://github.com/crocs-muni/roca/
Tool for factorization (made public by Lange&Bernstein)
  Our implementation of factorization tool provided to Infineon in February 2017
  Random 2048b key: 6442450944000000 vCPU years
  Infineon 2048b key: 140 vCPU years
https://roca.crocs.fi.muni.cz
Attack is perfectly parallelizable 1000 cores => 1000x speedup

## Slide 38: Algorithmic flaw in Infineon’s RSALib (CVE-2017-15361)
https://roca.crocs.fi.muni.cz
Austria, Estonia, Slovakia, Spain…
25-30% TPMs worldwide, Bitlocker, ChromeOS…
Firmware update available
Commit signing,
Application signing
GitHub, Maven…
Gemalto .NET
Yubikey 4…
Yubikey 4…
Very few keys, but all tied to SCADA management

## Slide 39: Flawed use of random data to make primes
~310 bits of entropy
for 1024-bit prime
Factorization difficulty
  Random 2048b key: 6442450944000000 vCPU years
  Infineon 2048b key: 140 vCPU years
Special structure of primes to facilitate its faster generation

## Slide 40: Transformation of prime to make the attack practical

## Slide 41: Power analysis
Non-invasive side-channel attacks

## Slide 42: Basic setup for power analysis
Smart card
Smart card reader
Inverse card connector
Oscilloscope
Resistor
20-80 ohm
Probe

## Slide 43: More advanced setup for power analysis
Ethernet
Tested smartcard
External power supply
SCSAT04 measurement board

## Slide 44: Simple vs. differential power analysis
Simple power analysis
  Direct observation of single / few power traces
  Visible operation => reverse engineering
  Visible patterns => data dependency
Differential power analysis
  Statistical processing of many power traces
  More subtle data dependencies found

## Slide 45: Reverse engineering of Java Card bytecode
Goal: obtain code back from smart card
  JavaCard defines around 140 bytecode instructions
  JVM fetch instruction and execute it
(source code)
m_ram1[0] = (byte) (m_ram1[0] % 1);
(bytecode)
getfield_a_this 0;
sconst_0;
baload;
sconst_1;
srem;
bastore;
(power trace)
compiler
oscilloscope

## Slide 46: Conditional jumps
may reveal sensitive info
keys, internal branches, …
(bytecode)
sload_1;
ifeq_w L2;
L1: getfield_a_this 0;
sconst_0;
sconst_0;
bastore;
goto L3;
L2: getfield_a_this 0;
sconst_0;
sconst_1;
bastore;
goto L3;
L3: …
(source code)
if (key == 0) m_ram1[0] = 1;
else m_ram1[0] = 0;
compiler
oscilloscope
(power trace, k != 0)
(power trace, k == 0)
Can you use
timing attack?

## Slide 47: Simple power analysis – data leakage
Data revealed directly when processed
  e.g., Hamming weight of instruction argument
    hamming weight of separate bytes of key (256 238)

## Slide 48: Differential power analysis (DPA)
DPA attack recovers secret key (e.g., AES)
Requires large number of power traces (102-106)
  Every trace measured on AES key invocation with different input data
Key recovered iteratively
  One recovered byte at the time (KEYi  INPUT_DATAi)
  Guess possible key byte value (0-255), group measurements, compute average, determine match

## Slide 49: Differential power analysis
Very Powerful attack on secret values (keys)
  E.g., KEY  INPUT_DATA
Obtain multiple power traces with (fixed) key usage and variable data
  103-105 traces with known I/O data => S(n)
  KEY  KNOWN_DATA
Guess key byte-per-byte
  All possible values of single byte tried (256)
  D = HammWeight(KEY  KNOWN_DATA > 4)
  Correct guess reveals correlation with traces
  Incorrect guess not
Divide and test approach
  Traces divided into 2 groups
  Groups are averaged A0,A1 (noise reduced)
  Subtract group’s averaged signals T(n)
  Significant peaks if guess was correct
No need for knowledge of exact implementation
  big advantage

## Slide 50: Tool: DPA simulator
Generate simulated DPA traces
Perform DPA
Can be used to inspect influence of noise, number of traces…
  https://github.com/crocs-muni/PowerTraceSimulator

## Slide 51: Timing attacks
Non-invasive side-channel attacks

## Slide 52: Timing attack: principle
+
 57ms
+
 49ms

## Slide 53: Timing attacks
Execution of crypto algorithm takes different time to process input data with some dependence on secret value (secret/private key)
  Due to performance optimizations (developer, compiler)
  Due to conditional statements (branching)
  Due to cache misses
  Due to operations taking different number of cycles
Measurement techniques
  Start/stop time (aggregated time, local/remote measurement)
  Power/EM trace (very precise if operation can be located)

## Slide 54: Naïve modular exponentiation (RSA/DH)
M = Cd mod N
M = C * C * C * … * C mod N
Easy, but extremely slow for large d (1000s bits)
  Faster algorithms exist
d-times
Is there dependency
of time on secret value?

## Slide 55: Square and multiply algorithm
How to measure?
  Exact detection from simple power trace
  Extraction from overall time of multiple measurements
Gilbert Goodwill, http://www.embedded.com/print/4408435
// M = C^d mod N
// Square and multiply algorithm
x = C // start with ciphertext
for j = 1 to n { // process all bits of private exponent
x = x*x mod N // shift to next bit by x * x (always)
if (d_j == 1) { // j-th bit of private exponent d
x = x*C mod N // if 1 then multiple by Ciphertext
}
}
return x // plaintext M
Executed only when d_j == 1
Executed always
Notes: How to attack:
What if you have debugger?
What if you have just breakpoint inside d_j condition?

## Slide 56: Example: Remote extraction OpenSSL RSA
Brumley, Boneh, Remote timing attacks are practical
  https://crypto.stanford.edu/~dabo/papers/ssl-timing.pdf
Scenario: OpenSSL-based TLS with RSA on remote server
  Local network, but multiple routers
  Attacker submits multiple ciphertexts and observe processing time (client)
OpenSSL’s RSA CRT implementation
  Square and multiply with sliding windows exponentiation
  Modular multiplication in every step: x*y mod q (Montgomery alg.)
  From timing can be said if normal or Karatsuba was used
    If x and y has unequal size, normal multiplication is used (slower)
    If x and y has equal size, Karatsuba multiplication is used (faster)
Attacker learns bits of prime by adaptively chosen ciphertexts
  About 300k queries needed

## Slide 57: Defense introduced by OpenSSL
RSA blinding: RSA_blinding_on()
  https://www.openssl.org/news/secadv_20030317.txt
Decryption without protection: M = cd mod N
Blinding of ciphertext c before decryption
  Generate random value r and compute re mod N
  Compute blinded ciphertext b = c * re mod N
  Decrypt b and then divide result by r
    r is removed and only decrypted plaintext remains

## Slide 58: Example: Practical TEMPEST for $3000
ECDH Key-Extraction via Low-Bandwidth Electromagnetic Attacks on PCs
  https://eprint.iacr.org/2016/129.pdf
E-M trace captured (across a wall)

## Slide 59: Example: Practical TEMPEST for $3000
ECDH implemented in latest GnuPG's Libgcrypt
Single chosen ciphertext – used operands directly visible

## Slide 60: Example: How to evaluate attack severity?
What was the cost?
  Not high: $3000
What was the targeted implementation?
  Widely used implementation: latest GnuPG's Libgcrypt
What were preconditions?
  Physical presence, but behind the wall
Is it possible to mitigate the attack?
  Yes: fix in library, physical shielding of device, perimeter…
  What is the cost of mitigation?

## Slide 61: Example: Acoustic side channel in GnuPG
RSA Key Extraction via Low-Bandwidth Acoustic Cryptanalysis
  Insecure RSA computation in GnuPG
  https://www.tau.ac.il/~tromer/papers/acoustic-20131218.pdf
Acoustic emanation used as side-channel
  4096-bit key extracted in one hour
  Mobile phone 4 meters away

## Slide 62: Example: Cache-timing attack on AES
Attacks not limited to asymmetric cryptography
  Daniel J. Bernstein, http://cr.yp.to/antiforgery/cachetiming-20050414.pdf
Scenario: Operation with secret AES key on remote server
  Key retrieved based on response time variations of table lookups cache hits/misses
  225 x 600B random packets + 227 x 400B + one minute brute-force search
Very difficult to write high-speed but constant-time AES
  Problem: table lookups are not constant-time
  Not recognized by NIST during AES competition

## Slide 63: Other types of side-channel attacks
Acoustic emanation
  keyboard clicks
  capacitor noise
  Speech eavesdropping based on high-speed camera
Cache-occupation side-channel
  Cache miss has impact on duration of operation
  Other process can measure own cache hits/misses if cache is shared
Branch prediction side-channel (Meltdown, Spectre)…

## Slide 64: Mitigations

## Slide 65: Side-channels mitigation
Don’t use own implementation
  Very hard to prevent side-channels
Don’t do data dependency
  Fixed or completely randomized timings
Be very careful with optimizations
  Data-dependent pre-computed tables
  Data-dependent conditional branches (naïve Montgomery)
Lower layer leakage can be prevented on higher level
  Blinding/masking…
  Don’t use vulnerable constructions (ifeq instruction)
  Implementation secure on higher level can be compromised on lower level

## Slide 66: Generic protection techniques
Shielding - preventing leakage outside
  Acoustic shielding, noisy environment
Creating additional “noise”
  Parallel software load, noisy power consumption circuits
Compensating for leakage
  Perform inverse computation/storage
Harden algorithm
  Ciphertext blinding…

## Slide 67: How to test real implementation?
Be aware of various side-channels
Obtain measurement for given side-channel
  Many times (103 - 107), compute statistics
  Same input data and key
  Same key and different data
  Different keys and same data…
Compare groups of measured data
  Is difference visible? => potential leakage
  Is distribution uniform? Is distribution normal?
Try to measure again with better precision 

## Slide 68: Example: NaCl (“salt”) library
Relatively new cryptographic library (2012)
  Designed for usable security and side-channel resistance
  D. Bernstein, T. Lange, P. Schwabe
  https://cr.yp.to/highspeed/coolnacl-20120725.pdf
  Active fork is libsodium https://github.com/jedisct1/libsodium
Designed for usable security (hard to misuse)
  Fixed good algs (AE: Poly1305, Sign: EC Curve25519)
  c=crypto_box(m,n,pk,sk), m=crypto_box_open(c,n,pk,sk)
Implemented to have constant-time execution
  No data flow from secrets to load addresses
  No data flow from secrets to branch conditions
  No padding oracles (recall CBC padding oracle in PA193)
  Centralizing randomness and avoiding unnecessary randomness

## Slide 69: Semi-invasive attacks

## Slide 70: Semi-invasive attacks
“Physical” manipulation (but card still working)
Micro probes placed on the bus
  After removing epoxy layer
Fault induction
  liquid nitrogen, power glitches, light flashes…
  modify memory (RAM, EEPROM), e.g., PIN counter
  modify instruction, e.g., conditional jump

## Slide 71: PIN verification procedure
[Decrease counter, verify, increase] - correct
[Verify, decrease/increase]

## Slide 72: Fault induction
Attacker can induce bit faults in memory locations
  power glitch, flash light, radiation...
  harder to induce targeted then random fault
Protection with shadow variable
  every variable has shadow counterpart
  shadow variable contains inverse value
  consistency is checked every read/write to memory
Robust protection, but cumbersome for developer
01011010
10100101
01011010
10100101
if (a != ~a_inv) Exception();
a = 0x55;
a_inv = ~0x55;
01010101
10101010
01010000
if (a != ~a_inv) Exception();
a = 0x13;
a
a_inv

## Slide 73: Conclusions

## Slide 74: Morale
Preventing implementation attacks is extra difficult
  Naïve code is often vulnerable
    Not aware of existing problems/attacks
  Optimized code is often vulnerable
    Time/power/acoustic… dependency on secret data
    Dangerous optimizations (Infineon primes)
Use well-known libraries instead of own code
  And follow security advisories and patch quickly
Security / mitigations are complex issues
  Underlying hardware can leak information as well
  Don’t allow for large number of queries

## Slide 75: Mandatory reading
G. Goodwill, Defending against side-channel attacks
  http://www.embedded.com/print/4408435
  http://www.embedded.com/print/4409695
Focus on:
  What side channels are inspected?
  What step in executed operation is misused for attack?
  What are proposed defenses?

## Slide 76: Optional reading
Why Trust is Bad for Security, D. Gollman, 2006
  http://www.sciencedirect.com/science/journal/15710661/157/3
Focus on:
  Which definition of Trust Gollman uses?
  Why Gollman claims that Trust is bad for security?

## Slide 77: Conclusions
Trusted element is secure anchor in a system
  Understand why it is trusted and for whom
Trusted element can be attacked
  Non-invasive, semi-invasive, invasive methods
Side-channel attacks are very powerful techniques
  Attacks against particular implementation of algorithm
  Attack possible even when algorithm is secure (e.g., AES)
Use well-know libraries instead own implementation