## Slide 1: Chapter 7: Network Evolution
CCNA Routing and Switching
Connecting Networks v6.0
Notes: Cisco Networking Academy Program
Connecting Networks v6.0
Chapter 7: Network Evolution

## Slide 2: Chapter 7 - Sections & Objectives
7.1 Internet of Things
Explain the value of the Internet of Things.
  Describe the Cisco IoT System.
  Describe the pillars of the Cisco IoT System.
7.2 Cloud and Virtualization
  Explain why cloud computing and virtualization are necessary for evolving networks.
  Explain the importance of cloud computing.
  Explain the importance of virtualization.
  Describe the virtualization of network devices and services.
  7.3 Network Programming
  Explain why network programmability is necessary for evolving networks.
  Describe software-defined networking.
  Describe controllers used in network programming.
Notes: 2
Cisco Networking Academy Program
Connecting Networks v6.0
Chapter 7: Network Evolution

## Slide 3: 7.1 Internet of Things
Notes: 7 – Network Evolution
7.1 – Remote Access Connections

## Slide 4: Internet of Things What is the IoT?
It is predicted that the Internet will interconnect 50 billion things by 2020.
Using existing and new technologies, we are connecting the physical world to the Internet.
It is by connecting the unconnected that we transition from the Internet to the Internet of Things (IoT).
Notes: 7.1 – Internet of Things
7.1.1 – IoT Elements
7.1.1.1 – What is the IoT?

## Slide 5: IoT Elements The Converged Network and Things
Dissimilar networks are converging to share the same infrastructure.
This infrastructure includes comprehensive security, analytics, and management capabilities.
The connection of the components into a converged network that uses IoT technologies increases the power of the network to help people improve their daily lives.
Notes: 7.1 – Internet of Things
7.1.1 – IoT Elements
7.1.1.2 – The Converged Network and Things

## Slide 6: IoT Elements Video - Challenges of Connecting Things
Digitization means connecting people and things, and making sense of the data in a meaningful and secure way.
Notes: 7.1 – Internet of Things
7.1.1 – IoT Elements
7.1.1.3 – Challenges of Connecting Things

## Slide 7: IoT Elements The Six Pillars of the Cisco IoT System
Cisco IoT System uses six pillars to identify foundational elements.
Notes: 7.1 – Internet of Things
7.1.1 – IoT Elements
7.1.1.4 – The Six Pillars of the Cisco IoT System

## Slide 8: IoT Pillars Video - The Network Connectivity Pillar
All IoT devices need network connectivity and the equipment needed varies depending on the type of network.
Home networks typically consist of a wireless broadband router, while business networks will have multiple switches, APs, a firewall or firewalls, routers, and more.
Notes: 7.1 – Internet of Things
7.1.2 – IoT Pillars
7.1.2.1 – The Network Connectivity Pillar

## Slide 9: IoT Pillars The Fog Computing Pillar
Fog computing
  This IoT network model identifies a computing infrastructure closer to the network edge.
  Edge devices run applications locally and make immediate decisions.
  Data does not need to be sent over network connections.
  Enhances resiliency by allowing IoT devices to operate when network connections are lost.
  Enhances security by keeping sensitive data from being transported beyond the edge where it is needed.
Client-Server Model
Cloud Computing Model
Fog Computing Model
Notes: 7.1 – Internet of Things
7.1.2 – IoT Pillars
7.1.2.2 – The Fog Computing Pillar

## Slide 10: IoT Pillars The Security Pillar
IoT introduces new attack vectors not typically encountered with normal enterprise networks.
Cybersecurity solutions include:
  Operational Technology (OT) specific security – OT is the hardware and software that keeps power plants running and manages factory process lines.
  IoT Network security – Includes network and perimeter security devices.
  IoT Physical security - Cisco Video Surveillance IP Cameras.
Cisco FirePOWER Appliance
Cisco Industrial Security Appliance
Cisco Video Surveillance Cameras
Notes: 7.1 – Internet of Things
7.1.2 – IoT Pillars
7.1.2.3 – The Security Pillar

## Slide 11: IoT Pillars Video - Data Analytics Pillar
IoT can connect billions of devices capable of creating exabytes of data every day. To provide value, this data must be rapidly processed and transformed into actionable intelligence.
  Need to bring centers of data together and take advantage of data.
Notes: 7.1 – Internet of Things
7.1.2 – IoT Pillars
7.1.2.4 – Data Analytics Pillar

## Slide 12: IoT Pillars Management and Automation Pillar
IoT expands the size and diversity of the network to include the billions of smart objects that sense, monitor, control, and react. Each of these areas also has distinctive requirements, including the need to track specific metrics.
Cisco management and automation products can be customized for specific industries to provide enhanced security and control and support.
Management Tools: Cisco IoT Field Network Director, Cisco Prime, Cisco Video Surveillance Manager, and more.
Notes: 7.1 – Internet of Things
7.1.2 – IoT Pillars
7.1.2.5 – Management and Automation Pillar

## Slide 13: IoT Pillars Video – Application Enablement Platform Pillar
Provides the infrastructure for application hosting and application mobility between cloud and Fog computing.
Cisco IOx which is a combination of Cisco IOS and Linux, allows routers to host applications close to the objects they need to monitor, control, analyze, and optimize.
Listen to the Interview about IOx!
Notes: 7.1 – Internet of Things
7.1.2 – IoT Pillars
7.1.2.6 – Video – Application Enablement Platform Pillar

## Slide 14: 7.2 Cloud and Virtualization
Notes: 7 – Network Evolution
7.2 – Cloud and Virtualization

## Slide 15: Cloud Computing Video – Cloud and Virtualization
Notes: 7.2 – Cloud and Virtualization
7.2.1 – Cloud Computing
7.2.1.1 – Video – Cloud and Virtualizaion

## Slide 16: Cloud Computing Video – Cloud and Virtualization (Cont.)
Notes: 7.2 – Cloud and Virtualization
7.2.1 – Cloud Computing
7.2.1.1 – Video – Cloud and Virtualizaion (Cont.)

## Slide 17: Cloud Computing Cloud Overview
Cloud computing
  The “pay-as-you-go” model where capital expenditures are transferred to operating expenses.
  Large numbers of networked computers physically located anywhere.
  Providers rely heavily on virtualization.
  Reduce operational costs by using resources more efficiently.
  Supports a variety of data management issues:
      Enables access to organizational data anywhere and at any time
      Streamlines the organization’s IT operations by subscribing only to needed services
      Eliminates or reduces the need for onsite IT equipment, maintenance, and management
      Reduces cost for equipment, energy, physical plant requirements, and personnel training needs
      Enables rapid responses to increasing data volume requirements
Notes: 7.2 – Cloud and Virtualization
7.2.1 – Cloud Computing
7.2.1.2 – Cloud Overview

## Slide 18: Cloud Computing Cloud Services
Cloud computing services defined by the National Institute of Standards and Technology (NIST):
  Software as a Service (SaaS): Access to services, such as email and Office 365 that are delivered over the Internet.
  Platform as a Service (PaaS): Access to the development tools and services used to deliver the applications.
  Infrastructure as a Service (IaaS): Access to the network equipment, virtualized network services, and supporting network infrastructure.
  IT as a Service (ITaaS): IT Professionals support applications, platforms and infrastructure.
Notes: 7.2 – Cloud and Virtualization
7.2.1 – Cloud Computing
7.2.1.3 – Cloud Services

## Slide 19: Cloud Computing Cloud Models
Public clouds: Application and services made available to the general population. Services may be free or are offered on a pay-per-use model, such as paying for online storage. Uses the Internet to provide services.
Private clouds: Applications and services are intended for a specific organization or entity, such as the government. A private cloud can be set up using the organization’s private network, though this can be expensive to build and maintain. A private cloud can also be managed by an outside organization with strict access security.
Hybrid clouds: Made up of two or more clouds (example: part private, part public), where each part remains a distinctive object, but both are connected using a single architecture.
Community clouds: A community cloud is created for exclusive use by a specific community. For example, healthcare organizations must remain compliant with policies and laws (e.g., HIPAA) that require special authentication and confidentiality.
Notes: 7.2 – Cloud and Virtualization
7.2.1 – Cloud Computing
7.2.1.4 – Cloud Models

## Slide 20: Cloud Computing Cloud Computing versus Data Center
Data center: Typically a data storage and processing facility run by an in-house IT department or leased offsite.
Cloud computing: Typically an off-premise service that offers on-demand access to a shared pool of configurable computing resources. These resources can be rapidly provisioned and released with minimal management effort.
Cloud computing is possible because of data centers.
Cloud computing is often a service provided by data centers.
Notes: 7.2 – Cloud and Virtualization
7.2.1 – Cloud Computing
7.2.1.5 – Cloud Computing versus Data Center

## Slide 21: Virtualization Cloud Computing and Virtualization
Virtualization is the foundation of cloud computing. Without it, cloud computing would not be possible.
Cloud computing separates the application from the hardware.
Virtualization separates the OS from the hardware.
Amazon Elastic Compute cloud (Amazon EC2) web service provides a simple way for customers to dynamically provision the computer resources they need. These virtualized instances of servers are created on demand in Amazon’s EC2.
Notes: 7.2 – Cloud and Virtualization
7.2.2 – Virtualization
7.2.2.1 – Cloud Computing and Virtualization

## Slide 22: Virtualization Dedicated Servers
Notes: 7.2 – Cloud and Virtualization
7.2.2 – Virtualization
7.2.2.2 – Dedicated Servers

## Slide 23: Virtualization Server Virtualization
In the figure, the previous eight dedicated servers have been consolidated into two servers using hypervisors to support multiple virtual instances of the operating systems.
Hypervisor is a program, firmware, or hardware that adds an abstraction layer on top of the real physical hardware.
The abstraction layer is used to create virtual machines which have access to all the hardware of the physical machine such as CPUs, memory, disk controllers, and NICs.
It is not uncommon for 100 physical servers to be consolidated as virtual machines on top of 10 physical servers that are using hypervisors.
Notes: 7.2 – Cloud and Virtualization
7.2.2 – Virtualization
7.2.2.3 – Server Virtualization

## Slide 24: Virtualization Advantages of Virtualization
One major advantage of virtualization is overall reduced cost:
  Less equipment is required - Server consolidation and lower maintenance costs.
  Less energy is consumed - Consolidating servers lowers the monthly power and cooling costs.
  Less space is required - Fewer servers, network devices, and racks reduce the amount of required floor space.
Additional benefits of virtualization:
  Easier prototyping
  Faster server provisioning
  Increased server uptime
  Improved disaster recovery
  Legacy Support
Notes: 7.2 – Cloud and Virtualization
7.2.2 – Virtualization
7.2.2.4 – Advantages of Virtualization

## Slide 25: Virtualization Abstraction Layers
A hypervisor is installed between the firmware and the OS. The hypervisor can support multiple instances of OSs.
Notes: 7.2 – Cloud and Virtualization
7.2.2 – Virtualization
7.2.2.5 – Abstraction Layers

## Slide 26: Virtualization Type 2 Hypervisors
A hypervisor is software that creates and runs VM instances.
The computer, on which a hypervisor is supporting one or more VMs, is a host machine.
Type 2 hypervisors are also called hosted hypervisors. This is because the hypervisor is installed on top of the existing OS, such as Mac OS X, Windows, or Linux.
Type 2 hypervisors are very popular with consumers and for organizations experimenting with virtualization. Common Type 2 hypervisors include:
  Virtual PC
  VMware Workstation
  Oracle VM VirtualBox
  VMware Fusion
  Mac OS X Parallels
“Hosted” Approach
Notes: 7.2 – Cloud and Virtualization
7.2.2 – Virtualization
7.2.2.6 – Type 2 Hypervisors

## Slide 27: Virtual Network Infrastructure Type 1 Hypervisors
Hypervisor is installed directly on the hardware.
Usually used on enterprise servers and data center networking devices.
Instances of an OS are installed on the hypervisor.
Type 1 hypervisors have direct access to the hardware resources.
Improve scalability, performance, and robustness.
“Bare Metal” Approach
Notes: 7.2 – Cloud and Virtualization
7.2.3 – Virtual Network Infrastructure
7.2.3.1 – Type 1 Hypervisors

## Slide 28: Virtual Network Infrastructure Installing a VM on a Hypervisor
Type 1 hypervisors require a “management console” to manage the hypervisor.
Management software is used to manage multiple servers using the same hypervisor.
The management console can automatically consolidate servers and power on or off servers as required.
Assume that Server1 in the figure becomes low on resources. To make more resources available, the management console moves the Windows instance to the hypervisor on Server2.
Notes: 7.2 – Cloud and Virtualization
7.2.3 – Virtual Network Infrastructure
7.2.3.2 – Installing a VM on a Hypervisor

## Slide 29: Virtual Network Infrastructure Installing a VM on a Hypervisor (Cont.)
The management console provides recovery from hardware failure.
If a server component fails, the management console automatically and seamlessly moves the VM to another server.
The management console for the Cisco Unified Computing System (UCS) is shown in the figure. Cisco UCS Manager controls multiple servers and manages resources for thousands of VMs.
Notes: 7.2 – Cloud and Virtualization
7.2.3 – Virtual Network Infrastructure
7.2.3.2 – Installing a VM on a Hypervisor (Cont.)

## Slide 30: Virtual Network Infrastructure Network Virtualization
Server virtualization hides server resources from server users. This practice can create problems if the data center is using traditional network architectures.
For example, Virtual LANs (VLANs) used by VMs must be assigned to the same switch port as the physical server running the hypervisor. However, VMs are movable, and the network administrator must be able to add, drop, and change network resources and profiles. This process is difficult to do with traditional network switches.
Another problem is that traffic flows differ substantially from the traditional client-server model. Typically, a data center has a considerable amount of traffic being exchanged between virtual servers (referred to as East-West traffic). These flows change in location and intensity over time, requiring a flexible approach to network resource management.
Existing network infrastructures can respond to changing requirements related to the management of traffic flows by using Quality of Service (QoS) and security level configurations for individual flows. However, in large enterprises using multivendor equipment, each time a new VM is enabled, the necessary reconfiguration can be very time-consuming.
Notes: 7.2 – Cloud and Virtualization
7.2.3 – Virtual Network Infrastructure
7.2.3.3 – Network Virtualization

## Slide 31: 7.3 Network Programming
Notes: 7 – Network Evolution
7.2 – Cloud and Virtualization

## Slide 32: Software-Defined Networking Video – Network Programming, SDN, and Controllers
Notes: 7.3 – Network Programming
7.3.1 – Software-Defined Networking
7.3.1.1 – Video – Network Programming, SDN, and Controllers

## Slide 33: Software-Defined Networking Control Plane and Data Plane
A network device contains the following planes:
  Control plane - Regarded as the brains of a device. Used to make forwarding decisions. Information sent to the control plane is processed by the CPU.
  Data plane - Also called the forwarding plane, this plane is the switch fabric connecting the various network ports on a device. The data plane of each device is used to forward traffic flows.
CEF is an advanced, Layer 3 IP switching technology that enables forwarding of packets to occur at the data plane without consulting the control plane. Packets are forwarded directly by the data plane based on the information contained in the Forwarding Information Base (FIB) and adjacency table, without needing to consult the information in the control plane.
Notes: 7.3 – Network Programming
7.3.1 – Software-Defined Networking
7.3.1.2 – Control Plane and Data Plane

## Slide 34: Software-Defined Networking Control Plane and Data Plane (Cont.)
To virtualize the network, the control plane function is removed from each device and is performed by a centralized controller.
The centralized controller communicates control plane functions to each device.
Each device can now focus on forwarding data while the centralized controller manages data flow, increases security, and provides other services.
Notes: 7.3 – Network Programming
7.3.1 – Software-Defined Networking
7.3.1.2 – Control Plane and Data Plane (Cont.)

## Slide 35: Software-Defined Networking Virtualizing the Network
Two major network architectures have been developed to support network virtualization:
  Software Defined Networking (SDN) - A network architecture that virtualizes the network.
  Cisco Application Centric Infrastructure (ACI) - A hardware solution for integrating cloud computing and data center management.
These are some other network virtualization technologies, some of which are included as components in SDN and ACI:
  OpenFlow - The OpenFlow protocol is a basic element in building SDN solutions.
  OpenStack - This approach is a virtualization and orchestration platform available to build scalable cloud environments and provide an infrastructure as a service (IaaS) solution.
Notes: 7.3 – Network Programming
7.3.1 – Software-Defined Networking
7.3.1.3 – Virtualizing the Network

## Slide 36: Software-Defined Networking SDN Architecture
In a traditional router or switch architecture, the control plane and data plane functions occur in the same device. Routing decisions and packet forwarding are the responsibility of the device operating system.
Software defined networking (SDN) is a network architecture that has been developed to virtualize the network. SDN can virtualize the control plane. SDN moves the control plane from each network device to a central network intelligence and policy-making entity called the SDN controller.
Notes: 7.3 – Network Programming
7.3.1 – Software-Defined Networking
7.3.1.4 – SDN Architecture

## Slide 37: Software-Defined Networking SDN Architecture (Cont.)
The SDN controller enables network administrators to manage and dictate how the data plane of virtual switches and routers should handle network traffic.
The SDN controller uses northbound APIs to communicate with the upstream applications. These APIs help network administrators shape traffic and deploy services.
The SDN controller also uses southbound APIs to define the behavior of the downstream virtual switches and routers.
An API is a set of standardized requests that define the proper way for an application to request services from another application.
OpenFlow is the original and widely implemented southbound API.
Notes: 7.3 – Network Programming
7.3.1 – Software-Defined Networking
7.3.1.4 – SDN Architecture (Cont.)

## Slide 38: Controllers SDN Controller and Operations
SDN controller defines the data flows that occur in the SDN Data Plane. A flow could consist of all packets with the same source and destination IP addresses, or all packets with the same VLAN identifier.
Each flow traveling through the network must first get permission from the SDN controller. If the controller allows a flow, it computes a route for the flow to take and adds an entry for that flow in each of the switches along the path.
The controller populates and the switches manage the flow tables. Each OpenFlow switch connects to other OpenFlow switches. They can also connect to end-user devices that are part of a packet flow.
To the switch, a flow is a sequence of packets that matches a specific entry in a flow table.
Notes: 7.3 – Network Programming
7.3.2 – Controllers
7.3.2.1 – SDN Controller and Operations

## Slide 39: Controllers Video - Cisco Application Centric Infrastructure
Notes: 7.3 – Network Programming
7.3.2 – Controllers
7.3.2.2 – Video - Cisco Application Centric Infrastructure

## Slide 40: Controllers Core Components of ACI
Three core components of the ACI architecture:
  Application Network Profile (ANP) - Collection of end-point groups (EPG), their connections, and the policies that define those connections.
  Application Policy Infrastructure Controller (APIC) – The brains of the ACI architecture. A centralized software controller that is designed for programmability and centralized management. Translates application policies into network programming.
  Cisco Nexus 9000 Series switches – Provide an application-aware switching fabric and work with an APIC to manage the virtual and physical network infrastructure.
APIC is positioned between the ANP and the ACI-enabled network infrastructure. The APIC translates the application requirements into a network configuration to meet those needs.
Notes: 7.3 – Network Programming
7.3.2 – Controllers
7.3.2.3 – Core Components of ACI

## Slide 41: Controllers Spine-Leaf Topology
Cisco ACI fabric is composed of the APIC and the Cisco Nexus 9000 series switches using two-tier spine-leaf topology, as shown in the figure.
Leaf switches always attach to the spines, but they never attach to each other.
Spine switches only attach to the leaf and core switches (not shown).
Cisco APICs and all other devices in the network physically attach to leaf switches.
When compared to SDN, the APIC controller does not manipulate the data path directly.
The APIC centralizes the policy definition and programs the leaf switches to forward traffic based on the defined policies.
Notes: 7.3 – Network Programming
7.3.2 – Controllers
7.3.2.4 – Spine-Leaf Topology

## Slide 42: Controllers SDN Types
To better understand APIC-EM, it is helpful to take a broader look at the three types of SDN:
  Device-based SDN - The devices are programmable by applications running on the device itself or on a server in the network. Cisco OnePK is an example of a device-based SDN. It enables programmers to build applications to integrate and interact with Cisco devices.
  Controller-based SDN - Uses a centralized controller that has knowledge of all devices in the network. The applications can interface with the controller responsible for managing devices and manipulating traffic flows throughout the network. The Cisco Open SDN Controller is a commercial distribution of OpenDaylight.
Notes: 7.3 – Network Programming
7.3.2 – Controllers
7.3.2.5 – SDN Types

## Slide 43: Controllers SDN Types (Cont.)
  Policy-based SDN - Similar to controller-based SDN where a centralized controller has a view of all devices in the network. Includes an additional Policy layer. Uses built-in applications that automate advanced configuration tasks via a guided workflow and user-friendly GUI. No programming skills are required. Cisco APIC-EM is an example of this type of SDN.
Policy-based SDN is the most robust, providing for a simple mechanism to control and manage policies across the entire network.
Notes: 7.3 – Network Programming
7.3.2 – Controllers
7.3.2.5 – SDN Types (Cont.)

## Slide 44: Controllers APIC-EM Features
Cisco APIC-EM provides the following features:
  Discovery - Supports a discovery functionality that is used to populate the controller's device and host inventory database.
  Device Inventory - Collects detailed information from devices within the network including device name, device status, MAC address, IPv4/IPv6 addresses, IOS/Firmware, platform, up time, and configuration.
  Host Inventory - Collects detailed information from hosts with the network including host name, user ID, MAC address, IPv4/IPv6 addresses, and network attachment point.
  Policy - Ability to view and control policies across the entire network including QoS.
  Topology - Supports a graphical view of the network (topology view).
  Policy Analysis - Inspection and analysis of network access control policies. Ability to trace application specific paths between end devices to quickly identify ACLs in use and problem areas.
Notes: 7.3 – Network Programming
7.3.2 – Controllers
7.3.2.6 – APIC-EM Features

## Slide 45: Controllers APIC-EM ACL Analysis
One of the most important features of the APIC-EM controller is the ability to manage policies across the entire network.
APIC-EM ACL Analysis and Path Trace provide tools to allow the administrator to analyze and understand ACL policies and configurations.
  ACL Analysis Tool - Enables ACL inspection and interrogation across the entire network, exposing any problems and conflicts.
  ACL Path Trace - This tool examines specific ACLs on the path between two end nodes, displaying any potential issues.
ACL Analysis
ACL Path Trace
Notes: 7.3 – Network Programming
7.3.2 – Controllers
7.3.2.7 – APIC-EM ACL Analysis

## Slide 46: 7.4 Summary
Notes: 7 – Network Evolution
7.4 – Summary

## Slide 47: Conclusion Chapter 7: Network Evolution
Explain the value of the Internet of Things.
Explain why cloud computing and virtualization are necessary for evolving networks.
Explain why network programmability is necessary for evolving networks.
Notes: 7.4 – Summary
7.4.1 – Conclusion
7.4.1.1 - Chapter 7: Network Evolution

## Slide 48: Chapter 7: Network Evolution New Terms and Commands
Internet of Things (IoT) Cloud computing virtualization Software-defined networking (SDN) Machine-to-Machine (M2M) sensors Cisco IoT System network connectivity pillar Cloud computing model Fog computing model fog computing pillar Fog applications security pillar Operational Technology (OT) security Operational Technology (OT) | IoT Network security IoT Physical security data analytics pillar application programming interfaces (APIs) System management and automation pillar Application Enablement Platform pillar Cisco IOx National Institute of Standards and Technology (NIST) Software as a Service (SaaS) Platform as a Service (PaaS) Infrastructure as a Service (IaaS) IT as a Service (ITaaS) Public cloud Private cloud
Notes: New Terms and Commands

## Slide 49: Chapter 7: Network Evolution New Terms and Commands (Cont.)
Hybrid cloud Community cloud Data center server operating system (OS) single point of failure server sprawl hypervisors virtual machines (VMs) management console Cisco Unified Computing System (UCS) Cisco UCS Manager East-West traffic Cisco Network Foundation Protection (NFP) Control plane Management plane | Data plane VMware Cisco Application Centric Infrastructure (ACI) OpenFlow OpenStack Application Programming Interfaces (APIs) northbound APIs southbound APIs North-South traffic SDN controllers Transport Layer Security (TLS) Flow Table Group Table Meter Table Application Network Profile (ANP)
Notes: New Terms and Commands

## Slide 50: Chapter 7: Network Evolution New Terms and Commands (Cont.)
end-point groups (EPG) Application Policy Infrastructure Controller (APIC) Cisco Nexus 9000 Series switches spine-leaf topology ACL Analysis ACL Path Trace | 
Notes: New Terms and Commands