## Slide 1: PV204 Security technologies
Trusted Boot, TPM, SGX
Petr Švenda svenda@fi.muni.cz @rngsec
Centre for Research on Cryptography and Security, Masaryk University

## Slide 2: Overview
Booting chain of programs
BIOS as root of trust
Verified and Measured boot
Trusted boot in the wild
  Trusted Platform Module
  Chromium, Windows 8/10, UEFI…
Dynamic root of trust
  Intel’s TXT, SGX

## Slide 3: Motivation – untrusted host platform
Traditional role of operating system
  Isolate processed
  Manage privileges, authorize operations
But how to deal with
  Debugger, disassembler
  Intercepted multimedia output
  Malware run along with banking app
  Keyloggers, Evil maid
  System administrators, Service providers
  …

## Slide 4: Solution?
Code signing (e.g., Microsoft AuthentiCode)
  Application binary is signed, PKI used to verify certificate
  If not signed, user is notified
  Mandatory signing for selected applications (drivers…)
Signed == Secure?

## Slide 5: Signed == Secure?

## Slide 6: Trust in program’s functionality
Trust in a program’s code?
  Signed code can still contain bugs and vulnerabilities
Trust only in a program’s code?
  Underlying OS layers
  Underlying firmware
  Underlying hardware
  Memory used by the program
  Other code with access to the program’s memory/code
  …
The program is almost never executed “alone”

## Slide 7: Problem statement
How to make sure that valid programs run only within valid environment?
Is it possible to start valid environment on previously compromised machine?
Is it possible to prevent tampering of apps against attacker with physical access?
How to prove to remote party what apps are running on local machine?

## Slide 8: Classical boot chain
http://www.thegeekstuff.com/2011/02/linux-boot-process/
http://social.technet.microsoft.com/wiki/contents/articles/11341.the-windows-7-boot-process-sbsl.aspx
Linux
Windows (7)
How to detect that BIOS or
OS Loader was modified?
(evil maid, bootkit…)

## Slide 9: How to arrive at expected chain of apps?
Just trust the whole boot process
Make all applications in protected read-only memory
  If read-only => cannot be updated. But is it really what is running?
Signature-based approach: “Verified boot”
  Before next app is executed, its signature is verified
  Requires valid (unforged) public key (integrity)
  Requires trust to owner of private key (signs only valid applications)
Create un-spoofable log what executed: “Measured” boot
  Before next app is executed, its hash (“measurement”) is computed added to un-spoofable log (TPM’s PCR)
  Will NOT prevent run of unwanted app, but environment cannot lie about what was executed (after-the-fact examination)
  Requires (protected) log storage (Trusted Platform Module)
  May require authentication of log (Remote attestation)

## Slide 10: “Verified” boot (signatures)
“Measured” boot
(cumulative hash)
Trusted boot

## Slide 11: “Verified” boot
BIOS
MBR
GRUB
Kernel
User app
…
VERIFY (RSA)
VERIFY (RSA)
VERIFY (RSA)
VERIFY (RSA)
MEASURE: PCR = H(PCR | H(MBR))
MEASURE: PCR = H(PCR | H(GRUB))
MEASURE: PCR = H(PCR | H(Kernel))
MEASURE: PCR = H(PCR | H(User app))
Nothing => BIOS is Root of Trust
What verifies or
measures BIOS?
RESET: PCR = 0
PCR = H(…H(H(0|H(MBR))|H(GRUB)…H(User app))
=>
“Measured” boot

## Slide 12: Root of trust (for verified/measured boot)
Verified and Measured boot need some root of trust
  Initial piece of code that nobody verifies/measures
Static root of trust
  Start building trusted chain after reset of whole device
Dynamic root of trust
  Start building trusted chain without reset of device (faster)
What can be root of trust?
  static root of trust: BIOS, UEFI firmware, Intel Boot Guard
  dynamic root of trust: Intel TXT, Intel SGX
Root of trust requires special protection
  As nobody verifies than nobody will detect eventual modification

## Slide 13: BIOS as root of trust
First code executed on CPU of target machine
Privileged access to hardware
  E.g., can write into memory of OS code via DMA
Provides code for System Management Mode (SMM)
  Routines executed during the whole platform runtime
  x86 feature since 386, all normal execution is suspended
  Used for power management, memory errors, hardware-assisted debugger…
  Very powerful mode (=> also target of “ring -2” rootkits)

## Slide 14: BIOS – security considerations
How BIOS verifies integrity of next module to run?
Where public key(s) for verification are stored?
How to handle updates of signing keys?
How BIOS checks signatures on its own updates?
How BIOS can be compromised?

## Slide 15: How BIOS can be compromised?
Maliciously written by BIOS vendor (backdoor)
Replacement of genuine BIOS by malicious one
  By physical flash (SPI programmer) of BIOS code
  By lack of flashing protection mechanism by original BIOS
  By code logic flaws in BIOS locking mechanisms
Modification of other code/data used by BIOS
  Bug in parsing unsigned data…
Currently used protections:
  Chipset-enforced protection of flash memory with BIOS
  BIOS signature verification before new version is written
  Hardware-aided check of executed code (TPM, TXT, SGX)
  Check of BIOS signature before execution by CPU (IBG)

## Slide 16: BIOS write locking – “locks”
Prevent unauthorized BIOS flash (from host OS)
Allow for authorized BIOS changes
  BIOS upgrade, signing keys update
  Change of persistent configurations (boot device…)
Locking mechanism (locks) for BIOS memory write
  Locks are unlocked after reboot
  Signature on new BIOS version is verified by old BIOS, and new is flashed eventually (before locking locks)
  BIOS configuration (boot device priority) is written before locking locks
  Locks locked before handling execution to other code

## Slide 17: Attacks against BIOS locks
Attacks typically via BIOS code vulnerability
  BIOS usually does not takes (much) user input, but may parse BIOS update blob with some parts unsigned (logo)
  Buffer overflow in logo parsing => Locks are not locked yet => write own BIOS
  http://invisiblethingslab.com/resources/bh09usa/Attacking%20Intel%20BIOS.pdf
Write into flash memory by SPI programmer
Which one is more serious? Different attacker models
1. Is remote, but patchable
2. Is local attacker, but requires design changes to prevent

## Slide 18: Impact: Attack against Tails live-CD distro
Tails is live-CD Linux distribution
Designed to provide security even on previously compromised computer
  Boot complete fresh OS from live-CD + security tools
Attack 1: Physical BIOS modification
  Modified BIOS inserts malicious code into Tails during boot time
  Known thread, physical access to computer assumed
Attack 2: SMM rootkit (LightEater)
  Bug in BIOS exploited by remote party to modify SMM routines
Main issue: Tails tries to start with clean erased computer, but some elements still persist erase (BIOS modifications)

## Slide 19: Intel Boot Guard (IBG)

## Slide 20: Intel Boot Guard (IBG)
Recently (2014) introduced feature to protect BIOS
  Piece of trusted processor-provided, ROM-based code
  Runs first after reset, verifies Initial Boot Block (IBB)
“Measured” boot mode (TPM-based)
  Passively extends TPM’s PCRs by hash of IBB
“Verified” boot mode (digital signature)
  OEM vendor hardcodes public key via fuses into CPU
  Intel Boot Guard checks signature of IBB by OEM’s key
  Only vendor-approved IBB=>BIOS=>OS is executed
Combination of measured and verified mode

## Slide 21: Intel Boot Guard – new root of trust
BIOS
BIOS
MBR
GRUB
Kernel
User app
…
Intel Boot Guard (CPU)
VERIFY (RSA)
VERIFY (RSA)
VERIFY (RSA)
VERIFY (RSA)
VERIFY (RSA)
MEASURE: PCR = H(BIOS-IBB)
MEASURE: PCR = H(PCR | H(MBR))
MEASURE: PCR = H(PCR | H(GRUB))
MEASURE: PCR = H(PCR | H(Kernel))
MEASURE: PCR = H(PCR | H(User app))
IBG: Measured mode
IBG: Verified mode

## Slide 22: Intel Boot Guard – security improvements
What attacks are mitigated by Intel Boot Guard?
Direct BIOS flash by SPI programmer
  Mitigated, signature/measurement mismatch
Remote change of BIOS / BIOS data
  Mitigated, signature/measurement mismatch
Other bug(s) in BIOS code
  Not mitigated, signed code still contains bug
Any new attacks opened by IBG?

## Slide 23: How hard is to incorporate backdoor?
OEM vendor can sign backdoored BIOS
  But multiple OEM vendors exist, open-source coreboot
Intel Boot Guard is written by Intel only
  But OEM fuses own verification public key, right?
  But it is the IBG code that actually verifies
Trivial backdoor (inside IBG code inside CPU)
  if (IBB[SOME_OFFSET] == BACKDOOR_MAGIC) then always load provided BIOS (no signature check)
  Or possibly verify by some other public key (secure even when BACKDOOR_MAGIC is leaked)

## Slide 24: Short summary
Signature-based “verified” boot approach
  Whitelisting approach – run only what is signed
  Robust signature process needed (trust in private key owner)
  Integrity of verification public key is critical
  Key management is necessary (multiple keys, key updates)
“Measured” boot approach
  Un-spoofable log of hashes of executed code
  Can be remotely verified (remote attestation, explained later)
Root of trust needs to be protected
  Historically was BIOS (+ update signatures + write locks)
  Recently Intel Boot Guard inside CPU (signature of BIOS)

## Slide 25: Trusted platform module

## Slide 26: TPM hardware
Cryptographic smart card connected/inside to device
  Secure storage, secure crypto environment…
  (But not programmable JavaCard )
Physical placement
  Additional chip on motherboard
  Incorporated inside CPU
  Incorporated in peripheral (Ethernet card)
Accessed during boot time
  “Measured” boot (TPM’s PCR registers)
  Bitlocker encrypted drive keys
Accessed later (private key operation)

## Slide 27: Trusted platform module
Author: Guillaume Piolle

## Slide 28: Trusted Platform Module (TPM)
ISO/IEC 11889 standard for secure crypto-processor
Versions published by Trusted Computing Group
  https://trustedcomputinggroup.org
  TPM 1.2 (2011)
  TPM 2.0 (2016, not compatible with 1.2, but downgrade switch)
Tools to communicate with TPM
  Windows: Microsoft PCPTool, TSS.MSR, Windows API
  Linux: tpm_tools, tpm2_tools, GUI TPMManager

## Slide 29: TPM 1.2 vs. TPM 2.0
https://en.wikipedia.org/wiki/Trusted_Platform_Module
TPM 2.0 introduced algorithm flexibility (no fixed SHA-1)
  If (some) algorithm is broken, no need to create “TPM 3.0”
TPM 2.0 often supports legacy API 1.2 (switch in BIOS)
TPM 2.0 seems to focus on IoT-like devices (support TLS)

## Slide 30: Provided security functions
“Measured” boot with remote attestation
  Provide signed log of what executed on platform (PCR)
Storage of keys (disk encryption, private keys…)
  Can be additionally password protected
Binding and Sealing of data
  Encryption key wrapped by concrete TPM’s public key
Platform integrity
  Software will not start if current PCR value is not right

## Slide 31: TPM Trusted Software Stack stack
Infineon, http://www.cs.unh.edu/~it666/reading_list/Hardware/tpm_fundamentals.pdf

## Slide 32: TPM PCR
Platform Configuration Register (PCR)
Measurement cumulatively stored in PCR
  measurement = SHA1(next block to execute)
  PCR[i] = SHA1(PCR[i] | new_measurement)
  Current block measure & store next before passing control
PCR cannot be erased until reboot
  Every part that was executed is stored
  Possible to perform after-the-fact verification what executed
Idea: boot what you want, but PCR will hold trace
Multiple PCRs to support finer grained reporting

## Slide 33: Platform attestation – PCR registers
W: PCPTool.exe GetPCRs
L: cat `find /sys/class/ -name "tpm0"`/device/pcrs

## Slide 34: Remote attestation of platform state
So you measured your boot. How to prove your state to remote party?
Idea:
  Take PCR values (inside TPM)
  Sign it (inside TPM) by TPM’s private key (AIK)
  Remote party holds public key and can verify signature => trust in authenticity of PCR values

## Slide 35: Remote attestation of platform state
Apps running on your computer measured in PCRs
Your TPM contains unique Endorsement key
You can generate Attestation key inside TPM (AIK)
  And sign AIK by Endorsement key (inside TPM)
You can sign your PCRs by AIK (inside TPM)
Remote party can verify signature on AIK key
  Using public key of Endorsement key
Remote party can verify signature on PCRs
  Using public key of AIK key
Remote party now knows “what” you are running

## Slide 36: Remote attestation
Multiple PCRs to support finer grained reporting
  not just single cumulative value
Multiple PCRs available
  BIOS, ROM, Memory Block Register [index 0-4]
  OS loaders [5-7], Operating System [8-15]
  Debug [16], Localities, Trusted OS [17-22]
  Application specific [23]
What is PCR measurement good for?
  PCR content can be signed by TPM’s private key and exported
  List of applications claimed to be executed (=> PCR expected value can be recomputed by remote party)
  => Remote attestation

## Slide 37: Platform attestation – PCR registers
<PlatformAttestation size="30591">
<Magic>PADS<!-- 0x53444150 --></Magic>
<Platform>TPM_VERSION_12</Platform>
<HeaderSize>28</HeaderSize>
<PcrValues size="480">
<PCR Index="0">8cb1a2e093cf41c1a726bab3e10bc1750180bbc5</PCR>
<PCR Index="1">b2a83b0ebf2f8374299a5b2bdfc31ea955ad7236</PCR>
<PCR Index="2">b2a83b0ebf2f8374299a5b2bdfc31ea955ad7236</PCR>
<PCR Index="3">b2a83b0ebf2f8374299a5b2bdfc31ea955ad7236</PCR>
<PCR Index="4">68fffb7e5c5f6e6461b3527a0694f41ebd07e4e1</PCR>
<PCR Index="5">8e33d52190def152c9939e9dd9b0ea84da25d29b</PCR>
<PCR Index="6">b2a83b0ebf2f8374299a5b2bdfc31ea955ad7236</PCR>
<PCR Index="7">b2a83b0ebf2f8374299a5b2bdfc31ea955ad7236</PCR>
<PCR Index="8">0000000000000000000000000000000000000000</PCR>
<PCR Index="9">0000000000000000000000000000000000000000</PCR>
<PCR Index="10">0000000000000000000000000000000000000000</PCR>
<PCR Index="11">b2a83b0ebf2f8374299a5b2bdfc31ea955ad7236</PCR>
<PCR Index="12">7c84e69cd581eefd7ebe1406666711fd4fda8aa8</PCR>
<PCR Index="13">01788a8a31f2dafcd9fe58c5a11701e187687d49</PCR>
<PCR Index="14">26cda47f1db41bedc2c2b1e6c91311c98b4e2246</PCR>
<PCR Index="15">0000000000000000000000000000000000000000</PCR>
<PCR Index="16">0000000000000000000000000000000000000000</PCR>
<PCR Index="17">ffffffffffffffffffffffffffffffffffffffff</PCR>
<PCR Index="18">ffffffffffffffffffffffffffffffffffffffff</PCR>
<PCR Index="19">ffffffffffffffffffffffffffffffffffffffff</PCR>
<PCR Index="20">ffffffffffffffffffffffffffffffffffffffff</PCR>
<PCR Index="21">ffffffffffffffffffffffffffffffffffffffff</PCR>
<PCR Index="22">ffffffffffffffffffffffffffffffffffffffff</PCR>
<PCR Index="23">0000000000000000000000000000000000000000</PCR>
</PcrValues>
…

## Slide 38: TPM platform info
Provides information about your platform state
Included in PCR12 (Operating System information)
<PlatformCounters>
<OsBootCount>44</OsBootCount>
<OsResumeCount>2</OsResumeCount>
<CurrentBootCount>0</CurrentBootCount>
<CurrentEventCount>66</CurrentEventCount>
<CurrentCounterId>179136858</CurrentCounterId>
<InitialBootCount>0</InitialBootCount>
<InitialEventCount>64</InitialEventCount>
<InitialCounterId>179136858</InitialCounterId>
</PlatformAttestation>
<PlatformCounters>
<OsBootCount>45</OsBootCount>
<OsResumeCount>0</OsResumeCount>
<CurrentBootCount>0</CurrentBootCount>
<CurrentEventCount>67</CurrentEventCount>
<CurrentCounterId>179136858</CurrentCounterId>
<InitialBootCount>0</InitialBootCount>
<InitialEventCount>67</InitialEventCount>
<InitialCounterId>179136858</InitialCounterId>
</PlatformAttestation>
Reboot =>

## Slide 39: Trusted boot – real implementations

## Slide 40: Verified boot - Chromium OS
Starts with read-only part of firmware/BIOS (root of trust)
  Cannot be forged, but also cannot be not updated
  Contains permanently stored root RSA public key
“Verified” boot strategy is used
  Verifies that all executed code is from Chromium OS source tree
  Code signatures verified by (shorter) keys signed by root key
    speed tradeoff + possibility to update compromised keys
Does not completely prevent user to boot other OSes
  Developer mode turned on => signature on kernel not checked
  TPM is used to provide mode reporting (normal/devel/recovery)
https://www.chromium.org/chromium-os/chromiumos-design-docs/verified-boot
https://www.chromium.org/chromium-os/chromiumos-design-docs/verified-boot-crypto

## Slide 41: Chromium OS uses of TPM
Limited remote attestation (PCR[0] used)
  to store developer and recovery mode switches
Prevent rollback attack
  Prevented by strictly increasing version of key & firmware
  Version is written in TPM’s NV RAM location, only read-only firmware can update this location
  Key version prevents update to older (compromised) key
  Firmware version prevents update to vulnerable firmware
Store selected user’s private keys (secure storage)
Wrap selected disk encryption keys by TPM’s system key
https://www.chromium.org/developers/design-documents/tpm-usage

## Slide 42: UEFI secure boot
Secured and Trusted Boot

## Slide 43: UEFI secure boot principles
Platform key (RSA 2048b, PK) for authentication of platform owner
Key exchange keys (KEKs) for authentication of other components (drivers, OS components…)
“Setup" mode – platform key (PK) is not loaded yet
  Everybody can write its own platform key (become owner)
  Once PK is written, switch to “user” mode
“User” mode
  New keys (PKs, KEKs) can be written only if signed by PK
  New software components loaded only if signed by KEKs

## Slide 44
Microsoft, Secured Boot and Measured Boot: Hardening Early Boot Components Against Malware

## Slide 46: Windows 8/10 trusted boot
Secured and Trusted Boot

## Slide 47: Windows 8/10 trusted boot
Certified Windows 8/10 devices have trusted boot by default
  “Verified” boot used (UEFI+OS sign)
  “Measured” boot used (TPM)
TPM PCRs used for measurements
TPM used for keys protection
  BitLocker disk encryption key
  ROCA relevant CVE-2017-15361
    If Infineon TPM used, patch!
http://technet.microsoft.com/en-US/windows/dn168167.aspx

## Slide 48: Usage of TPM in BitLocker (disk encryption)
Source of Volume Master Key (VMK)
M. Russinovich et. al., Windows Internals Part 2, 6th Edition

## Slide 49: Attack: Sniffing keys for BitLocker
Nice writeup how to sniff BitLocker key when send from TPM to OS, then decrypt disk image
  https://pulsesecurity.co.nz/articles/TPM-sniffing

## Slide 50
Add slide with reasoning about the attack

## Slide 51: Windows 8/10 – secure boot process
Certified Windows 8/10 devices must have secure boot enabled by default
Microsoft, Secured Boot and Measured Boot: Hardening Early Boot Components Against Malware

## Slide 52: TPM owner password
You “own” TPM if you can set owner password
  One owner password per single TPM
Password set during TPM initialization phase
  can be repeated, but content is erased
Password protected storage of keys (Bitlocker…)
Run tpm.msc

## Slide 54: Basic components

## Slide 55: TPM keys
Endorsement key (EK)
  Generated during manufacturing, permanent
  Remain in TPM device during whole chip lifetime
TPM Storage Root Key (SRK)
  Generated by use after taking ownership
  New Storage root key can be generated after TPM clear
  Used to protect TPM keys created by application
Various delegate keys
  Separate keys signed/wrapped by EK, SRK…
  Application can generate and store own keys
  Good practice: do not have single key for everything

## Slide 56: TPM storage keys
Application keys encrypted under SRK
Exported as protected blob
Stored on mass-storage
If needed, decrypted back and placed into slot
Key usable until removed
http://www.cs.unh.edu/~it666/reading_list/Hardware/tpm_fundamentals.pdf

## Slide 57: TPM policy
TPM releases secret only when PCR contains particular value
Enforcement even in measured-only mode
  Key is not released if unexpected component was started (started => is included in measurements)
Conditions can use ANDs and ORs
How to handle policy updates?
  Change policy of state only from already valid state

## Slide 58: Programming with TPM
TPM Platform Crypto-Provider Toolkit
  https://research.microsoft.com/en-us/downloads/74c45746-24ad-4cb7-ba4b-0c6df2f92d5d/
  Source code examples for Attestation and Trusted boot
The TPM Software Stack from Microsoft Research (Java, C#)
  https://github.com/Microsoft/TSS.MSR
Measured Boot Tool
  https://mbt.codeplex.com/, List of most important functions, example code
  Demonstrates TPM secure boot and remote attestation on Windows 8/10
TrouSerS: open-source stack for TCG
  Linux version (2008)
    http://trousers.sourceforge.net/
    https://sourceforge.net/projects/trousers/files/tpm-tools/
  Windows port (2010)
    http://security.polito.it/trusted-computing/trousers-for-windows/

## Slide 59: Usage of TPM in cloud-computing
Combination of virtualization and trusted computing
Modified Xen hypervisor used to make standard TPM available for secret-less virtual machine
Results in significant decrease in the size of trusted computational base (TCB)
http://bleikertz.com/research/acns2013.pdf

## Slide 60: Dynamic root of trust

## Slide 61: Static Root of Trust Measurement (SRTM)
Start trusted immutable piece of firmware
  E.g., BIOS loader or Intel Boot Guard
Initiates measurement process
  Integrity of every next component is added to TPM’s PCRs
  Start  BIOS  PCI EEPROM  MBR  OS …
But do we need to start (trusted boot) only after reboot?
  Takes relatively long time
  Can we execute the same process, but dynamically?
  Can we exclude long chain (BIOS, PCI…)?
    Long chain => large Trusted Computing Base (TCB)!

## Slide 62: Dynamic Root Trust Measurement (DRTM)
Launch of measured environment at any time
  “Late lunch” option
  No need to reset whole platform
  Can be also terminated after some time
Measurement process similar to static root of trust
  Application trust chain executed from dynamic root
Implementation of DRTM
  Intel’s TXT (not used much in practice, server CPUs typically)
  Intel’s SGX (all Skylake processors and newer, from 2015)

## Slide 63: Intel’s Trusted Execution Technology
Intel’s TXT uses a processor-based root of trust
  Option given in TCG specifications
Goal: shorten chain of trust
  Run specific program in verified/trusted chain without restart
Goal: provide independent root of trust (CPU-based)
  Processor isolates memory of Measured Launched Environment (MLE) from other processes
Intel’s TXT still uses TPM to store measurements
http://www.intel.com/content/dam/www/public/us/en/documents/guides/intel-txt-software-development-guide.pdf
Outdated, abounded in favor of SGX

## Slide 64: Intel’s TXT issues
TXT still relies on BIOS provided code (SMM)
  TXT-started chain can be compromised by forged BIOS
  Hard to patch (design decision, not implementation bug)
  Proposed defence by hardening and sandboxing SMM
Bugs in TXT implementation
  Memory corruption, misconfiguring VT-d …
  Can be fixed after discovery
Bugs in processing residual state of pre-TXT lunch
  Maliciously modified ACPI tables
  Can be fixed after discovery

## Slide 65: tboot – open-source implementation
Pre-kernel/VMM module
Based on Intel’s Trusted Execution Technology
Performs a measured and verified launch of an OS kernel/VMM
http://sourceforge.net/projects/tboot/

## Slide 66: Intel’s SGX : Security enclave
Intel’s Software Guard Extension (SGX)
  New set of CPU instructions intended for future cloud server CPUs
Protection against privileged attacker
  Server admin with physical access, privileged malware
Application requests private region of code and data
  Security enclave (4KB for heap, stack, code)
  Encrypted enclave is stored in main RAM memory, decrypted only inside CPU
  Access from outside enclave is prevented on CPU level
  Code for enclave is distributed as part of application
Trusted Computing Base significantly limited! 
  But proprietary Intel code inside CPU 

## Slide 67: Intel’s SGX – some details
EGETKEY instruction generates new enclave key
  SGX security version numbers
  Device ID (unique number of CPU)
  Owner epoch – additional entropy from user
EREPORT instruction generates signed report
  Local/remote attestation of target platform
Debugging possible if application opt in
Enclave cannot be emulated by VM

## Slide 68: SGX hardened password verification
https://jbp.io/2016/01/17/using-sgx-to-hash-passwords/

## Slide 69: Intel SGX is very active research area
Many small enclaves to cover whole program
  User-annotated code split into many enclaves (“microns”)
    Secure interaction between microns (attest, auth. encryption)
  Tor, H2O, FreeTDS and OpenSSL successfully transformed
    2685, 154, 473 and 307 LOC changes required respectively
    TCB only 20KLOC, PANOPLY specific overhead 24%
Memory randomization of code inside enclave
  SGX program modified with custom LLVM compiler
  Added in-enclave loader for ASLR & swDEP (2703 LOC)
  Code&data split into 32/64B units randomized separately
Full library OS based on SGX (Haven, Graphene-SGX)

## Slide 70: Recent attacks against SGX
SGX is not a silver bullet
Vulnerable to side-channels
  Attacker with physical access explicitly excluded from attacker model
  Impacted by Spectre attack (2017)
    https://github.com/lsds/spectre-attack-sgx
    https://github.com/osusecLab/SgxPectre
  Impacted by Foreshadow attack (CVE-2018-3615) https://foreshadowattack.eu/
    Reading out attestation private key
Bugs of enclave code are still problem (developer)
Not everything is running inside enclave (other code, user input…)

## Slide 71: Programming with Intel’s SGX
Intel SGX SDK
  https://software.intel.com/en-us/sgx-sdk
  6th generation core processor (or later) based platform with SGX enabled BIOS support
Example: Hardened password hashing
  https://jbp.io/2016/01/17/using-sgx-to-hash-passwords/
  https://github.com/ctz/sgx-pwenclave
More SGX info
  http://theinvisiblethings.blogspot.cz/2013/08/thoughts-on-intels-upcoming-software.html
  http://theinvisiblethings.blogspot.cz/2013/09/thoughts-on-intels-upcoming-software.html

## Slide 72: Trusted computing - Critique

## Slide 73: Trusted computing - controversy
For whom is your computed trusted?
  Secure against you as an owner?
Is TC preventing users to run code of their choice?
  Custom OS distribution?
  Open OEM system – locked on first installation
  Physical switch to unlock later
Why some people from Trusted Computing consortium think that Trustworthy Computing might be better title?

## Slide 74: Trusted computing - controversy
R. Anderson, `Trusted Computing' FAQ (2003)
  http://www.cl.cam.ac.uk/~rja14/tcpa-faq.html
J. Edge, UEFI and "secure boot“
  http://lwn.net/Articles/447381/
R. Stallman, Can You Trust Your Computer?
  https://www.gnu.org/philosophy/can-you-trust.html
Selected problems addressed in current designs

## Slide 75: Summary
Two principal solutions for trusted boot
  Verified boot (signatures) and Measured boot (PCR+RA)
Start from clean (and trusted) point
  Allow only intended software to run
  Or prove what actually executed
Additional hardware inside motherboard / CPU provides wide range of new possibilities (TPM)
Size of Trusted Computing Base matters (TPM/SGX)
Controversy about implication of trusted boot
  Who owns and control target platform