## Slide 1: Instructor Materials Chapter 6: Network Layer
CCNA Routing and Switching
Introduction to Networks v6.0
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 6: Network Layer

## Slide 2: Instructor Materials – Chapter 6 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 20
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Introduction to Network 6.0 Planning Guide
Chapter 6: Network Layer
Notes: Introduction to Network Planning Guide
Chapter 6: Configure a Network Operating System

## Slide 4: Chapter 6: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
6.0.1.2 | Class Activity | The Road Less Travelled | Optional
6.1.2.6 | Class Activity | IP Characteristics | Recommended
6.1.3.2 | Video Demonstration | Sample IPv4 Headers in Wireshark | -
6.1.3.3 | Class Activity | IPv4 Header Fields | Recommended
6.1.4.5 | Video Demonstration | Sample IPv6 Headers in Wireshark | -
6.1.4.6 | Class Activity | IPv6 Header Fields | Recommended
6.2.3.3 | Video Demonstration | Introducing the IPv4 Routing Table | -
6.2.2.7 | Video Demonstration | Explaining the IPv4 Routing Table | -
6.2.2.8 | Class Activity | Identify Elements of a Router Routing Table Entry | Recommended
6.3.1.7 | Class Activity | Identify Router Components | Recommended
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 6: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
6.3.1.8 | Packet Tracer | Exploring Internetworking Devices | Optional
6.3.2.3 | Video Demonstration | Router Bootup Process | -
6.3.2.5 | Video Demonstration | The show version Command | -
6.3.2.6 | Class Activity | The Router Boot Process | Recommended
6.3.2.7 | Lab | Exploring Router Physical Characteristics | Recommended
6.4.1.2 | Syntax Checker | Configuring a Cisco Router | Recommended
6.4.1.3 | Packet Tracer | Configure Initial Router Settings | Recommended
6.4.2.1 | Syntax Checker | Configuring LAN Interfaces | Recommended
6.4.3.2 | Syntax Checker | Configuring a Switch Default Gateway | Recommended
6.4.3.3 | Packet Tracer | Connect a Router to a LAN | Recommended
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5

## Slide 6: Chapter 6: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
6.4.3.4 | Packet Tracer | Troubleshooting Default Gateway Issues | Recommended
6.5.1.1 | Class Activity | Can You Read This Map? | Optional
6.5.1.2 | Lab | Building a Switch and Router Network | Recommended
6.5.13 | Packet Tracer | Skill Integration Challenge | Recommended
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 6

## Slide 7: Chapter 6: Assessment
Students should complete Chapter 6, “Assessment” after completing Chapter 6.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 7

## Slide 8
Prior to teaching Chapter 6, the instructor should:
Complete Chapter 6, “Assessment.”
The objectives of this chapter are:
  Describe the purpose of the network layer in data communication.
  Explain why the IPv4 protocol requires other layers to provide reliability.
  Explain the role of the major header fields in the IPv4 packet.
  Explain the role of the major header fields in the IPv6 packet.
  Explain how a host device using routing tables to direct packets to itself, a local destination, or a default gateway.
  Compare a host routing table to a routing table in a router.
  Describe the common components and interfaces of a router.
  Describe the boot-up process of a Cisco IOS router.
  Configure initial settings on a Cisco IOS router.
  Configure two active interfaces on a Cisco IOS router.
  Configure devices to use the default gateway.
Chapter 6: Best Practices
Notes: 8

## Slide 9
Chapter 6: Best Practices (Cont.)
Section 6.1
The network layer, or OSI Layer 3, provides services to allow end devices to exchange data across the network.
To accomplish this end-to-end transport, the network layer uses four basic processes: Addressing end devices, Encapsulation, Routing, De-encapsulation
IP Header + Data = Packet
IP protocol - Connectionless (like regular US Mail), Best Effort (unreliable), Media Independent
Connectionless – No dedicated end-to-end connection
Notes: 9

## Slide 10
Chapter 6: Best Practices (Cont.)
Section 6.1 (Cont.)
US Mail Analogy:
  The sender doesn’t know
        If the receiver is present
        If the letter arrived
        If the receiver can read the letter
      The receiver doesn’t know
        When it is coming
Notes: 10

## Slide 11
Chapter 6: Best Practices (Cont.)
Section 6.1 (cont.)
Best Effort Delivery
  IP is unreliable because packet delivery is not guaranteed.
  IP packets are sent with information about the location of delivery, but it contains no information that can be processed to inform the sender whether delivery was successful.
  Packets may arrive at the destination corrupted, out of sequence, or not at all.
  Based on the information provided in the IP header, there is no capability for packet retransmissions if errors such as these occur.
  Other protocols manage the tracking of packets and ensuring their delivery.
Notes: 11

## Slide 12
Chapter 6: Best Practices (Cont.)
Section 6.1 (cont.)
IPv4 Packet
  This information will be tested in Activity 6.1.3.3
  IPv4 = 0100
  Protocol – Identifies the upper-layer protocol to be used next
        Example: ICMP (1), TCP (6) or UDP (17)
  Time-to-Live – Commonly referred to as hop count
  Differentiated Services – Identifies the priority of each packet
  Source and Destination IPs
Notes: 12

## Slide 13
Chapter 6: Best Practices (Cont.)
Section 6.1 (cont.)
IPv6 Packet Header
  This information will be tested in Activity 6.1.4.6
  Version = 0110
  Traffic Class - Classifies packets for congestion control (similar to IPv4 Differentiated Services)
  Flow Label - To suggest that all packets receive the same type of handling by IPv5 routers
  Payload Length - Total length of entire packet including header (same as IPv4 Total Length)
  Next Header - Identifies the application type to the upper-layer protocol (same as IPv4 protocol field)
  Hop Limit - When this value reaches 0, the sender is notified that the packet was not delivered (same as IPv4 TTL field)
Notes: 13

## Slide 14
Chapter 6: Best Practices (Cont.)
Section 6.2
Routing is the process of identifying the best path to a destination.
Default Gateway is the interface on the router that is connected to the LAN. It is only used when a host must forward packets to a remote network.
Section 6.3
Routers require:
Operating system (OS)
Central processing unit (CPU)
Random-access memory (RAM)
Read-only memory (ROM)
Special memory - Flash and nonvolatile random-access memory (NVRAM)
Notes: 14

## Slide 15
Chapter 6: Best Practices (Cont.)
Section 6.3 (cont.)
Stored in RAM – Cisco IOS, running-config, routing table, ARP cache, packet buffer
RAM – Loses content when the router is powered down or restarted
ROM – Bootup instructions, POST, limited IOS
NVRAM – startup-config
ROM and NVRAM – Does not lose contents when power is turned off
Flash – Permanent storage of IOS and other system files
Router loads two files into RAM when booted – The IOS (from flash) and the startup-config (from NVRAM)
Startup-config becomes the running-config when router first boots
Notes: 15

## Slide 16
Chapter 6: Best Practices (Cont.)
Section 6.3 (cont.)
Display the boot process of a router so that students can view the process and see how long it actually takes to load.
Router bootup process
  Perform the POST and load the bootstrap program.
  Locate and load the operating system.
  Locate and load the startup configuration file or enter setup mode.
Notes: 16

## Slide 17
Chapter 6: Best Practices (Cont.)
Section 6.4
Verify interface configuration
  show ip interface brief
  show ip route
  show interfaces
  show ip interface
Recommendation – Students should keep notes of “show commands” and the results.
Notes: 17

## Slide 18: Chapter 6: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at: https://www.netacad.com/group/communities/community-home
Best practices from around the world for teaching CCNA Routing and Switching. https://www.netacad.com/group/communities/ccna-blog
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Students can enroll in Packet Tracer Know How 1: Packet Tracer 101 (self-enroll)
Notes: 18

## Slide 20: Chapter 6: Network Layer
Introduction to Networks v6.0
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 6: Network Layer

## Slide 21: Chapter 6 - Sections & Objectives
6.1 Network Layer Protocols
  Describe the purpose of the network layer in data communication.
  Explain why the IPv4 protocol requires other layers to provide reliability.
  Explain the role of the major header fields in the IPv4 and IPv6 packet.
6.2 Routing
  Explain how a host device uses routing tables to direct packets to itself, a local destination, or a default gateway.
  Compare a host routing table to a routing table in a router.
6.3 Routers
  Describe the common components and interfaces of a router.
  Describe the boot-up process of a Cisco IOS router.
6.4 Configure a Cisco Router
  Configure initial settings on a Cisco IOS router.
  Configure two active interfaces on a Cisco IOS router.
  Configure devices to use the default gateway.
Notes: 21

## Slide 22: 6.1 Network Layer Protocols
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 6: Network Layer

## Slide 23: Network Layer Protocols Network Layer in Communications
The Network Layer
  End to End Transport processes
  Addressing end devices
  Encapsulation
  Routing
  De-encapsulating
Network Layer Protocols
  IPv4
  IPv6
Notes: 6.1 – Network Layer Protocols
6.1.1 – Network Layer in Communications

## Slide 24: Network Layer Protocols Characteristics of the IP Protocol
Encapsulating IP
  Segments are encapsulated into IP packets for transmission.
  The network layer adds a header so packets can be routed to the destination.
IP - Connectionless
  Sender doesn’t know if the receiver is listening or the message arrived on time.
  Receiver doesn’t know data is coming.
IP – Best Effort Delivery
  No guarantees of delivery are made.
IP – Media Independent
  IP can travel over different types of media.
Notes: 6.1 – Network Layer Protocols
6.1.2 – Characteristics of the IP Protocol

## Slide 25: Network Layer Protocols IPv4 Packet
IPv4 Packet Header
Version = 0100
DS = Packet Priority
TTL = Limits life of Packet
Protocol = Upper layer protocol such as TCP
Source IP Address = source of packet
Destination IP Address = destination of packet
Notes: 6.1 – Network Layer Protocols
6.1.3 - IPv4 Packet

## Slide 26: Network Layer Protocols IPv6 Packet
Limitations of IPv4
  IP address depletion
  Internet routing table expansion
  Lack of end-to-end connectivity
Introducing IPv6
  Increased address space
  Improved packet handling
  Eliminates the need for NAT
EncapsulatingIPv6
  Simplified header format
  No checksum process requirement
  More efficient Options Header mechanism
  Flow Label field makes it more efficient.
IPv6 Packet Header
  xx
Notes: 6.1 – Network Layer Protocols
6.1.4 – IPv6 Packet

## Slide 27: Network Layer Protocols IPv6 Packet (Cont.)
IPv6 Packet Header
  xx
Version = 0110
Traffic Class = Priority
Flow Label = same flow will receive same handling
Payload Length = same as total length
Next Header = Layer 4 Protocol
Hop Limit = Replaces TTL field
Notes: 6.1 – Network Layer Protocols
6.1.4 – IPv6 Packet (Cont.)

## Slide 28: 6.2 Routing
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 6: Network Layer

## Slide 29: Routing How a Host Routes
Host Forwarding Decision
  Three types of destination: itself, local host, remote host.
Default Gateway
  Routes traffic to other networks
  Has a local IP address in the same address range as other hosts on the network
  Can take data in and forward data out
Using the Default Gateway
  Hosts will use the default gateway when sending packets to remote networks.
Host Routing Tables
  Use the netstat –r command to display the
  host routing table on a Windows machine.
Notes: 6.2 – Routing
6.2.1 – How a Host Routes

## Slide 30: Routing How a Host Routes (Cont.)
Notes: 6.2 – Routing
6.2.1 – How a Host Routes (Cont.)

## Slide 31: How a Host Routes Router Routing Tables
Router Packet Forwarding Decision
  Routers and hosts forward packets in a similar fashion.
  The main difference is that routers have more interfaces while hosts often have only one.
  Devices on directly connected networks can be reached directly.
  Devices on remote networks are reached through gateway.
IPv4 Router Routing Table
  The router routing table stores network routes the router knows about.
  Use the show ip route command to display the routing table on a Cisco router.
  The router routing table also has information on: how the route was learned, its trustworthiness and rating.
  It also contains which interface to use to reach that specifc destination.
Directly Connected Routing Table Entries
  C - Identifies a directly-connected network, automatically created when an interface is configured with an IP address and activated.
  L - Identifies that this is a local interface. This is the IPv4 address of the interface on the router.
Remote Network Routing Table Entries
  Xx
Next-Hop Address
  xx
Notes: 6.2 – Routing
6.2.2 – Router Routing Tables

## Slide 32: How a Host Routes Router Routing Tables (Cont.)
Remote Network Routing Table Entries
  Remote destinations can’t be reached directly.
  Remote routes contain the address of the intermediate network device to be used to reach the destination.
Next-Hop Address
  Next-Hop address is the address of the intermediate device used to reach a specifc remote destination.
Notes: 6.2 – Routing
6.2.2 – Router Routing Tables (Cont.)

## Slide 33: 6.3 Routers
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 6: Network Layer

## Slide 34: Routers Anatomy of a Router
A Router is a Computer
  Routers have CPU, memory and I/O devices
  Cisco routers use IOS as their operating system.
Router Memory
  Just as a computer, routers have memory.
  Routers contain RAM, ROM, NVRAM and Flash memory.
Inside a Router
  Routers have the same general structure.
Connect to a Router
  Routers have may ports to support connections.
LAN and WAN Interfaces
  Routers have LAN and WAN ports.
  Different models ship with different ports.
  Ethernet is very common on different router
  models.
Notes: 6.3 – Routers
6.3.1 – Anatomy of a Router

## Slide 35: Routers Anatomy of a Router
Bootset Files
  IOS image file, stored in the Flash, contains the IOS.
  The Flash also stores other system files.
  The NVRAM stores configuration parameters.
Router Bootup Process
  Perform the POST and load the bootstrap program.
  Locate and load the Cisco IOS software.
  Locate and load the startup configuration file or enter setup mode
Show Version Output
  The show version command is very useful.
  It provides information on the amounts of memory installed, what IOS images was loaded during boot and more.
Notes: 6.3 – Routers
6.3.2 – Router Boot-up

## Slide 36: 6.4 Configuring a Cisco Router
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 6: Network Layer

## Slide 37: Configure a Cisco Router Configure Initial Settings
Basic Switch Configuration Steps
  Configure device name
  Secure EXEC mode
  Secure VTY lines
  Secure privilege EXEC mode
  Secure all passwords
  Provide legal notification
  Configure the management SVI
  Save the configuration
Basic Router Configuration Steps
  Configure device name
  Secure EXEC mode
  Secure VTY lines
  Secure privilege EXEC mode
  Secure all passwords
  Provide legal notification
  Configure the management SVI
  Save the configuration
Notes: 6.4 – Configure a Cisco Router
6.4.1 – Configure Initial Settings

## Slide 38: Configure a Cisco Router Configure Interfaces
Configure Router Interfaces
  Enter the interface sub-configuration mode.
  Add a description to the Interface (optional)
  Configure an IPv4 or IPv6 address.
  Activate the interface with a no shutdown command
Verify Interface Configuration
  show ip route - Displays the contents of the IPv4 routing table stored in RAM.
  show interfaces - Displays statistics for all interfaces on the device.
  show ip interface - Displays the IPv4 statistics for all interfaces on a router.
Notes: 6.4 – Configure a Cisco Router
6.4.2 – Configure Interfaces

## Slide 39: Configure a Cisco Router Configure the Default Gateway
Default Gateway for a Host
Default Gateway for a Switch
  A default gateway is required for remote network communication.
  If a switch is to be managed via its VTY lines, it needs a default gateway.
  Use the ip default-gateway command to configure the default gateway for a switch.
Notes: 6.4 – Configure a Cisco Router
6.4.3 – Configure the Default Gateway

## Slide 40: 6.5 Chapter Summary
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 6: Network Layer

## Slide 41: Chapter Summary Summary
Explain how network layer protocols and services support communications across data networks.
Explain how routers enable end-to-end connectivity in a small to medium-sized business network.
Explain how devices route traffic in a small to medium-sized business network.
Configure a router with basic configurations.
Notes: 6.5.1 - Summary

## Slide 42: Section 6.1 New Terms and Commands
encapsulation
routing
de-encapsulation
data
packet
frame
Internet Protocol Version 4 (IPv4)
Internet Protocol Version 6 (IPv6)
Network Layer PDU = IP Packet
Transport Layer PDu
Segment Header
IP Header
Auxiliary port (AUX)
connectionless
best effort delivery
media independent
Connectionless
unreliable
maximum transmission unit (MTU)
Version
Differentiated Services (DS)
Time-to-Live (TTL)
Internet Control Message Protocol (ICMP)
data payload
Identification, Flags, Fragment Offset fields
keyword
Network Address Translation (NAT)
Traffic Class
Flow Label
Payload Length
Next Header
Hop Limit
local host
remote host
default gateway
Notes: New Terms and Commands

## Slide 43: Section 6.2 New Terms and Commands
netstat –r
route print
interface list
IPv4 Route Table
IPv6 Route Table
directly-connected routes
remote routes
default route
show ip route
route source
destination network
outgoing interface
administrative distance
metric
next-hop
route timestamp
branch routers
WAN routers
service provider routers
Notes: New Terms and Commands

## Slide 44: Section 6.3 New Terms and Commands
Power-on-self-test POST
RAM
ROM
NVRAM
Flash
Synchronous dynamic RAM (SDRAM)
WIC
high-speed WIC (HWIC)
ROMMON
Advanced Integration Module (AIM)
Enhanced high-speed WAN interface card (eHWIC)
Serial module
Ethernet interfaces
Auxiliary (AUX) RJ-45 port
In-band router interfaces
Console
Out-of-band
Secure Shell (SSH)
Telnet
startup-config
running-config
bootstrap program
Trivial File Transport Protocol (TFTP)
setup mode
show version
Notes: New Terms and Commands

## Slide 45: Section 6.4 New Terms and Commands
interface type-and-number
ip address ipv4-address subnet-mask
description description-text
no shutdown
show ip interface brief
ping ip address
show ip route
show interfaces
show ip interface brief
ip default-gateway ip-address
Notes: New Terms and Commands