## Slide 1: Instructor Materials Chapter 7: IP Addressing
CCNA Routing and Switching
Introduction to Networks v6.0
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 7: IP Addressing

## Slide 2: Instructor Materials - Chapter 7 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 14
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Introduction to Networks v6.0
Planning Guide
Chapter 7: IP Addressing
Notes: Course Planning Guide
Introduction to Networks v6.0
Chapter 7: IP Addressing

## Slide 4: Chapter 7: Activities
What activities are associated with this chapter?
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Page # | Activity Type | Activity Name | Optional? Y/N
7.0.1.2 | Class Activity | Modeling the Internet of Everything (IoE) | Optional
7.1.1.4 | Interactive Activity | Binary to Decimal Conversions | Recommended
7.1.1.7 | Video | Decimal to Binary Conversions | 
7.1.1.8 | Interactive Activity | Decimal to Binary Conversions | Recommended
7.1.1.9 | Interactive Activity | Binary Game | Optional
7.1.2.4 | Interactive Activity | ANDing to Determine the Network Address | Optional
7.1.2.7 | Video Demonstration | Network, Host, and Broadcast Addresses | 
7.1.2.8 | Lab | Using the Windows Calculator with Network Addresses | Optional
7.1.2.9 | Lab | Converting IPv4 Addresses to Binary | Recommended
7.1.3.7 | Interactive Activity | Unicast, Broadcast, or Multicast | Optional
7.1.3.8 | Packet Tracer | Investigate Unicast, Broadcast, and Multicast Traffic | Optional
Notes: 4

## Slide 5: Chapter 7: Activities (Cont.)
What activities are associated with this chapter?
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Page # | Activity Type | Activity Name | Optional? Y/N
7.1.4.2 | Interactive Activity | Pass or Block IPv4 Addresses | Optional
7.1.4.7 | Interactive Activity | Public or Private IPv4 Addresses | Optional
7.1.4.9 | Lab | Identifying IPv4 Addresses | Optional
7.2.1.3 | Interactive Activity | IPv4 Issues and Solutions | Optional
7.2.2.4 | Interactive Activity | Practicing IPv6 Address Representations | Recommended
7.2.3.5 | Interactive Activity | Identify Types of IPv6 Address | Optional
7.2.4.2 | Syntax Checker | Configuring IPv6 on a Router | Recommended
7.2.4.8 | Syntax Checker | Verifying IPv6 Address Configuration | Recommended
7.2.4.9 | Packet Tracer | Configuring IPv6 Addressing | Recommended
7.2.5.3 | Lab | Identifying IPv6 Addresses | Optional
7.2.5.4 | Lab | Configuring IPv6 Addresses on Network Devices | Recommended
Notes: 5

## Slide 6: Chapter 7: Activities (Cont.)
What activities are associated with this chapter?
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Page # | Activity Type | Activity Name | Optional? Y/N
7.3.2.5 | Packet Tracer | Verifying IPv4 and IPv6 Addressing | Optional
7.3.2.6 | Packet Tracer | Pinging and Tracing to Test the Path | Optional
7.3.2.7 | Lab | Testing Network Connectivity with Ping and Traceroute | Optional
7.3.2.8 | Lab | Mapping the Internet | Recommended
7.3.2.9 | Packet Tracer | Troubleshooting IPv4 and IPv6 Addressing | Recommended
7.4.1.1 | Class Activity | The Internet of Everything…Naturally! | Optional
7.4.1.2 | Packet Tracer | Skills Integration Challenge | Recommended
Notes: 6

## Slide 7: Chapter 7: Assessment
Students should complete Chapter 7, “Assessment” after completing Chapter 7.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 7

## Slide 8
Prior to teaching Chapter 7, the instructor should:
  Complete Chapter 7, “Assessment.”
Section 7.1
  Remind students of the positional notation-place value in decimal to help explain binary place values (see video 7.1.1.7).
  Have students create their own place values chart for binary.
  Encourage students to practice conversions until they are comfortable with the process without using calculators. By doing the conversions manually, students will learn how bits can be manipulated to produce the binary equivalent of a decimal value. No calculators are permitted during CCNA certification exams.
  Direct the students to the binary game to test their binary-decimal conversion skills.
    http://forums.cisco.com/CertCom/game/binary_game_page.htm
Chapter 7: Best Practices
Notes: 8

## Slide 9
Section 7.1 (Cont.)
  Explain the hierarchical structure of an IP address by using analogies like mailing address and phone numbers.
  Demonstrate the ANDing process.
    Recommend activity 7.1.2.4 and video 7.1.2.7.
  Students must know the private address blocks.
    Recommend they do activity 7.1.4.7.
    Discuss the addressing scheme used in their home and at your institution.
  Legacy Classful Addressing.
    Do not spend much time on this.
    It is useful to see the foundation of IPv4 addressing and the reasons for depletion of addresses.
Chapter 7: Best Practices (Cont.)
Notes: 9

## Slide 10
Section 7.2
  Explain the structure of an IPv6 address.
    IPv6 addresses are128 bits and are represented using hexadecimal values.
    Four bits can be represented with a single hexadecimal value. Four hex digits =hextet
    The prefix length is used to indicate the network portion of an IPv6 address can range from 0 to 128. Typical LAN prefix length /64
  Encourage students to use activity 7.2.4.4 to practice representing IPv6 addresses.
  Point out the important features of the IPv6 link-local address
    Enables a device to communicate with other IPv6-enabled devices on the same link.
    Every IPv6-enabled network interface is required to have a link-local address.
    If not configured manually on an interface, it will be automatically created.
    Link-local addresses are in the FE80::/10 range.
Chapter 7: Best Practices
Notes: 10

## Slide 11
  Explain the parts of an IPv6 Global Unicast address and compare it to IPv4.
    Global routing prefix the network portion of the address that is assigned by the provider, such as an ISP.
    The Subnet ID can be used by an organization to identify subnets within its site.
    Interface ID is equivalent to the host portion of an IPv4 address.
  Learn about the basics of an IPv6 address at this URL.
    https://www.youtube.com/watch?v=rljkNMySmuM
  Learn about configuring IPv6 at this URL.
    https://www.youtube.com/watch?v=FVf-GvUVm5U
  Learn about IPv6 Stateless Address Autoconfiguration (SLAAC) at this URL.
    https://www.youtube.com/watch?v=zbkBa8Zl568
Section 7.3
  Use Packet Tracer to demonstrate verifying IPv4 and IPv6 Addressing on page 7.3.2.5.
  Use Packet Tracer to demonstrate using Ping and Traceroute to test connectivity on page 7.3.2.6.
Chapter 7: Best Practices (Cont.)
Notes: 11

## Slide 12: Chapter 7: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at: https://www.netacad.com/group/communities/community-home
Best practices from around the world for teaching CCNA Routing and Switching. https://www.netacad.com/group/communities/ccna-blog
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Notes: 12

## Slide 14: Chapter 7: IP Addressing
CCNA Routing and Switching
Introduction to Networks v6.0
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 7: IP Addressing

## Slide 15: Chapter 7 - Sections & Objectives
7.1 IPv4 Network Addresses
  Convert between binary and decimal numbering systems.
  Describe the structure of an IPv4 address including the network portion, the host portion, and the subnet mask.
  Compare the characteristics and uses of the unicast, broadcast, and multicast IPv4 addresses.
  Explain public, private, and reserved IPv4 addresses.
7.2 IPv6 Network Addresses
  Explain the need for IPv6 addressing.
  Describe the representation of an IPv6 address.
  Describe types of IPv6 network addresses.
  Configure global unicast addresses.
  Describe multicast addresses.
7.3 Connectivity Verification
  Explain how ICMP is used to test network connectivity.
  Use ping and traceroute utilities to test network connectivity.
Notes: 15

## Slide 16: 7.1 IPv4 Network Addresses
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 7: IP Addressing

## Slide 17: IPv4 Network Addresses Binary and Decimal Conversion
IPv4 Addresses
  consists of a string of 32 bits, divided into four sections called octets.
  Each octet contains 8 bits (or 1 byte) separated with a dot.
Conversion between Binary to Decimal
  Use the chart to help with conversion
Notes: 7.1 – IPv4 Network Addresses
7.1.1 – Binary and Decimal Conversion

## Slide 18: IPv4 Network Addresses IPv4 Address Structure
Network and Host Portions
The Subnet Mask
Logical AND
  What is the network address for graphics?
Prefix Length
  What is the prefix length for the graphics?
Network, Host, and Broadcast Addresses
  Network Address?
  Range of Valid Hosts?
  Broadcast Address?
Notes: 7.1 – IPv4 Network Addresses
7.1.2 – IPv4 Address Structure

## Slide 19: IPv4 Network Addresses IPv4 Unicast, Broadcast, and Multicast
IPv4 Addressing Assignment to a Host
  Static – Type in manually
  Dynamic - Dynamic Host Configuration Protocol (DHCP)
IPv4 Communication
  Unicast - send packets from one host to an individual host
  Broadcast - send packets from one host to all the hosts in the network
  Multicast - send a packet from one host to a selected group of hosts in the same or different network
  Which types of communication are the graphics on the right?
Notes: 7.1 – IPv4 Network Addresses
7.1.3 – IPv4 Unicast, Broadcast, and Multicast

## Slide 20: IPv4 Network Addresses Types of IPv4 Addresses
Public and Private IPv4 Addresses
  Private addresses are not routed over the Internet
  Private Addresses:
    10.0.0.0/8 or 10.0.0.0 to10.255.255.255
    172.16.0.0 /12 or 172.16.0.0 to 172.31.255.255
    192.168.0.0 /16 or 192.168.0.0 to 192.168.255.255
Special User IPv4 Addresses
  Loopback addresses
    127.0.0.0 /8 or 127.0.0.1 to 127.255.255.254
  Link-Local addresses or Automatic Private IP Addressing (APIPA) addresses
    169.254.0.0 /16 or 169.254.0.1 to 169.254.255.254
  TEST-NET addresses
    192.0.2.0/24 or 192.0.2.0 to 192.0.2.255
Classless Addressing
  CIDR
  Allocated IPv4 addresses based on prefix length
Assignment of IP Addresses
Notes: 7.1 – IPv4 Network Addresses
7.1.4 – Types of IPv4 Addresses

## Slide 21: 7.2 IPv6 Network Addresses
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 7: IP Addressing

## Slide 22: IPv6 Network Addresses IPv4 Issues
The Need for IPv6
  Depletion of IPv4 address space
  Internet of Everything
IPv4 and IPv6 Coexistence
  Dual Stack – IPv4 and IPv6 on the same network
  Tunneling – IPv6 packets inside IPv4 packets
  Translation - IPv6 packet is translated to an IPv4 packet, and vice versa.
Notes: 7.2 – IPv6 Network Addresses
7.2.1 – IPv4 Issues

## Slide 23: IPv6 Network Addresses IPv6 Addressing
IPv6 Address Representation
  x:x:x:x:x:x:x:x, where x represents 4 hexadecimal values
Apply the rules to simply these IPv6 Addresses
  Rule 1: Omit Leading 0s
  Rule 2: Omit All 0 Segments
    2001:0DB8:0000:1133:0000:0000:0000:0200
    2001:0DB8:CAFE:0000:1111:0000:0000:0200
    2001:0DB8:000A:0000:0000:0000:0000:1000
    2001:0DB8:ACAD:1234:0000:0000:0000:0000
    2001:0DB8:0000:1111:0020:0000:ACAD:0000
    FF02:0000:0000:0000:0000:0000:0000:0001
    FE80:0000:0000:0000:0000:0000:0000:0003
    0000:0000:0000:0000:0000:0000:0000:0000
Notes: 7.2 – IPv6 Network Addresses
7.2.2 – IPv6 Addressing

## Slide 24: IPv6 Network Addresses Types of IPv6 Addresses
IPv6 Address Types
  Unicast
  Multicast
  Anycast
IPv6 Prefix Length
  Indicates the network portion
  Format: IPv6 address /prefix length
  Prefix length range from 0 to 128
  Typical length is /64
Common Types of IPv6 Addresses
  Unicast Addresses
    Unique, Internet routable addresses
    Configured statically or assigned dynamically
  Link-Local Unicast Addresses
    Communicate with other IPv6 enabled devices on the same link
    Device creates its own link local address without DHCP server
  Unique Local Addresses
    Unique local unicast
    Used for local addresses within a site or between a limited number of sites
Notes: 7.2 – IPv6 Network Addresses
7.2.3 – Types of IPv6 Addresses

## Slide 25: IPv6 Network Addresses IPv6 Unicast Addresses
Structure of an IPv6 Global Unicast Address
  Global Routing Prefix
  Subnet ID
  Interface ID
Static Configuration of a Global Unicast Address
  ipv6 address ipv6-address/prefix-length
Dynamic Configuration
  SLAAC
  DHCPv6
Link-Local Addresses
  Dynamic or Static
Verifying IPv6 Address Configuration
  show ipv6 interface brief
Notes: 7.2 – IPv6 Network Addresses
7.2.4 – IPv6 Unicast Addresses

## Slide 26: IPv6 Network Addresses IPv6 Multicast Addresses
Assigned IPv6 Multicast Addresses
  IPv6 multicast addresses have the prefix FF00::/8
    FF02::1 All-nodes multicast group
    FF02::2 All-routers multicast group
Solicited-Node IPv6 Multicast Addresses
Notes: 7.2 – IPv6 Network Addresses
7.2.5 – IPv6 Multicast Addresses

## Slide 27: 7.3 Connectivity Verification
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 7: IP Addressing

## Slide 28: Connectivity Verification ICMP
ICMPv4 and ICMPv6
  Host Confirmation
  Destination or Service Unreachable
  Time Exceeded
  Router Redirection
ICMPv6 Router Solicitation and Router Advertisement Messages
  Messaging between an IPv6 router and an IPv6 device:
    Router Solicitation (RS) message
    Router Advertisement (RA) message
  Messaging between IPv6 devices:
    Neighbor Solicitation (NS) message
    Neighbor Advertisement (NA) message
  Duplicate Address Detection (DAD)
Notes: 7.3 – Connectivity Verification
7.3.1 – ICMP

## Slide 29: Connectivity Verification Testing and Verification
Ping
  Testing the Local Stack
    127.0.0.1 (IPv4) or ::1 (IPv6)
  Testing Connectivity to the Local LAN
  Testing Connectivity to Remote
Traceroute
  Testing the Path
    Round Trip Time (RTT)
    IPv4 TTL and IPv6 Hop Limit
Notes: 7.3 – Connectivity Verification
7.3.2 – Testing and Verification

## Slide 30: 7.4 Chapter Summary
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 7: IP Addressing

## Slide 31: Chapter Summary Summary
Explain the use of IPv4 addresses to provide connectivity in a small to medium-sized business network.
Configure IPv6 addresses to provide connectivity in small to medium-sized business networks.
Use common testing utilities to verify network connectivity.
Notes: 7.4.1.3 - Summary

## Slide 34: Section 7.1 New Terms and Commands
ANDing
Binary Numbering System
Broadcast
Broadcast Address
Broadcast Domain
Class A
Class B
Class C
Class D
Class E
Classless Inter-domain Routing (CIDR)
DHCP Server
DHCP Client Dynamic Assignment
Directed Broadcast
Dotted Decimal Format
Dynamic Host Configuration Protocol (DHCP)
Host Address
Internet Assigned Numbers Authority (IANA)
Internet Service Providers (ISPs)
IPv4 Loopback Address
Limited Broadcast
Link-local Addresses
Multicast Transmission
Multicast
Multicast Addresses
Network Address
Octet
Positional Notation
Prefix Length
Private Address
Public Address
radix
Regional Internet Registries (RIRs)
RFC 1918
Slash Notation
Static IP Addressing
Subnet Mask
TEST-NET Addresses
Unicast
Notes: New Terms and Commands

## Slide 35: Section 7.2 New Terms and Commands
Address Resolution
Assigned multicast
Destination or Service Unreachable
Dual-stack
Duplicate Address Detection
EUI-64 Process
FF02::1 All-nodes multicast group
FF02::2 All-routers multicast group
Global Unicast Address
Hextet
Host confirmation
ICMPv6
IPv4 Time-to-Live (TTL)
IPv6
IPv6 Anycast
IPv6 Hop Limit
IPv6 link-local address
IPv6 Loopback Address
IPv6 Multicast
IPv6 Prefix Length
IPv6 Unicast
Leading Zeros
Link-local Address
Network Address Translation (NAT64)
Round Trip Time (RTT)
Route redirection
Router Advertisement
Router Solicitation
show ipv6 interface brief
show ipv6 route
Solicited node multicast
Stateless Address Autoconfiguration (SLAAC)
Time exceeded
Tunneling
Unique Local Address
Unspecified Address
Notes: New Terms and Commands