## Slide 1: Instructor Materials Chapter 11: Build a Small Network
CCNA Routing and Switching
Introduction to Networks v6.0
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 11: Build a Small Network

## Slide 2: Instructor Materials – Chapter 11 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 13
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Introduction to Networks v6.0
Planning Guide
Chapter 11: Build a Small Network
Notes: Course Planning Guide
Introduction to Networks v6.0
Chapter 11: Build a Small Network

## Slide 4: Chapter 11: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional? Y/N
11.0.1.2 | Class Activity | Did you notice . . .? | Recommended
11.2.1.4 | Interactive Activity | Security Threats and Vulnerabilities | Recommended
11.2.2.5 | Interactive Activity | Types of Attack | Recommended
11.2.2.6 | Lab | Researching Network Security Threats | Optional
11.2.4.5 | Packet Tracer | Configuring Secure Passwords and SSH | Recommended
11.2.4.6 | Lab | Accessing Network Devices with SSH | Optional
11.2.4.7 | Lab | Examining Telnet and SSH in Wireshark | Optional
11.2.4.8 | Lab | Securing Network Devices | Recommended
11.3.2.3 | Packet Tracer | Test Connectivity with traceroute | Recommended
11.3.2.4 | Lab | Testing Network Latency with Ping and Traceroute | Recommended
11.3.3.2 | Video | The show version Command | 
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 11: Activities (Cont.)
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional? Y/N
11.3.3.3 | Packet Tracer | Using show Commands | Recommended
11.3.4.5 | Interactive Activity | Show Commands | Recommended
11.3.4.6 | Lab | Using the CLI to Gather Network Device Information | Optional
11.4.1.4 | Interactive Activity | Order the Troubleshooting Steps | Recommended
11.4.3.5 | Lab | Troubleshooting Cables and Interfaces | Recommended
11.4.3.6 | Packet Tracer | Troubleshooting Connectivity Issues | Recommended
11.5.1.1 | Class Activity | Design and Build a Small Business Network | Optional
11.5.1.2 | Packet Tracer | Skills Integration Challenge | Recommended
11.5.1.3 | Packet Tracer | Troubleshooting Challenge | Recommended
Appendix | Packet Tracer | Configuring a Linksys Router | Deeper
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5

## Slide 6: Chapter 11: Assessment
Students should complete Chapter 11, “Assessment” after completing Chapter 11.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 6

## Slide 7
Prior to teaching Chapter 11, the instructor should:
Complete Chapter 11, “Assessment.”
Ensure that students have a good knowledge of the TCP/IP and OSI models and IP addressing. This chapter shows how these are implemented in a small network.
Section 11.1
  Highlight the function of switches and routers and the importance of hierarchical network design.
  Explain the factors to be considered when selecting a switch and router for an organization. These factors include the number of users/networks needed, cost, performance, expandability, redundancy, and required features. Work with your school’s IT department or a local small business and have students research upgrades to the network.
  Visit the Cisco Baseline Process Best Practices white paper:
    http://www.cisco.com/en/US/tech/tk869/tk769/technologies_white_paper09186a008014fb3b.shtml
Chapter 11: Best Practices
Notes: 7

## Slide 8
Section 11.2
  Discuss network security and recent cyber attacks on business and government.
  Visit http://map.norsecorp.com/ to see a map of network attacks.
  Learn about 1941 password recovery: http://www.cisco.com/c/en/us/support/docs/routers/3800-series-integrated-services-routers/112058-c1900-pwd-rec-00.html
  Learn about the Password Recovery Catalyst 2960:
  http://www.cisco.com/c/en/us/support/switches/catalyst-2960-series-switches/products-password-recoveries-list.html
  For more information about managing configuration files visit:
    http://www.cisco.com/en/US/docs/ios/fundamentals/configuration/guide/usb_flash_keys_ps6350_TSD_Products_Configuration_Guide_Chapter.html
Chapter 11: Best Practices (Cont.)
Notes: 8

## Slide 9
Section 11.3
  Students should become very familiar with the basic host and IOS commands used to acquire information about the devices in a network. Provide as much hands-on opportunity to practice these as possible.
  Host commands: ipconfig, ping, tracert
  IOS commands: show running-config, show version, show interfaces, show ip interface brief, show cdp neighbors, traceroute, show ip route
Section 11.4
  Students should become familiar with the troubleshooting process.
  Use host and IOS commands to assist with troubleshooting.
Section 11.5
  The following activities are strongly recommended
    Packet Tracer 11.5.1.2 Skills Integration Challenge
    Packet Tracer 11.5.1.3 Troubleshooting Challenge
Chapter 11: Best Practices (Cont.)
Notes: 9

## Slide 10
Section 11.3
  Students should become very familiar with the basic host and IOS commands used to acquire information about the devices in a network. Provide as much hands-on opportunity to practice these as possible.
  Host commands: ipconfig, ping, tracert
  IOS commands: show running-config, show version, show interfaces, show ip interface brief, show cdp neighbors, show flash, traceroute, show ip route
Section 11.5
  The following activities are strongly recommended
    Packet Tracer 11.5.1.2 Skills Integration Challenge
    Packet Tracer 11.5.1.3 Troubleshooting Challenge
Chapter 11: Best Practices (Cont.)
Notes: 10

## Slide 11: Chapter 11: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at: https://www.netacad.com/group/communities/community-home
Best practices from around the world for teaching CCNA Routing and Switching. https://www.netacad.com/group/communities/ccna-blog
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Notes: 11

## Slide 13: Chapter 11: Build a Small Network
Introduction to Networks v6.0
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 11: Build a Small Network

## Slide 14: Chapter 11 - Sections & Objectives
11.1 Network Design
  Identify the devices used in a small network.
  Identify the protocols used in a small network.
  Explain how a small network serves as the basis of larger networks.
11.2 Network Security
  Explain why security measures are necessary on network devices.
  Identify security vulnerabilities.
  Identify general mitigation techniques.
  Configure network devices with device hardening features to mitigate security threats.
  Apply the commands to back up and restore an IOS configuration file.
Notes: 14

## Slide 15: Chapter 11 - Sections & Objectives (Cont.)
11.3 Basic Network Performance
  Use the output of the ping command to establish relative network performance.
  Use the output of the tracert command to establish relative network performance.
  Use show commands to verify the configuration and status of network devices.
  Use host and IOS commands to acquire information about network devices.
11.4 Network Troubleshooting
  Apply troubleshooting methodologies to resolve problems
  Troubleshoot interface and cable issues
  Troubleshoot client connectivity issues involving DNS
Notes: 15

## Slide 16: 11.1 Network Design
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 11: Build a Small Network

## Slide 17: Network Design Devices in a Small Network
Small Network Topologies
  Comprises one router, a couple of switches, and the user PCs.
  Access to Internet through a single WAN link, cable or DSL.
  Management usually by a third party company.
Device Selection for a Small Network
  Security, QoS, VoIP, L3 switching, NAT, and DHCP
IP Addressing for a Small Network
  Address space is a crucial component of a network design.
  All devices connected to the network require an address.
  The address scheme must be planned, documented, and maintained.
  Address space documentation can be very useful for:
  troubleshooting and control
  Address documentation is also very important when controlling resource access.
Notes: 11.1 – Network Design
11.1.1 – Devices in a Small Network

## Slide 18: Network Design Devices in a Small Network (Cont.)
Redundancy in a Small Network
  A network should reliable by design.
  Network failures are usually very costly.
  Redundancy increases reliability by eliminating single points of failure.
  Network redundancy can be achieved by duplicating network equipment and links.
  A good example is a network’s link to the Internet or to a server farm.
Traffic Management
  Traffic type and patterns are should also be considered when designing a network.
  A good network design categorizes traffic according to priority.
Notes: 11.1 – Network Design
11.1.1 – Devices in a Small Network

## Slide 19: Network Design Small Network Applications and Protocols
Common Applications
  Network Applications
    Used to communicate over the network.
    Email clients and web browsers are examples of this type of application.
  Application Layer Services
    Programs that interface with the network and prepare the data for transfer.
    Each service uses protocols, which define the standards and data formats to be used.
Common Protocols
  Processes on either end of a communication session
  How messages are sent and the expected response
  Types and syntax of messages
  Meaning of informational fields
  Interaction with the next lower layer
Voice and Video Applications
  Infrastructure
  VoIP
  IP Telephony
  Real-time Applications
Notes: 11.1 – Network Design
11.1.2 – Small Network Application and Protocols

## Slide 20: Network Design Scale to Larger Networks
Small Network Growth
  To scale a network, several elements are required:
    Network documentation
    Device inventory
    Budget
    Traffic analysis
Protocol Analysis
  Understand the protocols in use in the network.
  Protocol analyzers are tools designed to help in that task.
  Capture traffic in high-utilization times and in different locations of the network.
  Analysis results allow for more efficient way to manage traffic.
Employee Network Utilization
  Be aware of how network use is changing.
  A network administrator can create in-person IT snapshots” of employee application utilization.
Notes: 11.1 – Network Design
11.1.3 – Scale to Larger Networks

## Slide 21: 11.2 Network Security
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 11: Build a Small Network

## Slide 22: Network Security Security Threats and Vulnerabilities
Types of Threats
  Digital intrusion can be costly.
  Intruders can gain access through software vulnerabilities, hardware attacks, or stolen credentials.
  Common types of digital threats include those listed in this graphic.
Physical Security
  Hardware
  Environmental
  Electrical
  Maintenance
Types of Vulnerabilities
  Three primary vulnerabilities: technological, configuration, and security policy
  Endpoints can be under attack ,such as servers and desktop computers.
  Any of these three vulnerabilities can be exploited and used in attacks.
Notes: 11.2 – Network Security
11.2.1 – Security Threats and Vulnerabilities

## Slide 23: Network Security Network Attacks
Types of Malware
  Viruses
  Worms
  Trojan Horses
Reconnaissance Attacks
  Discovery and mapping of systems and services
  Acquire enough information on the target system or network to facilitate the search for vulnerabilities.
  Common tools rely mostly on free and public Internet services, such as DNS and Whois.
  Port-scanners and packet sniffers are also commonly used in reconnaissance.
Notes: 11.2 – Network Security
11.2.2 – Network Attacks

## Slide 24: Network Security Network Attacks (Cont.)
Access Attacks
  Password Attacks
  Trust Exploitation
  Port Redirection
  Man-in-the-Middle
Denial of Service Attacks
  Although simple, DoS attacks are still dangerous.
  Prevent authorized people from using a service by consuming system resources.
  Prevent DoS attacks by applying the latest security updates.
  Common DoS Attacks:
    Ping of Death
    SYN Flood
    DDoS
    Smurf Attack
Notes: 11.2 – Network Security
11.2.2 – Network Attacks

## Slide 25: Network Security Network Attack Mitigation
Backup, Upgrade, Update, and Patch
  Keeping up-to-date with the latest developments
  Enterprises need to keep current with the latest versions of antivirus software.
  Patches for all known vulnerabilities must be applied.
  A central patch server for managing a large number of servers and systems.
  Patches should be installed without user intervention.
Authentication, Authorization, and Accounting
  AAA services provide access control on a network device.
    Authentication - access a resource
    Authorization – what they can do
    Accounting – actions performed while accessing the resource
  The AAA framework can be very helpful when mitigating network attacks.
Notes: 11.2 – Network Security
11.2.3 – Network Attack Mitigation

## Slide 26: Network Security Network Attack Mitigation (Cont.)
Firewalls
  A firewall controls the traffic and helps prevent unauthorized access
  Techniques for determining what is permitted or denied access to a network include:
    Packet filtering
    Application filtering
    URL filtering
    Stateful packet inspection (SPI)
Endpoint Security
  Common endpoints are laptops, desktops, servers, smartphones, and tablets.
  Securing endpoint devices is challenging.
  Employees need to be trained on proper use of the network.
  Policies often include the use of antivirus software and host intrusion prevention.
  More comprehensive endpoint security solutions rely on network access control.
Notes: 11.2 – Network Security
11.2.3 – Network Attack Mitigation

## Slide 27: Network Security Device Security
Device Security Overview
  Default settings are dangerous because they are well-known.
  Cisco routers have the Cisco AutoSecure feature.
  In addition, the following apply for most systems:
    Change default usernames and passwords immediately
    Restrict access to system resources to authorized individuals only.
    Turn off unnecessary services.
    Update any software and install any security patches prior to production operation.
Passwords
  Use strong passwords. A strong password has/is:
    At least 8 characters, preferably 10 or more
    A mix of uppercase and lowercase letters, numbers, symbols, and spaces.
    No repetition, no common dictionary words, no letter or number sequences, no usernames, relative, or pet names, and no other easily identifiable pieces of information
    Misspelled words
    Changed often
  Cisco routers support the use of a phrase made of many words, which is called a passphrase.
Notes: 11.2 – Network Security
11.2.4 – Device Security

## Slide 28: Network Security Device Security (Cont.)
Basic Security Practices
  Strong passwords are only as useful as they are secret.
  The service password-encryption command encrypts the passwords in the configuration.
  The security passwords min-length command ensures all configured passwords have a minimum specified length.
  Blocking several consecutive login attempts helps minimize password brute-force attacks.
  login block-for 120 attempts 3 within 60 will block login attempts for 120 seconds if there are three failed login attempts within 60 seconds.
  exec timeout automatically disconnect idle users on a line
Enable SSH
  Telnet is not secure.
  It is highly recommended to use SSH for remote shell protocol.
  To configure a Cisco device to support SSH takes four steps:
    Step 1. Ensure that the router has a unique hostname and a IP domain name.
    Step 2. Generate the SSH keys.
    Step 3. Create a local username.
    Step 4. Enable vty inbound SSH sessions.
  The router can now be remotely accessed only by using SSH.
Notes: 11.2 – Network Security
11.2.4 – Device Security

## Slide 29: 11.3 Basic Network Performance
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 11: Build a Small Network

## Slide 30: Basic Network Performance The ping Command
Interpreting Ping Results
  Using the ping command is an effective way to test connectivity.
  Use the Internet Control Message Protocol (ICMP) to verify Layer 3 connectivity.
  Help to identify the source of the problem.
  What do these common ping indicators tell you?
    ! . U
  Extended Ping
    Allows for more options
Network Baseline
  Built over a period of time.
  Saved results from commands, such as ping
  or trace, along with error messages
  an response times
  Time stamped for later comparison.
  Increased response time could indicate latency issue.
Notes: 11.3 – Basic Network Performance
11.3.1 – The ping Command

## Slide 31: Basic Network Performance The traceroute and tracert Command
Interpreting Trace Message
  Returns a list of hops as a packet is routed through a network.
  Use tracert for Windows-based systems.
  Use traceroute for Cisco IOS and UNIX-based systems.
Extended Traceroute
  Allows adjustment of parameters
  Command terminates when:
    Destination responds with an ICMP
    echo reply
    User interrupts the trace with the
    escape sequence
Notes: 11.3 – Basic Network Performance
11.3.2 – The traceroute and tracert Command

## Slide 32: Basic Network Performance Show Commands
The Cisco IOS CLI show commands are powerful troubleshoot tools.
The show commands display configuration files, checking the status of device interfaces and processes, and verifying the device operational status.
The status of nearly every process or function of the router can be displayed using a show command.
Some of the more popular show commands are:
  show running-config
  show interfaces
  show arp
  show ip route
  show protocols
  show version
Notes: 11.3 – Basic Network Performance
11.3.3 – Show Commands

## Slide 33: Basic Network Performance Host and IOS Commands
The ipconfig Command
  Display IP and default gateway information on a Windows-based computer.
  What do these commands display?
    ipconfig /all
    ipconfig /displaydns
The arp Command
  The arp –a command lists all devices currently in the ARP cache of the host.
  The cache can be cleared by using the arp -d command.
Notes: 11.3 – Basic Network Performance
11.3.4 – Host and IOS Commands

## Slide 34: Basic Network Performance Host and IOS Commands (Cont.)
The show cdp neighbors Command
  CDP is a Cisco-proprietary protocol that runs at the data link layer.
  Two or more Cisco network devices can learn about each other even if Layer 3 connectivity does not exist.
  CDP can be a security risk.
  To disable CDP globally, use the global configuration command no cdp run.
  To disable CDP on an interface, use the interface command no cdp enable.
  What information does the cdp neighbors details command provide?
The show ip interface brief Command
  Displays a summary of the key information for all the network interfaces on a router.
  Verify the status of the switch interfaces.
Notes: 11.3 – Basic Network Performance
11.3.4 – Host and IOS Commands

## Slide 35: Basic Network Performance Debugging
The debug Command
  Allows the administrator to display
  messages generated by the following
  processes in real-time for analysis:
    IOS processes
    Protocols
    Mechanisms
    Events
  undebug all turns off all debug commands
  What are the available debug commands?
  What can you do to limit the amount of displayed messages?
The terminal monitor Command
  Displays the log messages while connected remotely, such as SSH
  Stop displaying the log message: terminal no monitor
Notes: 11.3 – Basic Network Performance
11.3.4 – Debugging

## Slide 36: 11.4 Network Troubleshooting
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 11: Build a Small Network

## Slide 37: Network Troubleshooting Troubleshooting Methodologies
Basic Troubleshooting Approaches
  Identify the Problem
  Establish a Theory of Probable Causes
  Test the Theory to Determine Cause
  Establish a Plan of Action to Resolve the Problem and Implement the Solution
  Verify Full System Functionality and Implement Preventative Measures
  Document Findings, Actions, and Outcomes
Resolve or Escalate?
Verify and Monitor Solution
  What IOS commands can you use to verify and monitor the solution?
Notes: 11.4 – Network Troubleshooting
11.4.1 – Troubleshooting Methodologies

## Slide 38: Network Troubleshooting Troubleshoot Cables and Interfaces
Duplex Operation
  Direction of data transmission between two devices
  Two connected Ethernet network interfaces should operate in the same duplex mode for best performance
Duplex Mismatch
  Log messages can indicate duplex mismatches.
  What IOS commands can you use to determine duplex mismatch?
Notes: 11.4 – Network Troubleshooting
11.4.2 – Troubleshooting Cables and Interfaces

## Slide 39: Network Troubleshooting Troubleshooting Scenarios
IP Addressing Issues on IOS Devices
  Manual assignment mistakes
  DHCP-related issues
  Which show commands?
IP Addressing Issues on End Devices
  169.254.0.0/16 on Windows-based system
  ipconfig to verify IP addresses assigned to a Windows-based system
Default Gateway Issues
  Unable to communicate outside the network
  ipconfig to verify default gateway assigned to a Windows-based system
Troubleshooting DNS Issues
  ipconfig /all to determine DNS server used
  nslookup to manually place DNS queries and analyze DNS response
Notes: 11.4 – Network Troubleshooting
11.4.3 – Troubleshooting Scenarios

## Slide 40: 11.5 Chapter Summary
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 11: Build a Small Network

## Slide 41: Chapter Summary Summary
Explain how a small network can scale into a larger network.
Configure switches and routers with device hardening features to enhance security.
Use common show commands and utilities to establish a relative performance baseline for the network.
Apply troubleshooting methodologies and command host and IOS commands to resolve problems.
Explain how a small network of directly connected segments is created, configured, and verifies.
Notes: 11.5.1.4 - Summary

## Slide 44: Section 11.2 New Terms and Commands
Application Filtering
Authentication, Authorization, and Accounting (AAA)
auto secure (command)
exec timeout (command)
crypto key generate rsa general-keys modulus modulus-size (command)
endpoint security
ip domain-name domain-name (command)
login block-for 120 attempts 3 within 60 (command)
Packet Filtering
passphrase
Personal firewalls
security passwords min-length (command)
Stateful Packet Inspection (SPI)
service password-encryption (command)
transport input ssh
URL Filtering
Notes: New Terms and Commands

## Slide 45: Section 11.3 New Terms and Commands
! . U
Address Resolution Protocol (ARP)
exec timeout (command)
crypto key generate rsa general-keys modulus modulus-size (command)
ip domain-name domain-name (command)
ipconfig (host command)
login block-for 120 attempts 3 within 60 (command)
loopback address 127.0.0.1
ping (command)
security passwords min-length (command)
service password-encryption (command)
show cdp neighbors (IOS command)
show ip interface brief (IOS command)
tracert (host command)
traceroute (IOS command)
transport input ssh
Notes: New Terms and Commands