## Slide 1: Instructor Materials Chapter 9: Transport Layer
CCNA Routing and Switching
Introduction to Networks v6.0
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 9: Transport Layer

## Slide 2: Instructor Materials – Chapter 9 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 15
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Introduction to Network 6.0 Planning Guide
Chapter 9: Transport Layer
Notes: Introduction to Network Planning Guide
Chapter 9: Transport Layer

## Slide 4: Chapter 9: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
9.0.1.2 | Class Activity | We Need to Talk – Game | Optional
9.1.2.0 | Interactive Activity | Compare TCP and UDP Characteristics | Recommended
9.2.1.5 | Video Demonstration | TCP 3-Way Handshake | -
9.2.1.6 | Lab | Using Wireshark to Observe the TCP 3-Way Handshake | Recommended
9.2.1.7 | Interactive Activity | TCP Connection and Termination Process | Recommended
9.2.2.2 | Video Demonstration | Sequence Numbers and Acknowledments | -
9.2.2.3 | Video Demonstration | Data Loss and Retransmissions | -
9.2.3.5 | Lab | Using Wireshark to Examine a UDP DNS Capture | Recommended
9.2.4.3 | Lab | Using Wireshark to Examine a FTP TFTP Captures | Optional
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 9: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
9.2.4.4 | Interactive Activity | TCP, UDP or Both | Recommended
9.3.1.1 | Class Activity | We Need to Talk, Again – Game | Optional
9.3.1.2 | Packet Tracer | TCP and UDP Communications | Optional
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5

## Slide 6: Chapter 9: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
8.4.1.1 | Class Activity | Can You Call Me Now? | Optional
8.4.1.2 | Packet Tracer | Skills Integration Challenge | Recommended
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 6

## Slide 7: Chapter 9: Assessment
Students should complete Chapter 9, “Assessment” after completing Chapter 9.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 7

## Slide 8
Prior to teaching Chapter 9, the instructor should:
Complete Chapter 9, “Assessment.”
The objectives of this chapter are:
  Describe the purpose of the transport layer in managing the transportation of data in end-to-end communication.
  Describe characteristics of the TCP and UDP protocols, including port numbers and their uses.
  Explain how TCP session establishment and termination processes facilitate reliable communication.
  Explain how TCP protocol data units are transmitted and acknowledged to guarantee delivery.
  Describe the UDP client processes to establish communication with a server.
  Compare features of UDP and TCP.
Chapter 9: Best Practices
Notes: 8

## Slide 9
Chapter 9: Best Practices (Cont.)
Review the OSI model and the TCP/IP protocol stack. Review the process of encapsulation to set the stage for this chapter.
Section 9.1
Describe the segmentation and multiplexing concepts (the need to segment data for transmission).
Explain the two Transport layer protocols UDP and TCP.
Discuss the advantages/disadvantages of TCP and UDP. Discuss why developers choose an application layer protocol to use TCP or UDP.
Section 9.2
Explain the need to identify segments using sequence numbers so they can be reassembled in the correct order at the destination.
Notes: 9

## Slide 10
Chapter 9: Best Practices (Cont.)
Section 9.2 (cont.)
Explain multiple simultaneous data conversations at the host and destination, and the need to let the upper layers know by which application the data should be handled.
Define session establishment, termination, reliability in relation to delivery, flow control, and the purpose for each.
Stress the reliability-related processes of segment tracking, acknowledgement, and retransmission.
Explain the use of port numbers to identify the correct application for each communication stream.
Students need to memorize the most commonly used port numbers.
Notes: 10

## Slide 11
Chapter 9: Best Practices (Cont.)
Section 9.2 (cont.)
Use Wireshark to examine FTP and TFTP captures. Complete lab 9.2.4.3 as a demonstration.
The following video is appropriate for high school students and explains the difference between TCP and UDP.
  https://www.youtube.com/watch?v=KSJu5FqwEMM
Discuss which applications and services use UDP and/or TCP.
Ask students about services and applications they use and to identify if these use UDP or TCP or both.
Notes: 11

## Slide 12: Chapter 9: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at: https://www.netacad.com/group/communities/community-home
Best practices from around the world for teaching CCNA Routing and Switching. https://www.netacad.com/group/communities/ccna-blog
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Students can enroll in Packet Tracer Know How 1: Packet Tracer 101 (self-enroll)
Notes: 12

## Slide 14: Chapter 9: Transport Layer
Introduction to Networks v6.0
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 9: Transport Layer

## Slide 15: Chapter 9 - Sections & Objectives
9.0 Introduction
9.1 Subnetting an IPv4 Network
  Describe the purpose of the transport layer in managing the transportation of data in end-to-end communication.
  Describe characteristics of the TCP and UDP protocols, including port numbers and their uses.
9.2 Addressing Schemes
  Explain how TCP session establishment and termination processes facilitate reliable communication.
  Explain how TCP protocol data units are transmitted and acknowledged to guarantee delivery.
  Describe the UDP client processes to establish communication with a server.
  Compare UDP and TCP.
9.3 Summary
Notes: 15

## Slide 16: 9.1 Transport Layer Protocols
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 9: Transport Layer

## Slide 17: Transport Layer Protocols Transportation of Data
Role of the Transport Layer
  Responsible for establishing a temporary communication session between two applications and delivering data between them.
  Provides Connection-oriented data stream support, Reliability, Flow control, Multiplexing
Transport Layer Responsibilities
  Track individual conversations.
  Segment Data and Reassemble Segments.
  Identify the Applications.
Conversation Multiplexing
  Segments data into small chunks.
  Label data chunks according to the conversation.
Transport Layer Reliability
  Two protocols provided: TCP and UDP.
  TCP supports reliability while UDP doesn’t.
Notes: 9.1 – Transport Layer Protocols
9.1.1 – Transportation of Data

## Slide 18: Transport Layer Protocols Transportation of Data (Cont.)
TCP
  Supports packet delivery confirmation.
  There are three basic operations that enable reliability with TCP:
    Numbering and tracking data segments transmitted to a specific host from a specific application
    Acknowledging received data
    Retransmitting any unacknowledged data after a certain period of time
UDP
  UDP provides the basic functions for delivering data segments between the appropriate applications, with very little overhead and data checking.
  Perfect for applications that don’t require reliability.
The Right Transport Layer Protocol for the Right Application
  TCP is better for databases, web browsers, email clients, etc.
  UDP is better for live audio or video streaming, VoIP, etc.
Notes: 9.1 – Transport Layer Protocols
9.1.1 – Transportation of Data (Cont.)

## Slide 19: Transport Layer Protocols TCP and UDP Overview
TCP Features
  Establishing a session
  Reliable delivery
  Same-Order delivery
  Flow control
TCP Header
  TCP is a stateful protocol.
  TCP adds 20 bytes of overhead in the segment header.
Notes: 9.1 – Transport Layer Protocols
9.1.2 – TCP and UDP Overview

## Slide 20: Transport Layer Protocols TCP and UDP Overview (Cont.)
UDP Features
  Simple and fast.
UDP Header
  UDP is a stateless protocol.
  Reliability must be handled by the application.
  The pieces of communication in UDP are called Datagrams.
  UDP adds only 8 bytes of overhead.
Notes: 9.1 – Transport Layer Protocols
9.1.2 – TCP and UDP Overview (Cont.)

## Slide 21: Transport Layer Protocols TCP and UDP Overview (Cont.)
Multiple Separate Conversations
  The transport layer separate sand manages multiple communications with different transport requirements.
  Different applications are sending and receiving data over the network simultaneously.
  Unique header values allow TCP and UDP to manage these multiple and simultaneous conversations by identifying these applications.
  These unique identifiers are the port numbers.
Port Numbers
  Usually seen in pairs: source port and destination port.
  The source port is dynamically chosen by the sender.
  The destination port is used to identify an application on the server (destination).
Notes: 9.1 – Transport Layer Protocols
9.1.2 – TCP and UDP Overview (Cont.)

## Slide 22: Transport Layer Protocols TCP and UDP Overview (Cont.)
Socket Pairs
  The combination of the source IP address and source port number, or the destination IP address and destination port number, is known as a socket.
  The socket is used to identify the server and service being requested by the client.
  Two sockets combine to form a socket pair: (192.168.1.5:1099, 192.168.1.7:80).
  Sockets enable multiple processes running on a client and multiple connections to a server process to be distinguished from each other.
Port Number Groups
  The IANA has created three port number groups:
  Well-known ports (0 to 1023)
  Registered Ports (1024 to 49151)
  Private and/or Dynamic Ports (49152 to 65535)
The netstat Command
  Netstat allows a user to see active connections in a host.
  Netstat also displays the process using the connection.
Notes: 9.1 – Transport Layer Protocols
9.1.2 – TCP and UDP Overview (Cont.)

## Slide 23: 9.2 TCP and UDP
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 9: Transport Layer

## Slide 24: Transport Layer Protocols TCP Communication Process
TCP Server Processes
  Each application process running on the server uses a port number.
  An individual server cannot have two services assigned to the same port number within the same transport layer service.
  An active server application assigned to a specific port is considered to be open.
  Any incoming client request addressed to an open port is accepted and processed by the server application bound to that port.
  There can be many ports open simultaneously on a server, one for each active server application.
TCP Connection Establishment
  A TCP connection is established in three steps:
    The initiating client requests a client-to-server communication session with the server.
    The server acknowledges the client-to-server communication session and requests a server-to-client communication session.
    The initiating client acknowledges the server-to-client communication session.
Notes: 9.2 – TCP and UDP
9.2.1 – TCP Communication Process

## Slide 25: Transport Layer Protocols TCP Communication Process (Cont.)
TCP Session Termination
  The FIN TCP flag is used to terminate a TCP connection.
    When the client has no more data to send in the stream, it sends a segment with the FIN flag set.
    The server sends an ACK to acknowledge the receipt of the FIN to terminate the session from client to server.
    The server sends a FIN to the client to terminate the server-to-client session.
    The client responds with an ACK to acknowledge the FIN from the server.
    When all segments have been acknowledged, the session is closed.
TCP Three-way Handshake Analysis
  The three-way handshake:
    Establishes that the destination device is present on the network.
    Verifies that the destination device has an active service and is accepting requests on the destination port number that the initiating client intends to use
    Informs the destination device that the source client intends to establish a communication session on that port number.
Notes: 9.2 – TCP and UDP
9.2.1 – TCP Communication Process (Cont.)

## Slide 26: Transport Layer Protocols Reliability and Flow Control
TCP Reliability – Ordered Delivery
  TCP segments use sequence numbers to uniquely identify and acknowledge each segment, keep track of segment order, and indicate how to reassemble and reorder received segments.
  An initial sequence number (ISN) is randomly chosen during the TCP session setup. The ISN is then incremented by the number of transmitted bytes.
  The receiving TCP process buffers the segment data until all data is received and reassembled.
  Segments received out of order are held for later processing.
  The data is delivered to the application layer only when it has been completely received and reassembled.
Notes: 9.2 – TCP and UDP
9.2.2 – Reliability and Flow Control

## Slide 27: Transport Layer Protocols Reliability and Flow Control (Cont.)
TCP Flow Control – Window Size and Acknowledgments
  TCP provides mechanisms for flow control.
  Flow control ensures the TCP endpoints can receive and process data reliably.
  TCP handles flow control by adjusting the rate of data flow between source and destination for a given session.
  TCP flow control function relies on a 16-bit TCP header field called the Window size. The window size is the number of bytes that the destination device of a TCP session can accept and process at one time.
  TCP source and destination agree on the initial window size when the TCP session is established
  TCP endpoints can adjust the window size during a session if necessary.
Notes: 9.2 – TCP and UDP
9.2.2 – Reliability and Flow Control

## Slide 28: Transport Layer Protocols Reliability and Flow Control (Cont.)
TCP Flow Control – Congestion Avoidance
  Network congestion usually results in discarded packets.
  Undelivered TCP segments trigger re-transmission. TCP segment retransmission can make the congestion even worse.
  The source can estimate a certain level of network congestion by looking at the rate at which TCP segments are sent but not acknowledged.
  The source can reduce the number of bytes it sends before receiving an acknowledgement upon congestion detection.
  The source reduces the number of unacknowledged bytes it sends and not the window size, which is determined by the destination.
  The destination is usually unaware of the network congestion and sees no need to suggest a new window size.
Notes: 9.2 – TCP and UDP
9.2.2 – Reliability and Flow Control

## Slide 29: Transport Layer Protocols UDP Communication
UDP Low Overhead Vs. Reliability
  UDP has much lower overhead than TCP.
  UDP is not connection-oriented and does not offer the sophisticated retransmission, sequencing, and flow control mechanisms.
  Applications running UDP can still use reliability, but it must be implemented in the application layer.
  However, UDP is not inferior.
UDP Datagram Reassembly
  UDP simply reassembles the data in the order in which it was received.
  The application must identify the proper sequence, if necessary.
UDP Server Processes and Requests
  UDP-based server applications are also assigned well-known or registered port numbers.
  Requests received on a specific port are forwarded to the proper application based on port numbers.
Notes: 9.2 – TCP and UDP
9.2.3 – UDP Communication

## Slide 30: Transport Layer Protocols UDP Communication (Cont.)
UDP Client Processes
  UDP client-server communication is also initiated by a client application.
  The UDP client process dynamically selects a port number and uses this as the source port.
  The destination port is usually the well-known or registered port number assigned to the server process.
  The same source-destination pair of ports is used in the header of all datagrams used in the transaction.
  Data returning to the client from the server uses a flipped source and destination port numbers in the datagram header.
Notes: 9.2 – TCP and UDP
9.2.3 – UDP Communication

## Slide 31: Transport Layer Protocols TCP or UDP
Applications that Use TCP
  TCP handles all transport layer related tasks.
  This frees the application from having to manage any of these tasks.
  Applications can simply send the data stream to the transport layer and use the services of TCP.
Applications that Use UDP
  Live video and multimedia applications - Can tolerate some data loss, but require little or no delay. Examples include VoIP and live streaming video.
  Simple request and reply applications - Applications with simple transactions where a host sends a request and may or may not receive a reply. Examples include DNS and DHCP.
  Applications that handle reliability themselves – Unidirectional communications where flow control, error detection, acknowledgements, and error recovery is not required or can be handled by the application. Examples include SNMP and TFTP.
Notes: 9.2 – TCP and UDP
9.2.4 – TCP or UDP

## Slide 32: 9.3 Summary
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 9: Transport Layer

## Slide 33: Chapter Summary Summary
Implement an IPv4 addressing scheme to enable end-to-end connectivity in a small to medium-sized business network.
Given a set of requirements, implement a VLSM addressing scheme to provide connectivity to end users in a small to medium-sized network.
Explain design considerations for implementing IPv6 in a business network.
Notes: 9.3.1 - Summary

## Slide 34: Chapter 9 New Terms and Commands
Segmentation
Multiplexing
Transmission Control Protocol (TCP)
Flow Control
User Datagram Protocol (UDP)
Port Addressing
Socket
Three-way Handshake
Initial Sequence Number (ISN)
Sequence Numbers
Window Size
Flow Control – Congestion Avoidance
Notes: New Terms and Commands