## Slide 1: Instructor Materials Chapter 10: Application Layer
CCNA Routing and Switching
Introduction to Networks v6.0
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 10: Application Layer

## Slide 2: Instructor Materials – Chapter 10 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 13
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Introduction to Network 6.0 Planning Guide
Chapter 10: Application Layer
Notes: Introduction to Network Planning Guide
Chapter 10: Application Layer

## Slide 4: Chapter 10: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
10.0.1.2 | Class Activity | Application Investigation | Optional
10.1.1.4 | Interactive Activity | Application and Presentation (Protocols and Standards) | Recommended
10.1.2.5 | Lab | Researching Peer-To-Peer File Sharing Issues | Optional
10.2.1.7 | Packet Tracer | Web and Email | Optional
10.2.2.4 | Syntax Checker | DNS CLI Commands in windows and Linux | -
10.2.2.7 | Packet Tracer | DHCP and DNS Servers | Optional
10.2.2.8 | Lab | Observing DNS Resolution | Recommended
10.2.3.3 | Packet Tracer | FTP | Optional
10.2.3.4 | Lab | Exploring FTP | Recommended
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 10: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
10.3.1.1 | Class Activity | Make It Happen! | Optional
10.3.1.2 | Packet Tracer | Explore a Network | Optional
10.3.1.3 | Packet Tracer Multiuser | Tutorial | Optional
10.3.1.4 | Packet Tracer Multiuser | Implement Services | Optional
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5

## Slide 6: Chapter 10: Assessment
Students should complete Chapter 10, “Assessment” after completing Chapter 10.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 6

## Slide 7
Prior to teaching Chapter 10, the instructor should:
Complete Chapter 10, “Assessment.”
The objectives of this chapter are:
  Explain how the functions of the application layer, session layer, and presentation layer work together to provide network services to end user applications.
  Explain how common application layer protocols interact with end user applications.
  Explain how web and email protocols operate.
  Explain how IP addressing protocols operate.
  Explain how file transfer protocols operate.
Chapter 10: Best Practices
Notes: 7

## Slide 8
Chapter 10: Best Practices (Cont.)
The Application layer is where data enters the data network. Use a short discussion to introduce many well-known internet/network applications. Examples include web-browsers, email, telnet, etc.
Explain to students that an understanding of services and protocols is crucial because network traffic can be manipulated based on the service and corresponding protocol used. Therefore, differing types of network traffic can be identified by the protocol used to transport the traffic.
A good analogy for application services is a business that provides services to people. For example, if a person needs a carpet cleaned, they would use the services of a carpet cleaning business. In the context of the carpet cleaning analogy, a protocol would be the methods and rules the carpet cleaners use to provide the service of carpet cleaning.
DHCP Protocol – “DORA the Explorer” – Discover, Offer, Request, Acknowledge
Notes: 8

## Slide 9
Chapter 10: Best Practices (Cont.)
Explain that the job of DNS is to make human interaction with the network easier by converting the URLs we use with application software into numeric addresses the data network uses. Explain that DNS is both a service and a protocol.
Use Wireshark to capture a packet stream to a popular website. Point out the DNS request for an IP address to the website URL and the reply with the IP address.
Explain that the job of DHCP is to make human interaction with the network easier by enabling users to automatically obtain IP addresses for their computers.
    - DHCP is a client-server service with client software on a computer and server software on a server.
    - It is a request/reply service in which the DHCP server listens for and responds to DHCP requests from the client.
    - When a computer configured to use DCHP is turned on, it sends a DHCP request to get an IP address. Any available DHCP server then responds with an IP address (along with other IP configuration information).
Notes: 9

## Slide 10
Chapter 10: Best Practices (Cont.)
In peer-to-peer networking, each computer can be either a client or a server. Because each device can perform both tasks, they are called peers.
  Explain that a peer-to-peer network is difficult to manage because management is decentralized; that is, each user is in charge of his own access policies.
  Decentralized management also makes security difficult to enforce.
  Ensure that students do not confuse peer-to-peer networking with peer-to-peer applications, such as Napster and Gnutella.
  Peer-to-peer networks allow computers to act as both clients and servers during the same communication. Peer-to-peer applications allow users to directly share specified file types across peer-to-peer or client/server networks.
Notes: 10

## Slide 11: Chapter 10: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at: https://www.netacad.com/group/communities/community-home
Best practices from around the world for teaching CCNA Routing and Switching. https://www.netacad.com/group/communities/ccna-blog
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Students can enroll in Packet Tracer Know How 1: Packet Tracer 101 (self-enroll)
Notes: 11

## Slide 13: Chapter 10: Application Layer
Introduction to Networks v6.0
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 10: Application Layer

## Slide 14: Chapter 10 - Sections & Objectives
10.0 Introduction
10.1 Application Layer Protocols
  Explain how the functions of the application layer, session layer, and presentation layer work together to provide network services to end user applications.
  Explain how common application layer protocols interact with end user applications.
10.2 Well-Known Application layer Protocols and Services
  Explain how web and email protocols operate.
  Explain how the IP addressing protocols operate.
  Explain how file transfer protocols operate.
10.3 Summary
Notes: 14

## Slide 15: 10.1 Application Layer Protocols
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 10: Application Layer

## Slide 16: Application Layer Protocols Application, Presentation, Session
Application Layer
  Closest to the end user.
  Application layer protocols help exchange data between programs running on the source and destination hosts.
  The TCP/IP application layer performs the functions of the upper three layers of the OSI model.
  Common application layer protocols include: HTTP, FTP, TFTP, DNS.
Presentation and Session Layer
  Format data, compress and encrypt data
  Common standards for video include QuickTime and Motion Picture Experts Group (MPEG).
  Common graphic image formats are: GIF, JPEG and PNG
  The session layer creates and maintains dialogs between source and destination applications.
  The session layer handles the exchange of information to initiate dialogs, keep them active, and to restart sessions that are disrupted or idle.
Notes: 10.1 – Application Layer Protocols
10.1.1 – Application, Presentation, Session

## Slide 17: Application Layer Protocols Application, Presentation, Session (Cont.)
TCP/IP Application Layer Protocols
  TCP/IP application protocols specify the format and control information necessary for common Internet functions.
  Application layer protocols must be implemented in both the source and destination devices.
  Application layer protocols implemented on the source and destination host must be compatible to allow communication.
Notes: 10.1 – Application Layer Protocols
10.1.1 – Application, Presentation, Session (Cont.)

## Slide 18: Application Layer Protocols How Application Protocols Interact with End-User Applications
Client-Server Model
  Clients request information while servers provide it.
  Client and server processes are considered to be in the application layer.
  The contents of the data exchange will depend of the application in use.
  Email is an example of a Client-Server interaction.
Peer-to-Peer Networks
  Data is accessed without the use of a dedicated server.
  Two or more computers can be connected to a P2P network to share resources.
  Every connected end device (a peer) can function as both a server and a client.
  The roles of client and server are set on a per-request basis.
Notes: 10.1 – Application Layer Protocols
10.1.2 – How Application Protocols Interact with End-User Applications

## Slide 19: Application Layer Protocols How Application Protocols Interact with End-User Applications (Cont.)
Peer-to-Peer Applications
  Some P2P applications use a hybrid system, where resource sharing is decentralized.
  Indexes that point to resource locations are stored in a centralized directory.
  In a hybrid system, each peer accesses an index server to get the location of a resource stored on another peer.
Common P2P Applications
  Common P2P networks include: eDonkey, G2, BitTorrent.
  Many P2P applications allow users to share pieces of many files with each other at the same time.
  A small torrent file contains information about the location of other users and tracker computers.
  Trackers are computers keeping track of the files hosted by users.
  This technology is called BitTorrent. There are many BitTorrent clients, including BitTorrent, uTorrent, Frostwire, and qBittorrent.
Notes: 10.1 – Application Layer Protocols
10.1.2 – How Application Protocols Interact with End-User Applications (Cont.)

## Slide 20: 10.2 Well-Known Application Layer Protocols and Services
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 10: Application Layer

## Slide 21: Well-Known Application Layer Protocols and Services Web and Email Protocols
Hypertext transfer Protocol and Hypertext Markup Language
  A URL is a reference to a web server.
  URLs and URIs are the names most people associate with web addresses.
  URLs contain the protocol, the server name and the requested filename.
  Using DNS, the server name portion of the URL is then translated to the associated IP address before the server can be contacted.
HTTP and HTTPS
  The browser sends a GET request to the server’s IP address and asks for the index.html file.
  The server sends the requested file to the client.
  The index.html was specified in the URL and contains the HTML code for this web page.
  The browser processes the HTML code and formats the page for the browser window based on the code in the file.
  HTTP Is not secure. Messages can be intercepted.
  HTTPS uses authentication and encryption to secure data.
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.1 – Web and Email Protocols

## Slide 22: Well-Known Application Layer Protocols and Services Web and Email Protocols (Cont.)
Email Protocols
  Email is a store-and-forward method of sending, storing, and retrieving electronic messages.
  Email messages are stored on mail servers.
  Email clients communicate with mail servers to send and receive email.
  Mail servers communicate with other mail servers to transport messages from one domain to another.
  Email relies on three separate protocols for operation: SMTP,POP and IMAP.
SMTP Operation
  SMTP message formats require a message header and body.
  The header must have a properly formatted recipient email address and a sender address.
  An SMTP client sends an email by connecting to a SMTP server on port 25.
  The server receives the message and stores it in a local mailbox or relays the message to another mail server.
  Users use email clients to retrieve messages stored on the server.
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.1 – Web and Email Protocols (Cont.)

## Slide 23: Well-Known Application Layer Protocols and Services Web and Email Protocols (Cont.)
POP Operation
  Messages are downloaded from the server to the client.
  Email clients direct their POP requests to mail servers on port TCP 110.
  POP allows for email messages to be downloaded to the client’s device (computer or phone) and removed from the server.
  A downloaded message resides on the device that triggered the download.
IMAP Protocols
  IMAP is another protocol used to retrieve email messages.
  Allows for messages to be displayed to the user rather than downloaded.
  The original messages reside on the server until manually deleted by the user.
  Users view copies of the messages in their email client software.
  Support folder hierarchy to organize and store mail.
  When a user decides to delete a message, the server synchronizes that action and deletes the message from the server.
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.1 – Web and Email Protocols (Cont.)

## Slide 24: Well-Known Application Layer Protocols and Services IP Addressing Services
Domain Name Service
  IP addresses are not easy to memorize.
  Domain names make server addresses more user-friendly.
  Computers still need the actual numeric address before they can communicate.
  The DNS protocol allows for the dynamic translation of a domain name into the associated IP address.
DNS Message Format
  Common DNS records are A, NS, AAAA and MX.
  DNS servers search its own records first, relaying the client’s request to other servers if it can’t resolve the request.
  The response is then forwarded to the client.
  The client often stores previous name resolutions. Use the ipconfig /displaydns to list cached DNS entries on Windows.
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.2 – IP Addressing Services

## Slide 25: Well-Known Application Layer Protocols and Services IP Addressing Services (Cont.)
DNS Hierarchy
  The DNS protocol uses a hierarchical system.
  The naming structure is broken down into small, manageable zones.
  Each DNS server is only responsible for managing name-to-IP mappings for a small portion of the DNS structure.
  Requests for zones not stored in a specific DNS server are forwarded to other servers for translation.
  Top-level domains represent either the type of domain or the country of origin. Examples of top-level domains are .com, .org, .au and .co
The nslookup Command
  Use nslookup to place DNS queries.
  Useful for DNS troubleshooting.
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.2 – IP Addressing Services (Cont.)

## Slide 26: Well-Known Application Layer Protocols and Services IP Addressing Services (Cont.)
Dynamic Host Configuration Protocol
  Computers need network IP information to communicate over a network.
  IP information include host and gateway addresses, mask, and DNS server.
  DHCP allows for automated and scalable distribution of IP information.
  DHCP-distributed addresses are leased for a set period of time.
  Addresses are returned to the pool for reuse when no longer in use.
  DHCP supports IPv4 and DHCPv6 supports IPv6.
DHCP Operation
  The client broadcasts a DHCPDISCOVER.
  A DHCP server replies with DHCPOFFER.
  The client sends a DHCPREQUEST message to the server it wants to use (in case of multiple offers).
  A client may also request an address previously been allocated by the server.
  The server returns a DHCPACK to confirm the lease has been finalized.
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.2 – IP Addressing Services (Cont.)

## Slide 27: Well-Known Application Layer Protocols and Services File Sharing Services
File Transfer Protocol
  FTP was developed to allow the transfer of files over the network.
  An FTP client is an application that runs on a client computer used to push and pull data from an FTP server.
  FTP requires two connections between the client and the server: one connection for commands and replies and another connection for the actual file transfer.
  The client initiates and establishes the first connection to the server for control traffic on TCP port 21.
  The client then establishes the second connection to the server for the actual data transfer on TCP port 20.
  The client can download (pull) data from the server or upload (push) data to the server.
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.3 – File Sharing Services

## Slide 28: Well-Known Application Layer Protocols and Services File Sharing Services (Cont.)
Server Message Block
  SMB is a client/server file sharing protocol.
  All SMB messages share a common format.
  SMB file-sharing and print services have become the mainstay of Windows networking.
  Microsoft products now support TCP/IP protocols to directly support SMB resource sharing.
  After the connection is established, the user of the client can access the resources on the server as if the resource is local to the client host.
  The Mac, LINUX, and UNIX operating systems have their own implementation of SMB.
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.3 – File Sharing Services (Cont.)

## Slide 29: 10.3 Summary
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 10: Application Layer

## Slide 30: Chapter Summary Summary
Explain the operation of the application layer in providing support to end-user applications.
Explain how well-known TCP/IP application layer protocols and services operate.
Notes: 9.3.1 - Summary

## Slide 31: Chapter 10 New Terms and Commands
Hypertext Transfer Protocol (HTTP)
File Transfer Protocol (FTP)
Trivial File Transfer Protocol (TFTP)
Internet Message Access Protocol (IMAP)
Domain Name System (DNS)
Simple Mail Transport Protocol (SMTP)
Post Office Protocol (POP)
Dynamic Host Configuration Protocol (DHCP)
QuickTime and Motion Picture Experts Group (MPEG)
Graphics Interchange Format (GIF)
Joint Photographic Experts Group (JPEG)
Portable Network Graphics (PNG)
BOOTP
HTTPS
Client-server model
Peer-to-peer network (P2P)
P2P networks
P2P applications
Gnutella protocol
BitTorrent
Uniform Resource Locator (URL)
Uniform Resource Identifier (URIs)
Get
Post
Put
HTTP Secure (HTTPS)
Secure Socket Layer (SSL)
Simple Mail Transfer Protocol (SMTP)
Post Office Protocol (POP)
Notes: New Terms and Commands

## Slide 32: Chapter 10 New Terms and Commands
IMAP
Port 25 (SMTP)
TCP Port 110 (POP)
Domain name
DNS Protocol
Record types: A, NS, AAAA, MX
ipconfig /displaydns
Top-level domains are: .com, .org, .au, .co
10.2.2.4
Nslookup
10.2.2.5
Dynamic Host Configuration Protocol (DHCP) for IPv4
DHCPv6
10.2.2.6
DHCP Discover
DHCP Offer
DHCP Request
DHCP Acknowledgement
DHCP Negative Acknowledgement
DHCPv6: SOLICIT, ADVERTISE, INFORMATION REQUEST, and REPLY
10.2.3.1
FTP daemon (FTPd)
10.2.3.2
Server Message Block (SMB)
Notes: New Terms and Commands