## Slide 1: Instructor Materials Chapter 6: EIGRP
CCNA Routing and Switching
Scaling Networks
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 6: EIGRP

## Slide 2: Instructor Materials – Chapter 6 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
Information to help you become familiar with the chapter
Teaching aids
Instructor Class Presentation
Optional slides that you can use in the classroom
Begins on slide # 11
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Scaling Network
Planning Guide
Chapter 6: EIGRP
Notes: Course Planning Guide
Chapter 6: EIGRP

## Slide 4: Chapter 6: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
6.0.1.2 | Class Activity | Classless EIGRP | Optional
6.1.2.5 | Activity | Identify the EIGRP Packet Type | -
6.1.2.6 | Video | Observing EIGRP Protocol Communications | -
6.2.1.5 | Syntax Checker | Configuring the EIGRP Router ID | -
6.2.1.7 | Syntax Checker | Configuring the Network Command and Wildcard Mask | -
6.2.1.8 | Syntax Checker | EIGRP Passive Interface | -
6.2.2.4 | Packet Tracer | Configuring Basic EIGRP with IPv4 | Recommended
6.2.2.5 | Lab | Configuring Basic EIGRP with IPv4 | Optional
6.3.1.4 | Activity | Identify the Steps in Establishing EIGRP Neighbor Adjacencies | -
6.3.2.7 | Activity | Calculate the EIGRP Metric | -
6.3.3.8 | Activity | Determine the Feasible Successor | -
6.3.4.4 | Packet Tracer | Investigating DUAL FSM | Optional
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 6: Activities (cont.)
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
6.4.1.4 | Activity | Compare EIGRPv4 and EIGRPv6 | -
6.4.2.2 | Syntax Checker | Configuring IPv6 Link-local Address | -
6.4.2.3 | Syntax Checker | Configuring the EIGRP for IPv6 Routing Process | -
6.4.2.4 | Syntax Checker | Enable EIGRP for IPv6 on the Interface | -
6.4.3.4 | Packet Tracer | Configuring Basic EIGRP with IPv6 | Recommended
6.4.3.5 | Lab | Configuring Basic EIGRP with IPv6 | Optional
6.5.1.1 | Class Activity | Portfolio RIP and EIGRP | Optional
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5

## Slide 6: Chapter 6: Assessment
Students should complete Chapter 6, “Assessment” after completing Chapter 6.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 6

## Slide 7
Prior to teaching Chapter 6, the instructor should:
Complete Chapter 6, “Assessment.”
Ensure this chapter becomes as hand-on as possible.
Review the classification of routing protocols – interior, exterior, distance vector and link state – where does EIGRP fit?
Identify stress advantages of EIGRP as an advanced distance vector protocol:
Triggered updates
Bounded updates
Partial updates
Backup routes – feasible successors
Outline the EIGRP packet types – Hello, Update, Query, and Reply, focusing on Hello and Update.
The reserved EIGRP multicast address for IPv4 is 224.0.0.10.
The reserved EIGRP multicast address for IPv6 is FF02::A.
Present the method used to compute the EIGRP metric emphasizing that bandwidth and delay are primary – other components set to 0.
Chapter 6: Best Practices
Notes: 7

## Slide 8
Explain DUAL as the convergence algorithm used by EIGRP.
Highlight the three tables used by EIGRP:
Neighbor (show ip eigrp neighbors)
Topology (show ip eigrp topology)
Routing (show ip route)
Emphasize the importance of the topology table entries
Successor and Feasible Successor
Passive and Active
Explain FD, RD, and FC
Demonstrate how to configure EIGRP for ipv4
Using the router eigrp autonomous-system command
Verifying that directly connected networks and wildcard masks are configured
To calculate the wildcard mask (also known as the inverse of the subnet mask):
255.255.255.255
255.255.255.248 subnet mask
0. 0. 0. 7 wildcard mask
Chapter 6: Best Practices (Cont.)
Notes: 8

## Slide 9
Demonstrate how EIGRP for IPv6 configuration differs from IPv4:
IPv6 routing protocols use link-local addresses for unicast addressing and next-hop addresses and are, therefore, manually configured.
The ipv6 unicast-routing command must be configured to allow routing.
Use the ipv6 router eigrp autonomous-system command to enable EIGRP.
The no shutdown command is required to activate EIGRP for the IPv6 process.
Different methods to enable an interface for EIGRP IPv6:
Instead of using the network command, EIGRP for IPv6 is configured directly on the interface using the ipv6 eigrp interface command.
Use the show ipv6 protocols command to verify the configuration.
Chapter 6: Best Practices (Cont.)
Notes: 9

## Slide 10: Chapter 6: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at community.netacad.net.
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Notes: 10

## Slide 12: Chapter 6: EIGRP
Scaling Networks
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 6: EIGRP

## Slide 13: Chapter 6 - Sections & Objectives
6.1 EIGRP Characteristics
Explain the features and characteristics of EIGRP
6.2 Implement EIGRP for IPv4
Implement EIGRP for IPv4 in a small to medium-sized business network
6.3 EIGRP Operation
Explain how EIGRP operates in a small to medium-sized business network
6.4 Implement EIGRP for IPv6
Implement EIGRP for IPv6 in a small to medium-sized business network
Notes: 13

## Slide 14: 6.1 EIGRP Characteristics
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 6: EIGRP

## Slide 15: EIGRP Characteristics EIGRP Basic Features
Features of EIGRP
Uses the Diffusing Update Algorithm (DUAL) to calculate paths and back-up paths.
Establishes Neighbor Adjacencies.
Uses the Reliable Transport Protocol to provide delivery of EIGRP packets to neighbors.
Partial and Bounded Updates. Sends updates only when there is a change and only to the routers that need the information.
Supports Equal and Unequal Cost Load Balancing.
Protocol Dependent Modules – responsible for network layer protocol-specific tasks
Sends and receives EIGRP packets that are encapsulated in IPv4
Parses EIGRP packets and informs DUAL of the new information and DUAL makes routing decisions. The results are stored in the IPv4 routing table.
Notes: 6.1 - EIGRP Characteristics
6.1.1 - EIGRP Basic Features

## Slide 16: EIGRP Characteristics EIGRP Basic Features (Cont.)
Reliable Transport Protocol
Used for the delivery and reception of EIGRP packets
Can send EIGRP packets as unicast or multicast.
Reserved IPv4 multicast address 224.0.0.10.
Reserved IPv6 multicast address FF02::A.
Authentication
Only accepts routing information from other routers with the same authentication information
Does not encrypt the routing updates
Notes: 6.1 - EIGRP Characteristics
6.1.1 - EIGRP Basic Features (Cont.)

## Slide 17: EIGRP Characteristics EIGRP Packet Types
EIGRP Hello Packets
Are sent as multicasts and uses RTP for unreliable delivery
Used to form and maintain EIGRP neighbor adjacencies
EIGRP Update and Acknowledgment Packets
Update packets propagate updated routing information when necessary to the routers that require the information using RTP
Acknowledgment packets are send to acknowledge the update was received.
EIGRP Query and Reply Packets
Searches for networks
Uses reliable delivery
Queries are multicast or unicast. Replies are always unicast.
Notes: 6.1 - EIGRP Characteristics
6.1.2 - EIGRP Packet Types

## Slide 18: EIGRP Characteristics EIGRP Messages
Encapsulating EIGRP Messages
The EIGRP packet headers and TLV are encapsulated in an IP packet.
EIGRP Packet Header and TLV
EIGRP Packet Header
EIGRP Packet Type: Update, Query, Reply, and Hello
Autonomous System Number is the ID for the EIGRP routing process
EIGRP Parameters TLV
K values: K1 and K3 are set to 1. Other K values are set to 0
Hold Time: Maximum time the router should wait for the next hello
Internal TLV
The IP internal message is used to advertise EIGRP routes within an autonomous system.
Important metric fields: delay, bandwidth, prefix length, and destination
EIGRP TLV: External Routes
The IP external message is used when external routes are imported into the EIGRP routing process.
Notes: 6.1 - EIGRP Characteristics
6.1.3 - EIGRP Messages

## Slide 19: 6.2 Implement EIGRP for IPv4
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 6: EIGRP

## Slide 20: Implement EIGRP for IPv4 Configure EIGRP with IPv4
Autonomous System Numbers
IANA globally assigned autonomous numbers
Used by ISP and other large institutions
Used in exterior routing protocol, such as BGP, to propagate routing information
router eigrp autonomous-system command
Autonomous system number is only significant to local EIGRP local domain
Autonomous system number functions as a process ID
All routers within the same domain must have the same autonomous system number
The command is used to begin the EIGRP routing protocol
EIGRP Router ID – uniquely identifies each router in the EIGRP routing domain
Determined in 3 ways using the following order:
The router router-id ipv4-address command
The highest active IPv4 address of any of the loopback address
The highest active IPv4 address of any of the physical interface
Notes: 6.2 - Implement EIGRP for IPv4
6.2.1 - Configure EIGRP with IPv4

## Slide 21: Implement EIGRP for IPv4 Configure EIGRP with IPv4 (Cont.)
The network ipv4-network-address router configuration mode command
Enables any interface on the router that matches the network address in the network command to send and receive EIGRP updates
By default, ipv4-network-address is the classful network address for each directly connected network
The network command and Wildcard Mask
network network-address [wildcard-mask]
Wildcard mask is the inverse of a subnet mask
To calculate the wildcard mask:
255.255.255.255
- 255.255.255.252 Subnet mask
-----------------
0. 0. 0. 3 Wildcard mask
Passive Interface - prevent the neighbor adjacencies
Suppress unnecessary update traffic
Increase security controls
passive-interface interface-type interface-number
Notes: 6.2 - Implement EIGRP for IPv4
6.2.1 - Configure EIGRP with IPv4 (Cont.)

## Slide 22: Implement EIGRP for IPv4 Verify EIGRP with IPv4
The show commands are useful in verifying EIGRP operations and for debugging and troubleshooting purposes.
show ip eigrp neighbors command
View the neighbor table
Verify neighbor adjacencies have been established
show ip protocols Command
Identify the parameters and other information about the current state of any active IPv4 routing protocol processes configured on the router
What information can you get from this show command?
show ip route
Verify the routes are installed in the IPv4 routing table as expected
Check for convergence
Notes: 6.2 - Implement EIGRP for IPv4
6.2.2 - Verify EIGRP with IPv4

## Slide 23: 6.3 EIGRP Operation
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 6: EIGRP

## Slide 24: EIGRP Operation EIGRP Initial Route Discovery
Can you describe the initial route discovery process?
Notes: 6.3 – EIGRP Operation
6.3.1 – EIGRP Initial Route Discovery

## Slide 25: EIGRP Operation EIGRP Metrics
Composite Metric
EIGRP uses bandwidth and delay values in the composite metric to calculate the preferred path to a network.
The k values and EIGRP AS number must match to form an adjacency.
The show ip protocols command can be used to verify k values.
Bandwidth Metric (BW)
The bandwidth kilobits-bandwidth-value command is used to modify the bandwidth metric.
Use the show interfaces command to verify the bandwidth changes
Delay Metric (DLY)
Delay is the measure of the time it takes for a packet to traverse a route.
Use the show interfaces command to view the delay values.
Notes: 6.3 – EIGRP Operation
6.3.2 – EIGRP Metrics

## Slide 26: EIGRP Operation EIGRP Metrics (Cont.)
Complete Composite Metric Formula
(𝐾1 ∗𝑏𝑎𝑛𝑑𝑤𝑖𝑑𝑡ℎ+ 𝐾2 ∗𝑏𝑎𝑛𝑑𝑤𝑖𝑑𝑡ℎ 256 −𝑙𝑜𝑎𝑑 +𝐾3 ∗𝑑𝑒𝑙𝑎𝑦)∗ 𝐾5 𝑟𝑒𝑙𝑖𝑎𝑏𝑖𝑙𝑖𝑡𝑦+𝐾4 ∗256
Using the default metric weight, the formula becomes
Metric = (𝐾1 ∗𝑏𝑎𝑛𝑑𝑤𝑖𝑑𝑡ℎ+ 𝐾3 ∗𝑑𝑒𝑙𝑎𝑦)∗256
where K1 and K3 equal to 1, K2, K4, and K5 equal to 0 when not in use, and If K5 = 0, 𝐾5 𝑟𝑒𝑙𝑖𝑎𝑏𝑖𝑙𝑖𝑡𝑦+𝐾4 becomes 1.
Calculate the EIGRP metric between R2 and R3
Metric = 256 ∗( 10 7 𝑏𝑎𝑛𝑑𝑤𝑖𝑑𝑡ℎ + sum of delay 10 )
What is bandwidth of the slowest link?
What is the sum of all delays?
What command is used to verify the metric?
Notes: 6.3 – EIGRP Operation
6.3.2 – EIGRP Metrics (Cont.)

## Slide 27: EIGRP Operation DUAL and the Topology Table
Diffusing Update Algorithm (DUAL) provides
Loop-free paths
Loop-free backup paths that can be used immediately
Fast convergence
Successor and Feasible Distance
A successor is a neighboring router that is used for packet forwarding and is the least-cost route to the destination network.
Feasible Distance is the metric listed in the routing table entry
Feasible Successors, Feasibility Condition, and Reported Distance
The reported distance is an EIGRP neighbor's feasible distance to the destination network.
The feasibility condition (FC) is met when a neighbor's reported distance (RD) to a network is less than the local router's feasible distance to the same destination network.
A feasible successor is a neighbor that has a loop-free backup path to the same network as the successor, and it satisfies the Feasibility Condition
Notes: 6.3 – EIGRP Operation
6.3.3 – DUAL and the Topology Table

## Slide 28: EIGRP Operation DUAL and the Topology Table (Cont.)
The show ip eigrp topology command
Displays the Topology Table
Topology Table
Lists all successors and FSs to destination networks
Only successors are installed in the routing tables
Can you name all the highlighted parts in the topology table below?
Which is the successor?
Which is not a feasible successor?
Notes: 6.3 – EIGRP Operation
6.3.3 – DUAL and the Topology Table (Cont.)

## Slide 29: EIGRP Operation DUAL and Convergence
DUAL Finite State Machine (FSM)
Contains all of the logic used to calculate and compare routes in an EIGRP network
DUAL: Feasible Successor
When a path to the successor goes down with FS in the topology table:
Router informs all EIGRP neighbors of the lost link.
Router updates its own routing and topology table.
DUAL: No Feasible Successor
When a path to the successor goes down with no FS in the topology table:
DUAL puts the route into an active state.
DUAL sends EIGRP queries asking other routers for a path to the network.
Other routers return EIGRP replies, letting the sender of the EIGRP query know that they have a path to the requested network. If there is no reply, the sender of the query does not have a route to this network.
If the sender receives EIGRP replies with a path to the requested network, the preferred path is added as the new successor and also added to the routing table.
Notes: 6.3 – EIGRP Operation
6.3.4 – DUAL and Convergence

## Slide 30: 6.4 Implement EIGRP for IPv6
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 6: EIGRP

## Slide 31: Implement EIGRP for IPv6 EIGRP for IPv6
EIGRP for IPv6
Similar functionality as EIGRP for IPv4
Uses IPv6 for communication with EIGRP for IPv6 peers and advertising IPv6 routes
Uses DUAL
EIGRP for IPv6 is a separate process from EIGRP for IPv4
IPv6 Link-local Address
Packets with a source or destination link- local address cannot be routed beyond the link from where the packet originated.
IPv6 link-local addresses are in the FE80::/10 range.
Notes: 6.4 – Implement EIGRP for IPv6
6.4.1 - EIGRP for IPv6

## Slide 32: Implement EIGRP for IPv6 Configure EIGRP for IPv6
Configuring IPv6 Link-local Addresses
Link-local address can be automatically created or manually configured
When created automatically, the router creates the link-local address using FE80::/10 prefix and the EUI-64 process. Use the ipv6 address link-local-address link-local command to manually configure the link-local address using the FE80::10 prefix
Link-local addresses must be unique on the same local link.
Notes: 6.4 – Implement EIGRP for IPv6
6.4.2 - Configure EIGRP for IPv6

## Slide 33: Implement EIGRP for IPv6 Configure EIGRP for IPv6 (Cont.)
Configuring the EIGRP for IPv6 Routing Process
The ipv6 unicast-routing command enable IPv6 routing
The ipv6 route eigrp autonomous-system command is used to enter the router configuration mode. The process needs to be activated with the no shutdown command.
To configure the Router ID, use the eigrp router-id command.
Both the no shutdown command and a router ID are required for the router to form neighbor adjacencies.
The ipv6 eigrp interface Command
EIGRP for IPv6 is configured directly on the interface.
ipv6 eigrp autonomous-system
Configure passive interface in the router configuration mode
passive-interface interface
Notes: 6.4 – Implement EIGRP for IPv6
6.4.2 - Configure EIGRP for IPv6 (Cont.)

## Slide 34: Implement EIGRP for IPv6 Verify EIGRP for IPv6
IPv6 Neighbor Table
The show ipv6 eigrp neighbors command is used to display neighbor adjacencies
The show ip protocols Command
Displays the parameters and other information about the state of any active IPv6 routing protocol processes currently configured on the router.
Displays different types of output specific to each IPv6 routing protocol.
The EIGRP for IPv6 Routing Table
The show ipv6 route command is used to view the IPv6 routing table
Notes: 6.4 – Implement EIGRP for IPv6
6.4.3 - Verify EIGRP for IPv6

## Slide 35: 6.5 Chapter Summary
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 6: EIGRP

## Slide 36: Chapter Summary Summary
EIGRP (Enhanced Interior Gateway Routing Protocol) is a classless, distance vector routing protocol.
EIGRP uses the source code of "D" for DUAL in the routing table. EIGRP has a default administrative distance of 90 for internal routes and 170 for routes imported from an external source, such as default routes. These features include: Diffusing Update Algorithm (DUAL), establishing neighbor adjacencies, Reliable Transport Protocol (RTP), partial and bounded updates, and equal and unequal cost load balancing.
EIGRP uses PDMs (Protocol Dependent Modules) giving it the capability to support different Layer 3 protocols including IPv4 and IPv6. EIGRP uses reliable delivery for EIGRP updates, queries and replies; and uses unreliable delivery for EIGRP Hellos and acknowledgments. Reliable RTP means an EIGRP acknowledgment must be returned.
Before any EIGRP updates are sent, a router must first discover its neighbors using EIGRP Hello packets. The Hello and hold-down values do not need to match for two routers to become neighbors. The show ip eigrp neighbors command is used to view the neighbor table and verify that EIGRP has established an adjacency with its neighbors.
EIGRP sends partial or bounded updates, which include only route changes. Updates are sent only to those routers that are affected by the change. EIGRP composite metric uses bandwidth, delay, reliability, and load to determine the best path. By default only bandwidth and delay are used.
Notes: 6.5.1.2 – Summary

## Slide 37: Chapter Summary Summary (Cont.)
At the center of EIGRP is DUAL (Diffusing Update Algorithm). The DUAL Finite State Machine is used to determine best path and potential backup paths to every destination network. The successor is a neighboring router that is used to forward the packet using the least-cost route to the destination network. Feasible distance (FD) is the lowest calculated metric to reach the destination network through the successor. A feasible successor (FS) is a neighbor who has a loop-free backup path to the same network as the successor, and also meets the feasibility condition. The feasibility condition (FC) is met when a neighbor's reported distance (RD) to a network is less than the local router's feasible distance to the same destination network. The reported distance is simply an EIGRP neighbor's feasible distance to the destination network.
EIGRP is configured with the router eigrp autonomous-system command. The autonomous-system value is actually a process-id and must be the same on all routers in the EIGRP routing domain. The network command is similar to that used with RIP. The network is the classful network address of the directly connected interfaces on the router. A wildcard mask is an optional parameter that can be used to include only specific interfaces.
EIGRP for IPv6 shares many similarities with EIGRP for IPv4. However, unlike the IPv4 network command, IPv6 is enabled on the interface using the ipv6 eigrp autonomous-system interface configuration command.
Notes: 6.5.1.2 – Summary (Cont.)