## Slide 1: Instructor Materials Chapter 10: OSPF Tuning and Troubleshooting
CCNA Routing and Switching
Scaling Networks
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 10: OSPF Tuning and Troubleshooting

## Slide 2: Instructor Materials – Chapter 10 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
Information to help you become familiar with the chapter
Teaching aids
Instructor Class Presentation
Optional slides that you can use in the classroom
Begins on slide # 13
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Scaling Network
Planning Guide
Chapter 10: OSPF Tuning and Troubleshooting
Notes: Course Planning Guide
Chapter 10: OSPF Tuning and Troubleshooting

## Slide 4: Chapter 10: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
10.0.1.2 | Class Activity | DR and BDR Elections | Optional
10.1.1.9 | Syntax Checker | Verify the Role and Adjacencies | -
10.1.1.10 | Activity | Identify OSPF Network Type Terminology | -
10.1.1.11 | Activity | Select the Designated Router | -
10.1.1.12 | Packet Tracer | Determining the DR and BDR | Optional
10.1.1.13 | Lab | Configuring OSPFv2 on a Multiaccess Network | Optional
10.1.2.2 | Syntax Checker | Verifying a Propagated Default Route on R1 and R3 | -
10.1.2.4 | Syntax Checker | Verifying a IPv6 Default Route on R1 | -
10.1.2.5 | Packet Tracer | Propagating a Default Route in OSPFv2 | Recommended
10.1.3.4 | Packet Tracer | Configuring OSPF Advance Features | Optional
10.1.3.5 | Lab | Configuring OSPFv2 Advance Features | Recommended
10.2.1.5 | Activity | Identify the Troubleshooting Command | -
10.2.2.3 | Packet Tracer | Troubleshooting Single-Area OSPFv2 | Recommended
10.2.3.3 | Lab | Troubleshooting Basic Single-Area OSPFv2 and OSPFv3 | Recommended
10.2.3.4 | Lab | Troubleshooting Advanced Single-Area OSPFv2 | Optional
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 10: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
10.2.4.3 | Packet Tracer | Troubleshooting Multiarea OSPFv2 | Recommended
10.2.4.4 | Packet Tracer | Troubleshooting Multiarea OSPFv3 | Recommended
10.2.4.5 | Lab | Troubleshooting Multiarea OSPFv2 and OSPFv3 | Optional
10.3.1.1 | Class Activity | OSPF Troubleshooting Mastery | Optional
10.3.1.2 | Packet Tracer | Skills Integration Challenge | Recommended
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5

## Slide 6: Chapter 10: Assessment
Students should complete Chapter 10, “Assessment” after completing Chapter 10.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 6

## Slide 7: Chapter 10: Best Practices
Prior to teaching Chapter 10, the instructor should:
Complete Chapter 10 Assessment.
Ensure this chapter becomes as hand-on as possible.
Set the stage. In the classification of dynamic routing protocols, where does OSPF fit? (Compare and contrast OSPF to EIGRP.)
Reinforce the fact that OSPF routers form adjacencies using Hello packets. Adjacencies only formed when the following match:
Network type
Area ID
Hello and Dead timers
Show examples of different network types.
Demonstrate the output of the show ip ospf neighbor command with a Packet Tracer OSPF network. (Show neighbor adjacencies and their state: Full/DR or Full/DROTHER.)
Notes: 7

## Slide 8: Chapter 10: Best Practices (Cont.)
Describe the problems that could occur in an OSPF network without a DR and BDR using the following formula:
n(n–1)/2 (n=number of routers)
For example: Eight routers would have 8(7)/2 = 56/2 = 28 adjacencies
This is very inefficient; thus, the election of the DR and BDR reduces all update traffic on the network.
Demonstrate the election process on an OSPF network by having the network configured with an active DR. Disconnect the DR and with the debug ip ospf events command, and watch the election take place.
Demonstrate the lab several times by changing router IDs, priorities, and loopbacks so that students can see the rule for election in action.
The router with the highest interface priority is elected as the DR; the router with the second highest interface priority is elected as the BDR.
The priority can be configured between 0–255.
Priority of 0 – router cannot become the DR.
Notes: 8

## Slide 9: Chapter 10: Best Practices (Cont.)
Explain that if interface priorities are equal, then the router with the highest router ID is elected DR and the second highest is the BDR.
Identify the three ways to determine the router ID:
The router ID can be manually configured.
If not configured, the ID is determined by highest loopback IP address.
If no loopbacks, the ID is determined by the highest active IPv4 address.
Emphasize that in an IPv6 network, the router ID must be manually configured.
Explain that propagating a route in OSPF, the same command is used in OSPFv2 and v3.
Router(config)# router ospf 4
Router(config-router)# default-information originate
Explain that, unlike EIGRP, OSPF Hello and Dead intervals must match or a neighbor adjacency will not occur.
Notes: 9

## Slide 10: Chapter 10: Best Practice (Cont.)
Enable MD5 authentication on OSPF routers.
Troubleshoot OSPF commands:
OSPFv2 OSPFv3
show ip protocols show ipv6 protocols
show ip ospf neighbor show ipv6 ospf neighbor
show ip ospf interface show ipv6 ospf interface
show ip ospf show ipv6 ospf
show ip route ospf show ipv6 route ospf
clear ip ospf [id] process clear ip ospf [id] process
Notes: 10

## Slide 11: Chapter 10: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at community.netacad.net.
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Notes: 11

## Slide 13: Chapter 10: OSPF Tuning and Troubleshooting
Scaling Networks
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 10: OSPF Tuning and Troubleshooting

## Slide 14: Chapter 10 - Sections & Objectives
10.1 Advanced Single-Area OSPF Configurations
Configure OSPF to improve network performance.
10.2 Troubleshooting Single-Area OSPF Implementations
Troubleshoot common OSPF configuration issues in a small to medium-sized business network.
Notes: 14

## Slide 15: 10.1 Advanced Single-Area OSPF Configurations
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 10: OSPF Tuning and Troubleshooting

## Slide 16: Advanced Single-Area OSPF Configurations OSPF in Multiaccess Networks
OSPF Network Types
Point-to-point
Broadcast multiaccess
Nonbroadcast multiaccess (NBMA)
Point-to-multipoint
Virtual links
OSPF challenges for OSPF
Creation of multiple adjacencies
Extensive flooding of LSAs
OSPF Designated Router
OSPF elects a DR to be the collection and distribution point for LSAs sent and received.
Notes: 10.1 – Advanced Single-Area OSPF Configurations
10.1.1 – OSPF in Multiaccess Networks

## Slide 17: Advanced Single-Area OSPF Configurations OSPF in Multiaccess Networks (Cont.)
Verifying DR/BDR Roles
To verify the roles of the OSPFv2 router, use the show ip ospf interface command.
For the equivalent OSPFv3 command, simply substitute ip with ipv6.
Verifying DR/BDR Adjacencies
To verify the OSPFv2 adjacencies, use the show ip ospf neighbor command.
The normal state for an OSPF router is usually FULL.
Default DR/BDR Election Process
The routers in the network elect the router with the highest interface priority as the DR.
The router with the second highest interface priority is elected as the BDR.
The OSPF Priority
To configure the OSPF priority, use the ip ospf priority value interface command. For the equivalent OSPFv3 command, simply substitute ip with ipv6.
With the OSPF priority of 0, the router does not become a DR or BDR.
For values 1 – 255, the higher the value, the more likely the router becomes the DR or BDR on the interface.
Notes: 10.1 – Advanced Single-Area OSPF Configurations
10.1.1 – OSPF in Multiaccess Networks (Cont.)

## Slide 18: Advanced Single-Area OSPF Configurations Default Route Propagation
Propagating a Default Static Route in OSPFv2
To propagate a default route, the edge router must be configured with:
A default static route using the ip route 0.0.0.0 0.0.0.0 {ip-address | exit-intf} command.
The default-information originate router configuration mode command.
Verifying the Propagated IPv4 Default Route
Verify the default route settings on using the show ip route command
Notes: 10.1 – Advanced Single-Area OSPF Configurations
10.1.2 – Default Route Propagation

## Slide 19: Advanced Single-Area OSPF Configurations Default Route Propagation (Cont.)
Propagating a Default Static Route in OSPFv3
The process of propagating a default static route in OSPFv3 is almost identical to OSPFv2
To propagate a default route, the edge router must be configured with:
A default static route using the ipv6 route ::/0 {ipv6-address | exit-intf} command
The default-information originate router configuration mode command.
Verifying the Propagated IPv6 Default Route
Verify the default static route setting on R2 using the show ipv6 route static command
Notes: 10.1 – Advanced Single-Area OSPF Configurations
10.1.2 – Default Route Propagation (Cont.)

## Slide 20: Advanced Single-Area OSPF Configurations Fine-tuning OSPF Interfaces
OSPF Hello and Dead Intervals
The OSPF Hello and Dead intervals are configurable on a per-interface basis.
The OSPF intervals must match or a neighbor adjacency does not occur.
Modifying OSPFv2 Intervals
OSPFv2 Hello and Dead intervals can be modified manually:
ip ospf hello-interval seconds
ip ospf dead-interval seconds
Use the no ip ospf hello- interval and no ip ospf dead-interval commands to reset the intervals to their default.
Notes: 10.1 – Advanced Single-Area OSPF Configurations
10.1.3 - Fine-tuning OSPF Interfaces

## Slide 21: Advanced Single-Area OSPF Configurations Fine-tuning OSPF Interfaces (Cont.)
Modifying OSPFv3 Intervals
OSPFv2 Hello and Dead intervals can be modified manually:
ipv6 ospf hello-interval seconds
ipv6 ospf dead-interval seconds
Use the no ipv6 ospf hello-interval and no ipv6 ospf dead-interval commands to reset the intervals to their default.
Notes: 10.1 – Advanced Single-Area OSPF Configurations
10.1.3 - Fine-tuning OSPF Interfaces (Cont.)

## Slide 22: 10.2 Troubleshooting Single-Area OSPF Implementations
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 10: OSPF Tuning and Troubleshooting

## Slide 23: Troubleshooting Single-Area OSPF Implementations Components of Troubleshooting Single-Area OSPF
Notes: 10.2 Troubleshooting Single-Area OSPF Implementations
10.2.1 – Components of Troubleshooting Single-Area OSPF

## Slide 24: Troubleshooting Single-Area OSPF Implementations Components of Troubleshooting Single-Area OSPF (Cont.)
OSPF States
When troubleshooting OSPF neighbors, be aware that the FULL or 2WAY states are normal.
All other states are transitory.
OSPF Troubleshooting Commands
show ip protocols
show ip ospf neighbor
show ip ospf interface
show ip ospf
show ip route ospf
clear ip ospf [process-id] process
For the equivalent OSPFv3 command, simply substitute ip with ipv6.
Notes: 10.2 - Troubleshooting Single-Area OSPF Implementations
10.2.1 – Components of Troubleshooting Single-Area OSPF (Cont.)

## Slide 25: Troubleshooting Single-Area OSPF Implementations Components of Troubleshooting Single-Area OSPF (Cont.)
Components of Troubleshooting OSPF
Neighbor table is not correct
Are the interfaces operational? Are the interfaces enabled for OSPF? Does the OSPF area match? Is there an interface that is configured as passive?
Routing table is not correct
Are the networks being advertised? Is there an ACL that is blocking advertisements? Is there another routing protocol with a lower AD being used as well? Are all areas connected to Area 0?
Traffic does not take the desired path
Verify the OSPF cost on an interface. Verify the OSPF reference bandwidth.
Notes: 10.2 - Troubleshooting Single-Area OSPF Implementations
10.2.1 – Components of Troubleshooting Single-Area OSPF (Cont.)

## Slide 26: Troubleshooting Single-Area OSPF Implementations Troubleshoot Single-Area OSPFv2 Routing Issues
Troubleshooting Neighbor Issues
For an interface to be enabled for OSPFv2, a matching network command must be configured under the OSPFv2 routing process.
If connected interfaces on two routers are not enabled for OSPF, the neighbors will not form an adjacency
Recall that the passive-interface command stops both outgoing and incoming routing updates because the effect of the command causes the router to stop sending and receiving Hello packets over an interface.
Notes: 10.2 Troubleshooting Single-Area OSPF Implementations
10.2.2 – Troubleshoot Single-Area OSPFv2 Routing Issues

## Slide 27: Troubleshooting Single-Area OSPF Implementations Troubleshoot Single-Area OSPFv2 Routing Issues (Cont.)
Troubleshooting OSPFv2 Routing Table Issues
For an interface to be enabled for OSPFv2, a matching network command must be configured under the OSPFv2 routing process.
Notes: 10.2 Troubleshooting Single-Area OSPF Implementations
10.2.2 – Troubleshoot Single-Area OSPFv2 Routing Issues (Cont.)

## Slide 28: Troubleshooting Single-Area OSPF Implementations Troubleshoot Single-Area OSPFv3 Routing Issues
OSPFv3 Troubleshooting Commands
show ipv6 protocols
show ipv6 ospf neighbor
show ipv6 ospf interface
show ipv6 ospf
show ipv6 route ospf
clear ip ospfv6 [process-id] process
Troubleshooting OSPFv3
Unlike OSPFv2, OSPFV3 does not use the network command. Instead OSPFv3 is enabled directly on the interface.
Notes: 10.2 - Troubleshooting Single-Area OSPF Implementations
10.2.3 – Troubleshoot Single-Area OSPFv3 Routing Issues

## Slide 29: Troubleshooting Single-Area OSPF Implementations Troubleshoot Multiarea OSPFv2 and OSPFv3
Multiarea OSPF Troubleshooting Skills
Before you can begin to diagnose and resolve problems related to a multiarea OSPF implementation, you must be able to do the following:
Understand the processes OSPF uses to distribute, store, and select routing information.
Understand how OSPF information flows within and between areas.
Use Cisco IOS commands to gather and interpret the information necessary to troubleshoot OSPF operation.
Multiarea OSPF Troubleshooting Data Structures
OSPF stores routing information in four main data structures:
Interface table
Neighbor table
Link-state database (LSDB)
Routing table
Notes: 10.2 - Troubleshooting Single-Area OSPF Implementations
10.2.4 - Troubleshoot Multiarea OSPFv2 and OSPFv3

## Slide 30: 10.3 Chapter Summary
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 10: OSPF Tuning and Troubleshooting

## Slide 31: Chapter Summary Summary
OSPF defines five network types: point-to-point, broadcast multiaccess, nonbroadcast multiaccess, point-to-multipoint, and virtual links.
Multiaccess networks can create two challenges for OSPF regarding the flooding of LSAs: creation of multiple adjacencies and extensive flooding of LSAs. The solution to managing the number of adjacencies and the flooding of LSAs on a multiaccess network is the DR and BDR. If the DR stops producing Hellos, the BDR promotes itself and assumes the role of DR.
The routers in the network elect the router with the highest interface priority as DR. The router with the second highest interface priority is elected the BDR. The higher the priority, the likelier the router will be selected as the DR. If set to 0, the router is not capable of becoming the DR. The default priority of multiaccess broadcast interfaces is 1. Therefore, unless otherwise configured, all routers have an equal priority value and must rely on another tie breaking method during the DR/BDR election. If the interface priorities are equal, then the router with the highest router ID is elected the DR. The router with the second highest router ID is the BDR. The addition of a new router does not initiate a new election process.
To propagate a default route in OSPF, the router must be configured with a default static route and the default-information originate command must be added to the configuration. Verify routes with the show ip route or show ipv6 route command.
To assist OSPF in making the correct path determination, the reference bandwidth must be changed to a higher value to accommodate networks with links faster than 100 Mb/s. To adjust the reference bandwidth, use the auto-cost reference-bandwidth Mbps router configuration mode command. To adjust the interface bandwidth, use the bandwidth kilobits interface configuration mode command. The cost can be manually configured on an interface using the ip ospf cost value interface configuration mode command.
Notes: 10.3 - Summary
10.3.1.3 - Summary

## Slide 32: Chapter Summary Summary (Cont.)
The OSPF Hello and Dead intervals must match or a neighbor adjacency does not occur. To modify these intervals, use the following interface commands:
ip ospf hello-interval seconds
ip ospf dead-interval seconds
ipv6 ospf hello-interval seconds
ipv6 ospf dead-interval seconds
When troubleshooting OSPF neighbors, be aware that the FULL or 2WAY states are normal. The following commands summarize OSPFv2 troubleshooting:
show ip protocols
show ip ospf neighbor
show ip ospf interface
show ip ospf
show ip route ospf
clear ip ospf [process-id] process
Troubleshooting OSPFv3 is similar to OSPFv2. The following commands are the equivalent commands used with OSPFv3: show ipv6 protocols, show ipv6 ospf neighbor, show ipv6 ospf interface, show ipv6 ospf, show ipv6 route ospf, and clear ipv6 ospf [process-id] process.
Notes: 10.3 - Summary
10.3.1.3 – Summary (Cont.)