## Slide 1: Instructor Materials Chapter 9: Multiarea OSPF
CCNA Routing and Switching
Scaling Networks
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 9: Multiarea OSPF

## Slide 2: Instructor Materials – Chapter 9 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
Information to help you become familiar with the chapter
Teaching aids
Instructor Class Presentation
Optional slides that you can use in the classroom
Begins on slide # 9
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Scaling Network
Planning Guide
Chapter 9: Multiarea OSPF
Notes: Course Planning Guide
Chapter 9: Multiarea OSPF

## Slide 4: Chapter 9: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
9.0.1.2 | Class Activity | Leaving on a Jet Plane | Optional
9.1.1.5 | Activity | Identify the Multiarea OSPF Terminology | -
9.1.2.7 | Activity | Identify the OSPF LSA Type | -
9.1.3.3 | Activity | Order the Steps for OSPF Best Path Calculations | -
9.2.1.2 | Syntax Checker | Configuring Multiarea OSPF on R2 & R3 | -
9.2.1.3 | Syntax Checker | Configuring Multiarea OSPFv3 on R2 & R3 | -
9.2.2.2 | Syntax Checker | Verifying Multiarea OSPFv2 Status | -
9.2.2.3 | Syntax Checker | Verifying Multiarea OSPF Routesv2 on R2 and R3 | -
9.2.2.4 | Syntax Checker | Verifying the OSPFv2 LSDB on R2 and R3 | -
9.2.2.6 | Packet Tracer | Configuring Multiarea OSPFv2 | Optional
9.2.2.7 | Packet Tracer | Configuring Multiarea OSPFv3 | Optional
9.2.2.8 | Lab | Configuring Multiarea OSPFv2 | Recommended
9.2.2.9 | Lab | Configuring Multiarea OSPFv3 | Recommended
9.3.1.1 | Class Activity | Digital Trolleys | Optional
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 9: Assessment
Students should complete Chapter 9, “Assessment” after completing Chapter 9.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 5

## Slide 6: Chapter 9: Best Practices
In this chapter, the instructor should:
Consider setting up an large OSPF single area network and edit the topology to a multiarea network.
Discuss with students the differences between single-area OSPF and multiarea OSPF. Give them an assignment to draw a picture of OSPF single areas and multiple areas.
Make sure the students pay particular attention to the LSA types discussed on pages 9.1.2.2 – 9.1.2.6. These types should be memorized. Compare and contrast the LSA types.
Give the students plenty of practice with hands-on labs based on multiarea OSPF configuration.
Enlarge and print some of the graphics in this chapter or give the students an assignment of making posters with the concepts in this chapter.
Walk the students through all the commands in the chapter, but focus on the areas of possible confusion.
Notes: 6

## Slide 7: Chapter 9: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at community.netacad.net.
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Notes: 7

## Slide 9: Chapter 9: Multiarea OSPF
Scaling Networks
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 9: Multiarea OSPF

## Slide 10: Chapter 9 - Sections & Objectives
9.1 Multiarea OSPF Operation
Explain how multiarea OSPF operates in a small to medium-sized business network.
9.2 Implement Multiarea
Implement multiarea OSPFv2 and OSPFv3.
Notes: 10

## Slide 11: 9.1 Multiarea OSPF Operation
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 9: Multiarea OSPF

## Slide 12: Multiarea OSPF Operation Why Multiarea OSPF?
Single-Area OSPF
If the routes are not summarized, the routing table can become very large.
Each router must maintain detailed information about every network in the routing domain.
Multiarea OSPF
Smaller routing tables
Reduced link-state update overhead
Reduced frequency of SPF calculations
Notes: 9.1 – Multiarea OSPF Operation
9.1.1 – Why Multiarea OSPF?

## Slide 13: Multiarea OSPF Operation Why Multiarea OSPF?
OSPF Two-Layer Area Hierarchy
Backbone (Transit) area and Regular (Non-backbone) area
Types of OSPF Routers
Internal router
Backbone router
Area Border Router (ABR)
Autonomous System Boundary Router (ASBR)
Backbone
Regular
Notes: 9.1 – Multiarea OSPF Operation
9.1.1 – Why Multiarea OSPF?

## Slide 14: Multiarea OSPF Operation Multiarea OSPF LSA Operation
OSPF LSA Types
Individually, they act as database records and provide specific OSPF network details. In combination, they describe the entire topology of an OSPF network or area.
Notes: 9.1 – Multiarea OSPF Operation
9.1.2 – Multiarea OSPF LSA Operation

## Slide 15: Multiarea OSPF Operation Multiarea OSPF LSA Operation
OSPF LSA Types
Type 1 - Contains a list of the directly connected interfaces, link types, neighbors, and link states.
Type 2 - Contains the router ID and IP address of the DR, along with the router ID of all other routers on the multiaccess segment.
Type 3 - Used by ABRs to advertise networks from other areas.
Type 4 - Identifies the ASBR and provides a route to it.
Type 5 - Describe routes to networks outside the OSPF routing domain.
Notes: 9.1 – Multiarea OSPF Operation
9.1.2 – Multiarea OSPF LSA Operation

## Slide 16: Multiarea OSPF Operation OSPF Routing Table and Types of Routes
OSPF Routing Table Entries
O – Indicates the route is intra-area.
O IA – Indicates a summary LSA.
O E1 or O E2 – Indicates an external LSA.
OSPF Route Calculation
Each router uses the SPF algorithm against the LSDB to build the SPF tree. The SPF tree is used to determine the best path(s).
Notes: 9.1 – Multiarea OSPF Operation
9.1.3 – OSPF Routing Table and Types of Routes

## Slide 17: 9.2 Configuring Multiarea OSPF
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 9: Multiarea OSPF

## Slide 18: Configuring Multiarea OSPF Configuring Multiarea OSPF
Implementing Multiarea OSPF
The type of OSPF implementation chosen depends on the specific network design requirements and existing topology.
A router simply becomes an ABR when it has two network statements in different areas.
Notes: 9.2 – Configuring Multiarea OSPF
92.1 – Configuring Multiarea OSPF

## Slide 19: Configuring Multiarea OSPF Verifying Multiarea OSPF
Verifying Multiarea OSPF v2
The same verification commands used to verify single-area OSPFv2 also can be used to verify the multiarea OSPF topology.
For the equivalent OSPFv3 command, simply substitute ip with ipv6.
Verify General Multiarea OSPFv2 Settings
Use the show ip protocols command to verify the OSPFv2 status.
The Routing for Networks section identifies the networks and their respective areas.
Verify the OSPFv2 Routes
The most common command used to verify a multiarea OSPFv2 configuration is the show ip route command. Add the ospf parameter to display only OSPFv2-related information.
Notes: 9.2 – Configuring Multiarea OSPF
92.2 – Verifying Multiarea OSPF

## Slide 20: Configuring Multiarea OSPF Verifying Multiarea OSPF (Cont.)
Verify the Multiarea OSPFv2 LSDB
Use the show ip ospf database command to verify the contents of the OSPFv2 LSDB.
There are many command options available with the show ip ospf database command.
Verify Multiarea OSPFv3
Like OSPFv2, OSPFv3 provides similar OSPFv3 verification commands.
Notes: 9.2 – Configuring Multiarea OSPF
9.2.2 – Verifying Multiarea OSPF (Cont.)

## Slide 21: 9.3 Chapter Summary
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 9: Multiarea OSPF

## Slide 22: Chapter Summary Summary
Single-area OSPF is useful in smaller networks but in larger networks multiarea OSPF is a better choice. Multiarea OSPF solves the issues of large routing table, large link-state database, and frequent SPF algorithm calculations.
The main area is called the backbone area (area 0) and all other areas must connect to the backbone area. Routing still occurs between the areas while many of the routing operations, such as recalculating the database, are kept within an area.
There are four different types of OSPF routers: Internal router, Backbone router, Area Border Router (ABR), and Autonomous System Boundary Router (ASBR). A router can be classified as more than one router type.
Link State Advertisements (LSAs) are the building blocks of OSPF. This chapter concentrated on LSA type 1 to LSA type 5. Type 1 LSAs are referred to as the router link entries. Type 2 LSAs are referred to as the network link entries and are flooded by a DR. Type 3 LSAs are referred to as the summary link entries and are created and propagated by ABRs. A type 4 summary LSA is generated by an ABR only when an ASBR exists within an area. Type 5 external LSAs describe routes to networks outside the OSPF autonomous system. Type 5 LSAs are originated by the ASBR and are flooded to the entire autonomous system.
OSPFv2 routes in an IPv4 routing table are identified using the following descriptors: O, O IA, O E1 or O E2. Each router uses the SPF algorithm against the LSDB to build the SPF tree. The SPF tree is used to determine the best paths.
Notes: 9.3 – Chapter Summary
9.3.1.2 - Summary

## Slide 23: Chapter Summary Summary (Cont.)
There are no special commands required to implement a multiarea OSPF network. A router simply becomes an ABR when it has two network statements in different areas.
An example of multiarea OSPF configuration:
R1(config)# router ospf 10
R1(config-router)# router-id 1.1.1.1
R1(config-router)# network 10.1.1.1 0.0.0.0 area 1
R1(config-router)# network 10.1.2.1 0.0.0.0 area 1
R1(config-router)# network 192.168.10.1 0.0.0.0 area 0
Commands that are used to verify OSPFv2 configuration consist of the following:
show ip ospf neighbor
show ip ospf
show ip ospf interface
show ip protocols
show ip ospf interface brief
show ip route ospf
show ip ospf database
To use the equivalent OSPFv3 command, simply substitute ip with ipv6.
Notes: 9.3 – Chapter Summary
9.3.1.2 – Summary (Cont.)