## Slide 1: Instructor Materials Chapter 5: Dynamic Routing
CCNA Routing and Switching
Scaling Networks
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 5: Dynamic Routing

## Slide 2: Instructor Materials – Chapter 5 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
Information to help you become familiar with the chapter
Teaching aids
Instructor Class Presentation
Optional slides that you can use in the classroom
Begins on slide # 11
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Scaling Network
Planning Guide
Chapter 5: Dynamic Routing
Notes: Course Planning Guide
Chapter 5: Dynamic Routing

## Slide 4: Chapter 5: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
5.0.1.2 | Class Activity | How Much Does This Cost? | Optional
5.1.1.9 | Activity | Classify Dynamic Routing Protocols | -
5.1.1.10 | Activity | Compare Routing Protocols | -
5.1.1.11 | Activity | Match the Metric to the Protocol | -
5.2.1.6 | Packet Tracer | Investigating Convergence | Optional
5.2.2.3 | Activity | Identify Distance Vector Terminology | -
5.2.3.3 | Activity | Compare RIP and EIGRP | -
5.2.3.4 | Packet Tracer | Comparing RIP and EIGRP Path Selection | Optional
5.3.2.9 | Activity | Building the Link-State Database and SPF Tree | -
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 5: Assessment
Students should complete Chapter 5, “Assessment” after completing Chapter 5.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 5

## Slide 6
Prior to teaching Chapter 5, the instructor should:
Complete Chapter 5, “Assessment.”
During this chapter, consider setting up a large network as a Packet Tracer demonstration to allow students to see size and complexity.
Discuss with students the advantages and disadvantages of using routing protocols rather than static routing. Introduce terms such as metrics, convergence, distance vector, link state, classless, classful, IGP, and EGP.
Discriminating between link-state and distance vector protocols is sometimes difficult for students. Classroom activities that demonstrate convergence and routing updates in large networks will help students gain insight into the differences. Use of analogies and discussion is highly recommended.
Be sure that students understand that by using routing protocols, they are not giving up control of their network. They are merely allowing some administration to be done automatically. Dynamic routing protocols allow an internetwork to heal itself (re-converge) in the case of a link failure. Network professionals need to understand routing protocols in order to make correct choices for implementation, know how network traffic is routed, and easily scale a large internetwork.
Chapter 5: Best Practices
Notes: 6

## Slide 7
The purpose of this discussion is to stimulate thinking on key issues about dynamic routing.
In Class:
Divide the class into small groups of 3-5 students.
Pass out a copy of the discussion questions to each student.
Tell each group to discuss the questions related to static and dynamic routing.
Monitor the groups. Help them if they seem to be having trouble.
After 10-15 minutes, bring the groups together. Ask one of the questions and ask one group to share their thoughts.
Ask another group if they have anything to add.
Chapter 5: Best Practices (Cont.)
Notes: 7

## Slide 8
Discussion Questions
When do we need to use static routing?
When do we need to use dynamic routing?
What are the advantages and disadvantages of static and dynamic routing?
Compare and contrast the distance vector and link-state routing protocols.
What is the advantage of classless routing protocols over classful routing protocols?
Why do we want to have convergence in the shortest possible time after a change in a network?
Why do we need to have multiple metrics?
What affects the speed of convergence?
When you compare distance vector to link-state routing protocols, which of these would you expect to converge faster? Why?
Chapter 5: Best Practices (Cont.)
Notes: 8

## Slide 9: Chapter 5: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at community.netacad.net.
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Notes: 9

## Slide 11: Chapter 5: Dynamic Routing
Scaling Networks
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 5: Dynamic Routing

## Slide 12: Chapter 5 - Sections & Objectives
5.1 Dynamic Routing Protocols
Explain the features and characteristics of dynamic routing protocols.
5.2 Distance Vector Dynamic Routing
Explain how distance vector routing protocols operate.
5.3 Link-State Dynamic Routing
Explain how link-state protocols operate.
Notes: 12

## Slide 13: 5.1 Dynamic Routing Protocol
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 5: Dynamic Routing

## Slide 14: Dynamic Routing Protocols Types of Routing Protocols
Purpose of dynamic routing protocols
Discovery of remote networks
Maintaining up-to-date routing information
Choosing the best path to destination networks
Ability to find a new best path if the current path is no longer available
Types of Routing Protocols
Link-State
Distance Vector
Path-Vector
Notes: 5.1 – Dynamic Routing Protocols
5.1.1 – Types of Routing Protocols

## Slide 15: 5.2 Distance Vector Dynamic Routing
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 5: Dynamic Routing

## Slide 16: Distance Vector Dynamic Routing Distance Vector Fundamentals
Dynamic Routing Protocol Operation
Router sends and receives routing messages on its interfaces
Router shares routing messages and routing information with other routers that are using the same routing protocol.
Routers exchange routing information to learn about remote networks.
When a router detects a topology change, the routing protocol can advertise this change to other routers.
Describe the process to achieve convergence and build the routing table using the graphics above:
Which networks are directly connected (0 hop)?
Which networks are 1 hop or 2 hops away?
Notes: 5.2 – Distance Vector Dynamic Routing
5.2.1 – Distance Vector Fundamentals

## Slide 17: Distance Vector Dynamic Routing Distance Vector Routing Protocol Operation
Distance Vector Technologies
Neighbors are routers that share a link and are configured to use the same routing protocol.
The router is only aware of the network addresses of its own interfaces and the remote network addresses it can reach through its neighbors.
Routers using distance vector routing are not aware of the network topology.
Some distance vector routing protocols send periodic updates.
Distance Vector Algorithm
Sending and receiving routing information
Calculating the best paths and installing routes in the routing table
Detecting and reacting to topology changes
Notes: 5.2 – Distance Vector Dynamic Routing
5.2.2 – Distance Vector Routing Protocol Operation

## Slide 18: Distance Vector Dynamic Routing Types of Distance Vector Routing Protocols
What other enhancements were introduced in RIPv2 and EIGRP?
Notes: 5.2 – Distance Vector Dynamic Routing
5.2.3 – Types of Distance Vector Routing Protocols

## Slide 19: 5.3 Link-State Dynamic Routing
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 5: Dynamic Routing

## Slide 20: Link-State Dynamic Routing Link-State Routing Protocol Operation
Shortest Path First Protocols
OSPF and IS-IS
Dijkstra’s Algorithm
Using the diagram, determine the shortest path for the scenarios below:
R1 to R4
R1 to R5
R2 to R3
R3 to R5
R4 to R2
R5 to R2
Notes: 5.3 – Link-State Dynamic Routing
5.3.1 – Link-State Routing Protocol Operation

## Slide 21: Link-State Dynamic Routing Link-State Updates
Link-State Routing Process
Each router learns its own links and directly connected networks
Each router discovers its neighbors on directly connected networks with Hello packets.
Each router builds a link-state packet containing the state of each directly connected link.
Each router floods the LSP to all neighbors, who then store all LSPs received in a database.
Each router uses the database to construct a complete map of the topology and computes the best path to each destination network.
SPF Tree
Each router in the routing area uses the link-state database and SPF algorithm to construct the SPF tree.
Each router constructs its own SPF tree independently from all other routers.
The SPF trees must be identical on all routers.
The paths are added to the routing table.
Notes: 5.3 – Link-State Dynamic Routing
5.3.2 – Link-State Updates

## Slide 22: Link-State Dynamic Routing Link-State Routing Protocol Benefits
Advantages
Builds a complete topological map of the network to determine the shortest path
Floods the LSP immediately to achieve faster converge
Only sends out LSP with new information when there is a change in the topology
Uses the concept of areas and allows for summarization.
Disadvantages
Requires additional memory to maintain the database and SPF tree
Requires more CPU processing to calculate the SPF algorithm and create a complete map of the topology
Requires more bandwidth during initial startups of the routers and could be an issue on unstable networks
Notes: 5.3 – Link-State Dynamic Routing
5.3.3 – Link-State Routing Protocol Benefits

## Slide 23: 5.4 Chapter Summary
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 5: Dynamic Routing

## Slide 24: Chapter Summary Summary
Dynamic routing protocols are used by routers to facilitate the exchange of routing information between routers. They are used to discover remote networks, maintain up-to-date routing information, choose the best path to destination networks and has the ability to find a new best path when the topology changes.
Dynamic routing protocols require more CPU and bandwidth resources.
Networks typically use a combination of both static and dynamic routing. Dynamic routing is the best choice for large networks and static routing is better for stub networks.
The process of bringing all routing tables to a state of consistency, where all of the routers in the same routing domain or area have complete and accurate information about the network, is called convergence. Some routing protocols converge faster than others.
Metrics are used by routing protocols to determine the best path or shortest path to reach a destination network.
Distance vector protocols do not have the actual map of the network topology. The routers only have knowledge reach remote networks through the neighbors. Periodic updates are send to keep the routing tables up-to date. Modern distance vector protocols are RIPv2, RIPng and EIGRP.
A router configured with a link-state routing protocol can create a complete view or topology of the network by gathering information from all of the other routers. This information is collected using link-state packets (LSPs). Updates are send when topology changes.
Link-state routing protocols apply Dijkstra’s algorithm to calculate the best path route. The algorithm is commonly referred to as the shortest path first (SPF) algorithm. This algorithm uses accumulated costs along each path, from source to destination, to determine the total cost of a route. The link-state routing protocols are IS-IS and OSPF.
Notes: 5.4.1.1 - Summary