## Slide 1: Instructor Materials Chapter 7: EIGRP Tuning and Troubleshooting
CCNA Routing and Switching
Scaling Networks
Notes: Cisco Networking Academy Program
Course Name
Chapter 7: EIGRP Tuning and Troubleshooting

## Slide 2: Instructor Materials – Chapter 7 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
Information to help you become familiar with the chapter
Teaching aids
Instructor Class Presentation
Optional slides that you can use in the classroom
Begins on slide #10
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Scaling Network
Planning Guide
Chapter 7: EIGRP Tuning and Troubleshooting
Notes: Course Planning Guide
Chapter 7: EIGRP Tuning and Troubleshooting

## Slide 4: Chapter 7: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
7.0.1.2 | Class Activity | EIGRP – Back to the Future | Optional
7.1.1.3 | Syntax Checker | Configuring EIGRP Automatic Summarization on R3 | -
7.1.1.9 | Activity | Determine the Classful Summarization | -
7.1.1.10 | Activity | Determine the Exit Interface for a Given Packet | -
7.1.2.4 | Packet Tracer | Propagating a Default Route in EIGRP for IPv4 and IPv6 | Optional
7.1.3.1 | Syntax Checker | Configuring Bandwidth Utilization on R2 and R3 | -
7.1.3.2 | Syntax Checker | Configuring Timers on R2 | -
7.1.3.5 | Activity | Determine the EIGRP Fine Tuning Commands | -
7.1.3.6 | Lab | Configuring Advanced EIGRP for IPv4 Features | Recommended
7.2.1.3 | Activity | Identify the Troubleshooting Command | -
7.2.2.4 | Activity | Troubleshoot EIGRP Neighbor Issues | -
7.2.3.4 | Activity | Troubleshoot EIGRP Routing Table Issues | -
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 7: Activities (cont.)
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
7.2.3.5 | Packet Tracer | Troubleshooting EIGRP for IPv4 | Recommended
7.2.3.6 | Lab | Troubleshooting Basic EIGRP for IPv4 and IPv6 | Optional
7.2.3.7 | Lab | Troubleshooting Advanced EIGRP | Recommended
7.3.1.1 | Class Activity | Tuning EIGRP | Optional
7.3.1.2 | Packet Tracer | Skills Integration Challenge | Optional
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5

## Slide 6: Chapter 7: Assessment
Students should complete Chapter 7, “Assessment” after completing Chapter 7.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 6

## Slide 7
Prior to teaching Chapter 7, the instructor should:
Complete Chapter 7, “Assessment.”
Ensure that this chapter becomes as hands-on as possible.
Stress that the goal of this chapter is to make EIGRP run more efficiently.
Demonstrate how routing issues with EIGRP can occur by using autosummarization with a discontinuous network.
Show the Null0 interface in a routing table when using autosummarization.
Demonstrate the effect on routing when load balancing with EIGRP.
Demonstrate what can happen if a passive-interface command is issued on the wrong interface.
Chapter 7: Best Practices
Notes: 7

## Slide 8: Chapter 7: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at community.netacad.net.
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Notes: 8

## Slide 10: Chapter 7: EIGRP Tuning and Troubleshooting
Scaling Networks
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 7: EIGRP Tuning and Troubleshooting

## Slide 11: Chapter 7 - Sections & Objectives
7.1 Tune EIGRP
Configure EIGRP to improve network performance.
7.2 Troubleshoot EIGRP
Troubleshoot common EIGRP configuration issues in a small to medium-sized business network.
Notes: 11

## Slide 12: 7.1 Tune EIGRP
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 7: EIGRP Tuning and Troubleshooting

## Slide 13: Tune EIGRP Automatic Summarization
EIGRP Automatic Summarization
Summarization limits the number of routing advertisements and the size of the routing table
EIGRP performs automatic summarization at classful boundaries.
Configuring EIGRP Automatic Summarization
R1(config)# router eigrp as-number
R1(config-router)# auto-summary
Verifying Auto-Summary
show ip protocols
show ip eigrp topology all-links
show ip route
Null0 summary route exists when:
Automatic summarization is enabled.
There is at least one subnet that was learned via EIGRP.
There are two or more network EIGRP router configuration mode commands.
Automatic summarization could cause routing loops
Notes: 7.1 – Tune EIGRP
71.1 – Automatic Summarization

## Slide 14: Tune EIGRP Default Route Propagation
Propagating a Default Static Route
The default static route (0.0.0.0 / 0) is usually configured on the router that has a connection to a network outside the EIGRP routing domain; for example, to an ISP.
One way to propagate the default static route
The redistribute static command
Verifying the Propagated Default Route
D - This route was learned from an EIGRP routing update.
* - The route is a candidate for a default route.
EX - The route is an external EIGRP route, in this case a static route outside of the EIGRP routing domain.
170 - This is the administrative distance of an external EIGRP route.
EIGRP for IPv6: Default Route
To configure a IPv6 static default route: ipv6 route ::/0 exit-interface
To propapate a IPv6 static default route: redistribute static
To verify the propagation of IPv6 static default route: show ipv6 route
Notes: 7.1 – Tune EIGRP
71.2 – Automatic Summarization

## Slide 15: Tune EIGRP Fine-tuning EIGRP Interfaces
EIGRP Bandwidth Utilization
By default, EIGRP uses only up to 50 percent of an interface’s bandwidth for EIGRP information. This prevents the EIGRP process from over-utilizing a link and not allowing enough bandwidth for the routing of normal traffic.
Commands to configure the bandwidth percentage used by EIGRP on an interface:
IPv4: ip bandwidth-percent eigrp as-number percent
IPv6: ipv6 bandwidth-percent eigrp as-number percent
Hello and Hold Timers – Do not have to match with other EIGRP routers
Hello packets are used to establish and monitor the connection status of neighbors
Commands to configure the hello intervals per interface:
ip hello-interval eigrp as-number seconds
ipv6 hello-interval eigrp as-number seconds
Hold time tells the router the maximum time that the router should wait to receive the next Hello before declaring that neighbor as unreachable.
Commands to configure the hold time intervals per interface:
ip hold-time eigrp as-number seconds
ipv6 hold-time eigrp as-number seconds
What are the default hello intervals and hold times for EIGRP?
Notes: 7.1 – Tune EIGRP
71.3 – Fine-tuning EIGRP Interfaces

## Slide 16: Tune EIGRP Fine-tuning EIGRP Interfaces (Cont.)
Load Balancing
Equal-cost load balancing
The ability of a router to distribute outbound traffic using all interfaces that have the same metric from the destination address
IPv4 and IPv6: The maximum-paths value determines the maximum number of routes
Unequal-cost load balancing
The ability to balance traffic across multiple routes that have different metrics
IPv4 and IPv6: The variance command is used to install multiple loop-free routes with unequal cost in a local routing table
Notes: 7.1 – Tune EIGRP
71.3 – Fine-tuning EIGRP Interfaces (Cont.)

## Slide 17: 7.2 Troubleshoot EIGRP
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 7: EIGRP Tuning and Troubleshooting

## Slide 18: Troubleshoot EIGRP Components of Troubleshooting EIGRP
Basic EIGRP Troubleshooting Commands
Verify the neighbor adjacency
show ip eigrp neighbors
show ipv6 eigrp neighbors
Verify the learned route to remote networks
show ip route eigrp
show ipv6 route eigrp
Verify the various EIGRP settings
show ip protocols
show ipv6 protocols
Notes: 7.2 – Troubleshoot EIGRP
7.2.1 – Components of Troubleshooting EIGRP

## Slide 19: Troubleshoot EIGRP Troubleshoot EIGRP Neighbor Issues
Layer 3 Connectivity
Verify the connection
show ip interface brief or show ipv6 interface brief
ping ip address
EIGRP Parameters
Verify that the routers are in the same EIGRP domain with the same AS number
show ip protocols or show ipv6 protocols
Configure AS number
IPv4: router eigrp as-number
IPv6: ipv6 router eigrp as-number
EIGRP Interfaces
Verify that the router interfaces
are participating in the EIGRP network
show ip eigrp interfaces or show ipv6 eigrp interfaces
show ip protocols or show ipv6 protocols
show running-config | section eigrp
Notes: 7.2 – Troubleshoot EIGRP
7.2.2 – Troubleshoot EIGRP Neighbor Issues

## Slide 20: Troubleshoot EIGRP Troubleshoot EIGRP Routing Table Issues
Passive Interface
Prevent routers from becoming neighbors
show ip eigrp neighbors or show ipv6 eigrp neighbors
The show ip protocols or show ipv6 protocols command is used to verify whether the interface has been configured as passive
Passive interface is configured if neighbor adjacency is not desirable
Where would you configure passive interfaces in the graphics?
Missing Network Statement
Verify the advertised networks
show ip protocols or show ipv6 protocols
show ip route or show ipv6 route
Configure network statements
IPv4: network ip-address [mask]
IPv6: ipv6 eigrp autonomous-system command in interface configuration mode
Autosummarization
IPv4: Could cause inconsistent routing
Disable autosummarization: no auto-summary
IPv6: All summarization can only be accomplished using EIGRP manual summary routes.
Notes: 7.2 – Troubleshoot EIGRP
7.2.3 – Troubleshoot EIGRP Routing Table Issues

## Slide 21: 7.3 Chapter Summary
Notes: Cisco Networking Academy Program
Course Name
Chapter 7: EIGRP Tuning and Troubleshooting

## Slide 22: Chapter Summary Summary
EIGRP is one of the routing protocols commonly used in large enterprise networks. Modifying EIGRP features and troubleshooting problems is one of the most essential skills for a network engineer involved in the implementation and maintenance of large routed enterprise networks that use EIGRP.
Summarization decreases the number of entries in routing updates and lowers the number of entries in local routing tables. It also reduces bandwidth utilization for routing updates and results in faster routing table lookups. EIGRP for IPv4 automatic summarization is disabled by default beginning with Cisco IOS Release 15.0(1)M and 12.2(33). Prior to this, automatic summarization was enabled by default. To enable automatic summarization for EIGRP use the auto-summary command in router configuration mode. Use the show ip protocols command to verify the status of automatic summarization. Examine the routing table to verify that automatic summarization is working.
EIGRP automatically includes summary routes to Null0 to prevent routing loops that are included in the summary but do not actually exist in the routing table. The Null0 interface is a virtual IOS interface that is a route to nowhere, commonly known as "the bit bucket". Packets that match a route with a Null0 exit interface are discarded.
One method of propagating a default route within the EIGRP routing domain is to use the redistribute static command. This command tells EIGRP to include this static route in its EIGRP updates to other routers. The show ip protocols command verifies that static routes within the EIGRP routing domain are being redistributed.
Notes: 7.3.1.1 - Summary

## Slide 23: Chapter Summary Summary (Cont.)
Use the ip bandwidth-percent eigrp as-number percent interface configuration mode command to configure the percentage of bandwidth that can be used by EIGRP on an interface.
To configure the percentage of bandwidth that can be used by EIGRP for IPv6 on an interface, use the ipv6 bandwidth-percent eigrp command in interface configuration mode. To restore the default value, use the no form of this command.
Hello intervals and hold times are configurable on a per-interface basis in EIGRP and do not have to match with other EIGRP routers to establish or maintain adjacencies.
For IP in EIGRP, Cisco IOS software applies load balancing using up to four equal-cost paths by default. With the maximum-paths router configuration mode command, up to 32 equal-cost routes can be kept in the routing table.
The show ip route command verifies that the router learned EIGRP routes. The show ip protocols command is used to verify that EIGRP displays the currently configured values.
Notes: 7.3.1.1 – Summary (Cont.)