## Slide 1: Instructor Materials Chapter 8: Single-Area OSPF
CCNA Routing and Switching
Scaling Networks
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 8: Single-Area OSPF

## Slide 2: Instructor Materials – Chapter 8 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
Information to help you become familiar with the chapter
Teaching aids
Instructor Class Presentation
Optional slides that you can use in the classroom
Begins on slide # 11
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Scaling Network
Planning Guide
Chapter 8: Single-Area OSPF
Notes: Course Planning Guide
Chapter 8: Single-Area OSPF

## Slide 4: Chapter 8: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
8.0.1.2 | Class Activity | Can Submarines Swim? | Optional
8.1.1.6 | Activity | Identify OSPF Features and Terminology | -
8.1.2.6 | Activity | Identify the OSPF Packet Types | -
8.1.3.5 | Activity | Identify the OSPF States for Establishing Adjacency | -
8.1.3.6 | Video | Observing OSPF Protocol Communications | -
8.2.1.2 | Syntax Checker | Entering Router OSPF Configuration Mode on R2 | -
8.2.1.4 | Syntax Checker | Assigning a Router ID on R2 and R3 | -
8.2.1.5 | Syntax Checker | Modifying the Router ID | -
8.2.2.3 | Syntax Checker | Advertising Networks in OSPF | -
8.2.2.5 | Syntax Checker | Configuring Passive Interfaces | -
8.2.2.6 | Activity | Calculate the Subnet and Wildcard Masks | -
8.2.2.7 | Packet Tracer | Configuring OSPFv2 in a Single Area | Recommended
8.2.3.5 | Syntax Checker | Adjusting Interface Bandwidths | -
8.2.4.1 | Syntax Checker | Verifying OSPF Neighbors | -
8.2.4.2 | Syntax Checker | Verifying OSPF Protocol Settings | -
8.2.4.3 | Syntax Checker | Verifying OSPF Process Information | -
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 8: Activities (cont.)
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
8.2.4.4 | Syntax Checker | Verifying OSPF Interface Settings | -
8.2.4.5 | Lab | Configuring Basic Single-area OSPFv2 | Optional
8.3.1.5 | Activity | Compare and Contrast OSPFv2 and OSPFv3 | -
8.3.2.3 | Syntax Checker | Configuring Link-Local Addresses | -
8.3.2.4 | Syntax Checker | Assigning a Router ID | -
8.3.2.5 | Syntax Checker | Modifying the Router ID | -
8.3.2.6 | Syntax Checker | Enabling OSPFv3 on the R2 and R3 Interfaces | -
8.3.3.1 | Syntax Checker | Verifying OSPFv3 Neighbors for R1 | -
8.3.3.2 | Syntax Checker | Verifying OSPFv3 Protocol Settings for R2 and R3 | -
8.3.3.3 | Syntax Checker | Verifying OSPFv3 Interfaces on R2 and R3 | -
8.3.3.4 | Syntax Checker | Verifying the IPv6 Routing Table of R2 and R3 | -
8.3.3.5 | Packet Tracer | Configuring Basic OSPFv3 in a Single Area | Optional
8.3.3.6 | Lab | Configuring Basic Single-Area OSPFv3 | Recommended
8.4.1.1 | Class Activity | Stepping Through OSPFv3 | Optional
8.4.1.2 | Packet Tracer | Skills Integration Challenge | Recommended
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5

## Slide 6: Chapter 8: Assessment
Students should complete Chapter 8, “Assessment” after completing Chapter 8.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 6

## Slide 7: Chapter 8: Best Practices
During this chapter, consider setting up an OSPF network as a Packet Tracer demonstration.
Discuss with students the differences between single-area OSFP and multiarea OSPF. Give them an assignment to draw a picture of OSPF single areas and multiple areas.
Make sure the students pay particular attention to the packet types on graphic 8.1.2.5. If they understand this graphic, multiarea OSPF discussion in Chapter 9 will flow smoother. Rote memorization of such things as packet type is a step that leads to comprehension.
Provide wildcard mask worksheets.
Give the student plenty of practice on hands-on OSPF configuration.
Give the students assignments to memorize the steps of link-state operation.
Give the students assignments to compare/contrast OSPF, EIGRP, and RIPv2.
Notes: 7

## Slide 8: Chapter 8: Best Practices (Cont.)
It will be helpful to enlarge some of the graphics in this chapter and print out large examples for the classroom. Another option, give the students an assignment of making posters with concepts in this chapter.
Using Wireshark and a topology of three routers connected to one switch, view the OSPF process of establishing adjacencies.
Walk the students through all the commands in the chapter, but focus on the areas of possible confusion.
Help students to analyze the nature of multi-access networks and the OSPF processes. Using Wireshark and a topology of three routers connected to one switch, view the OSPF process of establishing adjacencies. Look for the designated router, backup designated router and DROTHERS.
Demonstrate both methods of modifying the OSPF cost. (bandwidth, cost)
Walk the students through all the commands in the chapter, but focus on the areas of possible confusion.
Notes: 8

## Slide 9: Chapter 8: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at community.netacad.net.
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Notes: 9

## Slide 11: Chapter 8: Single-Area OSPF
Scaling Networks
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 8: Single-Area OSPF

## Slide 12: Chapter 8 - Sections & Objectives
8.1 OSPF Characteristics
Explain how single-area OSPF operates.
8.2 Single-Area OSPFv2
Implement single-area OSPFv2.
8.3 Single-Area OSPFv3
Implement single-area OSPFv3.
Notes: 12

## Slide 13: 8.1 OSPF Characteristics
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 8: Single-Area OSPF

## Slide 14: OSPF Characteristics Open Shortest Path First
OSPF
Version 2 (OSPFv2) is available for IPv4 while OSPF version 3 (OSPFv3) is available for IPv6.
3 Main Components
Data Structures, Routing Protocol Messages, and Algorithm
Achieving Convergence:
Establish Neighbor Adjacencies
Exchange Link-State Advertisements
Build the Topology Table
Execute the SPF Algorithm
OSPF can be implemented in one of two ways:
Single-Area OSPF
Multi-area OSPF
Notes: 8.1 – OSPF Characteristics
8.1.1 – Open Shortest Path First

## Slide 15: OSPF Characteristics OSPF Messages
OSPFv2 messages contain:
LSP Types:
Type 1: Hello packet
Type 2: Database Description (DBD) packet
Type 3: Link-State Request (LSR) packet
Type 4: Link-State Update (LSU) packet
Type 5: Link-State Acknowledgment (LSAck) packet
Notes: 8.1 – OSPF Characteristics
8.1.2 – OSPF Messages

## Slide 16: OSPF Characteristics OSPF Messages (Cont.)
Hello Packets are used to:
Discover OSPF neighbors and establish neighbor adjacencies.
Advertise parameters on which two routers must agree to become neighbors.
Elect the Designated Router (DR) and Backup Designated Router (BDR) on multi-access networks like Ethernet and Frame Relay.
OSPF Hello packets are transmitted to multicast address 224.0.0.5 in IPv4 and FF02::5 in IPv6
Notes: 8.1 – OSPF Characteristics
8.1.2 – OSPF Messages (Cont.)

## Slide 17: OSPF Characteristics OSPF Operation
OSPF progresses through several states while attempting to reach convergence
Down state, Init state, Two-Way state, ExStart state, Exchange state, Loading state, and Full state
Establishing Adjacencies
When a neighboring OSPF-enabled router receives a Hello packet with a router ID that is not within its neighbor list, the receiving router attempts to establish an adjacency with the initiating router.
OSPF DR and BDR
On multiaccess networks, OSPF elects a DR to be the collection and distribution point for LSAs sent and received. A BDR is also elected in case the DR fails.
After the Two-Way state, routers transition to database synchronization states.
Notes: 8.1 – OSPF Characteristics
8.1.3 – OSPF Operation

## Slide 18: 8.2 Single-Area OSPFv2
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 8: Single-Area OSPF

## Slide 19: Single-Area OSPFv2 OSPF Router ID
Enabling OSPFv2
OSPFv2 is enabled using the router ospf process-id global configuration mode command.
The process-id value represents a number between 1 and 65,535 and is selected by the network administrator.
The process-id value is locally significant, which means that it does not have to be the same value on the other OSPF routers to establish adjacencies with those neighbors.
Notes: 8.2 – Single-Area OSPFv2
8.2.1 – OSPF Router ID

## Slide 20: Single-Area OSPFv2 OSPF Router ID (Cont.)
Router ID
The router ID is used by the OSPF-enabled router to uniquely identify the router and participate in the election of the DR
Router ID based on one of three criteria
Explicitly configured using the OSPF router-id rid command
Router chooses the highest IPv4 address of any of configured loopback interfaces
If no loopback interfaces are configured, then the router chooses the highest active IPv4 address of any of its physical interfaces
Clearing the OSPF process is the preferred method to reset the router ID.
Note: The router ID looks like an IPv4 address, but it is not routable and, therefore, is not included in the routing table, unless the OSPF routing process chooses an interface (physical or loopback) that is appropriately defined by a network command.
Notes: 8.2 – Single-Area OSPFv2
8.2.1 – OSPF Router ID (Cont.)

## Slide 21: Single-Area OSPFv2 Configure Single-Area OSPFv2
Enabling OSPF
Any interfaces on a router that match the network address in the network command are enabled to send and receive OSPF packets.
Wildcard Mask
In a wildcard mask, binary 0 is equal to a match and binary 1 is not a match.
Notes: 8.2 – Single-Area OSPFv2
8.2.2 – Configure Single-Area OSPFv2

## Slide 22: Single-Area OSPFv2 Configure Single-Area OSPFv2 (Cont.)
The network Command
OSPFv2 can be enabled using the network intf-ip-address 0.0.0.0 area area-id router configuration mode command.
The advantage of specifying the interface is that the wildcard mask calculation is not necessary.
Unneeded OSPFv2 messages affect the network:
Inefficient use of bandwidth, inefficient use of resources, and increased security risk
Configure passive interfaces
Use the passive-interface router configuration mode command to prevent the transmission of routing messages through a router interface, but still allow that network to be advertised to other routers.
A neighbor adjacency cannot be formed over a passive interface.
Notes: 8.2 – Single-Area OSPFv2
8.2.2 – Configure Single-Area OSPFv2 (Cont.)

## Slide 23: Single-Area OSPFv2 OSPF Cost
OSPF Metric = Cost
The cost of an interface is inversely proportional to the bandwidth of the interface.
Cost = reference bandwidth / interface bandwidth
The cost of an OSPF route is the accumulated value from one router to the destination network.
To adjust the reference bandwidth, use the auto-cost reference-bandwidth Mb/s router configuration command.
Notes: 8.2 – Single-Area OSPFv2
8.2.3 – OSPF Cost

## Slide 24: Single-Area OSPFv2 OSPF Cost (Cont.)
Default Interface Bandwidths
As with reference bandwidth, interface bandwidth values do not actually affect the speed or capacity of the link.
Use the show interfaces command to view the interface bandwidth setting.
Adjust Interface Bandwidth
To adjust the interface bandwidth use the bandwidth kilobits interface configuration command.
Use the no bandwidth command to restore the default value.
Set OSPF Cost Manually
The cost can be manually configured on an interface using the ip ospf cost value interface configuration command.
Notes: 8.2 – Single-Area OSPFv2
8.2.3 – OSPF Cost (Cont.)

## Slide 25: Single-Area OSPFv2 Verify OSPF
Verify OSPF Neighbors
Use the show ip ospf neighbor command to verify that the router has formed an adjacency with its neighboring routers.
Verify OSPF Protocol Settings
The show ip protocols command is a quick way to verify vital OSPF configuration information.
Verify OSPF Process Information
The show ip ospf command can also be used to examine the OSPFv2 process ID and router ID
Notes: 8.2 – Single-Area OSPFv2
8.2.4 – Verify OSPF

## Slide 26: Single-Area OSPFv2 Verify OSPF (Cont.)
Verify OSPF Interface Settings
The quickest way to verify OSPFv2 interface settings is to use the show ip ospf interface command.
To get a summary of OSPFv2-enabled interfaces, use the show ip ospf interface brief command.
Notes: 8.2 – Single-Area OSPFv2
8.2.4 – Verify OSPF (Cont.)

## Slide 27: 8.3 Single-Area OSPFv3
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 8:Single-Area OSPF

## Slide 28: Single-Area OSPFv3 OSPFv2 vs. OSPFv3
OSPFv3
Similar to its IPv4 counterpart, OSPFv3 exchanges routing information to populate the IPv6 routing table with remote prefixes
Packets with a source or destination link-local address cannot be routed beyond the link from where the packet originated.
Notes: 8.3 – Single-Area OSPFv3
8.3.1 – OSPFv2 vs. OSPFv3

## Slide 29: Single-Area OSPFv3 OSPFv2 vs. OSPFv3 (Cont.)
Link-Local Addresses
Link-local addresses are automatically created when an IPv6 global unicast address is assigned to the interface.
Assigning Link-Local Addresses
Link-local addresses can be configured manually using the same interface command used to create IPv6 global unicast addresses, but appending the link-local keyword to the ipv6 address command.
Configuring the OSPFv3 Router ID
OSPFv3 requires a 32-bit router ID to be assigned before OSPF can be enabled on an interface.
The router-id rid command is used to assign a router ID in OSPFv3.
Clearing the OSPF process is the preferred method to reset the router ID.
Notes: 8.3 – Single-Area OSPFv3
8.3.2 – Configuring OSPFv3 (Cont.)

## Slide 30: Single-Area OSPFv3 Configuring OSPFv3
Enabling OSPFv3 on Interfaces
To enable OSPFv3 on an interface, use the ipv6 ospf process-id area area-id interface configuration mode command.
Notes: 8.3 – Single-Area OSPFv3
8.3.2 – Configuring OSPFv3

## Slide 31: Single-Area OSPFv3 Verify OSPFv3
Verify OSPFv3 Neighbors
Use the show ipv6 ospf neighbor command to verify that the router has formed an adjacency with its neighboring routers.
Verify OSPFv3 Protocol Settings
The show ipv6 protocols command is a quick way to verify vital OSPFv3 configuration information, including the OSPFv3 process ID, the router ID, and the interfaces enabled for OSPFv3.
Verify OSPFv3 Interfaces
The quickest way to verify OSPFv3 interface settings is to use the show ipv6 ospf interface command.
To retrieve and view a summary of OSPFv3-enabled interfaces on R1, use the show ipv6 ospf interface brief command
Notes: 8.3 – Single-Area OSPFv3
8.3.2 – Verify OSPFv3

## Slide 32: Single-Area OSPFv3 Verify OSPFv3 (Cont.)
Verify the IPv6 Routing Table
The show ipv6 route ospf command provides specifics about OSPFv3 routes in the routing table.
Notes: 8.3 – Single-Area OSPFv3
8.3.2 – Verify OSPFv3 (Cont.)

## Slide 33: 8.4 Chapter Summary
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 8: Single-Area OSPF

## Slide 34: Chapter Summary Summary
The current version of OSPF for IPv4 is OSPFv2 introduced in RFC 1247 and updated in RFC 2328 by John Moy. In 1999, OSPFv3 for IPv6 was published in RFC 2740.
OSPF is a link-state routing protocol with a default administrative distance of 110, and is denoted in the routing table with a route source code of O.
OSPFv2 is enabled with the router ospf process-id global configuration mode command. The process-id value is locally significant, which means that it does not need to match other OSPFv2 routers to establish adjacencies with those neighbors.
The network command used with OSPFv2 has the same function as when used with other IGP routing protocols, but with slightly different syntax. The wildcard-mask value is the inverse of the subnet mask, and the area-id value should be set to 0.
By default, OSPF Hello packets are sent every 10 seconds on multi-access and point-to-point segments and every 30 seconds on NBMA segments (Frame Relay, X.25, ATM), and are used by OSPF to establish neighbor adjacencies. The Dead interval is four times the Hello interval, by default.
For routers to become adjacent, their Hello interval, Dead interval, network types, and subnet masks must match. Use the show ip ospf neighbors command to verify OSPFv2 adjacencies.
OSPF elects a DR to act as collection and distribution point for LSAs sent and received in the multi-access network. A BDR is elected to assume the role of the DR should the DR fail. All other routers are known as DROTHERs. All routers send their LSAs to the DR, which then floods the LSA to all other routers in the multi-access network.
The show ip protocols command is used to verify important OSPFv2 configuration information, including the OSPF process ID, the router ID, and the networks the router is advertising.
OSPFv3 is enabled on an interface and not under router configuration mode. OSPFv3 needs link-local addresses to be configured. IPv6 Unicast routing must be enabled for OSPFv3. A 32-bit router-ID is required before an interface can be enabled for OSPFv3. Similar verification commands used for OSPFv2 are used for OSPFv3.
Notes: 8.4 – Chapter Summary
8.4.1.3 - Summary