## Slide 1: Instructor Materials Chapter 3: STP
CCNA Routing and Switching
Scaling Networks
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 3: STP

## Slide 2: Instructor Materials – Chapter 3 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
Information to help you become familiar with the chapter
Teaching aids
Instructor Class Presentation
Optional slides that you can use in the classroom
Begins on slide # 14
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Scaling Network
Planning Guide
Chapter 3: STP
Notes: Course Planning Guide
Chapter 3: STP

## Slide 4: Chapter 3: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
3.0.1.2 | Class Activity | Stormy Traffic | Optional
3.1.1.5 | Packet Tracer | Examining a Redundant Design | Optional
3.1.2.10 | Activity | 802.1D Port Roles | -
3.1.2.11 | Video | Observing Spanning Tree Protocol Operation | -
3.1.2.12 | Lab | Building a Switched Network with Redundant Links | Optional
3.2.1.3 | Activity | Identify Types of Spanning Tree Protocols | -
3.2.2.4 | Activity | Identifying PVST+ Operation | -
3.2.3.5 | Activity | Identify Port Roles in Rapid PVST+ | -
3.2.3.6 | Activity | Compare PVST+ and Rapid PVST+ | -
3.3.1.2 | Syntax Checker | Configure and Verify the BID | -
3.3.1.3 | Syntax Checker | Configuring PortFast and BPDU Guard | -
3.3.1.4 | Syntax Checker | Configuring PVST+ Load Balancing | -
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 3: Activities (cont.)
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
3.3.1.5 | Packet Tracer | Configuring PVST+ | Optional
3.3.2.2 | Packet Tracer | Configuring Rapid PVST+ | Recommended
3.3.2.3 | Lab | Configuring Rapid PVST+, PortFast and BPDU Guard | Recommended
3.3.3.6 | Activity | Troubleshoot STP Configuration Issues | -
3.3.4.3 | Activity | Identify Switch Stacking Terminology | -
3.4.1.1 | Class Activity | Documentation Tree | Optional
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5

## Slide 6: Chapter 3: Assessment
Students should complete Chapter 3, “Assessment” after completing Chapter 3.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 6

## Slide 7: Chapter 3: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at community.netacad.net.
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Notes: 7
Cisco Networking Academy Program
Scaling Networks
Chapter 3 STP

## Slide 9: Chapter 3: STP
Scaling Networks
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 3: STP

## Slide 10: Chapter 3- Sections & Objectives
3.1 Spanning Tree Concepts
Examine the purpose of STP and how the spanning tree algorithm is used create a loop-free topology.
3.2 Varieties of Spanning Tree Protocols
Examine the varieties of Spanning Tree protocols including PVST+ and Rapid PVST+.
3.3 Spanning Tree Configuration
Configure PVST+ and Rapid PVST+ to improve network performance.
Notes: 10

## Slide 11: 3.1 Spanning Tree Concepts
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 3 STP

## Slide 12: Spanning Tree Concepts Purpose of Spanning Tree
Redundancy at OSI Layers 1 and 2
When multiple paths exist between two devices on a network, and there is no spanning tree implementation on the switches, a Layer 2 loop occurs.
Issues with Layer 1 Redundancy: MAC Database Instability
Ethernet has no mechanism enabled to block continued propagation of these frames on a switched network that continue to propagate between switches.
Issues with Layer 1 Redundancy: Broadcast Storms
A broadcast storm occurs when there are so many broadcast frames caught in a Layer 2 loop that all available bandwidth is consumed.
Notes: 3.1 - Spanning Tree Concepts
3.1.1 – Purpose of Spanning Tree

## Slide 13: Spanning Tree Concepts Purpose of Spanning Tree
Issues with Layer 1 Redundancy: Duplicate Unicast Frames
An unknown unicast frame is when the switch does not have the destination MAC address in its MAC address table and must forward the frame out all ports, except the ingress port.
Unknown unicast frames sent onto a looped network can result in duplicate frames arriving at the destination device.
Notes: 3.1 - Spanning Tree Concepts
3.1.1 – Purpose of Spanning Tree

## Slide 14: Spanning Tree Concepts STP Operation
Spanning Tree Algorithm: Introduction
STP ensures that there is only one logical path between all destinations on the network by intentionally blocking redundant paths that could cause a loop.
Spanning Tree Algorithm: Port Roles
Root ports - Ports closest to the root bridge.
Designated ports - Non-root ports permitted to forward traffic.
Alternate and backup ports - Blocking state to prevent loops.
Disabled ports - A disabled port is a switch port that is shut down.
Spanning Tree Algorithm: Root Bridge
The root bridge serves as a reference point for all STP calculations.
The switch with the lowest BID will become the root bridge
Notes: 3.1 - Spanning Tree Concepts
3.1.2 – STP Operation

## Slide 15: Spanning Tree Concepts STP Operation
Spanning Tree Algorithm: Root Path Cost
Default port costs are defined by the speed at which the port operates
Internal root path cost is determined by summing up the individual port costs along the path from the switch to the root bridge.
Use the spanning-tree cost value interface configuration command on both ends of a link to apply a custom cost.
Use the show spanning-tree command to verify the port and internal root path cost to the root bridge.
Notes: 3.1 - Spanning Tree Concepts
3.1.2 – STP Operation

## Slide 16: Spanning Tree Concepts STP Operation
Port Role Decisions for RSTP
Root bridge automatically configures all of its switch ports in the designated role.
Designated ports are configured for all LAN segments.
Designated and Alternate Ports
The switch with the lower cost path to the root bridge (root path cost) will have its port selected as the designated port.
The alternate port will not send or receive traffic on that segment.
Notes: 3.1 - Spanning Tree Concepts
3.1.2 – STP Operation

## Slide 17: Spanning Tree Concepts STP Operation
802.1D BPDU Frame Format
The spanning tree algorithm depends on the exchange of BPDUs.
The BPDU frame information is included in the Data portion of an Ethernet frame and identifies the following fields:
Notes: 3.1 - Spanning Tree Concepts
3.1.2 – STP Operation

## Slide 18: Spanning Tree Concepts STP Operation
802.1D BPDU Propagation and Process
By default, BPDU frames are sent every two seconds.
Each switch maintains local information about its own BID, the root ID, and the root path cost.
Extended System ID
The bridge ID (BID) is used to determine the root bridge on a network. The BID field of a BPDU frame contains three separate fields:
Bridge priority – Default 32768
Extended system ID - Identifies the VLAN participating in STP
MAC address - When the bridge priorities are equal, the MAC address is the deciding factor as to which switch is going to become the root bridge.
Notes: 3.1 - Spanning Tree Concepts
3.1.2 – STP Operation

## Slide 19: 3.2 Varieties of Spanning Tree Protocols
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 3 STP

## Slide 20: Varieties of Spanning Tree Protocols Overview
Types of Spanning Tree Protocols
Several varieties of spanning tree protocols have emerged since the original IEEE 802.1D.
Characteristics of the Spanning Tree Protocols
Notes: 3.2 – Varieties of Spanning Tree Protocols
3.2.1 – Overview

## Slide 21: Varieties of Spanning Tree Protocols PVST+
Overview of PVST+
Cisco developed PVST+ to run an independent instance of the Cisco implementation of IEEE 802.1D for each VLAN in the network.
Port States and PVST+ Operation
STP and PVST+ use five port states consisting of Blocking, Listening, Learning, Forwarding, and Disabled.
Extended System ID and PVST+ Operation
  Extended system ID ensures switches have unique BIDs for each VLAN.
  To manipulate the root-bridge election, assign a lower priority to the desired root bridge switch for the VLAN(s).
Notes: 3.2 – Varieties of Spanning Tree Protocols
3.2.2 – PVST+

## Slide 22: Varieties of Spanning Tree Protocols Rapid PVST+
Overview of Rapid PVST+
Rapid PVST+ is the Cisco implementation of per-VLAN RSTP.
RSTP can achieve much faster convergence.
RSTP BPDU
RSTP uses type 2, version 2 BPDUs and populates the flag byte in a slightly different manner than in the original 802.1D.
Edge Ports
RSTP edge port is a switch port that is never intended to be connected to another switch.
It immediately transitions to the forwarding state when enabled.
Notes: 3.2 – Varieties of Spanning Tree Protocols
3.2.3 – Rapid PVST+

## Slide 23: Varieties of Spanning Tree Protocols Rapid PVST+
Link Types
Point-to-Point - A port operating in full-duplex mode typically connects a switch to a switch and is a candidate for a rapid transition to a forwarding state.
Shared - A port operating in half-duplex mode connects a switch to a legacy hub that attaches multiple devices.
  RSTP must determine the port role:
  Root ports and Alternate (backup) ports do not use the link-type parameter in most cases.
  Designated ports make the most use of the link-type parameter and transition to the forwarding state if the link-type parameter is set to point-to-point.
Notes: 3.2 – Varieties of Spanning Tree Protocols
3.2.3 – Rapid PVST+

## Slide 24: 3.3 Spanning Tree Configuration
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 3 STP

## Slide 25: Spanning Tree Configuration PVST+ Configuration
Catalyst 2960 Default Configuration
Default spanning tree mode is PVST+.
Configuring and Verifying the Bridge ID
  Method 1:
  Use the spanning-tree vlan vlan-id root primary global config command.
  Method 2:
  Use the spanning-tree vlan vlan-id priority value global config command.
  Use the show spanning-tree command to verify the bridge priority of a switch.
Notes: 3.3 –Spanning Tree Configuration
3.3.1 – PVST+ Configuration

## Slide 26: Spanning Tree Configuration PVST+ Configuration
PortFast and BPDU Guard
PortFast immediately transitions an access port from blocking to forwarding state while BPDU guard puts an access port in an errdisabled (error-disabled) state if it receives a BPDU.
Use the spanning-tree portfast interface configuration mode command to enable PortFast on a switch port.
Use the spanning-tree bpduguard enable interface configuration mode command to enable BPDU guard on a Layer 2 access port.
Notes: 3.3 –Spanning Tree Configuration
3.3.1 – PVST+ Configuration

## Slide 27: Spanning Tree Configuration PVST+ Configuration
PVST+ Load Balancing
The goal is to configure two or more root bridges for different sets of VLANs and make use of redundant links.
S3(config)# spanning-tree vlan 20 root primary
S3(config)# spanning-tree vlan 10 root secondary
S3(config)#
S1(config)# spanning-tree vlan 10 root primary
S1(config)# spanning-tree vlan 20 root secondary
S1(config)#
Notes: 3.3 –Spanning Tree Configuration
3.3.1 – PVST+ Configuration

## Slide 28: Spanning Tree Configuration Rapid PVST+ Configuration
Spanning Tree Mode
Rapid PVST+ is the Cisco implementation of RSTP.
It supports RSTP on a per-VLAN basis.
Notes: 3.3 –Spanning Tree Configuration
3.3.2 – Rapid PVST+ Configuration

## Slide 29: Spanning Tree Configuration STP Configuration Issues
Analyzing the STP Topology
Use show cdp neighbors to discover topology
Use STP knowledge to determine the root switch
Use show spanning-tree vlan to verify which switch is the root and port status (forwarding or blocking).
Expected Topology versus Actual Topology
Troubleshooting consists of comparing the actual state of the network against the expected state of the network and spotting the differences.
Notes: 3.3 –Spanning Tree Configuration
3.3.3 – STP Configuration Issues

## Slide 30: Spanning Tree Configuration STP Configuration Issues
Overview of STP Status
Use the show spanning-tree command without specifying any additional options provides a quick overview of the status of STP for all VLANs that are defined on a switch.
  Use the show spanning-tree vlan vlan_id command to get STP information for a particular VLAN.
Notes: 3.3 –Spanning Tree Configuration
3.3.3 – STP Configuration Issues

## Slide 31: Spanning Tree Configuration STP Configuration Issues
Spanning Tree Failure Consequences
There are two types of STP failures:
STP might erroneously block ports that should have gone into the forwarding state.
STP might erroneously move one or more ports into the forwarding state
Repairing a Spanning Tree Problem
Manually remove redundant links in the switched network, either physically or through configuration, until all loops are eliminated.
Chances are that restoring the redundant links will trigger a new broadcast storm.
Before restoring the redundant links, determine and correct the cause of the spanning tree failure.
Carefully monitor the network to ensure that the problem is fixed.
Notes: 3.3 – Spanning Tree Configuration
3.3.3 – STP Configuration Issues

## Slide 32: Spanning Tree Configuration Switch Stacking Concepts
Switch Stacking Concepts
A switch stack can consist of up to nine Catalyst 3750 switches connected through their StackWise ports.
One of the switches controls the operation of the stack and is called the stack master.
The switch is managed as a single switch, through a single IP address, including passwords, VLANs, and interfaces.
Spanning Tree and Switch Stacks
Another benefit to switch stacking is the ability to add more switches to a single STP instance without increasing the STP diameter.
The IEEE recommends a maximum diameter of seven switches for the default STP timers.
Notes: 3.3 – Spanning Tree Configuration
3.3.4 – Switch Stacking and Chassis Aggregation

## Slide 33: 3.3 Chapter Summary
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 3 STP

## Slide 34: Chapter Summary Summary
Problems that can result from a redundant Layer 2 network include broadcast storms, MAC database instability, and duplicate unicast frames. STP is a Layer 2 protocol that ensures that there is only one logical path between all destinations on the network by intentionally blocking redundant paths that could cause a loop.
STP sends BPDU frames for communication between switches. One switch is elected as the root bridge for each instance of spanning tree. An administrator can control this election by changing the bridge priority. Root bridges can be configured to enable spanning tree load balancing by VLAN or by a group of VLANs, depending on the spanning tree protocol used. STP then assigns a port role to each participating port using a path cost. The root path cost is equal to the sum of all the port costs along the path to the root bridge. A port cost is automatically assigned to each port; however, it can also be manually configured. Paths with the lowest cost become preferred, and all other redundant paths are blocked.
PVST+ is the default configuration of IEEE 802.1D on Cisco switches. It runs one instance of STP for each VLAN. A newer, faster-converging spanning tree protocol, RSTP, can be implemented on Cisco switches on a per-VLAN basis in the form of Rapid PVST+. Multiple Spanning Tree (MST) is the Cisco implementation of Multiple Spanning Tree Protocol (MSTP), where one instance of spanning tree runs for a defined group of VLANs. Features such as PortFast and BPDU guard ensure that hosts in the switched environment are provided immediate access to the network without interfering with spanning tree operation.
Switch stacking allows connection of up to nine Catalyst 3750 switches to be configured and presented to the network as a single entity. STP views the switch stack as a single switch. This additional benefit helps ensure the IEEE recommended maximum diameter of seven switches.
Notes: 3.4 – Chapter Summary
3.3.4 – Summary