## Slide 1: Instructor Materials Chapter 2: Scaling VLANs
CCNA Routing and Switching
Scaling Networks
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 2: Scaling VLANs

## Slide 2: Instructor Materials – Chapter 2 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
Information to help you become familiar with the chapter
Teaching aids
Instructor Class Presentation
Optional slides that you can use in the classroom
Begins on slide # 9
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Scaling Network
Planning Guide
Chapter 2: Scaling VLANs
Notes: Course Planning Guide
Chapter 2: Scaling VLANs

## Slide 4: Chapter 2: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
2.1.1.7 | Activity | Identify VTP Concepts and Operations | -
2.1.2.6 | Syntax Checker | Configure and Verify VTP | -
2.1.3.2 | Syntax Checker | Create and Verify a VLAN | -
2.1.3.3 | Syntax Checker | Assign Ports to VLANs | -
2.1.3.4 | Syntax Checker | Verify VLAN Information | -
2.1.3.5 | Syntax Checker | Configure and Verify an Extended VLAN | -
2.1.4.3 | Activity | Predict DTP Behavior | -
2.1.4.4 | Packet Tracer | Configure VLANs, VTP, and DTP | Optional
2.1.4.5 | Lab | Configure Extended VLANs, VTP, and DTP | Recommended
2.2.2.3 | Activity | Identify the Troubleshooting Command for an Inter-VLAN Routing Issue | -
2.2.2.4 | Packet Tracer | Troubleshooting Inter-VLAN Routing | Recommended
2.2.2.5 | Lab | Troubleshoot Inter-VLAN Routing | Optional
2.2.3.3 | Packet Tracer | Troubleshoot VTP and DTP Issues | Recommended
2.3.1.5 | Packet Tracer | Configure Layer 3 Switching and inter-VLAN Routing | Recommended
2.3.2.3 | Activity | Troubleshoot Layer 3 Switching Issues | -
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 2: Assessment
Students should complete Chapter 2, “Assessment” after completing Chapter 2.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 5

## Slide 6: Chapter 2: Best Practices
  Make this chapter as hands on as possible. Students should complete all labs, Packet Tracer activities, and other activities.
  Emphasize the importance and advantages of switches now being widely used as Layer 3 devices.
  Emphasize the issues that can occur and the importance of completing the troubleshooting labs.
  When the students complete the troubleshooting labs, create additional challenges or have one team of students create problems on another team’s setup. Ensure that all changes and all solutions are documented.
Notes: 6

## Slide 7: Chapter 2: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at community.netacad.net.
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Notes: 7

## Slide 9: Chapter 2: Scaling VLANs
Scaling Networks
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 2: Scaling VLANs

## Slide 10: Chapter 2 - Sections & Objectives
2.1 VTP, Extended VLANs, and DTP
Configure enhanced inter-switch connectivity technologies.
2.2 Troubleshoot Multi-VLAN Issues
Troubleshoot issues in an inter-VLAN routing environment.
2.3 Layer 3 Switching
Implement inter-VLAN routing using Layer 3 switching to forward data in a small to medium-sized business LAN.
Notes: 10

## Slide 11: 2.1 VTP, Extended VLANs, and DTP
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 2: Scaling VLANs

## Slide 12: VTP, Extended VLANs, and DTP VTP Concepts and Operation
  VLAN trunking protocol (VTP) allows a network administrator to manage VLANs on a switch configured as a VTP server.
  VTP stores VLAN configurations in a database called vlan.dat.
  A switch can be configured in one of three VTP modes:
  Server
  Client
  Transparent
  VTP includes three types of
  advertisements:
  Summary
  Advertisement request
  Subset advertisements
Notes: 2.1 - VTP, Extended VLANs, and DTP
2.1.1 – VTP Concepts and Operation

## Slide 13: VTP, Extended VLANs, and DTP VTP Concepts and Operation (Cont.)
  VTP has 3 versions
  The show vtp status privileged EXEC command displays the VTP status.
  The configuration revision number is used when determining whether a switch should keep its existing VLAN database, or overwrite it with the VTP update sent by another switch.
  When a switch is added to a network, ensure that it has a default VTP configuration.
Notes: 2.1 - VTP, Extended VLANs, and DTP
2.1.1 – VTP Concepts and Operation

## Slide 14: VTP, Extended VLANs, and DTP VTP Configuration
There are 5 steps to VTP configuration:
Configure the VTP Server.
Configure the VTP Domain Name and Password.
Configure the VTP Clients.
Configure VLANs on the VTP Server.
Verify the VTP Clients have received the new VLAN information.
Notes: 2.1 - VTP, Extended VLANs, and DTP
2.1.2 – VTP Configuration

## Slide 15: VTP, Extended VLANs, and DTP Extended VLANs
  Normal range VLANs are identified by a VLAN ID between 1 and 1005.
  Extended range VLANs are identified by a VLAN ID between 1006 and 4094.
  VTP does not learn extended range VLANs.
  Creating a VLAN
  In addition to entering a single VLAN ID, a series of VLAN IDs can be entered that are separated by commas, or as range of VLAN IDs separated by hyphens.
Notes: 2.1 - VTP, Extended VLANs, and DTP
2.1.3 – Extended VLANs

## Slide 16: VTP, Extended VLANs, and DTP Extended VLANs (Cont.)
Assigning Ports to VLANs
After creating a VLAN, the next step is to assign ports to the VLAN.
Verifying VLAN Information
VLAN configurations can be validated using Cisco IOS show commands.
Configuring Extended VLANs
To configure an extended VLAN on a 2960 switch it must be set to VTP transparent mode.
Notes: 2.1 - VTP, Extended VLANs, and DTP
2.1.3 – Extended VLANs

## Slide 17: VTP, Extended VLANs, and DTP Dynamic Trunking Protocol
DTP
DTP manages trunk negotiation only if the port on the neighbor switch is configured in a trunk mode that supports DTP.
Turn off DTP on interfaces on a Cisco switch that is connected to devices that do not support DTP.
To enable trunking from a Cisco switch to a device that does not support DTP, use the switchport mode trunk and switchport nonegotiate interface configuration mode commands.
There are 5 commands to support different trunking modes:
switchport mode access
switchport mode dynamic auto
switchport mode dynamic desirable
switchport mode trunk
switchport nonegotiate
Notes: 2.1 - VTP, Extended VLANs, and DTP
2.1.4 – Dynamic Trunking Protocol

## Slide 18: 2.2 Troubleshoot Multi-VLAN Issues
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 2: Scaling VLANs

## Slide 19: Troubleshoot Multi-VLAN Issues Inter-VLAN Configuration Issues
  To delete a VLAN, use the no vlan vlan-id global configuration mode command.
  If a switch port is not configured for the correct VLAN, devices configured on that VLAN cannot connect to the router interface.
  When a problem is suspected with a switch configuration, use the various verification commands to examine the configuration and identify the problem.
Notes: 2.2 - Troubleshoot Multi-VLAN Issues
2.2.1 - Inter-VLAN Configuration Issues

## Slide 20: Troubleshoot Multi-VLAN Issues Inter-VLAN Configuration Issues (Cont.)
Interface Issues
When enabling inter-VLAN routing on a router, one of the most common configuration errors is to connect the physical router interface to the wrong switch port.
Verify Routing Configuration
With router-on-a-stick configurations, a common problem is assigning the wrong VLAN ID to the subinterface.
Using the show interfaces and the show running-config commands can be useful in troubleshooting this type of issue.
Notes: 2.2 - Troubleshoot Multi-VLAN Issues
2.2.1 - Inter-VLAN Configuration Issues

## Slide 21: Troubleshoot Multi-VLAN Issues IP Addressing Issues
IP Addresses and Subnet Masks
For inter-VLAN routing to operate, a router must be connected to all VLANs, either by separate physical interfaces or by subinterfaces.
Each interface, or subinterface, must be assigned an IP address that corresponds to the subnet to which it is connected.
Use the show running-config and show ip interface commands to verify IP address and subnet masks.
Notes: 2.2 - Troubleshoot Multi-VLAN Issues
2.2.2 – IP Addressing Issues

## Slide 22: Troubleshoot Multi-VLAN Issues VTP and DTP Issues
Troubleshoot VTP Issues
There are 5 common problems with VTP:
Incompatible VTP Versions
VTP Password Issues
Incorrect VTP Domain Name
All Switches Set to Client Mode
Incorrect Configuration Revision
Number
Troubleshoot DTP Issues
there are three common problems
associated with trunks.
Trunk mode mismatches
Allowed VLANs on trunks
Native VLAN mismatches
Notes: 2.2 - Troubleshoot Multi-VLAN Issues
2.2.3 – VTP and DTP Issues

## Slide 23: 2.3 Layer 3 Switching
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 2: Scaling VLANs

## Slide 24: Layer 3 Switching Layer 3 Switching Operation and Configuration
Layer 3 Switching
Modern enterprise networks use multilayer switches to achieve high-packet processing rates using hardware-based switching.
Catalyst multilayer switches support the following types of Layer 3 interfaces:
Routed port
Switch virtual interface (SVI)
Inter-VLAN Routing and SVIs
Routing can be transferred to the core
and the distribution layers (and
sometimes even the access layer) without impacting network performance.
An SVI can be created for any VLAN that exists on the switch.
SVIs are created the first time the VLAN interface configuration mode is entered for a particular VLAN SVI.
Notes: 2.3 – Layer 3 Switching
2.3.1 – Layer 3 Switching Operation and Configuration

## Slide 25: Layer 3 Switching Layer 3 Switching Operation and Configuration (Cont.)
Inter-VLAN Routing with Routed Ports
A routed port is a physical port that
acts similarly to an interface on a router.
A routed port is not associated with
a particular VLAN.
Routed ports on a Cisco IOS switch do
not support subinterfaces.
Routed ports are used for point-to-point
links.
To configure routed ports, use the
no switchport interface configuration mode
command on the appropriate ports.
Notes: 2.3 – Layer 3 Switching
2.3.1 – Layer 3 Switching Operation and Configuration

## Slide 26: Layer 3 Switching Troubleshoot Layer 3 Switching
Layer 3 Switch Configuration Issues
Check the following configurations for accuracy:
VLANs - VLANs must be defined across all the switches. VLANs must be enabled on the trunk ports. Ports must be in the right VLANs.
SVIs - SVIs must have the correct IP address or subnet mask. SVIs must be up. Each SVI must match with the VLAN number.
Routing - Routing must be enabled. Each interface or network should be added to the routing protocol, or static routes entered, where appropriate.
Hosts - Hosts must have the correct IP address or subnet mask. Hosts must have a default gateway associated with an SVI or routed port.
Notes: 2.3 – Layer 3 Switching
2.3.2 – Troubleshoot Layer 3 Switching

## Slide 27: 2.4 Chapter Summary
Notes: Cisco Networking Academy Program
Scaling Networks
Chapter 2: Scaling VLANs

## Slide 28: Chapter Summary Summary
VLAN Trunking Protocol (VTP) reduces administration of VLANs in a switched network. A switch configured as the VTP server distributes and synchronizes VLAN information over trunk links to VTP-enabled switches throughout the domain.
The three VTP modes are Server, Client and Transparent.
The configuration revision number is used when determining whether a VTP switch should keep or update its existing VLAN database. A switch will overwrite its existing VLAN database if it receives a VTP update from another switch in the same domain with a higher configuration revision number. Therefore, when a switch is being added to a VTP domain it must have the default VTP configuration or a lower configuration revision number than the VTP server.
Troubleshooting VTP can also involve dealing with errors caused by incompatible VTP versions and incorrectly configured domain names or passwords.
Notes: 2.4 – Chapter Summary

## Slide 29: Chapter Summary Summary (Cont.)
Trunk negotiation is managed by the Dynamic Trunking Protocol (DTP), which operates on a point-to-point basis between network devices. DTP is a Cisco proprietary protocol that is automatically enabled on Catalyst 2960 and Catalyst 3560 Series switches. A general best practice when a trunk link is required is to set the interface to trunk and nonegotiate. On links where trunking is not intended, DTP should be turned off.
When troubleshooting DTP, problems can be related to trunk mode mismatches, allowed VLANS on a trunk, and native VLAN mismatches.
Layer 3 switching using Switch Virtual Interfaces (SVIs) is a method of inter-VLAN routing that can be configured on Catalyst 2960 switches. An SVI with appropriate IP addressing is configured for each VLAN and provides Layer 3 processing for packets to or from all switch ports associated with those VLANs.
Another method of Layer 3 inter-VLAN routing is using routed ports. A routed port is a physical port that acts similarly to an interface on a router. Routed ports are mostly configured between switches in the core and distribution layer.
Troubleshooting inter-VLAN routing with a router or a Layer 3 switch are similar. Common errors involve VLAN, trunk, Layer 3 interface, and IP address configurations.
Notes: 2.4 – Chapter Summary