## Slide 1: Instructor Materials Chapter 5: Network Security and Monitoring
CCNA Routing and Switching
Connecting Networks
Notes: Cisco Networking Academy Program
Connecting Networks
Chapter 5: Network and Security Monitoring

## Slide 2: Instructor Materials – Chapter 5 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 9
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Connecting Networks
Planning Guide
Chapter 5: Network Security and Monitoring
Notes: Course Planning Guide
Chapter 5: Network and Security Monitoring

## Slide 4: Chapter 5: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
5.0.1.2 | Class Activity | Network Maintenance Development | Optional
5.1.1.7 | Activity | Identify Common Security Attacks | -
5.1.2.7 | Activity | Identify the Security Best Practice | -
5.2.1.8 | Activity | Identify Characteristics of SNMP Versions | -
5.2.1.9 | Lab | Research Network Monitoring Software | Optional
5.2.2.2 | Syntax Checker | Configuring and Verifying SNMPv2 | -
5.2.2.5 | Syntax Checker | Configuring and Verifying SNMPv3 | -
5.2.2.6 | Lab | Configuring SNMP | Recommended
5.3.1.5 | Activity | Identify SPAN Terminology | -
5.3.2.2 | Syntax Checker | Verify Local SPAN | -
5.3.2.3 | Lab | Implement Local SPAN | Recommended
5.3.3.2 | Lab | Troubleshoot LAN Traffic Using SPAN | Recommended
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 5: Assessment
Students should complete Chapter 5, “Assessment” after completing Chapter 5.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 5

## Slide 6: Chapter 5: Best Practices
Prior to teaching Chapter 5, the instructor should:
Complete Chapter 5 Assessment.
Ensure all activities are completed. This is a very important concept and hands-on time is vital.
Provide the students many network security and network monitoring activities.
Encourage students to login with their cisco.com login and download http://docwiki.cisco.com/wiki/Internetworking_Technology_Handbook
  Review the Security Technologies and the Network Management chapters.
Notes: 6

## Slide 7: Chapter 5: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at community.netacad.net.
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Notes: 7

## Slide 9: Chapter 5: Network Security and Monitoring
Connecting Networks
Notes: Cisco Networking Academy Program
Connecting Networks
Chapter 5: Network Security and Monitoring

## Slide 10: Chapter 5 - Sections & Objectives
5.1 LAN Security
  Explain how to mitigate common LAN security.
5.2 SNMP
  Configure SNMP to monitor network operations in a small to medium-sized business network.
5.3 Cisco Switch Port Analyzer (SPAN)
  Troubleshoot a network problem using SPAN.
Notes: 10

## Slide 11: 5.1 LAN Security
Notes: Cisco Networking Academy Program
Connecting Networks
Chapter 5: Network Security and Monitoring

## Slide 12: LAN Security LAN Security Attacks
Common attacks against the Layer 2 LAN infrastructure include:
  CDP Reconnaissance Attacks
  Telnet Attacks
  MAC Address Table Flooding Attacks
  VLAN Attacks
  DHCP Attacks
Notes: 5.1 - LAN Security
5.1.1 – LAN Security Attacks

## Slide 13: LAN Security LAN Security Best Practices
This topic covers several Layer 2 security solutions:
  Mitigating MAC address table flooding attacks using port security
  Mitigating VLAN attacks
  Mitigating DHCP attacks using DHCP snooping
  Securing administrative access using AAA
  Securing device access using 802.1X port authentication
Notes: 5.1 – LAN Security
5.1.2 – LAN Security Best Practices

## Slide 14: LAN Security LAN Security Best Practices
There are several strategies to help secure Layer 2 of a network:
  Always use secure variants of these protocols such as SSH, SCP, SSL, SNMPv3, and SFTP.
  Always use strong passwords and change them often.
  Enable CDP on select ports only.
  Secure Telnet access.
  Use a dedicated management VLAN where nothing but management traffic resides.
  Use ACLs to filter unwanted access.
Notes: 5.1 – LAN Security
5.1.2 – LAN Security Best Practices

## Slide 15: 5.2 SNMP
Notes: Cisco Networking Academy Program
Connecting Networks
Chapter 5: Network Security and Monitoring

## Slide 16: SNMP SNMP Operation
SNMP allows administrators to manage and monitor devices on an IP network.
SNMP Elements
  SNMP Manager
  SNMP Agent
  MIB
SNMP Operation
  Trap
  Get
  Set
Notes: 5.2 – SNMP
5.2.1 SNMP Operation

## Slide 17: SNMP SNMP Operation
SNMP Security Model and Levels
Notes: 5.2 – SNMP
5.2.1 – SNMP Operation

## Slide 18: SNMP Configuring SNMP
Configuration steps
  Configure community string
  Document location of device
  Document system contact
  Restrict SNMP Access
  Specify recipient of SNMP Traps
  Enable traps on SNMP agent
Notes: 5.2 – SNMP
5.2.2 – Configuring SNMP

## Slide 19: SNMP Configuring SNMP
Securing SNMPv3
Notes: 5.2 – SNMP
5.2.2 – Configuring SNMP

## Slide 20: 5.3 Cisco Switch Port Analyzer (SPAN)
Notes: Cisco Networking Academy Program
Connecting Networks
Chapter 5: Network Security and Monitoring

## Slide 21: Cisco Switch Port Analyzer SPAN Overview
Port mirroring
  The port mirroring feature allows a switch to copy and send Ethernet frames from specific ports to the destination port connected to a packet analyzer. The original frame is still forwarded in the usual manner.
Notes: 5.3 Cisco Switch Port Analyzer
5.3.1 SPAN Overview

## Slide 22: Cisco Switch Port Analyzer SPAN Overview
SPAN terminology
Notes: 5.3 – Switch Port Analyzer
5.3.1 – SPAN Overview

## Slide 23: Cisco Switch Port Analyzer SPAN Overview
RSPAN terminology
Notes: 5.3 – Switch Port Analyzer
5.3.1 – SPAN Overview

## Slide 24: Cisco Switch Port Analyzer SPAN Configuration
Use monitor session global configuration command
Notes: 5.3 – Cisco Switch Port Analyzer
5.3.2 – SPAN Configuration

## Slide 25: Cisco Switch Port Analyzer SPAN as a Troubleshooting Tool
SPAN allows administrators to troubleshoot network issues
Administrator can use SPAN to duplicate and redirect traffic to a packet analyzer
Administrator can analyze traffic from all devices to troubleshoot sub-optimal operation of network applications
Notes: 5.3 – Cisco Switch Port Analyzer
5.3.3 – SPAN as a Troubleshooting Tool

## Slide 26: 5.4 Chapter Summary
Notes: Cisco Networking Academy Program
Connecting Networks
Chapter 5: Network Security and Monitoring

## Slide 27: Chapter Summary Summary
At Layer 2, a number of vulnerabilities exist that require specialized mitigation techniques:
  MAC address table flooding attacks are addressed with port security.
  VLAN attacks are controlled by disabling DTP and following basic guidelines for configuring trunk ports.
  DHCP attacks are addressed with DHCP snooping.
The SNMP protocol has three elements: the Manager, the Agent, and the MIB. The SNMP manager resides on the NMS, while the Agent and the MIB are on the client devices.
  The SNMP Manager can poll the client devices for information, or it can use a TRAP message that tells a client to report immediately if the client reaches a particular threshold. SNMP can also be used to change the configuration of a device.
Notes: 5.4 - Chapter Summary

## Slide 28: Summary Continued
SNMPv3 is the recommended version because it provides security.
SNMP is a comprehensive and powerful remote management tool. Nearly every item available in a show command is available through SNMP.
Switched Port Analyzer (SPAN) is used to mirror the traffic going to and/or coming from the host. It is commonly implemented to support traffic analyzers or IPS devices.
Notes: 2.4 – Chapter Summary