## Slide 1: Instructor Materials Chapter 1: WAN Concepts
CCNA Routing and Switching
Connecting Networks
Notes: Cisco Networking Academy Program
Connecting Networks
Chapter 1: WAN Concepts

## Slide 2: Instructor Materials – Chapter 1 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 9
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Connecting Network
Planning Guide
Chapter 1: WAN Concepts
Notes: Course Planning Guide
Chapter 1: WAN Concepts

## Slide 4: Chapter 1: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name
1.0.1.2 | Class Activity | Branching Out
1.1.2.6 | Interactive Activity | Identify WAN Terminology
1.2.1.3 | Interactive Activity | Classify WAN Access Options
1.2.2.9 | Interactive Activity | Identify Private WAN Infrastructure Terminology
1.2.3.6 | Interactive Activity | Identify Public WAN Infrastructure Terminology
1.2.4.3 | Lab | Researching WAN Technologies
1.3.1.1 | Class Activity | WAN Device Modules
Notes: 4

## Slide 5: Chapter 1: Assessment
Students should complete Chapter 1, “Assessment” after completing Chapter 1.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 5

## Slide 6: Chapter 1: Best Practices
The instructor should:
Make this chapter as hands-on as possible.
Encourage students to do the chapter activities and labs.
Explain to students the WAN technologies and connection types used in their school.
Ask students to differentiate between the WAN technologies and connection types used in their home and used on their mobile devices.
Have students look for Cisco Validated Designs for WANs and ask them to look for chapter terminology in the documentation. For example:
  http://www.cisco.com/c/dam/en/us/td/docs/solutions/CVD/Oct2016/CVD-IWANDesign-2016OCT.pdf
Notes: 6

## Slide 7: Chapter 1: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at community.netacad.net.
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Notes: 7

## Slide 9: Chapter 1: WAN Concepts
Connecting Networks
Notes: Cisco Networking Academy Program
Connecting Networks
Chapter 1: WAN Concepts

## Slide 10: Chapter 1 - Sections & Objectives
1.1 WAN Technologies Overview
  Explain WAN access technologies available to small to medium-sized business networks.
1.2 Selecting a WAN Technology
  Select WAN access technologies to satisfy business requirements.
Notes: 10

## Slide 11: 1.1 WAN Technologies Overview
Notes: Cisco Networking Academy Program
Connecting Networks
Chapter 1: WAN Concepts

## Slide 12: WAN Technologies Overview Purpose of WANs
WANs connect LANs
WANs are used to connect remote sites to the enterprise network.
WANs connect home users to the Internet.
Enterprise networks are using security and privacy solutions over the Internet to connect remote sites and users.
Notes: 1.1 – WAN Technologies Overview
1.1.1 – Purpose of WANs

## Slide 13: WAN Technologies Overview Purpose of WANs
Common WAN topologies are:
  Point-to-Point – Typically a dedicated leased-line connection such as T1/E1
  Hub-and-Spoke – A single-homed, point-to-multipoint topology where a single interface on the hub router can be shared with multiple spoke routers through the use of virtual interfaces
  Full Mesh – Each router has a connection to every other router; requires a large number of virtual interfaces
  Dual-homed – Provides redundancy for a single-homed, hub-and-spoke topology by providing a second hub to connect to spoke routers
Point-to-Point
Hub-and-Spoke
Full Mesh
Dual-Homed
Notes: 1.1 – WAN Technologies Overview
1.1.1 – Purpose of WANs

## Slide 14: WAN Technologies Overview Purpose of WANs
As businesses grow, the topologies and WAN strategies change:
  Small Office – These businesses typically consist of one LAN at one location that connects to the Internet through a broadband technology.
  Campus Network – A small- to medium-sized business with one location and multiple LANs uses specialized equipment and technologies to connect to the Internet.
  Branch Networks – As the business grows, it adds more branch offices, each with its own campus network. WAN contracts to connect the remote networks are negotiated.
  Distributed Network – A multinational business has a network distributed across the globe. These businesses have complex WAN strategies to securely connect to regional offices, branch offices, partners, and telecommuters.
Small Office
Campus Network
Distributed Network
Notes: 1.1 – WAN Technologies Overview
1.1.1 – Purpose of WANs

## Slide 15: WAN Technologies Overview WAN Operations
WAN operations focus primarily on the physical layer (OSI Layer 1) and the data link layer (OSI Layer 2).
  Layer 1 protocols describe how to provide electrical, mechanical, operational, and functional connections
  Layer 2 protocols define how data is encapsulated
WAN Terms include:
  Customer Premises Equipment (CPE) – owned by the business or leased from the service provider.
  Data Communications Equipment (DCE) – provides an interface to connect subscribers to a communication link on the WAN cloud.
  Data Terminal Equipment (DTE) – connects to the local loop through the DCE.
  Demarcation Point – separates customer equipment from service provider equipment and is the place where the responsibility for the connection changes from the user to the service provider.
  Local Loop – cable that connects the CPE to the CO of the service provider (last mile).
  Central Office (CO) – local service provider facility or building that connects the CPE to the provider network.
  Toll network – all the cabling and equipment inside the WAN provider network.
Notes: 1.1 – WAN Technologies Overview
1.1.2 – WAN Operations

## Slide 16: WAN Technologies Overview WAN Operations
WAN devices include:
  Dialup modem – legacy WAN technology that converts digital signals into voice frequencies to be transmitted over the analog lines of the public telephone network.
  Access server – legacy WAN technology that coordinates dial-in and dial-out user communications.
  Broadband modem – used with high-speed DSL or cable Internet service
  CSU/DSU – used to convert digital, leased-line signals into frames that the LAN can interpret and vice versa.
  WAN switch – multiport internetworking device used in service provider networks
  Router – provides internetworking and WAN access interface ports to connect to the service provider network
  Core router/Multilayer switch – resides within the backbone of the WAN, supports multiple interfaces, and forwards IP packets at full line speed
Notes: 1.1 – WAN Technologies Overview
1.1.2 – WAN Operations

## Slide 17: WAN Technologies Overview WAN Operations
WANs can operate as circuit-switched or packet-switched networks:
  Circuit-switched Networks – establish a dedicated circuit between source and destination before the users may communicate, such as making a telephone call
  Packet-Switched Networks – split traffic into packets that are routed over a shared network and do not require a dedicated circuit between source and destination
Circuit-Switched
Packet-Switched
Notes: 1.1 – WAN Technologies Overview
1.1.2 – WAN Operations

## Slide 18: 1.2 Selecting a WAN Technology
Notes: Cisco Networking Academy Program
Connecting Networks
Chapter 1: WAN Concepts

## Slide 19: Selecting a WAN Technology WAN Services
Two way that a business can get WAN access:
Private WAN Infrastructure
  The business negotiates for dedicated or switched WAN access with a service provider.
Public WAN Infrastructure
  WAN access is achieved through the Internet using broadband connections. VPNs secure the connections.
Notes: 1.2 – Selecting a WAN Technology
1.2.1 – WAN Services

## Slide 20: Selecting a WAN Technology WAN Services (cont.)
This topology illustrates some of these WAN access technologies.
Notes: 1.2 – Selecting a WAN Technology
1.2.1 – WAN Services

## Slide 21: Selecting a WAN Technology Private WAN Infrastructures
Advantages:
Simplicity
Quality
Availability
Disadvantages:
Cost
Limited flexibility
Dialup
Notes: 1.2 – Selecting a WAN Technology
1.2.2 – Private WAN Infrastructures

## Slide 22: Selecting a WAN Technology Private WAN Infrastructures (Cont.)
ISDN
ISDN BRI
ISDN PRI
Sample ISDN Topology
Notes: 1.2 – Selecting a WAN Technology
1.2.2 – Private WAN Infrastructures

## Slide 23: Selecting a WAN Technology Private WAN Infrastructures (Cont.)
Frame Relay
PVCs carry both voice and data traffic.
PVCs are uniquely identified by a data-link connection identifier (DLCI).
PVCs and DLCIs ensure bidirectional communication from one DTE device to another.
R1 uses DLCI 102 to reach R2 while R2 uses DLCI 201 to reach R1.
Notes: 1.2 – Selecting a WAN Technology
1.2.2 – Private WAN Infrastructures

## Slide 24: Selecting a WAN Technology Private WAN Infrastructures (Cont.)
ATM
Built on a cell-based architecture, rather than on a frame-based architecture. ATM cells are always a fixed length of 53 bytes.
Notes: 1.2 – Selecting a WAN Technology
1.2.2 – Private WAN Infrastructures

## Slide 25: Selecting a WAN Technology Private WAN Infrastructures (Cont.)
Ethernet WAN
Features and Benefits of Ethernet WAN include:
Reduced expenses and administration
Easy integration with existing networks
Enhanced business productivity
Service providers now offer Ethernet WAN service using fiber-optic cabling.
Known as Metropolitan Ethernet (MetroE), Ethernet over MPLS (EoMPLS), and Virtual Private LAN Service (VPLS).
Note: Commonly used to replace the traditional Frame Relay and ATM WAN links.
Notes: 1.2 – Selecting a WAN Technology
1.2.2 – Private WAN Infrastructures

## Slide 26: Selecting a WAN Technology Private WAN Infrastructures (Cont.)
MPLS
Multiprotocol Label Switching (MPLS) is a multiprotocol high-performance WAN technology that directs data from one router to the next, based on short path labels rather than IP network addresses.
Notes: 1.2 – Selecting a WAN Technology
1.2.2 – Private WAN Infrastructures

## Slide 27: Selecting a WAN Technology Private WAN Infrastructures (Cont.)
VSAT
Very small aperture terminal (VSAT) - a solution that creates a private WAN using satellite communications.
Notes: 1.2 – Selecting a WAN Technology
1.2.2 – Private WAN Infrastructures

## Slide 28: Selecting a WAN Technology Public WAN Infrastructures
DSL
Always-on connection technology that uses existing twisted-pair telephone lines to transport high-bandwidth data, and provides IP services to subscribers.
A DSL modem converts an Ethernet signal from the user device to a DSL signal, which is transmitted to the central office.
Notes: 1.2 – Selecting a WAN Technology
1.2.3 – Public WAN Infrastructures

## Slide 29: Selecting a WAN Technology Public WAN Infrastructures (Cont.)
Cable
Network access is available from some cable television networks.
Cable modems provide an always-on connection and a simple installation.
Notes: 1.2 – Selecting a WAN Technology
1.2.3 – Public WAN Infrastructures

## Slide 30: Selecting a WAN Technology Public WAN Infrastructures (Cont.)
Wireless
New developments in broadband wireless technology:
Municipal Wi-Fi – Many cities have begun setting up municipal wireless
WiMAX – Worldwide Interoperability for Microwave Access (WiMAX) is a new technology that is just beginning to come into use.
Satellite Internet - Typically used by rural users where cable and DSL are not available.
Notes: 1.2 – Selecting a WAN Technology
1.2.3 – Public WAN Infrastructures

## Slide 31: Selecting a WAN Technology Public WAN Infrastructures (Cont.)
3G/4G
Common cellular industry terms include:
3G/4G Wireless – Abbreviation for 3rd generation and 4th generation cellular access. These technologies support wireless Internet access.
Long-Term Evolution (LTE) – A newer and faster technology, considered to be part of the 4th generation (4G) technology.
Notes: 1.2 – Selecting a WAN Technology
1.2.3 – Public WAN Infrastructures

## Slide 32: Selecting a WAN Technology Public WAN Infrastructures (Cont.)
Public WANs rely on VPNs for securing data between private networks as it crosses a public network, such as the Internet.
Benefits:
  Cost savings
  Security
  Scalability
  Compatibility with broadband technology
Two types of VPN:
  Site-to-site VPNs
  Remote-access VPNs
Site-to-Site
Remote-Access
Notes: 1.2 – Selecting a WAN Technology
1.2.3 – Public WAN Infrastructures

## Slide 33: Selecting a WAN Technology Selecting WAN Services
Answer the following questions when choosing a WAN Connection:
Notes: 1.2 – Selecting a WAN Technology
1.2.3 – Public WAN Infrastructures

## Slide 34: 1.3 Summary
Notes: Cisco Networking Academy Program
Connecting Networks
Chapter 1: WAN Concepts

## Slide 35: Chapter Summary Summary
WAN access standards operate at Layers 1 and 2 of the OSI model.
Permanent, dedicated point-to-point connections are provided by using leased lines.
Private WAN connections include:
  Dialup
  ISDN
  Frame Relay
  ATM
  Metro Ethernet
  MPLS
  VSAT
Security over public infrastructure connections can be provided by using remote-access or site-to-site Virtual Private Networks (VPNs).
Public WAN connections include:
  DSL
  Cable
  Wireless
  Cellular
Notes: 3.6 – Chapter Summary
3.6.1 – Summary