## Slide 1: Chapter 18: VRF, MPLS, and MPLS Layer 3 VPNs
Instructor Materials
CCNP Enterprise: Advanced Routing

## Slide 2: Chapter 18 Content
This chapter covers the following content:
Implementing and Verifying VRF-Lite - This section introduces VRF and how to configure and verify a VRF-Lite implementation.
An Introduction to MPLS Operations - This section introduces MPLS and explores the main MPLS topics, such as LSRs, LDP, LSP, and label switching.
An Introduction to MPLS Layer 3 VPNs - This section introduces the concept of MPLS Layer 3 VPNs.

## Slide 3: Implementing and Verifying VRF-Lite
VRF is a technology for creating separate virtual routers on a single physical router.
VRF-Lite provides VRF without MPLS. Router interfaces, routing tables, and forwarding tables are isolated on an instance-by-instance basis and therefore prevent traffic from one VRF instance from interfering with another VRF instance.
VRF is an essential component of the MPLS L3VPN architecture and provides increased router functionality through segmentation in lieu of using multiple devices.
This section introduces you to VRF and demonstrates how you can configure and verify VRF-Lite in a Cisco network.

## Slide 4: Implementing and Verifying VRF-Lite VRF-Lite Overview
By default, all router interfaces, the routing table, and any forwarding tables are associated with the global VRF instance.
What you’ve been calling your routing table is actually the routing table of the global VRF instance.
If you need to divide your router up into multiple virtual routers, you can do so by creating additional VRF instances, which also creates additional routing and forwarding tables.
Consider this scenario: for security reasons, you need to build three different networks so that traffic in each network is isolated from traffic in the other networks. However, you only want to build a single physical network to accomplish this. You can do this by using VRF. Figure 18-1 shows a single physical topology that is divided into three different logically isolated networks.

## Slide 5: Implementing and Verifying VRF-Lite Creating and Verifying VRF Instances
Example 18-1 shows how the ip vrf vrf-name command is used on each of the routers to create the VRF instances.
To verify that the VRF instances are created, use the show ip vrf command as shown in Example 18-2 for R1. Notice that the Interfaces column is empty. You need to assign interfaces to each of the VRF instances to separate and isolate the traffic.

## Slide 6: Implementing and Verifying VRF-Lite Creating and Verifying VRF Instances (Cont.)
To assign an interface to a VRF, use the ip vrf forwarding vrf-name command in interface configuration mode, as shown in in Example 18-3.
Using the show ip vrf command again, you can verify that each interface has been assigned to the correct VRF instance, as shown in Example 18-4.

## Slide 7: Implementing and Verifying VRF-Lite Creating and Verifying VRF Instances (Cont.)
If a single physical interface supports multiple VRF instances, the physical interface needs to be broken into subinterfaces. Therefore, Gi3/0 needs to be broken into subinterfaces.
Example 18-5 shows how to create the subinterfaces and assign them to the correct VRF instances. It also shows the use of the show ip vrf command to verify that the interfaces are in the correct VRF instances.

## Slide 8: Implementing and Verifying VRF-Lite Creating and Verifying VRF Instances (Cont.)
Next, you can configure network addressing on R1. Example 18-6 shows the IP addressing configuration of each of the interfaces on R1, based on Figure 18-1.
Notice that the subinterfaces must be configured with dot1q encapsulation, or you can’t assign an IP address to the interface. Also, note that when you configure R2’s subinterfaces connecting to R1, they need to be configured with the same VLAN numbers.
You can use the show ip vrf interfaces command to verify the IP address assigned to the interface, the VRF instance the interface is in, and whether the interface is up or down.

## Slide 9: Implementing and Verifying VRF-Lite Creating and Verifying VRF Instances (Cont.)
As soon as you created the VRF instance with the ip vrf vrf-name command, the virtual routing table was created for the network. You can use the show ip route command to display the global routing table, as shown in Example 18-8.
To view the routing table for a VRF instance, use the show ip route vrf vrf-name command.

## Slide 10: Implementing and Verifying VRF-Lite Creating and Verifying VRF Instances (Cont.)
You can now configure R2. Example 18-10 shows the configuration required on R2.

## Slide 11: Implementing and Verifying VRF-Lite Creating and Verifying VRF Instances (Cont.)
Example 18-11 displays the output of the show ip vrf interfaces command and the show ip route vrf vrf_name commands to verify that R2 has been configured correctly.

## Slide 12: Implementing and Verifying VRF-Lite Creating and Verifying VRF Instances (Cont.)
Now you can configure R3. Example 18-12 shows the configuration required on R3.

## Slide 13: Implementing and Verifying VRF-Lite Creating and Verifying VRF Instances (Cont.)
Example 18-13 shows the output of the show ip vrf interfaces command and the show ip route vrf command to verify that R3 has been configured correctly.
Above is a partial image of Example 18-13

## Slide 14: Implementing and Verifying VRF-Lite Creating and Verifying VRF Instances (Cont.)
To verify connectivity when using VRF instances, you must specify the VRF instance with the ping command. If you do not, the global routing table is used instead of the VRF routing table.
Example 18-14 shows a series of pings from R1 to R2. The first ping, with a destination of 10.0.12.2, fails because the VRF instance was not specified; therefore, the global routing table is being used. The second ping specifies the GREEN VRF but is using an IP address in the RED VRF; therefore, the ping fails. The last ping uses the correct VRF (RED) and an IP address in the RED VRF (10.0.12.2); therefore, the ping is successful. This is a great example of how VRF instances provide isolation.

## Slide 15: Implementing and Verifying VRF-Lite Creating and Verifying VRF Instances (Cont.)
Example 18-15 shows the output of the RED VRF routing table. At this point, you have only directly connected and local routes. For all the routers to learn about all the other networks, you can use static or dynamic routing. The following examples use EIGRP as the dynamic routing protocol to provide full connectivity for each of the VRF instances.

## Slide 16: Implementing and Verifying VRF-Lite Creating and Verifying VRF Instances (Cont.)
To configure EIGRP for multiple VRF instances, you use EIGRP named configuration mode because it permits you to create multiple address families, as shown in Example 18-16.
Enter the EIGRP named configuration mode by using the router eigrp name command in global configuration mode.
Next, create an address family for each of the VRF instances. You accomplish this with the address-family ipv4 vrf vrf-name autonomous-system as-number command.
Then specify any EIGRP configuration commands that are needed for your scenario. In this case, you are enabling the routing process on only certain interfaces.

## Slide 17: Implementing and Verifying VRF-Lite Creating and Verifying VRF Instances (Cont.)
To verify that the interfaces are participating in the EIGRP process for the correct VRF instance, use the show ip eigrp vrf vrf-name interfaces command.

## Slide 18: Implementing and Verifying VRF-Lite Creating and Verifying VRF Instances (Cont.)
When all the other routers have been configured for EIGRP, you can verify neighbor adjacencies by using the show ip eigrp vrf vrf-name neighbors command. As before, because you are dealing with multiple VRF instances, you will notice that each show command in Example 18-18 displays only the neighbors that are within that VRF instance.
By using the ping vrf vrf-name ipv4-address command, as shown in Example 18-20, you can verify that connectivity exists from R1 to R3.

## Slide 19: An Introduction to MPLS Operations
Multiprotocol Label Switching (MPLS) is a packet-forwarding method that makes forwarding decisions based on labels instead of on the Layer 3 destination of the packet.
MPLS was designed to support many different Layer 3 protocols, but in this section we focus on IP only.
MPLS is not much faster than traditional IP routing.
MPLS decreases forwarding overhead on core routers, making them more efficient.
MPLS can forward other Layer 3 protocols besides IPv4, and MPLS supports multiple services, such as unicast routing, multicast routing, VPNs, Traffic Engineering (TE), QoS, and Any Transport Over MPLS (AToM). Therefore, MPLS is very efficient and flexible.

## Slide 20: An Introduction to MPLS Operations MPLS LIB and LFIB
In Figure 18-2, notice that the control plane of the MPLS-enabled router is responsible for exchanging labels with other MPLS-enabled routers, using a label distribution protocol in addition to exchanging routing information using routing protocols to populate the IP routing table (RIB).
After labels have been exchanged, the label information is used to populate the LIB, and then the best label information can be used to populate the Forwarding Information Base (FIB) so unlabeled packets can be labeled and the LFIB labeled packets can be forwarded, or labels can be removed when packets need to be forwarded by the FIB.

## Slide 21: An Introduction to MPLS Operations Label Switching Routers
Examine Figure 18-3. Routers R1 through R5 are part of the MPLS domain. They are known as label switching routers (LSRs) because they support MPLS. They understand MPLS labels and can receive and transmit labeled packets on their interfaces.
In this case, R1 and R5 are considered edge LSRs, and R2, R3, and R4 are considered intermediate LSRs. An edge LSR sits at the edge of the MPLS domain and adds labels to packets that are entering the MPLS domain (known as an ingress LSR), removes labels from packets that will be leaving the MPLS domain (known as an egress LSR), and even forwards packets as needed based on labels or the lack of a label. An intermediate LSR sits within the MPLS domain and primarily forwards packets using label information.

## Slide 22: An Introduction to MPLS Operations Label-Switched Path
The label-switched path (LSP) is the cumulative labeled path (sequence of routers) that a labeled packet takes through the MPLS domain.
It is a unidirectional path, as shown in Figure 18-4; therefore, in a complex network with multiple potential paths between source and destination, it is possible that the LSP from source to destination could be different from the LSP that is used for the return traffic.
Typically the same path in reverse is used for the return traffic because of the underlying dynamic routing protocols, such as OSPF and EIGRP, that are used to build the symmetrical network and its forwarding paths.
In this case, the LSP from R1 to 10.0.0.0/24 uses labels 87, 11, 65, and 23. Along the path, each router examines the label to make a forwarding decision, removes the label, adds a new label if required, and then forwards the packet.

## Slide 23: An Introduction to MPLS Operations Labels
For MPLS to work, a label needs to be added to the packet. The label is added as a shim header between the Layer 2 frame header and the Layer 3 packet header. Figure 18-5 shows the placement of the MPLS label shim header. The label is 4 bytes (32 bits) in size and contains four different fields, as shown in Figure 18-6.
MPLS-enabled routers automatically assign labels to every network that they know about. How does a router know about a network? It can be locally configured by configuring an IP address on a router interface and issuing the no shutdown command on the interface, or through the propagation of routing information with dynamic routing protocols such as OSPF and EIGRP.

## Slide 24: An Introduction to MPLS Operations Label Distribution Protocol
In order to build the LSP, labels need to be shared/distributed with directly connected LSRs. This is done using a label distribution protocol such as Label Distribution Protocol (LDP), which is the most common protocol in use when sharing/distributing labels for IPv4 prefixes.
When MPLS has been enabled on an interface, LDP hello packets are sent out the interface to the destination multicast address 224.0.0.2 (the all routers multicast address), using UDP port 646. Any device on that same link that is also enabled for MPLS and that receives the hello packet forms an LDP TCP session using port 646 with the neighboring device so that label information can be exchanged.
Within the hello packet is an LDP ID that is used to uniquely identify the neighbor and the label space, which will either be per platform (same label used out all interfaces for a single destination) or per interface (different label used out each interface for a single network).
When establishing the LDP TCP session between two LSRs, one of the routers needs to be the active router. The active router is responsible for setting up the TCP session. The router with the higher LDP ID is selected as the active router and sets up the TCP session between the two routers.

## Slide 25: An Introduction to MPLS Operations Label Distribution Protocol (Cont.)
Figure 18-8 shows how R1 distributes its label of 19 for network 10.0.0.0/24 out all MPLS-enabled interfaces. R2 distributes its label of 87 for network 10.0.0.0/24 out all MPLS-enabled interfaces. R3 distributes its label of 11 for network 10.0.0.0/24 out all MPLS-enabled interfaces. R4 distributes its label of 65 for network 10.0.0.0/24 out all MPLS-enabled interfaces. And R5 distributes its label of 23 for network 10.0.0.0/24 out all MPLS-enabled interfaces after the TCP sessions have been established.

## Slide 26: An Introduction to MPLS Operations Penultimate Hop Popping
Review Figure 18-9 and pay close attention to R5. R5 must do two lookups when it receives a labeled packet destined to 10.0.0.0/24. First, it must look in the LFIB because it received a labeled frame. In this case, there is no label out. Therefore, it must remove the label and make a forwarding decision based on a second lookup, using the FIB to forward the packet. This is not efficient. The solution to this inefficiency is penultimate hop popping (PHP). With PHP, R4 pops the label before sending the packet to R5. IP address in network 10.0.0.0/24. In Figure 18-10, R5 has advertised the label “pop” to R4, and R4 has populated its LFIB accordingly.

## Slide 27: An Introduction to MPLS Layer 3 VPNs
MPLS Layer 3 VPNs provide peer-to-peer connectivity between private customer sites across a shared network.
The MPLS domain is referred to as the P-network, and the customer sites are referred to as the C-network.
This section explores how you can use MPLS Layer 3 VPNs to connect your private networks over your provider’s public network.

## Slide 28: An Introduction to MPLS Layer 3 VPNs MPLS Domain Connecting Customer Sites Together Example
Figure 18-11 shows a provider (such as an ISP) MPLS domain, with Customer A and Customer B both using the same MPLS domain to connect their own private sites together.

## Slide 29: An Introduction to MPLS Layer 3 VPNs MPLS Domain Connecting Customer Sites Together Example (Cont.)
The CE (customer edge) routers connect to the PE (provider edge) routers of the MPLS domain. The PE routers, PE_R1 and PE_R5 in Figure 18-11, are the ingress and egress LSRs for the MPLS domain.
The P (provider) routers, such as P_R2, P_R3, and P_R4 in Figure 18-11, are the intermediate LSRs of the MPLS domain.
The goal is to have Customer A Site 1 and Customer A Site 2 exchange their local routing information over the MPLS domain and then forward traffic as needed from Site 1 and Site 2 over the MPLS domain. The same would be true for Customer B Site 1 and Customer B Site 2.
Due to the nature of the MPLS Layer 3 VPN, overlapping address spaces between customers is of no concern. Therefore, Customer A and Customer B can be using the same private IP address space.

## Slide 30: An Introduction to MPLS Layer 3 VPNs MPLS Domain Connecting Customer Sites Together Example (Cont.)
In order to support multiple customers, the PE routers need to use VRF instances, as shown in Figure 18-12, to isolate customer information and traffic from other customers.
A different VRF instance needs to be created for each customer, and the interface that connects to the customer’s CE router needs to be associated with the VRF.
The CE router and the PE router exchange IPv4 routes using a routing protocol such as RIP (Routing Information Protocol), EIGRP (Enhanced Interior Gateway Routing Protocol), OSPF (Open Shortest Path First), or BGP (Border Gateway Protocol), and the routes are placed in the customer-specific VRF table on the PE router.
From the customer’s perspective, the PE router is simply another router in the customer’s network, but it is under the control of the provider. However, note that all P routers are hidden from the customer.

## Slide 31: An Introduction to MPLS Layer 3 VPNs MPLS Domain Connecting Customer Sites Together Example (Cont.)
After the PE routers learn routes from the CE routers, the PE routers redistribute the routes into Multiprotocol-Interior Border Gateway Protocol (MP-BGP) so they can be exchanged with other PE routers.
When another PE router receives the routes, they are redistributed into an IGP and placed in the correct customer VRF instance so they can be exchanged with the CE router, as shown in Figure 18-13.
The P routers are not participating in BGP. Only the PE routers are. They are forming an MP-IBGP neighbor relationship with each other and exchanging the routes using the underlying network that is built with an Interior Gateway Protocol (IGP) such as OSPF or Intermediate System-to-Intermediate System (IS-IS).
The PE routers and the P routers are using a dynamic routing protocol to learn about all the destinations in the P network, and only the PE routers are using MP-IBGP on top of that to exchange the customer routes.

## Slide 32: An Introduction to MPLS Layer 3 VPNs MPLS Layer 3 VPNv4 Address
If all customer routes are being redistributed into MP-BGP, BGP handles identical network prefixes that belong to different customers by using a route distinguisher (RD) to expand the customer’s IP prefix so that it includes a unique value that distinguishes it from the other identical prefixes.
The RD is generated and used by the PE routers on a per-customer VRF instance basis. The RD is used regardless of whether there are overlapping address spaces.
The unique 64-bit RD is prepended to the 32-bit customer prefix (IPv4 route) to create a 96-bit unique prefix called a VPNv4 address, as shown in Figure 18-14. This VPNv4 address is exchanged by the MP-IBGP neighboring routers.

## Slide 33: An Introduction to MPLS Layer 3 VPNs PE Routers Exchanging VPNv4 Routes
The following steps occur:
Step 1. The CE router and PE router exchange routes using a dynamic routing protocol such as OSPF or EIGRP.
Step 2. The PE router places the customer-specific routes in the customer-specific VRF table.
Step 3. The routes in the customer’s VRF table are redistributed into MP-BGP as VPNv4 routes.
Step 4. The PE routers exchange VPNv4 routes over their MP-IBGP peering.
Step 5. The PE router redistributes the VPNv4 routes as OSPF, EIGRP, and other types of routes into the customer-specific VRF table.
Step 6. The PE router and CE router exchange routes using a dynamic routing protocol such as OSPF or EIGRP.

## Slide 34: An Introduction to MPLS Layer 3 VPNs MPLS Layer 3 VPN Label Stack
For the MPLS domain to forward traffic, a label stack is required. Specifically, two labels are required for traffic to be successfully forwarded through the MPLS domain. The first label that is attached to the packet is a VPN label, and the second label that is attached is the LDP label, as shown in Figure 18-16.
When the IP packet arrives at the ingress PE router, the PE router attaches both labels.
The egress router uses the VPN label to determine customer specifics about the packet and what should be done with it.
The LDP label is used for label switching from PE to PE in the MPLS domain.
VPN labels are learned from PE routers over the MP-IBGP peering, and the LDP labels are learned using the methods we explored in the “An Introduction to MPLS Operations” section of this chapter.

## Slide 35: An Introduction to MPLS Layer 3 VPNs VPN Label Assignment
When PE_R5 learns of 10.0.2.0/24 from CE_RB, it places it in the Customer B VRF instance. It then redistributes it into MP-BGP and thus creates a VPNv4 route of 1:110:10.0.2.0/24. This VPNv4 route needs a VPN label created for it so that forwarding will be successful. In this case, PE_R5 assigns it the label 35. This label is shared with PE_R1 over the MP-IBGP peering they have. Any time PE_R1 receives an IP packet that is destined for 10.0.2.0/24, it knows to attach the label 35 so the packet can be forwarded. However, this label is known only by the PE routers. Therefore, if PE_R1 forwards this VPN packet to P_R2, it will be dropped because it has no idea what the VPN label 35 means. Therefore, the LDP label is needed to forward the packet from PE_R1 and PE_R5.

## Slide 36: An Introduction to MPLS Layer 3 VPNs Label Switched Path
Figure 18-18 shows how LDP is used to exchange labels that have been generated by the PE routers (ingress and egress LSRs) and the P routers (intermediate LSRs). PE_R5 tells P_R4 to pop the label. P_R4 tells P_R3 to use the label 52. P_R3 tells P_R2 to use the label 10. P_R2 tells PE_R1 to use the label 99.
In Figure 18-19, the complete LSP is now ready to label switch the VPN packet from PE_R1 to PE_R5.

## Slide 37: An Introduction to MPLS Layer 3 VPNs Label Switched Path (Cont.)
When an IP packet destined to 10.0.2.0/24 arrives at PE_R1 from CE_RA, PE_R1 determines that the packet needs a VPN label of 35. Now, PE_R5 will know what to do with the VPN packet and an LDP label of 99 so that the VPN packet can be label switched through the MPLS domain. When the label stack is complete, PE_R1 sends the labelstacked packet to P_R2. When P_R2 receives it, it only examines the LDP label. Based on the LFIB, it states that the label 99 needs to be swapped to 10 and forwarded to P_R3. When P_R3 receives it, it only examines the LDP label. Based on the LFIB, it states that the label 10 needs to be swapped to 52 and
forwarded to P_R4. When P_R4 receives it, it only examines the LDP label.
Based on the LFIB, it states that the label 52 needs to be popped and forwarded to P_R5. Now PE_R5 only needs to read the VPN label, which is 35. Based on the scenario, the label is removed, and the VRF instance for Customer B is used to forward the IP packet to the CE_RB router.

## Slide 38: Prepare for the Exam

## Slide 39: Prepare for the Exam Key Topics for Chapter 18
Description
The purpose of VRF
Configuring VRF on R1 with the ip vrf command
Assigning interfaces to the VRF instances with the ip vrf forwarding command
Creating subinterfaces on R1 and assigning them to the correct VRF instances
Verifying the interface IP address, VRF, and protocol configurations
Verifying the VRF routing tables

## Slide 40: Prepare for the Exam Key Topics for Chapter 18 (Cont.)
Description | 
MPLS LIB and LFIB | The benefit of PHP
Label switching routers | MPLS Layer 3 VPNs
Label-switched path | The Layer 3 VPNv4 address and route distinguishers
Labels | How routes are learned by CE routers over an MPLS Layer 3 VPN
Label Distribution Protocol | MPLS Layer 3 VPN label stack

## Slide 41: Prepare for the Exam Key Terms for Chapter 18
Term |  | 
VRF | intermediate LSR | MPLS Layer 3 VPN
VRF-Lite | egress LSR | P-network
MPLS | ingress LSR | C-network
LIB | LSP | CE router
LFIB | LDP | PE router
RIB | Label | P router
FIB | LDP label | VPNv4 address
LSR | VPN label | label stack
edge LSR | PHP | 

## Slide 42: Prepare for the Exam Command Reference for Chapter 18
Task | Command Syntax
Define a VRF instance and enter VRF configuration mode for the instance (in global configuration mode) | ip vrf vrf-name
Associate an interface or a subinterface with a VRF instance (in interface configuration mode) | ip vrf forwarding vrf-name
Display configured VRF instances and associated router interfaces | show ip vrf
Display the routes in the global routing table | show ip route
Display the routes in the routing table for the VRF specified in the command | show ip route vrf vrf-name
Display all VRF-enabled interfaces on the router, including their IP addresses and whether the protocol is up or down | show ip vrf interfaces
Test IP connectivity for a specific VRF | ping vrf vrf-name ipv4-address