## Slide 1: Chapter 21: Troubleshooting ACLs and Prefix Lists
Instructor Materials
CCNP Enterprise: Advanced Routing

## Slide 2: Chapter 21 Content
This chapter covers the following content:
Troubleshooting IPv4 ACLs - This section examines how to read IPv4 ACLs so that
you are more efficient at troubleshooting IPv4 ACL-related issues. It also shows the
commands and processes you use for troubleshooting IPv4 packet filtering with standard, extended, and time-based IPv4 ACLs.
Troubleshooting IPv6 ACLs - This section examines how to read IPv6 ACLs so that
you are more efficient at troubleshooting IPv6 ACL-related issues. It also shows the
commands and processes that you can use for troubleshooting IPv6 packet filtering.
Troubleshooting Prefix Lists - This section reviews how to efficiently examine a prefix
list for troubleshooting purposes so that when you are dealing with an issue that has a
prefix list associated with it, you can determine whether the prefix list is or is not the
problem.
Trouble Tickets - This section provides trouble tickets that demonstrate how to use a
structured troubleshooting process to solve a reported problem.

## Slide 3: Troubleshooting IPv4 ACLs
The purpose of an access control list is to identify traffic based on different criteria, such as source or destination IP address, source or destination port number, transport layer protocol, and quality of service (QoS) markings.
IPv4 ACLS can be used to identify the private IP addresses that will be translated to a public address with Network Address Translation (NAT) and Port Address Translation (PAT). They can also be used to control which routes will be redistributed, which packets will be subject to policy-based routing, and which packets will be permitted or denied through the router.
This section explains how to troubleshoot an IPv4 ACL to make sure it is correctly created for the purpose it is intended. The section also provides examples related to packet filtering.

## Slide 4: Troubleshooting IPv4 ACLs Reading an IPv4 ACL
Being able to read an ACL and understand what it’s created for is important for troubleshooting. Following this list of steps that IPv4 ACLs use to help you identify why an IPv4 ACL is behaving the way it is:
  Step 1. Top-down processing - An ACL is made up of various entries. These entries are processed from the top of the ACL to the bottom of the ACL, in order.
  Step 2. Immediate execution upon a match - The very first entry that matches the values in the packet that are being compared is the entry that is used. This may be a permit entry or a deny entry, and it dictates how the packet is treated based on the ACL implementation. It doesn’t matter if there is another entry later in the ACL that matches; only the first entry that matches matters.
  Step 3. Implicit deny any - If there is no matching entry for the packet, the packet is automatically denied based on the invisible implicit deny any entry at the end of an ACL.

## Slide 5: Troubleshooting IPv4 ACLs Standard Numbered and Extended Numbered ACLs
Example 21-1 shows a sample ACL with standard numbering that uses only source IPv4 addresses. In this example, the ACL is numbered 1 and has four entries. The entries are listed from most specific to least specific.
Example 21-2 provides a sample extended numbered ACL. In this example, it is numbered 100. It has four entries, listed from most specific to least specific.

## Slide 6: Troubleshooting IPv4 ACLs Using an IPv4 ACL for Filtering
Using an ACL for packet filtering requires you to apply the ACL to an interface. Use the ip access-group {acl_number | acl_name} {in | out} command in interface configuration mode, as shown in Example 21-3. The direction in which you apply the ACL on an interface is significant. Verify the ACLs that are applied to an interface by using the show ip interface interface_type interface_number command. Example 21-3 shows how access list 1is applied inbound on GigabitEthernet0/0 and access list 100 is applied outbound on Gig0/0.

## Slide 7: Troubleshooting IPv4 ACLs Using a Time-Based IPv4 ACL
Perhaps you want to allow traffic to the internet during open hours, but deny it after hours. To accomplish this, use time-based ACLs. Example 21-4 provides a sample time-based ACL. Notice that the ACL entry with sequence number 10 has the time-range option. The time range is based on values configured in the AFTERHOURS time range.
Example 21-5 shows the AFTERHOURS time range with the show time-range AFTERHOURS command. It has two weekdays entries, one from 5 p.m. to midnight and the other from midnight to 9 a.m. It also has a weekend entry that covers all day and all night. It also states that it is active and used in an ACL.
A time-based ACL is based on the device’s clock. If the clock is not correct, the time-based ACL may be active or inactive at the wrong time. Example 21-6 shows how you can verify the current time on a router by using the show clock command.

## Slide 8: Troubleshooting IPv6 ACLs
IPv6 ACLs allow you to classify traffic for different reasons. For example, you might need to classify traffic that will be subject to policy-based routing, or you might need to classify the traffic that will be filtered as it passes through the router.
IPv6 traffic filtering can be done on an interface-by-interface basis with IPv6 access lists.
This section explains how to read IPv6 access lists so that you can troubleshoot them efficiently and identify whether they have been correctly applied to an interface for filtering purposes.

## Slide 9: Troubleshooting IPv6 ACLs Reading an IPv6 ACL
Being able to read an IPv6 ACL and understand what it is created for is important for troubleshooting. IPv6 ACLS have four steps and steps 1, 2 and 4 are the same as steps 1, 2, and 3 for IPv4 ACLS.
For IPv6 ACLS, Step 3 is Implicit permit icmp nd: If the packet is an NA or NS message, permit it.
IPv6 relies on the Neighbor Discovery Protocol (NDP) NA (neighbor advertisement) and NS (neighbor solicitation) messages to determine the MAC address associated with an IPv6 address. Therefore, the implicit permit icmp nd entries for NA and NS messages have been added before the implicit deny any, so they are not denied:
    permit icmp any any nd-na
    permit icmp any any nd-ns
  Because these are implicit permit statements, all statically entered commands come before them. If you issue the deny ipv6 any any log command at the end of an IPv6 ACL, you will break the NDP process because NA and NS messages will be denied.

## Slide 10: Troubleshooting IPv6 ACLs Sample IPv6 ACL
With IPv6, you have just one type of ACL which is similar to an IPv4 extended ACL. Within an IPv6 ACL entry, you provide as little or as much information as you need to accomplish your goal.
Example 21-7 provides a sample IPv6 ACL that was created on R1. The IPv6 access list is named ENARSI, and you read it exactly as you read an IPv4 ACL.
Notice that there are no wildcard masks with IPv6. Instead, you specify a prefix, as shown in sequences 40 and 50 in Example 21-7, which accomplishes the same goal as the wildcard mask (defining a range of addresses).

## Slide 11: Troubleshooting IPv6 ACLs Using an IPv6 ACL for Filtering
To use an IPv6 ACL for packet filtering, you need to apply the IPv6 ACL to an interface.
Use the ipv6 traffic-filter acl_name {in | out} command in interface configuration mode. The direction in which you apply the IPv6 ACL on an interface is significant.
Verify the IPv6 ACLs that are applied to an interface by using the show ipv6 interface interface_type interface_number command.
Example 21-8 shows the IPv6 ACL named ENARSI is applied inbound on interface Gig0/0.

## Slide 12: Troubleshooting Prefix Lists
ACLs do not give you granular control when matching routes for route filtering. Prefix lists allow you to define the route and prefix that you want to match. This section explains how to read a prefix list so that when you are troubleshooting features that call upon a prefix list, you will have the ability to eliminate the prefix list as the cause of the issue or prove that the prefix list is the cause of the issue.
All the examples in this section are based on IPv4, but the content applies to both IPv4 prefix lists and IPv6 prefix lists.

## Slide 13: Troubleshooting Prefix Lists Reading a Prefix List
Example 21-9 shows the commands used to create a sample prefix list called ENARSI and the output of show ip prefix-list, which you can use to verify the IPv4 prefix lists configured on a router.
To verify IPv6 prefix lists, you use the command show ipv6 prefix-list.

## Slide 14: Troubleshooting Prefix Lists Reading a Prefix List (Cont.)
There are two different ways to read a prefix list entry, depending on whether there is an le (less than or equal to) or ge (greater than or equal to) at the end of the prefix list entry:
No ge or le - If the entry does not contain a ge or le, the prefix is treated as an address and a subnet mask. Refer to the entry with sequence number 10 in Example 21-9. There is no ge or le; therefore, the network 10.1.1.0/26 is matched exactly.
There is a ge or le - If the entry does contain a ge or le, the prefix is treated as an address and a wildcard mask. Refer to the entry with sequence number 20 in Example 21-9. Because there is a ge or le, the entry is defining a range of values.

## Slide 15: Troubleshooting Prefix Lists Prefix List Processing
The following is a list of steps that prefix lists use to help you identify why a prefix list is behaving the way it is:
Step 1. Top-down processing - A prefix list is made up of various sequences; these sequences are processed from the top of the prefix list to the bottom of the prefix list, in order of sequence number.
Step 2. Immediate execution upon a match - The very first sequence that matches is the sequence that is used. This may be a permit sequence or a deny sequence, and it dictates how the information is treated. It doesn’t matter if there is another sequence later in the prefix list that matches. Only the first sequence that matches matters.
Step 3. Implicit deny any - If there is no matching sequence, the information is automatically denied based on the invisible implicit deny any entry at the end of a prefix list.
Because there is an implicit deny any at the end of a prefix list, you need at least one permit sequence in a prefix list, or everything will be denied. To permit everything that does not match a prefix list sequence, you need to include an entry that does so.
  IPv4: ip prefix-list NAME seq 30 permit 0.0.0.0/0 le 32
  IPv6: ipv6 prefix-list NAME seq 30 permit ::/0 le 128

## Slide 16: Trouble Tickets
This section presents various trouble tickets relating to the topics discussed in this chapter. The purpose of these trouble tickets is to show a process that you can follow when troubleshooting in the real world or in an exam environment.

## Slide 17: Trouble Tickets Trouble Ticket 21-1: IPv4 ACL
Problem: A user at PC1 (see Figure 21-1) has indicated that he cannot Telnet to 192.0.2.1, and he needs to. However, he can ping 192.0.2.1 and access web-enabled resources.
Refer to your text for next steps and examples to troubleshoot and resolve this trouble ticket.

## Slide 18: Trouble Tickets Trouble Ticket 21-2: IPv6 ACL
Problem: A user at PC2 (see Figure 21-2) has indicated that she is not able to Telnet to 2001:db8:a:b::7, and she requires Telnet access. However, she can ping 2001:db8:a:b::7 and receive DHCP-related information from the DHCP server.
Refer to your text for next steps and examples to troubleshoot and resolve this trouble ticket.

## Slide 19: Trouble Tickets Trouble Ticket 21-3: Prefix List
Problem: Your junior admin has contacted you indicating that R1 (see Figure 21-3) is not
learning any routes from Enhanced Interior Gateway Routing Protocol (EIGRP). The admin has confirmed that neighbor relationships are being formed, interfaces are participating in the routing process, and other routers are learning about the routes. The admin has come to you for help. With your extensive knowledge, you ask your junior admin if he checked for any route filters. He says no.
Refer to your text for next steps and examples to troubleshoot and resolve this trouble ticket.

## Slide 20: Prepare for the Exam

## Slide 21: Prepare for the Exam Key Topics for Chapter 21
Description | 
The IPv4 ACL order of operations | Sample IPv6 ACL
Reading an IPv4 standard ACL | Verifying IPv6 access lists applied to interfaces
Reading an IPv4 extended ACL | Reading a prefix list
Verifying access lists applied to interfaces | The prefix list order of operations
Sample time-based ACL | Reading an IPv4 standard ACL
The IPv6 ACL order of operations | 

## Slide 22: Prepare for the Exam Key Terms for Chapter 21
Term | 
standard ACL | implicit deny
extended ACL | implicit permit
named ACL | prefix list
time-based ACL | ge
IPv6 ACL | le

## Slide 23: Prepare for the Exam Command Reference for Chapter 21
Task | Command Syntax
Display all the access lists configured on the device | show access-lists
Display all the IPv4 access lists configured on the devices | show ip access-lists
Display all the IPv6 access lists configured on the devices | show ipv6 access-list
Display the inbound and outbound IPv4 access lists applied to an interface | show ip interface interface_type interface_number
Display the inbound and outbound IPv6 access lists applied to an interface | show ipv6 interface interface_type interface_number
Display any time ranges that have been configured on the device | show time-range
Display the date and time on the device | show clock