## Slide 1: Chapter 14: Troubleshooting BGP
Instructor Materials
CCNP Enterprise: Advanced Routing

## Slide 2: Chapter 14 Content
This chapter covers the following content:
Troubleshooting BGP Neighbor Adjacencies - This section examines issues that may prevent a BGP neighbor relationship from forming and how to recognize and troubleshoot these issues. This section focuses primarily on IPv4 unicast BGP, the same issues arise with IPv6 unicast BGP.
Troubleshooting BGP Routes - This section focuses on issues that may prevent BGP routes from being learned or advertised and how to recognize and troubleshoot these issues. This section focuses mostly on IPv4 unicast BGP, the same issues arise with IPv6 unicast BGP routes as well.
Troubleshooting BGP Path Selection - This section explains how BGP determines the best path to reach a destination network and the importance of understanding how this process works for troubleshooting purposes.
Troubleshooting BGP for IPv6 - This section discusses the methods used to successfully troubleshoot additional issues related to BGP for IPv6 that are not seen with BGP for IPv4.
BGP Trouble Tickets - This section presents trouble tickets that demonstrate how to use a structured troubleshooting process to solve a reported problem.
MP-BGP Trouble Tickets - This section presents a trouble ticket that demonstrates how to use a structured troubleshooting process to solve a reported problem.

## Slide 3: Troubleshooting BGP Neighbor Adjacencies
With BGP, you need to establish neighbor adjacencies manually, unlike EIGRP and OSPF, where the neighbor adjacencies form dynamically.
BGP configurations are prone to human error, which means a greater effort is often needed during troubleshooting.
There are two flavors of BGP: Internal BGP (iBGP) and External BGP (eBGP). Understanding the differences between the two and the issues relating to each of them is important for troubleshooting.

## Slide 4: Troubleshooting BGP Neighbor Adjacencies Verifying IPv4 Unicast BGP Neighbors
To verify IPv4 unicast BGP neighbors, you can use two show commands: show bgp ipv4 unicast summary and show bgp ipv4 unicast neighbors.
For initial verification of neighbors, use show bgp ipv4 unicast summary because it provides condensed output.
Example 14-1 shows sample output of the show bgp ipv4 unicast summary command, which indicates that R1 has two BGP neighbors: 10.1.12.2 and 10.1.13.3.
Focus your attention on the State/PfxRcd column. If there is a number in this column (as there is in Example 14-1), it means you have successfully established a BGP neighbor relationship. If you see Idle or Active, there is a problem in the formation of the neighbor relationship.

## Slide 5: Troubleshooting BGP Neighbor Adjacencies Verifying IPv4 Unicast BGP Neighbors (Cont.)
The following are some of the reasons a BGP neighbor relationship might not form:
Interface is down - The interface must be up/up.
Layer 3 connectivity is broken - You need to be able to reach the IP address you are trying to form the adjacency with.
Path to the neighbor is through the default route - You must be able to reach the neighbor using a route other than the default route.
Neighbor does not have a route to the local router - The two routers forming a BGP peering must have routes to each other.
Incorrect neighbor statement - The IP address and ASN in the neighbor ip_address remote-as as_number statement must be accurate.
ACLs - An access control list (ACL) or a firewall may be blocking TCP (Transmission Control Protocol) port 179.
BGP packets sourced from the wrong IP address - The source IP (Internet Protocol) address of an inbound BGP packet must match the local neighbor statement.

## Slide 6: Troubleshooting BGP Neighbor Adjacencies Verifying IPv4 Unicast BGP Neighbors (Cont.)
The TTL (time-to-live) of the BGP packet expires - The peer may be further away than is permitted.
Mismatched authentication - The two routers must agree on the authentication parameters.
Misconfigured peer group - Peer groups simplify repetitive BGP configurations; however, if not carefully implemented, they can prevent neighbor relationships from forming or routes from being learned.
Timers - Timers do not have to match; however, if the minimum holddown from neighbor option is set, it could prevent a neighbor adjacency.
When troubleshooting BGP neighbor adjacencies, you need to be able to identify these issues and understand why they occur.

## Slide 7: Troubleshooting BGP Neighbor Adjacencies Interface is Down or No Layer 3 Connectivity
Interface is Down - The physical or logical interface with the IP address that is being used to form BGP neighbor relationships must be up/up. Use show ip interface brief to verify the status of the interface.
Layer 3 Connectivity is Broken – BGP neighbors do not have to be directly connected or in the same subnet to form a neighbor relationship, but you do need to have Layer 3 connectivity. Use the ping command in order to determine if you have Layer 3 connectivity. When reviewing the output of show bgp ipv4 unicast summary in Example 14-2, notice that the State/PfxRcd field says Idle. This state occurs when the local router is not able to make a TCP connection with the neighbor.

## Slide 8: Troubleshooting BGP Neighbor Adjacencies Path to the Neighbor is Through Default Route
When a ping is successful, but no specific route to the neighbor exists in the routing table, the ping may have used the default route to reach the neighbor. Even though you can reach the neighbor using the default route, BGP does not consider a default route valid for forming an adjacency. In the output of show bgp ipv4 unicast summary on R5 in Example 14-6, notice that the state is idle, which indicates that a TCP session cannot be formed.

## Slide 9: Troubleshooting BGP Neighbor Adjacencies Neighbor Does Not Have a Route to Local Router
The local router displays the state Idle when it does not have a route to the IP address it is trying to peer with. However, Idle also appears on a router when the neighbor does not have a route back to the local router.
In Example 14-7, you can see that R2, which is trying to form a BGP peering with R5, also displays the state Idle even though it has a route to 5.5.5.5. The Idle state appears because the routers cannot form the TCP session.

## Slide 10: Troubleshooting BGP Neighbor Adjacencies Incorrect Neighbor Statement
To form a BGP peering, you use the neighbor ip_address remote-as as_number command in BGP configuration mode. Example 14-8 displays two neighbor remote-as commands on R2. The neighbor 5.5.5.5 remote-as 65502 command forms an iBGP peering, and neighbor 10.1.12.1 remote-as 65501 forms an eBGP peering.
There are two very important parts to this command: the address of the peer with which you form the peering and the autonomous system that the peer is in. If you make a mistake with either of these, you see either the Active or Idle state. You can verify the state of the TCP session on the routers by using the show tcp brief all command, shown in Example 14-9.

## Slide 11: Troubleshooting BGP Neighbor Adjacencies BGP Packets Sourced from Wrong IP Address
In a redundant topology, a BGP router has multiple active IP addresses configured across its various interfaces. Figure 14-1 shows two BGP autonomous systems. Notice that R2, R3, and R4 could form a BGP peering with each other, using any physical interface, because of the multiple paths.
When you issue the neighbor ip_address remote-as as_number command on a router, the address specified is used by the router to determine whether the BGP open message came from a router it should establish a BGP peering with. The BGP open message has a source IP address, and the source IP address is compared with the address in the local neighbor ip_address remote-as as_number command. If they match, a BGP peering is formed; if not, no BGP peering is formed. By default, the source address is based on the exit interface of the router sending the BGP open message.

## Slide 12: Troubleshooting BGP Neighbor Adjacencies BGP Packets Sourced from Wrong IP Address (Cont.)
To control the IP address that is used when sending BGP messages, you use the neighbor ip_address update-source interface_type interface_number command.
Example 14-10 shows the output of show run | section router bgp on R2.
Example 14-11 shows the appropriate configuration on R4 to ensure that a BGP peering is successful.

## Slide 13: Troubleshooting BGP Neighbor Adjacencies ACLs
BGP uses TCP port 179 to establish TCP sessions. If an access control list (ACL) is blocking TCP port 179 anywhere in the path between the routers attempting to form a BGP peering, the peering does not happen.
At the bottom of Example 14-12, the state is Idle on R5 because the TCP session cannot be established with the neighbor at 2.2.2.2 because R4 is denying TCP traffic related to port 179.

## Slide 14: Troubleshooting BGP Neighbor Adjacencies ACLs (Cont.)
BGP sessions are server/client relationships. One router is using port 179 (server), and the other router is using an ephemeral port (client). By default, both routers try to establish a TCP session using the three-way handshake because both routers send a TCP syn packet sourced from an ephemeral port and destined to port 179. When both routers respond with an ACK to the request on port 179, two BGP sessions are created. This situation is called a BGP connection collision and the router with the higher BGP RID becomes the server.
To avoid BGP connection collisions, control the server and client roles right from the start by using the neighbor ip_address transport connection-mode {active | passive} command. In this command, active means client, passive means server.
In Example 14-13, the command show bgp ipv4 unicast neighbors | i ^BGP neighbor|Local port|Foreign port is used to display R2’s neighbors along with the local port number and the foreign port number.

## Slide 15: Troubleshooting BGP Neighbor Adjacencies The TTL of the BGP Packet Expires
By default, an eBGP peering occurs between directly connected routers. With an iBGP peering, the routers can be up to 255 router hops from each other and still form a peering. Example 14-14 shows the output of show bgp ipv4 unicast neighbors | include BGP neighbor|TTL, which indicates that the eBGP neighbor at 10.1.12.1 must be reachable in 1 router hop, and the iBGP neighbor at 5.5.5.5 can be up to 255 hops away. If the TTL is not large enough to support the distance required to form a BGP peering, the packet is discarded and no neighbor relationship is formed.

## Slide 16: Troubleshooting BGP Neighbor Adjacencies The TTL of the BGP Packet Expires (Cont.)
Example 14-15 shows the configuration of R1 and R2. Notice that R1 is peering with R2, using the neighbor address 2.2.2.2 (R2 loopback) and the source address of Loopback 0 (1.1.1.1). R2 is peering with R1 using the neighbor address 1.1.1.1 (R1 loopback) and source address of Loopback 0 (2.2.2.2). Note that these loopback interfaces are not directly connected (one hop away), and because it is an eBGP neighbor relationship, you can expect the peering to fail.

## Slide 17: Troubleshooting BGP Neighbor Adjacencies The TTL of the BGP Packet Expires (Cont.)
Example 14-15 shows the configuration of R1 and R2. Notice that R1 is peering with R2, using the neighbor address 2.2.2.2 (R2 loopback) and the source address of Loopback 0 (1.1.1.1). R2 is peering with R1 using the neighbor address 1.1.1.1 (R1 loopback) and source address of Loopback 0 (2.2.2.2). Note that these loopback interfaces are not directly connected (one hop away), and because it is an eBGP neighbor relationship, you can expect the peering to fail.
To solve this issue with eBGP neighbors, you can modify the TTL of eBGP packets by using the neighbor ip_address ebgp-multihop [TTL] command. In this case, 2 would be enough to solve the issue. Therefore, on R1, you can type neighbor 2.2.2.2 ebgp-multihop 2, and on R2, you can type neighbor 1.1.1.1 ebgp-multihop 2.

## Slide 18: Troubleshooting BGP Neighbor Adjacencies Mismatched Authentication
BGP supports Message Digest 5 (MD5) authentication between peers. As is typical with authentication, if any of the parameters do not match, a peering does not form, as shown in Example 14-18.
A BGP authentication mismatch generates a syslog message like the following from the TCP facility:
%TCP-6-BADAUTH: No MD5 digest from 2.2.2.2(179) to 1.1.1.1(45577) tableid – 0

## Slide 19: Troubleshooting BGP Neighbor Adjacencies Misconfigured Peer Groups
When troubleshooting peer group issues, you need to look for the following possible culprits:
You forgot to associate the neighbor ip address with the peer group - After the peer group is created, you need to use the neighbor ip_address peer-group peer_group_ name command to associate the neighbor with the configurations in the peer group.
The peer group is not configured correctly - It is possible that you overlooked the fact that what works for one neighbor might not work for the other.
The route filter applied to the group is not appropriate for all the peers - Be careful with filters and make sure they produce the desired results for all neighbors in the peer group.
Order of operations produces undesired results - If there are conflicting entries between the peer group and a specific neighbor statement, the neighbor statement wins.

## Slide 20: Troubleshooting BGP Neighbor Adjacencies Timers
BGP timers do not have to match. This is because BGP uses the lowest timers set between the two neighbors. Notice in Example 14-20 that R3 is configured with a minimum hold time of 90 seconds; if a neighbor is using more aggressive timers, those timers will not be used. The situation is far worse than the timers simply not being used. The neighbor relationship does not form at all.

## Slide 21: Troubleshooting BGP Neighbor Adjacencies Timers (Cont.)
Refer to Example 14-21. In this case, R1 has a hello interval set to 10 and hold time set to 30. R3 has the minimum hold time set to 90 seconds. Therefore, R3 does not agree with the 30-second hold time set by R1, and the neighbor relationship fails. You can see in the output that a BGP notification states that the hold time is not acceptable.

## Slide 22: Troubleshooting BGP Routes
After a BGP adjacency is formed, BGP routers exchange their BGP routes with each other. For various reasons, BGP routes might be missing from either the BGP table or the routing table.
This section explains those reasons and how to identify and troubleshoot them.

## Slide 23: Troubleshooting BGP Routes Missing Routes
Some common reasons BGP routes might be missing from either the BGP table or the routing table:
Missing or bad network mask command - An accurate network command is needed to advertise routes.
Next-hop router not reachable - To use a BGP route, the next hop must be reachable.
BGP split-horizon rule - A router that learns BGP routes through an iBGP peering does not share those routes with another iBGP peer.
Better source of information - If exactly the same network is learned from a more reliable source, it is used instead of the BGP-learned information.
Route filtering - A filter might be preventing a route from being shared with neighbors or learned from neighbors.

## Slide 24: Troubleshooting BGP Routes Missing Routes (Cont.)
To verify the IPv4 unicast BGP-learned routes or routes locally injected into the BGP table, you use the show bgp ipv4 unicast command as shown in Example 14-22. Routes appear in this table for the following reasons:
Another BGP router advertises them to the local router.
The network mask command matches a route in the local routing table.
A redistribute command is used to import the route from another local source.
The summary-address command is used to create a summary route.

## Slide 25: Troubleshooting BGP Routes Missing Routes (Cont.)
To display the routing table, you use the show ip route command. To view only the BGP routes, you issue the command show ip route bgp, as shown in Example 14-23. All BGP routes appear with the code B at the beginning of each entry.

## Slide 26: Troubleshooting BGP Routes Bad or Missing Network Mask
The network mask command is used to advertise routes into BGP. If you only remember one thing about this command, remember that it is extremely picky:
The network/prefix you want to advertise with BGP must be in the routing table from some other source (connected, static, or some other routing protocol).
The network mask command must be a perfect match to the network/prefix listed in the routing table.
It is important that you be able to recognize a bad or missing network mask command as being the reason for missing routes.

## Slide 27: Troubleshooting BGP Routes Next-Hop Router Not Reachable
For a BGP router to install a BGP route in the routing table, it must be able to reach the next-hop address listed for the network. A ping 1.1.1.1 command issued on router R5 fails, proving that the next hop to the 10.1.1.0/26 is not reachable.
There are many different ways to solve this problem. The key is to train R5 about how to get to the next hop. The following are a few examples:
Create a static default route on R2 and R3 and advertise it into the Interior Gateway Protocol (IGP) routing protocol.
Create a static default route on R5.
Create a static route on R5.
Advertise the next-hop address into the IGP routing protocol.
In addition, BGP has a built-in option. It is the neighbor ip_address next-hop-self command.

## Slide 28: Troubleshooting BGP Routes BGP Split-Horizon Rule
The BGP split-horizon rule states that a BGP router that receives a BGP route from an iBGP peering shall not advertise that route to another router that is an iBGP peer. For R5 to learn about the 10.1.1.0/26 network, it has to be an iBGP peer with the router that learned about the route from an eBGP peer or it has to be a peer with a route reflector.
Figure 14-5 indicates what the iBGP peerings should be to ensure that both R4 and R5 learn about 10.1.1.0/26 (as well as the other networks). This setup also ensures that redundancy is optimized in the BGP AS.

## Slide 29: Troubleshooting BGP Routes Better Source of Information
Example 14-30 shows the output of the IPv4 unicast BGP table on R5, using the show bgp ipv4 unicast command.
In the table, notice that the 10.1.5.0/24, 10.1.12.0/24, and 10.1.13.0/24 networks are best (installed in routing table), as indicated by the > symbol; however, they are not valid. They are listed as having a Routing Information Base (RIB) failure, as indicated by the r.
A RIB failure means that the BGP route was not able to be installed in the routing table; however, you can clearly see that the route is in the routing table because of the > symbol. In this case, the route in the routing table is from a better source.

## Slide 30: Troubleshooting BGP Routes Better Source of Information (Cont.)
With regard to the 10.1.12.0/24 network, the output of show bgp ipv4 unicast 10.1.12.0 in Example 14-32 indicates that it was learned from R2 and R3 using iBGP (internal), which has an AD of 200, much higher than EIGRP’s AD.
You can verify why a route is experiencing a RIB failure by using the show bgp ipv4 unicast rib-failure command, as shown in Example 14-33. In this example, all three RIB failures are due to the BGP route having a higher AD.

## Slide 31: Troubleshooting BGP Routes Route Filtering
When troubleshooting missing routes, you want to be able to determine whether a route filter is applied and whether it is the cause of the missing routes.
When a route is missing from the BGP table, check to see whether the route is being advertised before filters are applied.
As shown in Example 14-36, which displays the output of the show bgp ipv4 unicast neighbors ip_address advertised routes command, R2 and R3 are advertising the 10.1.13.0/24 network to R5.

## Slide 32: Troubleshooting BGP Routes Route Filtering (Cont.)
The show ip protocols command, as shown in Example 14-37, displays the incoming filter applied to the BGP autonomous system. It is a distribute list using the prefix list called FILTER_10.1.13.0/24. The prefix list is denying 10.1.13.0/24 and permitting all other routes.
This example focuses on a filter that applies to the entire BGP process. No matter which router the route 10.1.13.0/24 is received from, it is denied. You can apply a filter directly to a neighbor by using any one of the following commands:
neighbor ip_address distribute-list access_list_number {in | out}
neighbor ip_address prefix-list prefix_list_name {in | out}
neighbor ip_address route-map map_name {in | out}
neighbor ip_address filter-list access_list_number {in | out}

## Slide 33: Troubleshooting BGP Routes Route Filtering (Cont.)
In Example 14-38, an inbound distribute list is applied directly to the neighbor 2.2.2.2, as shown in the show ip protocols output. Notice that only the first six characters of the ACL are identified.
You can apply a route map, a prefix list, and a filter list directly to the neighbor command. The filter list appears under the FiltIn and FiltOut columns in the output of show ip protocols, and the route map appears under the RouteMap column in the show
ip protocols output. If the prefix list is applied directly to a neighbor statement, it does not
appear in the output of show ip protocols. You need to review the output of show bgp ipv4
unicast neighbors. To avoid the verbose output, use this shortcut:
show bgp ipv4 unicast neighbors ip_address | include prefix|filter|Route map

## Slide 34: Troubleshooting BGP Path Selection
Unlike OSPF and EIGRP, BGP does not consider a link’s bandwidth when making a route decision.
BGP uses various attributes when deciding which path is the best.
This section discusses the BGP best-path decision-making process. In addition, it examines private ASNs.

## Slide 35: Troubleshooting BGP Path Selection The Best-Path Decision-Making Process
Cisco routers review BGP attributes in the following order when deciding which path is the best:
Prefer the highest weight
Prefer the highest local preference
Prefer the route originated by the local router
Prefer the path with the shorter Accumulated Interior Gateway Protocol (AIGP) metric attribute
Prefer the shortest AS_Path
Prefer the lowest origin code
Prefer the lowest multi-exit discriminator (MED)
Prefer an external path over an internal path
Prefer the path through the closest IGP neighbor
Prefer the oldest route for eBGP paths
Prefer the path with the lowest neighbor BGP RID
Prefer the path with the lowest neighbor IP address

## Slide 36: Troubleshooting BGP Path Selection The Best-Path Decision-Making Process (Cont.)
When BGP finds a match, it stops and uses that attribute as the reason for choosing the path as the best—and it looks no further. In addition, if the next-hop IP address is not reachable, the router does not even go through the following process because it considers the next hop inaccessible:
Step 1. BGP first looks at weight. Higher is better. If the weight is tied, the next attribute is checked.
Step 2. Local preference is checked next. Higher is better. If local preference is tied, the next attribute is checked.
Step 3. The router checks whether it generated the BGP route. If it did, it is preferred. If it did not generate any of the routes, the next attribute is checked.
Step 4. AIGP is checked next only if it’s configured to be used, if not, then the next attribute is checked.

## Slide 37: Troubleshooting BGP Path Selection The Best-Path Decision-Making Process (Cont.)
Step 5. AS_Path is checked next. The shortest path is preferred. If the AS_Path is tied, the next attribute is checked.
Step 6. The origin code is checked next. IGP is better than EGP (the predecessor to BFP), which is better than incomplete. IGP means the route was generated with the network mask or summary-address, incomplete means the route was redistributed into BGP. If the origin code is the same, the next attribute is checked.
Step 7. MED (metric) is next. Lower is better. If the MED (metric) is the same for both, the next attribute has to be checked.
Step 8. Now eBGP is preferred over iBGP. If this attribute is tied as well, and the next has to be checked.
Step 9. The IGP path to the neighbor is compared now. If the metrics are the same, the next attribute has to be checked.

## Slide 38: Troubleshooting BGP Path Selection The Best-Path Decision-Making Process (Cont.)
Step 10. If they are eBGP paths, the ages of the routes are checked. If both paths are iBGP paths, the next attribute is checked.
Step 11. The BGP RIDs are now compared. Lower is better. If the RID is tied, the path through the neighbor with the lower IP address wins.

## Slide 39: Troubleshooting BGP Path Selection Private Autonomous System Numbers
Like IPv4 addresses, BGP ASNs also have a private range. The 2-byte AS range is 64,512 to 65,534, and the 4-byte AS range is 4,200,000,000 to 4,294,967,294.
These ASNs can be used for networks that are single-homed or dual-homed to the same ISP, thereby preserving the public ASNs for networks that are multihomed to multiple ISPs.
It is imperative that the private ASN not be in the AS_Path attribute when the routes are advertised to the Internet (in the global BGP table) because multiple ASs could be using the same private ASN, which would cause issues on the Internet.
If private ASNs are being sent into the global BGP table, they need to be stopped. You can accomplish this by using the neighbor ip_address remove-private-as command.

## Slide 40: Troubleshooting BGP Path Selection Using debug Commands
The majority of changes that occur with BGP generate syslog messages in real time. Therefore, you are notified through syslog if any neighbor issues occur. Avoid using the large number of debugs that are available because they place a lot of pressure on the routers’ resources.
Here are a few debug commands that may be useful:
debug ip routing – The output from this command shows updates to a router’s IP routing table.
debug ip bgp - This command can be useful in watching real-time state changes for IPv4 BGP peering relationships.
debug ip bgp updates - This command produces more detailed output than the debug ip bgp command. Specifically, you can see the content of IPv4 BGP updates.

## Slide 41
Troubleshooting BGP for IPv6
BGP for IPv4 and BGP for IPv6 are configured in the same BGP autonomous system configuration mode, known as Multiprotocol BGP (MP-BGP).
Implementing BGP for IPv4 and IPv6 on the same router requires the use of address families and the activation of neighbors for those address families.
This section examines the additional issues that you might encounter when using MP-BGP with IPv4 and IPv6 unicast routes.

## Slide 42: Troubleshooting BGP for IPv6 MP-BGP
There are two different ways to exchange IPv6 routes with BGP. You can exchange them over IPv4 TCP sessions or over IPv6 TCP sessions. Example 14-45 shows a sample BGP configuration in which IPv6 routes are exchanged over an IPv4 TCP session. Notice that there are two address families: one for IPv4 unicast, and one for IPv6 unicast.
The neighbors and remote ASNs are identified outside the address family (AF) configuration. You then activate the neighbor within the AF with the neighbor ip_address activate command.
In this example, the IPv6 AF is using an IPv4 neighbor address to establish the TCP session. Therefore, the TCP session is IPv4 based.
Example 14-45 MP-BGP Configuration for IPv6 Routes over an IPv4 TCP Session

## Slide 43: Troubleshooting BGP for IPv6 MP-BGP (Cont.)
To verify the IPv6 unicast routes that have been learned from all neighbors, you can issue the show bgp ipv6 unicast command, as shown in Example 14-47. Its output displays the IPv6 BGP table.
Examine the 2001:db8:2::/64 route. This is the route that was learned from R2 (the 2.2.2.2 neighbor). It is not installed in the routing table, as indicated by the absence of the *>.
The address ::FFFF:2.2.2.2 is a dynamically generated next hop that was created to replace the original next hop of 2.2.2.2. An IPv6 route cannot have an IPv4 next-hop address.
To solve this issue, create a route map on the advertising router that changes the next hop to a valid IPv6 address and attach it to the neighbor statement, as shown in Example 14-48.

## Slide 44: Troubleshooting BGP for IPv6 MP-BGP (Cont.)
As shown in Example 14-50, to form the IPv6 TCP session, define the neighbor by using the neighbor ipv6_address remote-as autonomous_system_number command outside the AF configuration, and then you activate the neighbor in the IPv6 AF configuration by using the neighbor ipv6_address activate command.

## Slide 45: Troubleshooting BGP for IPv6 MP-BGP (Cont.)
The output of show bgp ipv6 unicast summary, as shown in Example 14-51, indicates that R1 has formed an IPv6 BGP neighbor adjacency with the device at 2001:db8:12::2 using an IPv6 TCP session, and one prefix has been received.
The IPv6 BGP table, as displayed in the output of the show bgp ipv6 unicast command in Example 14-52, indicates that 2001:DB8:2::/64 can be reached with a next hop of 2001:DB8:12::2 and that it is installed in the routing table, as indicated by the *>.

## Slide 46: BGP Trouble Tickets
This section presents trouble tickets related to the topics discussed earlier in this chapter.
The purpose of these trouble tickets is to show a process that you can use when troubleshooting in the real world or in an exam environment.

## Slide 47: BGP Trouble Tickets Trouble Ticket 14-1: BGP Routes
Problem: You are the administrator for BGP AS 65502. While you were away on vacation, the link between R1 and R2 failed. When the link between R1 and R2 fails, the link between R1 and R3 is supposed to forward traffic to BGP AS 65501. However, that did not occur while you were away. Your co-worker had to restore connectivity between R1 and R2, and complaints kept flowing in from the users in 10.1.5.0/24 about connectivity to the 10.1.1.0/24
networks being down.
Refer to your text for next steps and examples to troubleshoot and resolve this trouble ticket.

## Slide 48: BGP Trouble Tickets Trouble Ticket 14-2: Layer 3 Connectivity
Problem: You are the administrator for BGP AS 65501. Users in the 10.1.1.0/26 and 10.1.1.64/26 networks have indicated that they are not able to access resources located at 10.1.5.5. However, they can access resources locally.
You begin troubleshooting by issuing two pings on R1 to 10.1.5.5 and sourcing them from 10.1.1.1 and 10.1.1.65.
Refer to your text for next steps and examples to troubleshoot and resolve this trouble ticket.

## Slide 49: BGP Trouble Tickets Trouble Ticket 14-3: Backup Link
Problem: You are the administrator for BGP AS 65502. Traffic reports indicate that all traffic out of the autonomous system is flowing through R3 and across the backup link. This is undesirable unless the link between R2 and R1 fails.
To verify the issue, you use traceroute from R5.
Refer to your text for next steps and examples to troubleshoot and resolve this trouble ticket.

## Slide 50: MP-BGP Trouble Ticket
This section presents trouble tickets related to the topics discussed earlier in this chapter.
The purpose of these trouble tickets is to show a process that you can use when troubleshooting in the real world or in an exam environment.

## Slide 51: MP-BGP Trouble Tickets Trouble Ticket 14-4: MP-eBGP
Problem: You are an administrator of BGP AS 65501. Another administrator in your AS has asked you for help. The default route from your ISP is not being learned by your router (R1) using BGP. As a result, no one in your AS is able to reach the Internet.
You start by confirming the issue by using the show ipv6 route command on R1.
Refer to your text for next steps and examples to troubleshoot and resolve this trouble ticket.

## Slide 52: Prepare for the Exam

## Slide 53: Prepare for the Exam Key Topics for Chapter 14
Description
Verifying BGP neighbors with show bgp ipv4 unicast summary
Considerations when troubleshooting BGP neighbor relationships
The path to the neighbor through the default route
Incorrect neighbor statement
How to control the source addresses of BGP packets
How BGP TCP sessions are formed and how you can control the server and client for the TCP session
Manipulating the TTL of an eBGP packet
How the minimum hold time parameter can prevent BGP neighbor relationships
The reasons a BGP route might be missing from the BGP table or the routing table

## Slide 54: Prepare for the Exam Key Topics for Chapter 14 (Cont.)
Description
Examining the BGP table
The requirements of the BGP network mask command
The BGP next-hop issue
Identifying BGP split-horizon issues
Troubleshooting filters that may be preventing BGP routes from being advertised or learned
The steps that BGP uses to successfully determine the best path to reach a given network
The next-hop issue that occurs when exchanging IPv6 BGP routes over IPv4 BGP TCP sessions
Solving the next-hop issue that occurs when IPv6 BGP routes are exchanged over IPv4 BGP TCP sessions

## Slide 55: Prepare for the Exam Key Terms for Chapter 14
Terms | 
BGP | TTL
EGP | Peer group
eBGP | Split-horizon rule (iBGP)
iBGP | Weight
MP-BGP | Local Preference
ISP | AS_Path
Address family | MED

## Slide 56: Prepare for the Exam Command Reference for Chapter 14
Task | Command Syntax
Display a router’s BGP RID, ASN, information about the BGP’s memory usage, and summary information about IPv4/IPv6 unicast BGP neighbors | show bgp {ipv4 ¦ ipv6} unicast summary
Display detailed information about all the IPv4/IPv6 BGP neighbors of a router | show bgp {ipv4 ¦ ipv6} unicast neighbors
Display the IPv4/IPv6 network prefixes present in the IPv4/IPv6 BGP table | show bgp {ipv4 ¦ ipv6} unicast
Show routes known to a router’s IPv4/IPv6 routing table that were learned from BGP | show {ipv4 ¦ ipv6} route bgp
Show real-time information about BGP events, such as the establishment of a peering relationship | debug ip bgp
Show real-time information about BGP updates sent and received by a BGP router | debug ip bgp updates
Display updates that occur in a router’s IP routing table | debug ip routing