## Slide 1: Chapter 23: Device Management and Management Tools Troubleshooting
Instructor Materials
CCNP Enterprise: Advanced Routing

## Slide 2: Chapter 23 Content
This chapter covers the following content:
Device Management Troubleshooting - This section explains how to identify and troubleshoot issues related to console and vty access, as well as remote transfer tools. Various protocols are covered, including Telnet, SSH, TFTP, HTTP, HTTPS, and SCP.
Management Tools Troubleshooting - This section examines how to use and troubleshoot various management tools, including syslog, SNMP, Cisco IP SLA, Object Tracking, NetFlow, and Flexible NetFlow. In addition, it examines Bidirectional Forwarding Detection (BFD) and Cisco DNA Center Assurance.

## Slide 3: Device Management Troubleshooting
When you have physical access to a device use the console line to access a Cisco IOS router for management purposes. Use vty lines to provide remote connectivity using Telnet or Secure Shell (SSH).
You may have to troubleshoot problems connecting to a device so that you can troubleshoot another issue that has been presented to you. It may be necessary to transfer configuration files or IOS images while you are solving a problem. You need to be able to troubleshoot issues related to your remote transfers using protocols such as TFTP, HTTP(S), and SCP.
This section explains why management access to a Cisco IOS router may fail, how you can determine why the problem is occurring, and how you can fix it. This section also discusses what to look out for when troubleshooting remote transfers. .

## Slide 4: Device Management Troubleshooting Console Access Troubleshooting
Here are some questions you should ask when troubleshooting console access:
Has the correct COM port been selected in the terminal program?
Are the terminal program’s settings configured correctly?
Is a line password used to authenticate to the console?
Are a local username and password used to authenticate to the console?
Is an AAA (authentication, authorization, and accounting) server used to authenticate to the console?
  Has a method list been created for login authentication?
Are the correct cable and drivers being used to connect to the console port?
  New devices use a mini-USB port, older devices use the serial-to-RJ45 console (rollover) cable.

## Slide 5: Device Management Troubleshooting vty Access Troubleshooting and Telnet
Most devices are administered remotely via the vty lines, which support protocols such as Telnet and SSH for remote access. Consider the following when troubleshooting Telnet access to a device:
Is the IP address of the remote router/switch reachable?
Are the correct transport protocols defined for the line?
Is the line configured to ask the user for credentials?
Is a password specified?
Is there an ACL (access control list) defining which management stations, based on IP address, can access the router/switch?
Are all vty lines busy?
Is there an ACL in the path between the client and the device blocking port 23?

## Slide 6: Device Management Troubleshooting vty Access Troubleshooting and SSH
With Secure Shell (SSH), you may experience the same issues as described with Telnet, in addition to several others. Consider the following additional issues when troubleshooting SSH access to a device:
Is the correct version of SSH specified?
Has the correct login command been specified?
Has the correct key size been specified?
Is there an ACL in the path between the client and the device blocking port 22?

## Slide 7: Device Management Troubleshooting Password Encryption Levels
By default, all passwords are stored in plaintext within the IOS configuration. For security, passwords should be encrypted or hashed in the configuration. Example 23-8 shows sample output of the passwords stored in the running configuration. The level 0 indicates no encryption. The level 4 indicates that SHA-256 was used. The level 5 indicates that Message Digest 5 (MD5) was used. The level 7 indicates that Type 7 encryption was used. The levels from strongest to weakest are 4, 5, 7, and then 0.

## Slide 8: Device Management Troubleshooting Remote Transfer Troubleshooting - TFTP
TFTP is an unsecure file transfer protocol you can use to transfer files to and from a Cisco device using a TFTP server. TFTP uses UDP port 69 and is considered an unreliable protocol. When troubleshooting TFTP issues consider the following:
When copying to a TFTP server, make sure the TFTP server has enough storage space.
When copying from a TFTP server, make sure the storage location on the Cisco device has enough storage space. Use the show flash command to verify the amount of free space available and compare it to the size of the file you want to copy.
Ensure that the TFTP server is reachable from the Cisco device.
Check along the path from source to destination for access lists that might be blocking TFTP traffic.
If you are using a management interface for TFTP traffic, use the ip tftp source-interface interface_type interface_number command to specify that the management interface will be used for sourcing TFTP traffic.
Ensure that you are using the copy command correctly
There is a 63-character limit on filenames in flash memory.

## Slide 9: Device Management Troubleshooting Remote Transfer Troubleshooting – HTTP(S)
To copy Cisco IOS image files, core files, configuration files, log files, and scripts to/from a remote web server, use unsecure protocol HTTP (TCP port 80), or secure protocol HTTPS (TCP port 443). Consider the following when troubleshooting HTTP(S) access for a device:
Your Cisco device must support the HTTP client. Check with the show ip http client all command.
Your router must connect to the web server. From the Cisco device, ping the URL of the web server or its IP address.
Ensure that the correct URL or IP address of the web server has been specified in the copy command. When copying to a web server from flash, the destination is the web server.
Ensure that the correct filename, username and password are specified in the copy command.
Check that the correct port is specified in the copy command.
Check that packets to the web server from the Cisco device are being sourced from the correct IP address.
Make sure you specified the correct protocol: HTTP or HTTPS.
For additional help with troubleshooting HTTP and HTTPS copy issues, use the debug ip http client all command.

## Slide 10: Device Management Troubleshooting Remote Transfer Troubleshooting – SCP
Secure Copy Protocol (SCP) is another way to copy files from a storage location to a Cisco device. It relies on Secure Shell (SSH) to provide a secure and authenticated method of transferring files. SCP requires AAA to be enabled so that the router can determine if the user is authorized to copy. Consider the following when troubleshooting SCP issues:
Ensure that SSH, authentication, and authorization have been configured correctly on the device.
Ensure that an RSA key is available and can be used for encryption.
Ensure that AAA is configured correctly and is functioning.
Ensure that SCP is enabled on the Cisco device using the ip scp server enable command.
Ensure that the copy command is being used correctly.
Verify that the correct username and password are being used for copying
For additional help troubleshooting SCP issues, use the debug ip scp command.

## Slide 11: Management Tools Troubleshooting
Being able to monitor your network using various tools will help you stay ahead of any issues. However, when the tools break or don’t provide the results you need, you have to troubleshoot the tools that help you troubleshoot.
This section examines how to troubleshoot issues with tools such as syslog, SNMP, IP SLA, Object Tracking, NetFlow, and Flexible NetFlow. It also explores the benefits of using BFD and examines how Cisco DNA Center Assurance can assist you with your troubleshooting efforts.

## Slide 12: Management Tools Troubleshooting Syslog Troubleshooting
To verify your syslog configuration, confirm that logging is enabled, and view the syslog messages stored in the buffer, use the show logging command. In Example 23-11, the console and monitor are configured with the level ‘informational’, the buffer is configured with the level ‘debugging’, and the trap logging (server) is configured with the level ‘warnings’.
When logging in to a server, specify the correct server IP address. Ensure that the server is reachable. Because syslog uses UDP port 514, ensure that no ACLs are blocking traffic destined to this port.
Finally, if you have remotely connected to a device by using Telnet or SSH, and no syslog messages are appearing, it is because the terminal monitor command has not been issued.

## Slide 13: Management Tools Troubleshooting SNMP2 Troubleshooting
You need to be able to ping the server from the agent. If Layer 3 connectivity does not exist, the SNMP NMS cannot access the information in the MIB on the agent. Keep the following in mind as you troubleshoot SNMPv2c:
Ensure that community strings match and the ACLs classifying servers are correct.
Ensure that configurations for notifications are correct, that traps are enabled.
Ensure that the host (NMS) IP address, the SNMP version, and the community string are all correct and specified.
Prevent index shuffling using the snmp-server ifindex persist command.
If you do not want all traps to be sent, you must specify the correct ones to send. In Example 23-12, the snmp-server host command indicates that SNMPv2c informs will be sent to the NMS at 10.1.100.100 with a community string of CISCO.

## Slide 14: Management Tools Troubleshooting SNMP3 Troubleshooting
SNMPv3 offers improved authentication and encryption over SNMPv2c. Keep the following in mind as you troubleshoot SNMPv3:
Appropriate nesting of users, views, and groups.
Specifying the correct security level.
Using the correct hashing and encrypting algorithms, and correct passwords.
Specifying the correct OIDs in the view.
Appropriate notification configuration.
Prevent index shuffling using the snmp-server ifindex persist command.
In Example 23-13, the snmp-server host command indicates that SNMPv3 will send traps related to the CPU to the NMS at 10.1.100.100, with the authentication and encryption provided by the username NMSERVER.

## Slide 15: Management Tools Troubleshooting Cisco IOS IP SLA Troubleshooting
Cisco IOS IP SLA lets you measure network performance and test network availability by generating a continuous, reliable probe (simulated traffic) in a predictable manner. You can collect information about packet loss, one-way latency, response times, jitter, network resource availability, application performance, server response times, and even voice quality.
IP SLA consists of an IP SLA source (which sends the probes) and IP SLA responder (which replies to the probes). Figure 23-1 shows a scenario with just the IP SLA source sending a ping to test connectivity. Figure 23-2 shows a scenario with an IP SLA source and an IP SLA responder measuring jitter (interpacket delay variance).

## Slide 16: Management Tools Troubleshooting Cisco IOS IP SLA Troubleshooting (Cont.)
When troubleshooting Cisco IOS IP SLA, consider the following:
Choose the correct operation for the metrics you intend to measure.
Ensure that the destination IP address is reachable and correctly defined.
Ensure that the source IP address is reachable from the destination and correctly defined.
Ensure that any necessary port numbers are correctly identified.
The SLA instance needs to be started.
If the operation needs an IP SLA responder, one must be configured and reachable.
To verify which operations are supported on the platform in addition to how many operations are configured and how many are currently active, use the show ip sla application command, as shown in Example 23-20.

## Slide 17: Management Tools Troubleshooting Object Tracking Troubleshooting
Object Tracking lets you dynamically control what occurs if the result of the tracking object is up or down. For example, you can attach an object to a static route; if the object is up, the route is installed in the routing table. If the object is down, the route is not installed in the routing table. You can track IP routes, IP SLA instances, interfaces, and groups of objects.
To verify the configuration of a tracking object and the status of the tracking object, use the show track command. In Example 23-26, tracking object 1 exists on SW1. It is tracking the reachability of an IP route, 10.1.43.0/24. If the route is in the routing table, the object is up. If the route is not in the routing table, the object is down. The object is attached to HSRP Group 10, as shown after Tracked by: in the output.

## Slide 18: Management Tools Troubleshooting NetFlow and Flexible NetFlow Troubleshooting
Cisco IOS NetFlow provides insight into your network traffic patterns. NetFlow distinguishes between different traffic flows. A flow is a series of packets, all of which have shared header information, such as source and destination IP addresses, protocol numbers, port numbers, and type of service (TOS) field information. NetFlow keeps track of the number of packets and bytes observed in each flow. This information is stored in a flow cache in the router’s memory. After the NetFlow collector has received flow information over a period of time, analysis software running on the NetFlow collector can produce reports detailing traffic statistics.
Example 23-28 provides a sample NetFlow configuration on a router. Notice that the ip flow ingress command is issued for Fast Ethernet 0/0, and ip flow egress is configured on Fast Ethernet 0/1.
.

## Slide 19: Management Tools Troubleshooting NetFlow and Flexible NetFlow Troubleshooting (Cont.)
When troubleshooting NetFlow, consider the following:
Traffic direction
Interface (Example 23-30)
Export destination
Export source (Example 23-31)
Version
Flows are temporary on the local Cisco device. If they are not exported to a NetFlow collector, the flows will be removed from the cache at some point to free up resources. Flows are exported to the NetFlow collector only if you set up the device to export the flows and only after the flows expire in the flow cache on the local device.

## Slide 20: Management Tools Troubleshooting NetFlow and Flexible NetFlow Troubleshooting (Cont.)
Flexible NetFlow lets you customize the traffic analysis parameters for your specific requirements, so you must verify more parameters while troubleshooting. When troubleshooting Flexible NetFlow, you will need to verify the flow records, flow monitors, flow exports, and interface configurations.
Flow records define what will be captured. You need to be able to verify that they are configured to capture what you want. With Cisco-predefined records, use Cisco documentation to identify what is captured as the list will evolve over time. When using user-defined records, use the show flow record command to verify that the correct match and collection conditions were specified in the flow record, or the show running-config flow record command, as shown in Example 23-33.

## Slide 21: Management Tools Troubleshooting Bidirectional Forwarding Detection (BFD)
Sometimes no carrier detect signaling mechanism is available to quickly detect whether the link between routers is down. Figure 23-3 illustrates three types of environments where a link failure may not occur on the directly connected interface.
BFD is a “detection” protocol that works with all media types, routing protocols, topologies, and encapsulations. It quickly detects reachability failures between two routers in the same Layer 3 network so that network issues can be identified as soon as possible, and convergence can occur at a far faster rate. BFD is a lightweight protocol which is less CPU intensive than fast routing protocol hellos. In Figure 23-4, R1 and R2 are using BFD to keep track of reachability: BFD packets are being sent every 100 msec, and if three consecutive packets are missed, BFD triggers a session failure and notifies EIGRP.

## Slide 22: Management Tools Troubleshooting Cisco DNA Center Assurance
With Cisco DNA Center Assurance, you can predict problems more quickly, thanks to proactive monitoring. Your first valuable troubleshooting tool is the Overall Health page, shown in Figure 23-5. This page provides an overview of the overall health of the networks and clients in the environment, which can be displayed based on information gathered from the most recent 3 hours, 24 hours, or 7 days. You can view health maps as well as hierarchical site/building maps by clicking on the Hide/Show button. The Top 10 Issues area at the bottom of the page displays the issues that should be addressed; when you click on them, you are presented with the issue details, including the impact of the issue, as well as suggested actions to fix the issue.
Figure 23-5 Cisco DNA Center Assurance Overall Health Page

## Slide 23: Management Tools Troubleshooting Network Health Page
Another valuable troubleshooting tool is the Network Health page, shown in Figure 23-6, which you can access in Cisco DNA Center Assurance by selecting Health and then Network. The Network Devices section lists all the devices on an individual basis and provides information such as the device type, address, OS version, reachability, issue count, and location. In addition, it provides an overall health score. Anything with a health score from 1 to 3 is a critical issue and is displayed in red. You can click on the device to get further details about a device in Device 360.
Figure 23-6 Part of the Network Health Page

## Slide 24: Management Tools Troubleshooting Client Health Page
Access the Client Health page, shown in Figure 23-7, in Cisco DNA Center Assurance by selecting Health and then Client. The Client Devices section of the Client Health page lists all the clients on an individual basis and provides information such as the identifier, address, type, when it was last seen, the switch or AP it is connected to, and location. In addition, it provides an overall health score. Anything with a health score from 1 to 3 is a critical issue and is displayed in red. You can click on the device to get further details about a device in Client 360.
Figure 23-7 Part of the Client Health Page

## Slide 25: Management Tools Troubleshooting Client 360 Dashboard
Figure 23-8 shows the Client 360 dashboard for the client with IP address 10.10.20.207. Notice that the client is experiencing poor RF (radio frequency) conditions. In this case, if you click on Wireless Client Experiencing Poor RF Conditions on SSID “sandbox,” you get a description of the issue, the impact of the last occurrence, and possibly suggested remediation actions.
Figure 23-8 Part of the Client 360 Page

## Slide 26: Management Tools Troubleshooting Device 360
Figure 23-9 shows the Device 360 page for a switch named spine1.abc.in with IP address 10.10.20.80. Notice in the image that there is one issue: The description states “Device experiencing high memory utilization.” If you click the issue, you get a description of the issue and possibly suggested actions you should take to resolve it (Figure 23-10).
Figure 23-9 Part of the Device 360 Page
Figure 23-10 Description and Suggested Actions for an Issue

## Slide 27: Management Tools Troubleshooting Path Trace
The next troubleshooting feature in DNA Center Assurance is Path Trace. With Path Trace, you can graphically see the path that applications and services running on a client will take through all the devices on the network to reach the destination. With a few clicks, you can use this tool to do multiple troubleshooting tasks that would take you 5 to 10 minutes at the command line. Figure 23-11 shows an example of using Path Trace between two devices. Path Trace can be accessed within Client 360 or Device 360.
Another great tool for troubleshooting in Cisco DNA Center Assurance is Network Time Travel. This tool allows you to hop into a time machine and see the cause of a network issue instead of trying to reproduce the issue.
Figure 23-11 Using Path Trace from the DNA Center Assurance Client 360 Page

## Slide 28: Management Tools Troubleshooting Global Issues
With the Global Issues page, you can access all open issues, resolved issues, and ignored issues in one place, as shown in Figure 23-12. You can access the Global Issues page from the Issues drop-down.
Figure 23-12 Global Issues Page

## Slide 29: Management Tools Troubleshooting Global Issues (Cont.)
Select the All Issues option from the Issues drop-down, as shown in Figure 23-13. The following categories are available:
Onboarding - Identifies issues related to wireless and wired client onboarding.
Connectivity - Identifies issues related to network connectivity, including OSPF, BGP, and tunnels.
Connected - Identifies issues related to clients.
Device - Identifies issues related to the device.
Availability - Identifies availability issues related to access points, wireless LAN controllers, etc.
Utilization - Identifies issues related to utilization of access points, wireless LAN controllers, radios, etc.
Application - Identifies issues related to application experience.
Sensor Test - Identifies any global sensor issues.
Figure 23-13 All Issues Page

## Slide 30: Prepare for the Exam

## Slide 31: Prepare for the Exam Key Topics for Chapter 23
Description | 
Considerations when troubleshooting issues related to console port access | Considerations when troubleshooting issues related to remote transfers with SCP
Considerations when troubleshooting issues related to Telnet | Verifying syslog configuration
Considerations when troubleshooting issues related to SSH | Considerations when troubleshooting issues related to SNMPv2c
Password encryption levels | Considerations when troubleshooting issues related to SNMPv3
Considerations when troubleshooting issues related to remote transfers with TFTP | Considerations when troubleshooting issues related to IP SLA
Considerations when troubleshooting issues related to remote transfers with HTTP(S) | Considerations when troubleshooting issues related to NetFlow

## Slide 32: Prepare for the Exam Key Topics for Chapter 23 (Cont.)
Description | 
Viewing Flexible NetFlow flow records | Health scores for the clients connected to the network on the Client Health page of Cisco DNA Center Assurance
Viewing Flexible NetFlow flow monitors | The Client 360 and Device 360 pages of Cisco DNA Center Assurance
Viewing Flexible NetFlow flow monitor cache format records | Path Trace in Cisco DNA Center Assurance
Viewing Flexible NetFlow-enabled interfaces | Categories in All Issues of Cisco DNA Center Assurance
Viewing Flexible NetFlow flow exporter information | 
Health scores for the network devices on the Network Health page of Cisco DNA Center Assurance | 

## Slide 33: Prepare for the Exam Key Terms for Chapter 23
Term |  | 
AAA | IP SLA | Port 22
BFD | Level 4 encryption | SSH
Cisco DNA Center Assurance | Level 5 encryption | SNMPv2c
Client 360 | Level 7 encryption | SNMPv3
Device 360 | Line | Syslog
Flexible NetFlow | Login | Telnet
Flow cache | Login local | 
Flow exporter | NetFlow | 
Flow record | Object Tracking | 
Flow monitor | Port 23 | 

## Slide 34: Prepare for the Exam Command Reference for Chapter 23
Task | Command Syntax
Display the ingress and egress allowed transport protocols on vty line | show line vty line_number ¦ include Allowed
Display only the ingress allowed transport protocols on a vty line | show line vty line_number ¦ include Allowed input transports
Display the vty line configuration in the running configuration | show run ¦ section line vty
Display the lines that are currently being used for management connectivity | show users
Display whether SSH is enabled or disabled, the version of SSH enabled, and the SSH RSA key | show ip ssh
Display the SSHv1 and SSHv2 connections to the local device | show ssh

## Slide 35: Prepare for the Exam Command Reference for Chapter 23 (Cont.)
Task | Command Syntax
Display information related to syslog, including level settings and messages logged for console, monitor, buffer, and traps logging; verify the buffer size and its contents for buffer logging and the IP address/port number of the syslog server | show logging
Display the conditional debug commands that have been configured on the router | show debug condition
Display SNMP group information, including the group name, the security mode, the read and write views, and any applied ACLs | show snmp group
Display any configured SNMP users; output includes the username, the authentication protocol used, the encryption protocol used, and the group the user is applied to | show snmp user
Display the local configuration of the SNMP server, including the IP address, UDP port, type, attached user, and security model being used | show snmp host

## Slide 36: Prepare for the Exam Command Reference for Chapter 23 (Cont.)
Task | Command Syntax
Display the SNMP views configured on the local device | show snmp view
Display which IP SLA operations are supported on the platform, how many operations are configured, and how many operations are currently active | show ip sla application
Display the IP SLA configuration values for the IP SLA instances | show ip sla configuration
Display the IP SLA operational results of IP SLA instances | show ip sla statistics
Display the operational results of the IP SLA responder | show ip sla responder
Display the configured tracking objects on the local device, including the current state and the service or feature it is attached to | show track
Display the local NetFlow flow cache as well as the configured timers | show ip cache flow
Display the interfaces enabled for NetFlow and the direction in which they are capturing information | show ip flow interface

## Slide 37: Prepare for the Exam Command Reference for Chapter 23 (Cont.)
Task | Command Syntax
Display the NetFlow exporter configuration, including the source and destination addresses, port number, and version of NetFlow | show ip flow export
Display all user-defined Flexible NetFlow flow records that are configured on the local device | show flow record
Display the locally configured Flexible NetFlow flow monitors; verify the attached flow record and flow exporter as well as the configured timers | show flow monitor
Display the interfaces enabled for Flexible NetFlow and the direction in which they are capturing information | show flow interface
Display the Flexible NetFlow exporter configuration, including the source and destination addresses, port number, and version of NetFlow | show flow exporter