## Slide 1: Chapter 16: Route Redistribution
Instructor Materials
CCNP Enterprise: Advanced Routing

## Slide 2: Chapter 16 Content
This chapter covers the following content:
Redistribution Overview - This section provides an overview of redistribution fundamentals and rules of redistribution of routes between routing protocols.
Protocol-Specific Configuration - This section explains protocol specific behaviors and configuration examples for redistribution of routes between routing protocols.

## Slide 3: Redistribution Overview
An organization might use multiple routing protocols, split up the routing domain between multiple instances (processes) of the same routing protocol, or need to merge networks with another organization that uses a different routing protocol.
The routes from one routing protocol process need to be exchanged with a different routing protocol process to provide full connectivity.
Redistribution is used to inject routes from one routing protocol into another routing protocol.

## Slide 4: Redistribution Overview Multiple Routing Protocol Topology
Figure 16-1 illustrates a network that has multiple routing protocols that are not working together.
R1, R2, and R3 exchange routes using Enhanced Interior Gateway Routing Protocol (EIGRP), and R3, R4, and R5 exchange routes with Open Shortest Path First (OSPF).
R1 and R5 advertise their Loopback 0 interfaces (192.168.1.1/32 and 192.168.5.5/32) into their appropriate routing protocol, but they cannot establish connectivity to each other.
Only R3 can connect to R1 and R5 because it is the only router that participates with both routing protocols and has a complete view of the network.

## Slide 5: Redistribution Overview Mutual Redistribution Topology
The routes are not automatically redistributed between the routing protocols.
Redistribution must be configured so that EIGRP routes are injected into OSPF and OSPF routes are injected into EIGRP.
In Figure 16-2, the R3 router is performing mutual redistribution.
The OSPF routes are present in EIGRP as external routes, and the EIGRP routes are present in the OSPF routing domain as external routes (Type 5 link-state advertisements [LSAs]).

## Slide 6: Redistribution Overview Redistribution Source Protocols
Redistribution always encompasses two routing protocols:
A source protocol and a destination protocol.
The source protocol provides the network prefixes that are to be redistributed, and the destination protocol receives the injected network prefixes.
The redistribution configuration exists under the destination protocol and identifies the source protocol.
Using a route map allows for the filtering or modification of route attributes during the injection into the destination protocol.
Table 16-2 provides a list of source protocols for redistribution.

## Slide 7: Redistribution Overview Redistribution Is Not Transitive
When redistributing between two or more routing protocols on a single router, redistribution is not transitive.
When a router redistributes protocol 1 into protocol 2, and protocol 2 redistributes into protocol 3, the routes from protocol 1 are not redistributed into protocol 3.
Example 16-1 provides sample logic for EIGRP mutually redistributing into OSPF and OSPF mutually redistributing into BGP.
Figure 16-3 illustrates redistribution on the router.
The EIGRP route 172.16.1.0/24 redistributes into OSPF but does not redistribute into BGP.
The BGP route 172.16.3.0/24 redistributes into OSPF but does not redistribute into EIGRP.
The prefix 172.16.2.0/24 redistributes to both EIGRP and BGP.

## Slide 8: Redistribution Overview Redistribution Is Not Transitive (Cont.)
For routes to be exchanged between all three routing protocols, mutual redistribution must be configured between all three protocols, as shown in Example 16-2.
Now that all three routing protocols are mutually redistributed, EIGRP’s 172.16.1.0/24 network exists in OSPF and BGP, OSPF’s 172.1.6.2.0/24 network exists in EIGRP and BGP, and BGP’s 172.16.3.0/24 network exists in OSPF and EIGRP. Figure 16-4 illustrates the router processing for all three network prefixes.

## Slide 9: Redistribution Overview Sequential Protocol Redistribution
Sequential protocol redistribution is redistribution between multiple protocols over a series of routers, as shown in Figure 16-5.
R2 redistributes the EIGRP 192.168.1.1/32 prefix into BGP, and R4 redistributes the BGP 192.168.1.1/32 prefix into OSPF.
All three routing protocols contain the 192.168.1.1/32 prefix.

## Slide 10: Redistribution Overview Routes Must Exist in the RIB
A route must exist in the RIB in order for it to be redistributed into the destination protocol. This ensures that the route is deemed reachable by the redistributing router.
The source protocol that redistributes into the destination protocol must be the source for the route in the RIB. This ensures that the router redistributes only the route it deems the best for the destination protocol.
The only exception for this logic is for directly connected interfaces participating in the source protocol because they have an administrative distance (AD) of 0.
In Figure 16-6, R1 and R3 both advertise the 10.13.1.0/24 network, and R5 is redistributing
RIP and OSPF routes into EIGRP.

## Slide 11: Redistribution Overview Routes Must Exist in the RIB (Cont.)
R5 receives route information for 10.13.1.0/24 from both RIP and OSPF routing protocols.
Example 16-3 provides verification that R5 contains an entry for the 10.13.1.0/24 network in RIP’s database and OSPF’s LSDB.
R5 determines that the most desirable path to reach 10.13.1.0/24 is the OSPF route because it has a lower AD than RIP. Example 16-4 displays R5’s routing table.
The 10.13.1.0/24 OSPF route is inserted into the RIB.
Example 16-5 shows the EIGRP topology table for the 10.13.1.0/24 network.
R5 checks the Routing Information Base (RIB) for the 10.13.1.0/24 network and verifies its existence in the RIB and confirms that the source protocol is the protocol that installed the route.
EIGRP identifies the source protocol as OSPF, with a path metric of 3.

## Slide 12: Redistribution Overview Seed Metrics
Every routing protocol uses a different methodology for calculating the best path for a
route.
For example, EIGRP can use bandwidth, delay, load, and reliability, whereas OSPF primarily uses the path metric for calculating the shortest path first (SPF) tree (SPT). OSPF cannot calculate the SPT using EIGRP path attributes, and EIGRP cannot run diffusing update algorithm (DUAL) using only the total path metric.
The destination protocol must provide relevant metrics to the destination protocols so that the destination protocol can calculate the best path for the redistributed routes.
Every protocol provides a seed metric at the time of redistribution that allows the destination protocol to calculate a best path. The seed metric is a baseline and may reflect a loss of information during redistribution when redistribution occurs between two different protocol types.
A route map modifies the seed metric for a route during redistribution. Table 16-3 provides a list of seed metrics for the destination routing protocol.

## Slide 13: Protocol-Specific Configuration
Every routing protocol has a unique redistribution behavior.

## Slide 14: Protocol-Specific Configuration Route Map Match Command
Every routing protocol has a unique redistribution behavior.
IOS and IOS XE routers use the following command syntax in the destination protocol to identify the source routing protocol:
redistribute {connected | static | eigrp as-number | ospf process-id [match
{internal | external [1|2]}] | bgp as-number} [destination-protocoloptions]
[route-map route-map-name].
Redistribution commonly uses route maps to manipulate or filter routes on the redistributing router. Table 16-4 lists additional conditional matching commands for route selection during redistribution.

## Slide 15: Protocol-Specific Configuration Route Map Match Set Command
Table 16-5 lists the route map set actions that modify the route as it is redistributed into the destination protocol.

## Slide 16: Protocol-Specific Configuration Source Specific Behaviors: Connected Networks
Connected networks are networks associated with primary and secondary IP addresses for any up interfaces that are not participating with the destination protocol.
At times during redistribution, only select interfaces need to be redistributed.
This is accomplished using a route map that selects only the desired interfaces.
Example 16-6 provides a reference route map for selecting the specific connected network 192.168.1.1/32 on the Loopback 0 interface.

## Slide 17: Protocol-Specific Configuration Source Specific Behaviors: BGP
By default, BGP redistributes only eBGP routes into IGP protocols.
In Figure 16-7, R3 advertises the 192.168.3.3/32 network, and R4 advertises the 192.168.4.4/32 network into BGP.
R2 is redistributing BGP into OSPF, but only the 192.168.4.4/32 address is redistributed because it is an eBGP route. The iBGP route from R3 was not included because of BGP loop-prevention rules. It is assumed that the IGP routing topology already has a path to reach the network.
BGP’s default behavior requires that a route have an AS_Path to redistribute into an IGP routing protocol.

## Slide 18: Protocol-Specific Configuration Source Specific Behaviors: BGP (Cont.)
BGP behavior can be changed so that all BGP routes are redistributed with the BGP
configuration command bgp redistribute-internal. To enable the iBGP route 192.168.3.3/32
to redistribute into OSPF, the bgp redistribute-internal command is required on R2.
BGP is designed to handle a large routing table, whereas IGPs are not. Redistributing
BGP into an IGP on a router with a larger BGP table (for example, the Internet table with
800,000+ routes) should use selective route redistribution. Otherwise, the IGP can become
unstable in the routing domain, which can lead to packet loss.
Redistributing iBGP routes into an IGP could result in routing loops. A more logical solution is to advertise the network into the IGP.

## Slide 19: Protocol-Specific Configuration Destination Specific Behaviors: EIGRP
External EIGRP routes are given an AD of 170 and use a default seed metric of infinity,
which prevents the installation of the routes into the EIGRP topology table.
If an EIGRP autonomous system redistributes into another EIGRP autonomous system, all the path metrics are included during redistribution.
The default path metric can be changed from infinity to specific values for bandwidth, load, delay, reliability, and maximum transmission unit (MTU), thereby allowing for the installation into the EIGRP topology table.
Routers can set the default metric with the address family configuration command default-metric bandwidth delay reliability load mtu.
Delay is entered in tens of microseconds (μs).
The metric can also be set within a route map or at the time of redistribution with this command:
redistribute source-protocol [metric bandwidth delay reliability
load mtu] [route-map route-map-name]
Named mode EIGRP configuration occurs in the topology base configuration.

## Slide 20: Protocol-Specific Configuration Destination Specific Behaviors: EIGRP Topology
Figure 16-8 provides a topology example in which R2 mutually redistributes OSPF into
EIGRP and R3 mutually redistributes BGP into EIGRP.
R1 is advertising the Loopback 0 address 192.168.1.1/32, and R4 is advertising the Loopback 0 address 192.168.4.4/32.
Example 16-7 shows the relevant EIGRP configuration. R2 uses the default-metric configuration command and is displayed with classic and named mode configurations.
Notice where the default metrics are placed with EIGRP named mode configuration. R3’s configuration specifies the seed metrics with the redistribution command.

## Slide 21: Protocol-Specific Configuration Destination Specific Behaviors: EIGRP Metrics
You can overwrite EIGRP seed metrics by setting K values with the route map command set metric bandwidth delay reliability load mtu.
Example 16-8 shows the configuration without the use of the default-metric command but by setting the EIGRP metric using a route map.
Example 16-9 shows the EIGRP topology table with the locally redistributed routes highlighted.
The redistributed routes are shown in the routing table with D EX and an AD of 170, as shown in Example 16-10.

## Slide 22: Protocol-Specific Configuration EIGRP-to-EIGRP Redistribution
Redistributing routes between EIGRP autonomous systems preserves the path metrics during redistribution.
Figure 16-9 shows a topology that includes multiple EIGRP autonomous systems.
R2 mutually redistributes routes between AS 10 and AS 20, and R3 mutually redistributes routes between AS 20 and AS 30.
R1 advertises the Loopback 0 interface (192.168.1.1/32) into EIGRP AS 10.
R4 advertises the Loopback 0 interface (192.168.4.4/32) into EIGRP AS 30.

## Slide 23: Protocol-Specific Configuration EIGRP-to-EIGRP Redistribution Configuration
Example 16-11 shows the configurations for R2 and R3.
The default seed metrics do not need to be set because they are maintained between EIGRP ASs.
R2 is using classic configuration mode, and R3 is using EIGRP named configuration mode.

## Slide 24: Protocol-Specific Configuration EIGRP-to-EIGRP Redistribution Verification
Example 16-12 provides verification that R1 has routes learned from AS 20 and AS 30, and R4 has learned routes from AS 10 and AS 20.

## Slide 25: Protocol-Specific Configuration EIGRP-to-EIGRP Redistribution Verification (Cont.)
Example 16-13 shows the EIGRP topology table for the route 192.168.4.4/32 in AS 10 and AS 20.
The EIGRP path metrics for bandwidth, reliability, load, and delay are the same between the autonomous systems.
Notice that the feasible distance (131,072) is the same for both autonomous systems, but the reported distance (RD) is 0 for AS 10 and 130,816 for AS 20.
The RD was reset when it was redistributed into AS 10.

## Slide 26: Protocol-Specific Configuration Destination Specific Behaviors: OSPF
The AD is set to 110 for intra-area, interarea, and external OSPF routes. External OSPF routes are classified as Type 1 or Type 2, with Type 2 as the default setting.
The seed metric is 1 for BGP-sourced routes and 20 for all other protocols.
The exception is that if OSPF redistributes from another OSPF process, the path metric is transferred.
The main differences between Type 1 and Type 2 External OSPF routes follow:
Type 1 routes are preferred over Type 2.
The Type 1 metric equals the redistribution metric plus the total path metric to the autonomous system boundary router (ASBR). In other words, as the LSA propagates away from the originating ASBR, the metric increases.
The Type 2 metric equals only the redistribution metric. The metric is the same for the router next to the ASBR as the router 30 hops away from the originating ASBR.
If two Type 2 paths have exactly the same metric, the lower forwarding cost is preferred. This is the default external metric type used by OSPF.

## Slide 27: Protocol-Specific Configuration Redistribution into OSPF
For redistribution into OSPF, you use this command:
redistribute source-protocol [subnets] [metric metric] [metric-type {1 | 2}]
[tag 0-4294967295] [route-map route-map-name]
If the optional subnets keyword is not included, only the classful networks are redistributed.
The optional tag keyword allows for a 32-bit route tag to be included on all redistributed routes.
The metric and metric-type keywords can be set during redistribution.
Figure 16-10 provides a topology example in which R2 mutually redistributes EIGRP into
OSPF and R3 mutually redistributes RIP into OSPF. R1 is advertising the Loopback 0 interface 192.168.1.1/32, and R4 is advertising the Loopback 0 interface 192.168.4.4/32.

## Slide 28: Protocol-Specific Configuration Redistribution into OSPF Configuration
Example 16-14 shows the relevant OSPF configuration. Notice that R2 and R3 use different OSPF process numbers but are still able to form an adjacency. The OSPF process numbers are locally significant in linking the OSPF-enabled interfaces to a process, as shown later in this section.

## Slide 29: Protocol-Specific Configuration Redistribution into OSPF LSDB
Example 16-15 shows the Type 5 LSAs for the external networks in the OSPF domain.
This example shows that the routes 10.12.1.0/24, 10.34.1.0/24, 192.168.1.1/32, and 192.168.4.4/32 successfully redistributed into OSPF.
The redistributed networks are Type 2 with a metric of 20.
The redistributed routes appear in the routing table with O E2 for Type 2 and O E1 for Type 1 external routes.

## Slide 30: Protocol-Specific Configuration Redistribution into OSPF Verification
In Example 16-16, the routers do not explicitly set a metric type, so all the redistributed routes from the topology are type E2.

## Slide 31: Protocol-Specific Configuration OSPF-to-OSPF Redistribution
Redistributing routes between OSPF processes preserves the path metric during redistribution, independent of the metric type.
Figure 16-11 shows a topology with multiple OSPF processes and areas.
Although the topology in Figure 16-11 looks discontiguous, OSPF is redistributing the routes between processes. This technique can be used to advertise routes over discontiguous OSPF networks, but it results in the loss of path information as the Type 1, Type 2, and Type 3 LSAs are not propagated through route redistribution.

## Slide 32: Protocol-Specific Configuration OSPF-to-OSPF Redistribution (Cont.)
Example 16-17 shows the relevant configurations for R2 and R3. Notice that the metric type is set at the time of redistribution into the destination protocol so that you can see the metric increase as the route travels between the OSPF processes.
Example 16-18 provides verification that R1 has routes learned from OSPF process 3 (R3 and R4) and that R4 has routes learned from OSPF process 1 (R1 and R2). Notice that the metrics have carried over through the redistribution.

## Slide 33: Protocol-Specific Configuration OSPF Forwarding Address
OSPF Type 5 LSAs include a field known as the forwarding address that optimizes forwarding traffic when the source uses a shared network segment.
The scenario defined in RFC 2328 is not common but is shown in Figure 16-12.
Example 16-19 shows the Type 5 LSA for the AS 100 route for 192.168.1.1/32.
Network traffic from R3 (and R5) takes the suboptimal route (R3→R5→R4→R2→R1), as shown in Example 16-20. The optimal route would use the directly connected 10.123.1.0/24 network.

## Slide 34: Protocol-Specific Configuration OSPF Forwarding Nondefault
The OSPF forwarding address changes from 0.0.0.0 to the next-hop IP address in the source routing protocol when:
OSPF is enabled on the ASBR’s interface that points to the next-hop IP address.
That interface is not set to passive.
That interface is a broadcast or nonbroadcast OSPF network type.
When the forwarding address is set to a value besides 0.0.0.0, the OSPF routers forward traffic only to the forwarding address.
Example 16-21 provides the Type 5 LSA for the 192.168.1.1/32 network. Now that OSPF has been enabled on R2’s 10.123.1.2 interface and the interface is a broadcast network type, the forwarding address has changed from 0.0.0.0 to 10.123.1.1.

## Slide 35: Protocol-Specific Configuration OSPF Forwarding Address Verification
Example 16-22 verifies that connectivity from R3 and R5 now takes the optimal path to R1 because the forwarding address has changed to 10.123.1.1.
If the Type 5 LSA forwarding address is not a default value, the address must be an intra-area or interarea OSPF route.
If the route does not exist, the LSA is ignored and is not installed into the RIB.
The OSPF forwarding address optimizes forwarding toward the destination network, but return traffic is unaffected. In Figure 16-13, outbound traffic from R3 or R5 still exits at R3’s Gi0/0 interface, but return traffic is sent directly to R2.

## Slide 36: Protocol-Specific Configuration Redistribution into BGP
Redistributing routes into BGP does not require a seed metric because BGP is a path vector protocol. Redistributed routes have the following BGP attributes set:
The origin is set to incomplete.
The next-hop address is set to the IP address of the source protocol.
The weight is set to 32,768.
The MED is set to the path metric of the source protocol.
Figure 16-14 shows a topology in which R2 mutually redistributes between OSPF and
BGP, and R3 mutually redistributes between EIGRP AS 65100 and BGP.

## Slide 37: Protocol-Specific Configuration Redistribution into BGP Configuration
Example 16-23 shows R2’s BGP configuration for redistributing OSPF into BGP on R2 and R3’s configuration for redistributing EIGRP into BGP.
R3 has disabled the default IPv4 address family configuration.
Notice that R2 and R3 have used the command bgp redistribute-internal, which allows for any iBGP learned prefixes to be redistributed into OSPF or EIGRP.
Example 16-24 shows the BGP table for AS 65100. Notice that the 192.168.1.1/32 and 192.168.4.4/32 networks have been installed into the BGP table. The metric is carried over from the IGP metric during redistribution.

## Slide 38: Protocol-Specific Configuration Redistribution into BGP Verification
Example 16-25 shows detailed BGP path information for the redistributed routes. The origin is incomplete, and the BGP metric matches the IGP metric at the time of redistribution.
Redistributing routes from OSPF to BGP does not include OSPF external routes by default. match external [1 | 2] is required to redistribute OSPF external routes.

## Slide 39: Prepare for the Exam

## Slide 40: Prepare for the Exam Key Topics for Chapter 16
Description | Description
Redistribution terminology | Destination protocol: EIGRP
Redistribution is not transitive | EIGRP seed metrics
Sequential protocol redistribution | EIGRP-to-EIGRP redistribution
Routes must exist in the RIB | Destination protocol: OSPF
Seed metrics | OSPF classful and classless redistribution
Redistribution source protocol chart | OSPF-to-OSPF redistribution
Source protocol: connected networks | OSPF forwarding address
Source protocol: BGP | Destination protocol: BGP

## Slide 41: Prepare for the Exam Key Terms for Chapter 16
Terms
destination protocol
mutual redistribution
source protocol
sequential protocol redistribution
seed metric

## Slide 42: Prepare for the Exam Command Reference for Chapter 16
Terms | 
Redistribute the source routing protocol into a destination routing protocol | redistribute {connected ¦ static ¦ eigrp as-number ¦ ospf process-id [match {internal ¦ external [1¦2]}] ¦ bgp as-number } [destinationprotocol- options] [route-map route-map-name]
Set the default EIGRP seed metric for redistributed prefixes | default-metric bandwidth delay reliability load mtu
Allow for the redistribution of iBGP learned prefixes into an IGP | bgp redistribute-internal