## Slide 1
Based on Cisco
IPSec fundamentals

## Slide 2: Layer 3 VPN
IPSec
Generic routing encapsulation (GRE)
Multiprotocol Label Switching (MPLS)
SOHO with a Cisco DSL Router
VPN
Internet
IPSec
IPSec

## Slide 3: Types of VPN Networks
MARS
VPN
VPN
Iron Port
Firewall
IPS
Web Server
Email Server
DNS
CSA
CSA
CSA
CSA
CSA
CSA
CSA
Regional branch with
a VPN enabled
Cisco ISR router
SOHO with a Cisco DSL Router
VPN
Mobile Worker
with a Cisco
VPN Client
Business Partner
with a Cisco Router
Site-to-Site
VPNs
Remote-access
VPNs
Internet
WAN

## Slide 4: Site-to-Site VPN
MARS
VPN
VPN
Iron Port
Firewall
IPS
Web Server
Email Server
DNS
CSA
CSA
CSA
CSA
CSA
CSA
CSA
Regional branch with
a VPN enabled
Cisco ISR router
SOHO with a Cisco DSL Router
VPN
Business Partner
with a Cisco Router
Site-to-Site
VPNs
Internet
WAN
Hosts send and receive normal TCP/IP traffic through a VPN gateway

## Slide 5: VPN Client Software
R1
R1-vpn-cluster.span.com
“R1”
In a remote-access VPN, each host typically has Cisco AnyConnect VPN Client software

## Slide 6: IPSec Framework
Diffie-Hellman
DH7

## Slide 7: IPSec Framework Protocols
All data is in plaintext.
R1
R2
Data payload is encrypted.
R1
R2
Authentication Header
Encapsulating Security Payload
AH provides the following:
  Authentication
  Integrity
ESP provides the following:
  Encryption
  Authentication
  Integrity

## Slide 8: Mode Types
IP HDR
ESP HDR
Data
ESP HDR
IP HDR
New IP HDR
Data
Tunnel Mode
Transport Mode
ESP
Trailer
ESP
Auth
ESP
Trailer
ESP
Auth
Authenticated
Authenticated
IP HDR
Data
Encrypted
Encrypted
Original data prior to selection of IPSec protocol mode

## Slide 9: IPSec facilities
IPSec
IKE
ISAKMP
Tasks to Configure IPsec:
Internet Key Exchange (IKEv1, IKEv2) is the protocol used to set up a security association (SA) in the IPsec protocol suite. IKE builds upon the Oakley* protocol, SKEME* and ISAKMP.
Internet Security Association and Key Management Protocol (ISAKMP) is the protocol for establishing Security association (SA) and cryptographic keys in an Internet environment. ISAKMP only provides a framework for authentication and key exchange and is designed to be key exchange independent.
Security Association (SA) is SA is a logical group of security parameters that enable the sharing of information to another entity.
  An SA may include attributes such as: cryptographic algorithm and mode; traffic encryption key; and parameters for the network data to be passed over the connection.
  SA is a simplex (one-way channel) and logical connection.
  Each SA has its own ID called SAID.
  There are two levels of SAs: ISAKMP SA and IPSec SA

## Slide 10: IPSec VPN Negotiation
IKE Phase 1
IKE Phase 2
ISAKMP SA
ISAKMP SA
IPsec SA
IPsec SA
Host A sends interesting traffic to Host B.
R1 and R2 negotiate an IKE (ISAKMP) Phase 1 session.
R1 and R2 negotiate an IKE (IPSEc) Phase 2 session.
Information is exchanged via IPsec tunnel.
The IPsec tunnel is terminated.
R1
R2
10.0.2.3
IPsec Tunnel
10.0.1.3
Authentication, keys negotiation
AH or ESP, security policy, parameters

## Slide 11: Configuring IPsec
Tasks to Configure IPsec:
Task 1: Ensure that ACLs are compatible with IPsec.
Task 2: Create ISAKMP (IKE) policy (Cisco: IKE≡ISAMP).
Task 3: Configure IPsec transform set.
Task 4: Create a crypto ACL.
Task 5: Create and apply the crypto map.

## Slide 12: Task 1 Configure Compatible ACLs
Ensure that protocols 50 (ESP), 51 (AH) and UDP port 500 (ISAKMP) traffic are not blocked by incoming ACLs on interfaces used by IPsec.
AH
ESP
IKE
Site 1
Site 2
10.0.1.3
10.0.2.3
R1
R2
Internet
S0/0/0 172.30.1.2
S0/0/0 172.30.2.2
10.0.1.0/24
10.0.2.0/24

## Slide 13: Permitting Traffic
R1(config)# access-list 102 permit ahp host 172.30.2.2 host 172.30.1.2
R1(config)# access-list 102 permit esp host 172.30.2.2 host 172.30.1.2
R1(config)# access-list 102 permit udp host 172.30.2.2 host 172.30.1.2 eq isakmp
R1(config)#
R1(config)# interface Serial0/0/0
R1(config-if)# ip address 172.30.1.2 255.255.255.0
R1(config-if)# ip access-group 102 in
!
R1(config)# exit
R1#
R1# show access-lists
access-list 102 permit ahp host 172.30.2.2 host 172.30.1.2
access-list 102 permit esp host 172.30.2.2 host 172.30.1.2
access-list 102 permit udp host 172.30.2.2 host 172.30.1.2 eq isakmp
R1#
AH
ESP
IKE
Site 1
Site 2
10.0.1.3
10.0.2.3
R1
R2
Internet
S0/0/0 172.30.1.2
S0/0/0 172.30.2.2
10.0.1.0/24
10.0.2.0/24

## Slide 14: Task 2 Configure ISAKMP
Defines the parameters within the IKE policy
crypto isakmp policy priority
router(config)#
R1(config)# crypto isakmp policy 110
R1(config–isakmp)# authentication pre-share
R1(config–isakmp)# encryption des
R1(config–isakmp)# group 1
R1(config–isakmp)# hash md5
R1(config–isakmp)# lifetime 86400
Tunnel
Policy 110
DES MD5
Preshare
86400 DH1
Site 1
Site 2
10.0.1.3
10.0.2.3
R1
R2
Internet
10.0.1.0/24
10.0.2.0/24

## Slide 15: ISAKMP Parameters
Parameter | Keyword | Accepted Values | Default Value | Description
encryption | des 3des aes aes 192 aes 256 | 56-bit Data Encryption Standard Triple DES 128-bit AES 192-bit AES 256-bit AES | des | Message encryption algorithm
hash | sha md5 | SHA-1 (HMAC variant) MD5 (HMAC variant) | sha | Message integrity (Hash) algorithm
authentication | pre-share rsa-encr rsa-sig | preshared keys RSA encrypted nonces RSA signatures | rsa-sig | Peer authentication method
group | 1 2 5 | 768-bit Diffie-Hellman (DH) 1024-bit DH 1536-bit DH | 1 | Key exchange parameters (DH group identifier)
lifetime | seconds | Can specify any number of seconds | 86,400 sec (one day) | ISAKMP-established SA lifetime
Notes: Note: Actual parameters vary based on IOS image.

## Slide 16: Multiple Policies
crypto isakmp policy 100
hash md5
authentication pre-share
!
crypto isakmp policy 200
hash sha
authentication rsa-sig
!
crypto isakmp policy 300
hash md5
authentication rsa-sig
crypto isakmp policy 100
hash md5
authentication pre-share
!
crypto isakmp policy 200
hash sha
authentication rsa-sig
!
crypto isakmp policy 300
hash md5
authentication pre-share
R1(config)#
R2(config)#
Site 1
Site 2
10.0.1.3
10.0.2.3
R1
R2
Internet
10.0.1.0/24
10.0.2.0/24

## Slide 17: Policy Negotiations
R1(config)# crypto isakmp policy 110
R1(config–isakmp)# authentication pre-share
R1(config–isakmp)# encryption 3des
R1(config–isakmp)# group 2
R1(config–isakmp)# hash sha
R1(config–isakmp)# lifetime 43200
Policy 110
Preshare
3DES SHA
DH2
43200
R2(config)# crypto isakmp policy 100
R2(config–isakmp)# authentication pre-share
R2(config–isakmp)# encryption 3des
R2(config–isakmp)# group 2
R2(config–isakmp)# hash sha
R2(config–isakmp)# lifetime 43200
R2 must have an ISAKMP policy configured with the same parameters.
Tunnel
Site 1
Site 2
10.0.1.3
10.0.2.3
R1
R2
Internet
10.0.1.0/24
10.0.2.0/24
R1 attempts to establish a VPN tunnel with R2 and sends its ISAKMP policy parameters
Notes:   Notice however, that policy numbers are only locally significant and do not have to match between IPsec peers.

## Slide 18: Crypto ISAKMP Key
The peer-address or peer-hostname can be used, but must be used consistently between peers.
If the peer-hostname is used, then the crypto isakmp identity hostname command must also be configured.
crypto isakmp key keystring address peer-address
router(config)#
crypto isakmp key keystring hostname peer-hostname
router(config)#
Parameter | Description
keystring | This parameter specifies the PSK. Use any combination of alphanumeric characters up to 128 bytes. This PSK must be identical on both peers.
peer-address | This parameter specifies the IP address of the remote peer.
hostname | This parameter specifies the hostname of the remote peer. This is the peer hostname concatenated with its domain name (for example, myhost.domain.com).

## Slide 19: Sample Configuration
R1(config)# crypto isakmp policy 110
R1(config–isakmp)# authentication pre-share
R1(config–isakmp)# encryption 3des
R1(config–isakmp)# group 2
R1(config–isakmp)# hash sha
R1(config–isakmp)# lifetime 43200
R1(config-isakmp)# exit
R1(config)# crypto isakmp key cisco123 address 172.30.2.2
R1(config)#
R2(config)# crypto isakmp policy 110
R2(config–isakmp)# authentication pre-share
R2(config–isakmp)# encryption 3des
R2(config–isakmp)# group 2
R2(config–isakmp)# hash sha
R2(config–isakmp)# lifetime 43200
R2(config-isakmp)# exit
R2(config)# crypto isakmp key cisco123 address 172.30.1.2
R2(config)#
Note:
The keystring cisco1234 matches.
The address identity method is specified.
The ISAKMP policies are compatible.
Default values do not have to be configured.
Site 1
Site 2
10.0.1.3
10.0.2.3
R1
R2
Internet
10.0.1.0/24
10.0.2.0/24

## Slide 20: Task 3 Configure the Transform Set
router(config)#
crypto ipsec transform–set transform-set-name transform1 [transform2] [transform3]]
crypto ipsec transform-set Parameters
Command | Description
transform-set-name | This parameter specifies the name of the transform set to create (or modify).
transform1, transform2, transform3 | Type of transform set. You may specify up to four "transforms": one Authentication Header (AH), one Encapsulating Security Payload (ESP) encryption, one ESP authentication. These transforms define the IP Security (IPSec) security protocols and algorithms.
A transform set is a combination of IPsec transforms that enact a security policy for traffic. Also called IPSec proposals!
Notes: A transform set can have one AH transform and up to two ESP transforms

## Slide 21: Transform Sets
Transform sets are negotiated during IKE Phase 2.
The 9th attempt found matching transform sets (CHARLIE - YELLOW).
Host B
10.0.1.3
10.0.2.3
R1
R2
Host A
transform-set ALPHA
esp-3des
tunnel
transform-set BETA
esp-des, esp-md5-hmac
tunnel
transform-set CHARLIE
esp-3des, esp-sha-hmac
tunnel
transform-set RED
esp-des
tunnel
transform-set BLUE
esp-des, ah-sha-hmac
tunnel
transform-set YELLOW
esp-3des, esp-sha-hmac
tunnel
Match
Internet
1
2
3
4
5
6
7
8
9
172.30.2.2
172.30.1.2

## Slide 22: Sample Configuration
R1(config)# crypto isakmp key cisco123 address 172.30.2.2
R1(config)# crypto ipsec transform-set MYSET esp-aes 128
R1(cfg-crypto-trans)# exit
R1(config)#
Site 1
Site 2
A
B
10.0.1.3
10.0.2.3
R1
R2
Internet
R2(config)# crypto isakmp key cisco123 address 172.30.1.2
R2(config)#crypto ipsec transform-set OTHERSET esp-aes 128
R2(cfg-crypto-trans)# exit
172.30.2.2
172.30.1.2
Note:
Peers must share the same transform set settings.
Names are only locally significant.

## Slide 23: Task 4 Configure the Crypto ACLs
Outbound indicates the data flow to be protected by IPsec.
Inbound filters and discards traffic that should have been protected by IPsec.
Host A
R1
Internet
Outbound Traffic
Inbound Traffic
Encrypt
Bypass (Plaintext)
Permit
Bypass
Discard (Plaintext)

## Slide 24: Command Syntax
10.0.1.3
10.0.2.3
R1
R2
Internet
router(config)#
access-list access-list-number [dynamic dynamic-name [timeout minutes]]{deny | permit} protocol source source-wildcard destination destination-wildcard [precedence precedence] [tos tos] [log]
access-list access-list-number Parameters
access-list access-list-number Command | Description
permit | This option causes all IP traffic that matches the specified conditions to be protected by cryptography, using the policy described by the corresponding crypto map entry.
deny | This option instructs the router to route traffic in plaintext.
protocol | This option specifies which traffic to protect by cryptography based on the protocol, such as TCP, UDP, or ICMP. If the protocol is IP, then all traffic IP traffic that matches that permit statement is encrypted.
source and destination | If the ACL statement is a permit statement, these are the networks, subnets, or hosts between which traffic should be protected. If the ACL statement is a deny statement, then the traffic between the specified source and destination is sent in plaintext.
10.0.1.0/24
Site 1
10.0.2.0/24
Site 2
S0/0/0
172.30.1.2
S0/0/0
172.30.2.2

## Slide 25: Symmetric Crypto ACLs
S0/1
10.0.1.3
10.0.2.3
R1
R2
Internet
Site 2
Applied to R1 S0/0/0 outbound traffic:
R1(config)# access-list 110 permit tcp 10.0.1.0 0.0.0.255 10.0.2.0 0.0.0.255
(when evaluating inbound traffic– source: 10.0.2.0, destination: 10.0.1.0)
S0/0/0
172.30.2.2
S0/0/0
172.30.1.2
Applied to R2 S0/0/0 outbound traffic:
R2(config)# access-list 101 permit tcp 10.0.2.0 0.0.0.255 10.0.1.0 0.0.0.255
(when evaluating inbound traffic- source: 10.0.1.0, destination: 10.0.2.0)
10.0.1.0/24
Site 1
10.0.2.0/24

## Slide 26: Task 5 Apply the Crypto Map
Crypto maps define the following:
  ACL to be used
  Remote VPN peers
  Transform set to be used
  Key management method
  SA lifetimes
Site 1
10.0.1.3
R1
R2
10.0.2.3
Site 2
Internet
Encrypted Traffic
Router Interface
or Subinterface

## Slide 27: Crypto Map Command
crypto map map-name seq-num ipsec-manual
crypto map map-name seq-num ipsec-isakmp [dynamic dynamic-map-name]
router(config)#
crypto map parameters
Command Parameters | Description
map-name | Defines the name assigned to the crypto map set or indicates the name of the crypto map to edit.
seq-num | The number assigned to the crypto map entry.
ipsec-manual | Indicates that ISAKMP will not be used to establish the IPsec SAs.
ipsec-isakmp | Indicates that ISAKMP will be used to establish the IPsec SAs.
cisco | (Default value) Indicates that CET will be used instead of IPsec for protecting the traffic.
dynamic | (Optional) Specifies that this crypto map entry references a preexisting static crypto map. If this keyword is used, none of the crypto map configuration commands are available.
dynamic-map-name | (Optional) Specifies the name of the dynamic crypto map set that should be used as the policy template.

## Slide 28: Crypto Map Configuration Mode Commands
Command | Description
set | Used with the peer, pfs, transform-set, and security-association commands.
peer [hostname ¦ ip-address] | Specifies the allowed IPsec peer by IP address or hostname.
pfs [group1 ¦ group2] | Specifies DH Group 1 or Group 2. (See next slide)
transform-set [set_name(s)] | Specify list of transform sets in priority order. When the ipsec-manual parameter is used with the crypto map command, then only one transform set can be defined. When the ipsec-isakmp parameter or the dynamic parameter is used with the crypto map command, up to six transform sets can be specified.
security-association lifetime | Sets SA lifetime parameters in seconds or kilobytes.
match address [access-list-id ¦ name] | Identifies the extended ACL by its name or number. The value should match the access-list-number or name argument of a previously defined IP-extended ACL being matched.
no | Used to delete commands entered with the set command.
exit | Exits crypto map configuration mode.

## Slide 29: PFS – Perfect Forward Secrecy
Forward Secrecy (FS), also known as Perfect Forward Secrecy (PFS)
IPsec property that ensures that derived session keys are not compromised if one of the private keys is compromised in the future.
PFS periodically creates a new key value based on values supplied by both parties in the exchange.
  Both parties contribute a random value known only to them, each new key generated is dissimilar to previously created keys.
  Using PFS means that even if a third party managed to intercept a symmetrical key, that party can only use the intercepted key for a short time.
  Typically uses an ephemeral Diffie–Hellman key Exchange.
If an adversary can make the random number generator predictable, then past traffic will be protected but all future traffic will be compromised.

## Slide 30: Sample Configuration
Multiple peers can be specified for redundancy.
R3
S0/0/0 172.30.3.2
R1(config)# crypto map MYMAP 10 ipsec-isakmp
R1(config-crypto-map)# match address 110
R1(config-crypto-map)# set peer 172.30.2.2 default
R1(config-crypto-map)# set peer 172.30.3.2
R1(config-crypto-map)# set pfs group1
R1(config-crypto-map)# set transform-set mine
R1(config-crypto-map)# set security-association lifetime seconds 86400
10.0.1.3
10.0.2.3
R1
R2
Internet
10.0.1.0/24
Site 1
10.0.2.0/24
Site 2
S0/0/0
172.30.2.2

## Slide 31: Assign the Crypto Map Set
Applies the crypto map to outgoing interface
Activates the IPsec policy
crypto map map-name
R1(config)# interface serial0/0/0
R1(config-if)# crypto map MYMAP
router(config-if)#
MYMAP
10.0.1.3
10.0.2.3
R1
R2
Internet
10.0.1.0/24
Site 1
10.0.2.0/24
Site 2
S0/0/0
172.30.1.2
S0/0/0
172.30.2.2

## Slide 32: CLI Commands
Show Command | Description
show crypto map | Displays configured crypto maps
show crypto isakmp policy | Displays configured IKE policies
show crypto ipsec sa | Displays established IPsec tunnels
show crypto ipsec transform-set | Displays configured IPsec transform sets
debug crypto isakmp | Debugs IKE events
debug crypto ipsec | Debugs IPsec events

## Slide 33: show crypto map
R1# show crypto map
Crypto Map “MYMAP" 10 ipsec-isakmp
  Peer = 172.30.2.2
  Extended IP access list 110
  access-list 102 permit ip host 10.0.1.3 host 10.0.2.3
  Current peer: 172.30.2.2
  Security association lifetime: 4608000 kilobytes/3600 seconds
  PFS (Y/N): N
  Transform sets={ MYSET, }
show crypto map
Displays the currently configured crypto maps
router#
10.0.1.3
10.0.2.3
R1
R2
Internet
10.0.1.0/24
Site 1
10.0.2.0/24
Site 2
S0/0/0
172.30.1.2
S0/0/0
172.30.2.2

## Slide 34: show crypto isakmp policy
show crypto isakmp policy
R1# show crypto isakmp policy
Protection suite of priority 110
encryption algorithm: 3DES - Data Encryption Standard (168 bit keys).
hash algorithm: Secure Hash Standard
authentication method: preshared
Diffie-Hellman group: #2 (1024 bit)
lifetime: 86400 seconds, no volume limit
Default protection suite
encryption algorithm: DES - Data Encryption Standard (56 bit keys).
hash algorithm: Secure Hash Standard
authentication method: Rivest-Shamir-Adleman Signature
Diffie-Hellman group: #1 (768 bit)
lifetime: 86400 seconds, no volume limit
router#
10.0.1.3
10.0.2.3
R1
R2
Internet
10.0.1.0/24
Site 1
10.0.2.0/24
Site 2
S0/0/0
172.30.1.2
S0/0/0
172.30.2.2

## Slide 35: show crypto ipsec transform-set
show crypto ipsec transform-set
Displays the currently defined transform sets
R1# show crypto ipsec transform-set
Transform set AES_SHA: { esp-128-aes esp-sha-hmac }
  will negotiate = { Tunnel, },
10.0.1.3
10.0.2.3
R1
R2
Internet
10.0.1.0/24
Site 1
10.0.2.0/24
Site 2
S0/0/0
172.30.1.2
S0/0/0
172.30.2.2

## Slide 36: show crypto ipsec sa
R1# show crypto ipsec sa
Interface: Serial0/0/0
Crypto map tag: MYMAP, local addr. 172.30.1.2
local ident (addr/mask/prot/port): (172.30.1.2/255.255.255.255/0/0)
remote ident (addr/mask/prot/port): (172.30.2.2/255.255.255.255/0/0)
current_peer: 172.30.2.2
PERMIT, flacs={origin_is_acl,}
#pkts encaps: 21, #pkts encrypt: 21, #pkts digest 0
#pkts decaps: 21, #pkts decrypt: 21, #pkts verify 0
#send errors 0, #recv errors 0
local crypto endpt.: 172.30.1.2, remote crypto endpt.: 172.30.2.2
path mtu 1500, media mtu 1500
current outbound spi: 8AE1C9C
10.0.1.3
10.0.2.3
R1
R2
Internet
10.0.1.0/24
Site 1
10.0.2.0/24
Site 2
S0/0/0
172.30.1.2
S0/0/0
172.30.2.2

## Slide 37: debug crypto isakmp
debug crypto isakmp
router#
This is an example of the Main Mode error message.
The failure of Main Mode suggests that the Phase I policy does not match on both sides.
Verify that the Phase I policy is on both peers and ensure that all the attributes match.
1d00h: ISAKMP (0:1): atts are not acceptable. Next payload is 0 1d00h: ISAKMP (0:1); no offers accepted!
1d00h: ISAKMP (0:1): SA not acceptable!
1d00h: %CRYPTO-6-IKMP_MODE_FAILURE: Processing of Main Mode failed with peer at 172.30.2.2

## Slide 38
Thank you