## Slide 1: Implementation of Solid State Drives to Enterprise Systems
Bc. Matej Fuček
Notes: Tu sa predstavim a poviem svoju temu

## Slide 2: Objective of the work
Is the SSD technology sufficient replacement for HDD in Enterprise Systems?
Are SSDs fast enough?
Can SSD unconditionally replace HDDs?
Notes: Tu by som spomenul moju motivaciu preco som si vybral danu temu. Dalej by som vysvetlil ze SSD su nova technologia a je notne prehodnotit ci a kde je vhodne pouzita pretoze vsetko ma svoje vyhody a nevyhody a je nutne najst balance pre najoptimalnejsie riesienie

## Slide 3: Experimental Performance Evaluation
Performance of Single SSDs vs. single HDDs
Performance of RAID 0 using only HDDs
Performance of RAID 0 using only SSDs
Performance of mixed RAID 0 (HDD + SSD)
Performance of RAID 1 using only HDDs
Performance of RAID 1 using only SSDs
Performance of mixed RAID 1 (HDD + SSD)
NTFS, FAT32 and exFAT performance

## Slide 4: Environment
Drives:
2x ADATA SX900 128GB
2x Kingston V300 120GB
Lite-ON IT LMT-128m6m 128GB
Western Digital 10EZEX-00RKKA0 1TB
Western Digital 20EFRX-68AX9N0 2TB
4x Patriot WARP 32GB (disqualified)
CPU | AMD A10-5700 Quad-core @3.7GHz with SilverStone Heligon HE02 cooler
RAM | 16GB Corsair Vengeance Low Profile Black 16GB (4x4GB) DDR3 1600
MotherBoard | GigaByte GA-F2A85X-D3H rev 1.0 AMDK15 IMC, AMD A85X FCH Bios AM –F1
System drive | Kingston V300 120GB
GPU | AMD Radeon HD7600D
PSU | Seasonic X-750, 750W
Operating System | Windows 7 Ultimate x64 + updates till 24th August 2014
Drivers | AMD Chipset Driver (include chipset \ sata raid \ VGA \ USB driver) v. 13.25 AMD RAID Driver v3.3.1540.40
PC case | LIAN-LI PC-V2120B, with 3x40mm and 5x120mm fan
Benchmark software | HD-Tune v5.50 CrystalDiskMark 3.0.3 x64 ATTO Disk Benchmark v2.46
Notes: Kingston failnul
Predstavit test tooly

## Slide 5: Performance SSD vs. HDD
Chart: Sequential Read and Write in MB/s, CrystalDiskMark 3.0.3 x64
| 1st ADATA SX900 128GB | 2nd ADATA SX900 128GB | Kingston V300 120GB | Lite-ON IT LMT-128m6m 128GB | Western Digital 10EZEX-00RKKA0 1TB | Western Digital 20EFRX-68AX9N0 2TB
Read <0Fill> | 470.5 | 472.6 | 466.7 | 482.1 | 186 | 155.1
Read <1Fill> | 469 | 471.1 | 464 | 479.2 | 186.2 | 158.7

Write <0Fill> | 445.3 | 444.2 | 444.4 | 322.1 | 182 | 154.2
Write <1Fill> | 443.6 | 445.4 | 443.1 | 321.6 | 181.6 | 157.7
Notes: Tu demonstrujem vysledky Sequential a ukazem ze SSD su vykonnejsie nez HDD

## Slide 6
Chart: Random 4K QD32 Read and Write in MB/s, CrystalDiskMark 3.0.3 x64
| 1st ADATA SX900 128GB | 2nd ADATA SX900 128GB | Kingston V300 120GB | Lite-ON IT LMT-128m6m 128GB | Western Digital 10EZEX-00RKKA0 1TB | Western Digital 20EFRX-68AX9N0 2TB
Read <0Fill> | 107.6 | 113.1 | 123.2 | 275 | 2.135 | 1.417
Read <1Fill> | 113.7 | 109.2 | 126.3 | 273.3 | 2.052 | 1.665

Write <0Fill> | 266.2 | 266.2 | 263 | 207.8 | 1.75 | 1.891
Write <1Fill> | 266.1 | 266.3 | 260.6 | 207.4 | 1.723 | 1.708
Notes: Tu ukazem ze SSD su nie len vykonnejsie ale v paralelnych pristupoch doslova prevalcuju HDD. Nasledne by som spomenul pri tomto slajde ze za tento vykon sa plati dan nizsou zivotnostnostou a kapacitou a vyssou cenou.
Liteon ma vyssi SandForce chip a asi aj sirsiu zbernicu

## Slide 7: RAID0 performance
Chart: Sequential Read and Write in MB/s, CrystalDiskMark 3.0.3 x64
| SSD RAID 0 | HDD RAID 0
Read <0Fill> | 914.9 | 302
Read <1Fill> | 938.5 | 321

Write <0Fill> | 962.7 | 296.8
Write <1Fill> | 957.5 | 313.5
Chart: 4KQD32 Read and Write in MB/s, CrystalDiskMark 3.0.3 x64
| SSD RAID 0 | HDD RAID 0
Read <0Fill> | 229.4 | 3.59
Read <1Fill> | 228.8 | 2.85

Write <0Fill> | 195.9 | 4.26
Write <1Fill> | 195.3 | 4.19
Notes: Tu prezentujem RAID 0 performance vysledky

## Slide 8: RAID1 Performance
Chart: Sequential Read and Write in MB/s, CrystalDiskMark 3.0.3 x64
| SSD RAID 1 | HDD RAID 1
Read <0Fill> | 503.2 | 158.7
Read <1Fill> | 504.3 | 161.9

Write <0Fill> | 481.6 | 151.9
Write <1Fill> | 480.8 | 153
Chart: Random 4K QD32 Read and Write in MB/s, CrystalDiskMark 3.0.3 x64
| SSD RAID 1 | HDD RAID 1
Read <0Fill> | 116.3 | 3.41
Read <1Fill> | 115.1 | 1.83

Write <0Fill> | 171 | 2
Write <1Fill> | 168 | 2.02
Notes: Tu prezentujem RAID 1 performance vysledky

## Slide 9: Enterprise Systems
Transactional Processing Server
Video Server
High Performance Computing Server
Virtualization Server
Internet/Network Server
Notes: Transactional- fast-backup index
Video – hierarchy types of videos
Storage attached or Server attached

## Slide 10: Additional findings
Old SSDs unsupported by systems
Hardware RAID not optimized for SSDs
Mixed SSD and HDD RAID are not as effective as expected
Special hardware RAID needed for optimized performance of mixed HDD, SSD solutions
RAID4, 5, 6 wear-leveling issue
NTFS/FAT32 and exFAT performance
Notes: Tu by som popisal zistenia a problems
Rozmyslam ze tuto cast roztiahnem na viac slajdov

## Slide 11: NTFS/FAT32 and exFAT performance
Chart: PCMark7 Storage tests in MB/s
| Windows Defender | Application Loading | Gaming | Importing Music | Windows Media Centre | Importing pictures | Video editing
NTFS | 5.35 | 56.5 | 16.75 | 1.39 | 8.24 | 29.51 | 23.05
FAT32 | 5.36 | 55.7 | 16.73 | 1.39 | 8.24 | 29.49 | 22.95
exFAT | 5.39 | 56.53 | 16.75 | 1.39 | 8.24 | 29.55 | 23.09

## Slide 12: Conclusions & Future Work
SSDs are much faster
More reliable but wear faster
SSD RAIDs still lack desired performance
File systems have minimal impact on performance
SSD deployment is still limited
Improve life expectancy of MTL and TLC by downgrading to SLC
Performance measurements of database systems –PostgreSQL
SSD RAID optimization
Notes: For future system ktory by spravil z MLC a TCL pri zaciatku failovani iba SLC pretoze tam je 4V buffer ktory by sa este dal vyuzit kapacita by sa znizila na 3x.

## Slide 13
Thank you
for your attention