## Slide 1: Chapter 7: Routing Dynamically
Routing & Switching

## Slide 2: Chapter 7
7.1 Dynamic Routing Protocols
7.2 Distance Vector Dynamic Routing
7.3 RIP and RIPng Routing
7.4 Link-State Dynamic Routing
7.5 The Routing Table
7.6 Summary

## Slide 3: Chapter 7: Objectives
Explain the basic operation of dynamic routing protocols.
Compare and contrast dynamic and static routing.
Determine which networks are available during an initial network discovery phase.
Define the different categories of routing protocols.
Describe the process by which distance vector routing protocols learn about other networks.
Identify the types of distance-vector routing protocols.
Configure the RIP routing protocol.
Configure the RIPng routing protocol.
Explain the process by which link-state routing protocols learn about other networks.

## Slide 4: Chapter 7: Objectives (cont.)
Describe the information sent in a link-state update.
Describe advantages and disadvantages of using link-state routing protocols.
Identify protocols that use the link-state routing process. (OSPF, IS-IS)
Determine the route source, administrative distance, and metric for a given route.
Explain the concept of a parent/child relationship in a dynamically built routing table.
Compare the IPv4 classless route lookup process and the IPv6 lookup process.
Analyze a routing table to determine which route will be used to forward a packet.

## Slide 5: Dynamic Routing Protocol Operation The Evolution of Dynamic Routing Protocols
Dynamic routing protocols used in networks since the late 1980s
Newer versions support the communication based on IPv6
Routing Protocols Classification
Notes: 7.1.1.1 The Evolution of Dynamic Routing Protocols

## Slide 6: Dynamic Routing Protocol Operation Purpose of Dynamic Routing Protocols
Routing Protocols are used to facilitate the exchange of routing information between routers.
The purpose of dynamic routing protocols includes:
Discovery of remote networks
Maintaining up-to-date routing information
Choosing the best path to destination networks
Ability to find a new best path if the current path is no longer available
Notes: 7.1.1.2 Purpose of Dynamic Routing Protocols

## Slide 7: Dynamic Routing Protocol Operation Purpose of Dynamic Routing Protocols (cont.)
Main components of dynamic routing protocols include:
Data structures - Routing protocols typically use tables or databases for its operations. This information is kept in RAM.
Routing protocol messages - Routing protocols use various types of messages to discover neighboring routers, exchange routing information, and other tasks to learn and maintain accurate information about the network.
Algorithm - Routing protocols use algorithms for facilitating routing information for best path determination.
Notes: 7.1.1.2 Purpose of Dynamic Routing Protocols (cont.)

## Slide 8: Dynamic Routing Protocol Operation Purpose of Dynamic Routing Protocols (cont.)
Notes: 7.1.1.2 Purpose of Dynamic Routing Protocols (cont.)

## Slide 9: Dynamic Routing Protocol Operation The Role of Dynamic Routing Protocols
Advantages of dynamic routing include:
Automatically share information about remote networks
Determine the best path to each network and add this information to their routing tables
Compared to static routing, dynamic routing protocols require less administrative overhead
Help the network administrator manage the time-consuming process of configuring and maintaining static routes
Disadvantages of dynamic routing include:
Part of a router’s resources are dedicated for protocol operation, including CPU time and network link bandwidth
Times when static routing is more appropriate
Notes: 7.1.1.3 The Role of Dynamic Routing Protocols

## Slide 10: Dynamic verses Static Routing Using Static Routing
Networks typically use a combination of both static and dynamic routing.
Static routing has several primary uses:
Providing ease of routing table maintenance in smaller networks that are not expected to grow significantly.
Routing to and from a stub network. A network with only one default route out and no knowledge of any remote networks.
Accessing a single default router. This is used to represent a path to any network that does not have a match in the routing table.
Notes: 7.1.2.1 Using Static Routing

## Slide 11: Dynamic verses Static Routing Using Static Routing (cont.)
Notes: 7.1.2.1 Using Static Routing (cont.)

## Slide 12: Dynamic verses Static Routing Static Routing Scorecard
Notes: 7.1.2.2 Static Routing Scorecard

## Slide 13: Dynamic verses Static Routing Dynamic Routing Scorecard
Notes: 7.1.2.4 Dynamic Routing Scorecard

## Slide 14: Routing Protocol Operating Fundamentals Dynamic Routing Protocol Operation
In general, the operations of a dynamic routing protocol can be described as follows:
The router sends and receives routing messages on its interfaces.
The router shares routing messages and routing information with other routers that are using the same routing protocol.
Routers exchange routing information to learn about remote networks.
When a router detects a topology change the routing protocol can advertise this change to other routers.
Notes: 7.1.3.1 Dynamic Routing Protocol Operation

## Slide 15: Routing Protocol Operating Fundamentals Cold Start
R1 adds the 10.1.0.0 network available through interface FastEthernet 0/0 and 10.2.0.0 is available through interface Serial 0/0/0.
R2 adds the 10.2.0.0 network available through interface Serial 0/0/0 and 10.3.0.0 is available through interface Serial 0/0/1.
R3 adds the 10.3.0.0 network available through interface Serial 0/0/1 and 10.4.0.0 is available through interface FastEthernet 0/0.
Routers running RIPv2
Notes: 7.1.3.2 Cold Start

## Slide 16: Routing Protocol Operating Fundamentals Network Discovery
R1:
Sends an update about network 10.1.0.0 out the Serial0/0/0 interface
Sends an update about network 10.2.0.0 out the FastEthernet0/0 interface
Receives update from R2 about network 10.3.0.0 with a metric of 1
Stores network 10.3.0.0 in the routing table with a metric of 1
Routers running RIPv2
Notes: 7.1.3.3 Network Discovery

## Slide 17: Routing Protocol Operating Fundamentals Network Discovery (cont.)
R2:
Sends an update about network 10.3.0.0 out the Serial 0/0/0 interface
Sends an update about network 10.2.0.0 out the Serial 0/0/1 interface
Receives an update from R1 about network 10.1.0.0 with a metric of 1
Stores network 10.1.0.0 in the routing table with a metric of 1
Receives an update from R3 about network 10.4.0.0 with a metric of 1
Stores network 10.4.0.0 in the routing table with a metric of 1
Routers running RIPv2
Notes: 7.1.3.3 Network Discovery (cont.)

## Slide 18: Routing Protocol Operating Fundamentals Network Discovery (cont.)
R3:
Sends an update about network 10.4.0.0 out the Serial 0/0/1 interface
Sends an update about network 10.3.0.0 out the FastEthernet0/0
Receives an update from R2 about network 10.2.0.0 with a metric of 1
Stores network 10.2.0.0 in the routing table with a metric of 1
Routers running RIPv2
Notes: 7.1.3.3 Network Discovery (cont.)

## Slide 19: Routing Protocol Operating Fundamentals Exchanging the Routing Information
R1:
Sends an update about network 10. 1. 0. 0 out the Serial 0/0/0 interface
Sends an update about networks 10. 2. 0. 0 and 10. 3. 0. 0 out the FastEthernet0/0 interface
Receives an update from R2 about network 10. 4. 0. 0 with a metric of 2
Stores network 10. 4. 0. 0 in the routing table with a metric of 2
Same update from R2 contains information about network 10. 3. 0. 0 with a metric of 1. There is no change; therefore, the routing information remains the same
Routers running RIPv2
Notes: 7.1.3.4 Exchanging the Routing Information

## Slide 20: Routing Protocol Operating Fundamentals Exchanging the Routing Information (cont.)
R2:
Sends an update about networks 10. 3. 0. 0 and 10. 4. 0. 0 out of Serial 0/0/0 interface
Sends an update about networks 10. 1. 0. 0 and 10. 2. 0. 0 out of Serial 0/0/1 interface
Receives an update from R1 about network 10. 1. 0. 0. There is no change; therefore, the routing information remains the same.
Receives an update from R3 about network 10. 4. 0. 0. There is no change; therefore, the routing information remains the same.
Routers running RIPv2
Notes: 7.1.3.4 Exchanging the Routing Information (cont.)

## Slide 21: Routing Protocol Operating Fundamentals Exchanging the Routing Information (cont.)
R3:
Sends an update about network 10. 4. 0. 0 out the Serial 0/0/1 interface
Sends an update about networks 10. 2. 0. 0 and 10. 3. 0. 0 out the FastEthernet0/0 interface
Receives an update from R2 about network 10. 1. 0. 0 with a metric of 2
Stores network 10. 1. 0. 0 in the routing table with a metric of 2
Same update from R2 contains information about network 10. 2. 0. 0 with a metric of 1. There is no change; therefore, the routing information remains the same.
Routers running RIPv2
Notes: 7.1.3.4 Exchanging the Routing Information (cont.)

## Slide 22: Routing Protocol Operating Fundamentals Achieving Convergence
The network is converged when all routers have complete and accurate information about the entire network:
Convergence time is the time it takes routers to share information, calculate best paths, and update their routing tables.
A network is not completely operable until the network has converged.
Convergence properties include the speed of propagation of routing information and the calculation of optimal paths. The speed of propagation refers to the amount of time it takes for routers within the network to forward routing information.
Generally, older protocols, such as RIP, are slow to converge, whereas modern protocols, such as EIGRP and OSPF, converge more quickly.
Notes: 7.1.3.5 Achieving Convergence

## Slide 23: Types of Routing Protocols Classifying Routing Protocols
Notes: 7.1.4.1 Classifying Routing Protocols

## Slide 24: Types of Routing Protocols IGP and EGP Routing Protocols
Interior Gateway Protocols (IGP) -
Used for routing within an AS
Include RIP, EIGRP, OSPF, and IS-IS
Exterior Gateway Protocols (EGP) -
Used for routing between AS
Official routing protocol used by the Internet
Notes: 7.1.4.2 IGP and EGP Routing Protocols

## Slide 25: Types of Routing Protocols Distance Vector Routing Protocols
Distance vector IPv4 IGPs:
RIPv1 - First generation legacy protocol
RIPv2 - Simple distance vector routing protocol
IGRP - First generation Cisco proprietary protocol (obsolete)
EIGRP - Advanced version of distance vector routing
For R1, 172.16.3.0/24 is one hop away (distance). It can be reached through R2 (vector).
Notes: 7.1.4.3 Distance Vector Routing Protocols

## Slide 26: Types of Routing Protocols Distance Vector or Link-State Routing Protocols
Distance vector protocols use routers as sign posts along the path to the final destination.
A link-state routing protocol is like having a complete map of the network topology. The sign posts along the way from source to destination are not necessary, because all link-state routers are using an identical map of the network. A link-state router uses the link-state information to create a topology map and to select the best path to all destination networks in the topology.
Notes: 7.1.4.3 Distance Vector Routing Protocols (cont.)

## Slide 27: Types of Routing Protocols Link-State Routing Protocols
Link-state IPv4 IGPs:
OSPF - Popular standards based routing protocol
IS-IS - Popular in provider networks.
Notes: 7.1.4.4 Link-State Routing Protocols

## Slide 28: Types of Routing Protocols Classful Routing Protocols
Classful routing protocols do not send subnet mask information in their routing updates:
Only RIPv1 and IGRP are classful.
Created when network addresses were allocated based on classes (class A, B, or C).
Cannot provide variable length subnet masks (VLSMs) and classless interdomain routing (CIDR).
Create problems in discontiguous networks.
Notes: 7.1.4.5 Classful Routing Protocols

## Slide 29: Types of Routing Protocols Classless Routing Protocols
Classless routing protocols include subnet mask information in the routing updates:
RIPv2, EIGRP, OSPF, and IS_IS
Support VLSM and CIDR
IPv6 routing protocols
Notes: 7.1.4.6 Classless Routing Protocols

## Slide 30: Types of Routing Protocols Routing Protocol Characteristics
Notes: 7.1.4.7 Routing Protocol Characteristics

## Slide 31: Types of Routing Protocols Routing Protocol Metrics
A metric is a measurable value that is assigned by the routing protocol to different routes based on the usefulness of that route:
Used to determine the overall “cost” of a path from source to destination.
Routing protocols determine the best path based on the route with the lowest cost.
Notes: 7.1.4.8 Routing Protocol Metrics

## Slide 32: Distance Vector Routing Protocol Operation Distance Vector Technologies
Distance vector routing protocols:
Share updates between neighbors
Not aware of the network topology
Some send periodic updates to broadcast IP 255.255.255.255 even if topology has not changed
Updates consume bandwidth and network device CPU resources
RIPv2 and EIGRP use multicast addresses
EIGRP will only send an update when topology has changed
Notes: 7.2.1.1 Distance Vector Technologies

## Slide 33: Distance Vector Routing Protocol Operation Distance Vector Algorithm
RIP uses the Bellman-Ford algorithm as its routing algorithm.
IGRP and EIGRP use the Diffusing Update Algorithm (DUAL) routing algorithm developed by Cisco.
Notes: 7.2.1.2 Distance Vector Algorithm

## Slide 34: Types of Distance Vector Routing Protocols Routing Information Protocol
RIPng is based on RIPv2 with a 15 hop limitation and the administrative distance of 120
Updates use UDP port 520
Routing updates broadcasted every 30 seconds
Notes: 7.2.2.1 Routing Information Protocol

## Slide 35: Types of Distance Vector Routing Protocols Enhanced Interior-Gateway Routing Protocol
EIGRP:
Is bounded triggered updates
Uses a Hello keepalives mechanism
Maintains a topology table
Supports rapid convergence
Is a multiple network layer protocol support
Notes: 7.2.2.2 Enhanced Interior-Gateway Routing Protocol

## Slide 36: Configuring the RIP Protocol Router RIP Configuration Mode Advertising Networks
Notes: 7.3.1.1 Router RIP Configuration Mode
7.3.1.2 Advertising Networks

## Slide 37: Configuring the RIP Protocol Examining Default RIP Settings
Notes: 7.3.1.3 Examining Default RIP Settings

## Slide 38: Configuring the RIP Protocol Enabling RIPv2
Notes: 7.3.1.4 Enabling RIPv2

## Slide 39: Configuring the RIP Protocol Disabling Auto Summarization
Similarly to RIPv1, RIPv2 automatically summarizes networks at major network boundaries by default.
To modify the default RIPv2 behavior of automatic summarization, use the no auto-summary router configuration mode command.
This command has no effect when using RIPv1.
When automatic summarization has been disabled, RIPv2 no longer summarizes networks to their classful address at boundary routers. RIPv2 now includes all subnets and their appropriate masks in its routing updates.
The show ip protocols now states that automatic network summarization is not in effect.
Notes: 7.3.1.5 Disabling Auto Summarization

## Slide 40: Configuring the RIP Protocol Configuring Passive Interfaces
Sending out unneeded updates on a LAN impacts the network in three ways:
Wasted Bandwidth
Wasted Resources
Security Risk
Notes: 7.3.1.6 Configuring Passive Interfaces

## Slide 41: Configuring the RIP Protocol Propagating a Default Route
Notes: 7.3.1.7 Propagating a Default Route

## Slide 42: Configuring the RIPng Protocol Advertising IPv6 Networks
Notes: 7.3.2.1 Advertising IPv6 Networks

## Slide 43: Configuring the RIPng Protocol Examining the RIPng Configuration
Notes: 7.3.2.2 Examining the RIPng Configuration

## Slide 44: Configuring the RIPng Protocol Examining the RIPng Configuration (cont.)
Notes: 7.3.2.2 Examining the RIPng Configuration (cont.)

## Slide 45: Link-State Routing Protocol Operation Shortest Path First Protocols
Notes: 7.4.1.1 Shortest Path First Protocols

## Slide 46: Link-State Routing Protocol Operation Dijkstra’s Algorithm
Notes: 7.4.1.2 Dijkstra's Algorithm

## Slide 47: Link-State Updates Link-State Routing Process
Notes: 7.4.2.1 Link-State Routing Process

## Slide 48: Link-State Updates Link and Link-State
The first step in the link-state routing process is that each router learns about its own links and its own directly connected networks.
Notes: 7.4.2.2 Link and Link-State

## Slide 49: Link-State Updates Say Hello
The second step in the link-state routing process is that each router is responsible for meeting its neighbors on directly connected networks.
Notes: 7.4.2.3 Say Hello

## Slide 50: Link-State Updates Say Hello
The third step in the link-state routing process is that each router builds a link-state packet (LSP) containing the state of each directly connected link.
R1; Ethernet network 10.1.0.0/16; Cost 2
R1 -> R2; Serial point-to-point network; 10.2.0.0/16; Cost 20
R1 -> R3; Serial point-to-point network; 10.7.0.0/16; Cost 5
R1 -> R4; Serial point-to-point network; 10.4.0.0/16; Cost 20
Notes: 7.4.2.4 Building the Link-State Packet

## Slide 51: Link-State Updates Flooding the LSP
The fourth step in the link-state routing process is that each router floods the LSP to all neighbors, who then store all LSPs received in a database.
Notes: 7.4.2.5 Flooding the LSP

## Slide 52: Link-State Updates Building the Link-State Database
The final step in the link-state routing process is that each router uses the database to construct a complete map of the topology and computes the best path to each destination network.
Notes: 7.4.2.6 Building the Link-State Database

## Slide 53: Link-State Updates Building the SPF Tree
Notes: 7.4.2.6 Building the Link-State Database (cont.)

## Slide 54: Link-State Updates Building the SPF Tree
Notes: 7.4.2.7 Building the SPF Tree

## Slide 55: Link-State Updates Adding OSPF Routes to the Routing Table
Notes: 7.4.2.8 Adding OSPF Routes to the Routing Table

## Slide 56: Why Use Link-State Routing Protocols Why Use Link-State Protocols?
Notes: 7.4.3.1 Why Use Link-State Protocols?

## Slide 57: Why Use Link-State Routing Protocols Why Use Link-State Protocols?
Notes: 7.4.3.1 Why Use Link-State Protocols?

## Slide 58: Why Use Link-State Routing Protocols Disadvantages of Link-State Protocols
Notes: 7.4.3.2 Support for Multiple Areas

## Slide 59: Why Use Link-State Routing Protocols Protocols that Use Link-State
There are only two link-state routing protocols:
Open Shortest Path First (OSPF) most popular
  began in 1987
  two current versions
  OSPFv2 - OSPF for IPv4 networks
  OSPFv3 - OSPF for IPv6 networks
IS-IS was designed by International Organization for Standardization (ISO )
Notes: 7.4.3.3 Protocols that Use Link-State

## Slide 60: Parts of an IPv4 Route Entry Routing Table Entries
Notes: 7.5.1.1 Routing Table Entries

## Slide 61: Parts of an IPv4 Route Entry Directly Connected Entries
Notes: 7.5.1.2 Directly Connected Entries

## Slide 62: Parts of an IPv4 Route Entry Remote Network Entries
Notes: 7.5.1.3 Remote Network Entries

## Slide 63: Dynamically Learned IPv4 Routes Routing Table Terms
Routes are discussed
in terms of:
Ultimate route
Level 1 route
Level 1 parent route
Level 2 child routes
Notes: 7.5.2.1 Routing Table Terms

## Slide 64: Dynamically Learned IPv4 Routes Ultimate Route
An ultimate route is a routing table entry that contains either a next-hop IP address or an exit interface. Directly connected, dynamically learned, and link local routes are ultimate routes.
Notes: 7.5.2.2 Ultimate Route

## Slide 65: Dynamically Learned IPv4 Routes Level 1 Route
Notes: 7.5.2.3 Level 1 Route

## Slide 66: Dynamically Learned IPv4 Routes Level 1 Parent Route
Notes: 7.5.2.4 Level 1 Parent Route

## Slide 67: Dynamically Learned IPv4 Routes Level 2 Child Route
Notes: 7.5.2.5 Level 2 Child Route

## Slide 68: The Routing Table Route Lookup Process
If the best match is a level 1 ultimate route, then this route is used to forward the packet.
If the best match is a level 1 parent route, proceed to the next step.
The router examines child routes (the subnet routes) of the parent route for a best match.
If there is a match with a level 2 child route, that subnet is used to forward the packet.
If there is not a match with any of the level 2 child routes, proceed to the next step.
Notes: 7.5.3.1 Route Lookup Process

## Slide 69: The Routing Table Route Lookup Process (cont.)
The router continues searching level 1 supernet routes in the routing table for a match, including the default route, if there is one.
If there is now a lesser match with a level 1 supernet or default routes, the router uses that route to forward the packet.
If there is not a match with any route in the routing table, the router drops the packet.
Notes: 7.5.3.1 Route Lookup Process (cont.)

## Slide 70: The IPv4 Route Lookup Process Best Route = Longest Match
Notes: 7.5.3.2 Best Route = Longest Match

## Slide 71: The IPv4 Route Lookup Process IPv6 Routing Table Entries
Components of the IPv6 routing table are very similar to the IPv4 routing table (directly connected interfaces, static routes, and dynamically learned routes).
IPv6 is classless by design, all routes are effectively level 1 ultimate routes. There is no level 1 parent of level 2 child routes.
Notes: 7.5.4.1 IPv6 Routing Table Entries

## Slide 72: Analyze an IPVv6 Routing Table Directly Connected Entries
Notes: 7.5.4.2 Directly Connected Entries

## Slide 73: Analyze an IPVv6 Routing Table Remote IPv6 Network Entries
Notes: 7.5.4.3 Remote IPv6 Network Entries

## Slide 74: Chapter 7: Summary
Dynamic routing protocols:
Used by routers to automatically learn about remote networks from other routers
Purpose includes: discovery of remote networks, maintaining up-to-date routing information, choosing the best path to destination networks, and ability to find a new best path if the current path is no longer available
Best choice for large networks but static routing is better for stub networks.
Function to inform other routers about changes
Can be classified as either classful or classless, distance-vector or link-state, and an interior or an exterior gateway protocol
Notes: Chapter 7 Summary

## Slide 75: Chapter 7: Summary (cont.)
Dynamic routing protocols:
A link-state routing protocol can create a complete view or topology of the network by gathering information from all of the other routers
Metrics are used to determine the best path or shortest path to reach a destination network
Different routing protocols may use different (hops, bandwidth, delay, reliability, and load)
Show ip protocols command displays the IPv4 routing protocol settings currently configured on the router, for IPv6, use show ipv6 protocols
Notes: Chapter 7 Summary

## Slide 76: Chapter 7: Summary (cont.)
Dynamic routing protocols:
Cisco routers use the administrative distance value to determine which routing source to use
Each dynamic routing protocol has a unique administrative value, along with static routes and directly connected networks, lower is preferred the route
Directly connected networks are preferred source, followed by static routes and then various dynamic routing protocols
An OSPF link is an interface on a router, information about the state of the links is known as link-states
Link-state routing protocols apply Dijkstra’s algorithm to calculate the best path route which uses accumulated costs along each path, from source to destination, to determine the total cost of a route
Notes: Chapter 7 Summary