## Slide 1: Instructor Materials Chapter 7: Access Control Lists
CCNA Routing and Switching
Routing and Switching Essentials v6.0
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 7: Access Control Lists

## Slide 2: Instructor Materials – Chapter 7 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 13
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Routing and Switching Essentials 6.0 Planning Guide
Chapter 7: Access Control Lists
Notes: Routing and Switching Essentials 6.0
Chapter 7: Access Control Lists

## Slide 4: Chapter 7: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
7.0.1.2 | Class Activity | Permit Me to Assist You | Optional
7.1.1.4 | Packet Tracer | ACL Demonstration | Recommended
7.1.2.6 | Activity | Determine the Correct Wildcard Mask | -
7.1.2.7 | Activity | Determine the Permit or Deny | -
7.1.3.3 | Activity | ACL Operation | -
7.2.1.5 | Activity | Configuring Standard IPv4 ACLs | -
7.2.1.6 | Packet Tracer | Configuring Numbered Standard IPv4 ACLs | Recommended
7.2.1.7 | Packet Tracer | Configuring Named Standard IPv4 ACLs | Recommended
7.2.2.7 | Lab | Configuring and Modifying Standard IPv4 ACLs | Optional
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 7: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
7.2.3.1 | Syntax Checker | Secure VTY Lines with a Standard IPv4 ACL | -
7.2.3.3 | Packet Tracer | Configuring an IPv4 ACL on VTY Lines | Recommended
7.2.3.4 | Lab | Configuring and Verifying VTY Restrictions | Optional
7.3.2.4 | Packet Tracer | Troubleshooting Standard IPv4 ACLs | Recommended
7.4.1.1 | Class Activity | FTP Denied | Optional
7.4.1.2 | Packet Tracer | Skills Integration Challenge | Recommended
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5

## Slide 6: Chapter 7: Assessment
Students should complete Chapter 7 “Assessment” after completing Chapter 7.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 6

## Slide 7
Prior to teaching Chapter 7, the instructor should:
Complete Chapter 7 “Assessment.”
The objectives of this chapter are:
  Explain how ACLs filter traffic.
  Explain how ACLs use wildcard masks.
  Explain how to create ACLs.
  Explain how to place ACLs.
  Configure standard IPv4 ACLs to filter traffic to meet networking requirements.
  Use sequence numbers to edit existing standard IPv4 ACLs.
  Configure a standard ACL to secure vty access.
  Explain how a router processes packets when an ACL is applied.
  Troubleshoot common standard IPv4 ACL errors using CLI commands.
Chapter 7: Best Practices
Notes: 7

## Slide 8
Chapter 7: Best Practices (Cont.)
Section 7.1
The instructor should ensure this chapter becomes as hands-on as possible.
Stress that an ACL is a sequential list of permit and/or deny statements. Order does matter.
Routers do not apply ACLs on themselves. Any traffic generated by the router does not have any ACLs applied, so testing ACLs from a router will not generate the results that are expected.
Notes: 8

## Slide 9
Chapter 7: Best Practices (Cont.)
Section 7.2
Demonstrate how students can use a text editor to create and then paste their ACLs into their terminal program. It makes it far easier for students to edit their ACLs.
Notes: 9

## Slide 10
Chapter 7: Best Practices (Cont.)
Section 7.3
Practice, Practice, Practice!
Have students conceptually create situations where packets need to be allowed and/or blocked.
.
Notes: 10

## Slide 11: Chapter 7: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at: https://www.netacad.com/group/communities/community-home
Best practices from around the world for teaching CCNA Routing and Switching. https://www.netacad.com/group/communities/ccna-blog
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Students can enroll in Packet Tracer Know How 1: Packet Tracer 101 (self-enroll).
Notes: 11

## Slide 13: Chapter 7: Access Control Lists
Routing and Switching Essentials v6.0
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 7: Access Control Lists

## Slide 14: Chapter 7 - Sections & Objectives
7.1 ACL Operation
  Explain how ACLs filter traffic.
  Explain how ACLs use wildcard masks.
  Explain how to create ACLs.
  Explain how to place ACLs.
7.2 Standard IPv4 ACLs
  Configure standard IPv4 ACLs to filter traffic to meet networking requirements.
  Use sequence numbers to edit existing standard IPv4 ACLs.
  Configure a standard ACL to secure vty access.
7.3 Troubleshoot ACLs
  Explain how a router processes packets when an ACL is applied.
  Troubleshoot common standard IPv4 ACL errors using CLI commands.
Notes: 14

## Slide 15: 7.1 ACL Operation
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 7: Access Control Lists

## Slide 16: Purpose of ACLs What is an ACL?
By default, a router does not have ACLs configured; therefore, by default a router does not filter traffic.
Notes: 7.1 – ACL Operation
7.1.1 – Purpose of ACLs
7.1.1.1 – What is an ACL?

## Slide 17: Purpose of ACLs Packet Filtering
Packet filtering, sometimes called static packet filtering, controls access to a network by analyzing the incoming and outgoing packets and passing or dropping them based on given criteria, such as the source IP address, destination IP addresses, and the protocol carried within the packet.
A router acts as a packet filter when it forwards or denies packets according to filtering rules.
An ACL is a sequential list of permit or deny statements, known as access control entries (ACEs).
Notes: 7.1 – ACL Operation
7.1.1 – Purpose of ACLs
7.1.1.2 – Packet Filtering

## Slide 18: Purpose of ACLs ACL Operation
Notes: 7.1 – ACL Operation
7.1.1 – Purpose of ACLs
7.1.1.3 – ACL Operation

## Slide 19: Wildcard Masks in ACLs Introducing ACL Wildcard Masking
Notes: 7.1 – ACL Operation
7.1.2 – Wildcard Masks in ACLs
7.1.2.1 – Introducing ACL Wildcard Masking

## Slide 20: Wildcard Masks in ACLs Introducing ACL Wildcard Masking (cont.)
Example
Notes: 7.1 – ACL Operation
7.1.2 – Wildcard Masks in ACLs
7.1.2.1 – Introducing ACL Wildcard Masking (cont.)

## Slide 21: Wildcard Masks in ACLs Wildcard Mask Examples
Notes: 7.1 – ACL Operation
7.1.2 – Wildcard Masks in ACLs
7.1.2.2 - Wildcard Mask Examples

## Slide 22: Wildcard Masks in ACLs Wildcard Mask Examples (cont.)
Notes: 7.1 – ACL Operation
7.1.2 – Wildcard Masks in ACLs
7.1.2.2 - Wildcard Mask Examples

## Slide 23: Wildcard Masks in ACLs Calculating the Wildcard Mask
Calculating wildcard masks can be challenging. One shortcut method is to subtract the subnet mask from 255.255.255.255.
Notes: 7.1 – ACL Operation
7.1.2 – Wildcard Masks in ACLs
7.1.2.3 - Calculating the Wildcard Mask

## Slide 24: Wildcard Masks in ACLs Wildcard Mask Keywords
Notes: 7.1 – ACL Operation
7.1.2 – Wildcard Masks in ACLs
7.1.2.4 - Wildcard Mask Keywords

## Slide 25: Wildcard Masks in ACLs Wildcard Mask Keyword Examples
Notes: 7.1 – ACL Operation
7.1.2 – Wildcard Masks in ACLs
7.1.2.5 - Wildcard Mask Keyword Examples

## Slide 26: Guidelines for ACL Creation General Guidelines for Creating ACLS
Notes: 7.1 – ACL Operation
7.1.3 – Guidelines for ACL Creation
7.1.3.1 - General Guidelines for Creating ACLS

## Slide 27: Guidelines for ACL Creation ACL Best Practices
Notes: 7.1 – ACL Operation
7.1.3 – Guidelines for ACL Creation
7.1.3.2 - ACL Best Practices

## Slide 28: Guidelines for ACL Placement Where to Place ACLs
Notes: 7.1 – ACL Operation
7.1.4 – Guidelines for ACL Placement
7.1.4.1 - Where to Place ACLs

## Slide 29: Guidelines for ACL Placement Where to Place ACLs (cont.)
Every ACL should be placed where it has the greatest impact on efficiency. The basic rules are:
  Extended ACLs - Locate extended ACLs as close as possible to the source of the traffic to be filtered.
  Standard ACLs - Because standard ACLs do not specify destination addresses, place them as close to the destination as possible.
  Placement of the ACL, and therefore the type of ACL used, may also depend on: the extent of the network administrator’s control, bandwidth of the networks involved, and ease of configuration.
Notes: 7.1 – ACL Operation
7.1.4 – Guidelines for ACL Placement
7.1.4.1 - Where to Place ACLs

## Slide 30: Guidelines for ACL Placement Standard ACL Placement
The administrator wants to prevent traffic originating in the 192.168.10.0/24 network from reaching the 192.168.30.0/24 network.
Notes: 7.1 – ACL Operation
7.1.4 – Guidelines for ACL Placement
7.1.4.2 - Standard ACL Placement

## Slide 31: 7.2 Standard IPv4 ACLs
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 7: VLANs

## Slide 32: Configure Standard IPv4 ACLs Numbered Standard IPv4 ACL Syntax
Router(config)# access-list access-list-number { deny | permit | remark } source [ source-wildcard ] [ log ]
Notes: 7.2 – Standard IPv4 ACLs
7.2.1 – Configure Standard IPv4 ACLs
7.2.1.1 - Numbered Standard IPv4 ACL Syntax

## Slide 33: Configure Standard IPv4 ACLs Applying Standard IPv4 ACLs to Interfaces
Notes: 7.2 – Standard IPv4 ACLs
7.2.1 – Configure Standard IPv4 ACLs
7.2.1.2 - Applying Standard IPv4 ACLs to Interfaces

## Slide 34: Configure Standard IPv4 ACLs Applying Standard IPv4 ACLs to Interfaces (cont.)
Notes: 7.2 – Standard IPv4 ACLs
7.2.1 – Configure Standard IPv4 ACLs
7.2.1.2 - Applying Standard IPv4 ACLs to Interfaces

## Slide 35: Configure Standard IPv4 ACLs Numbered Standard IPv4 ACL Examples
Notes: 7.2 – Standard IPv4 ACLs
7.2.1 – Configure Standard IPv4 ACLs
7.2.1.3 - Numbered Standard IPv4 ACL Examples

## Slide 36: Configure Standard IPv4 ACLs Numbered Standard IPv4 ACL Examples (cont.)
Notes: 7.2 – Standard IPv4 ACLs
7.2.1 – Configure Standard IPv4 ACLs
7.2.1.3 - Numbered Standard IPv4 ACL Examples

## Slide 37: Configure Standard IPv4 ACLs Named Standard IPv4 ACL Syntax
Notes: 7.2 – Standard IPv4 ACLs
7.2.1 – Configure Standard IPv4 ACLs
7.2.1.4 - Named Standard IPv4 ACL Syntax

## Slide 38: Configure Standard IPv4 ACLs Named Standard IPv4 ACL Syntax (cont.)
Notes: 7.2 – Standard IPv4 ACLs
7.2.1 – Configure Standard IPv4 ACLs
7.2.1.4 - Named Standard IPv4 ACL Syntax

## Slide 39: Modify IPv4 ACLs Method 1 – Use a Text Editor
Notes: 7.2 – Standard IPv4 ACLs
7.2.2 – Modify IPv4 ACLs
7.2.2.1 - Method 1 – Use a Text Editor

## Slide 40: Modify IPv4 ACLs Method 2 – Use Sequence Numbers
Notes: 7.2 – Standard IPv4 ACLs
7.2.2 – Modify IPv4 ACLs
7.2.2.2 - Method 2 – Use Sequence Numbers

## Slide 41: Modify IPv4 ACLs Editing Standard Named ACLs
Notes: 7.2 – Standard IPv4 ACLs
7.2.2 – Modify IPv4 ACLs
7.2.2.3 - Editing Standard Named ACLs

## Slide 42: Modify IPv4 ACLs Verifying ACLs
Notes: 7.2 – Standard IPv4 ACLs
7.2.2 – Modify IPv4 ACLs
7.2.2.4 - Verifying ACLs

## Slide 43: Modify IPv4 ACLs ACL Statistics
Notes: 7.2 – Standard IPv4 ACLs
7.2.2 – Modify IPv4 ACLs
7.2.2.5 - ACL Statistics

## Slide 44: Securing VTY Ports with a Standard IPv4 ACL The access-class Command
The access-class command configured in line configuration mode restricts incoming and outgoing connections between a particular VTY (into a Cisco device) and the addresses in an access list.
Notes: 7.2 – Standard IPv4 ACLs
7.2.3 – Securing VTY Ports with a Standard IPv4 ACL
7.2.3.1 - The access-class Command

## Slide 45: Securing VTY Ports with a Standard IPv4 ACL Verifying the VTY Port is Secured
Notes: 7.2 – Standard IPv4 ACLs
7.2.3 – Securing VTY Ports with a Standard IPv4 ACL
7.2.3.2 - Verifying the VTY Port is Secured

## Slide 46: 7.3 Troubleshoot ACLs
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 7: Access Control Lists

## Slide 47: Processing Packet with ACLs The Implicit Deny Any
At least one permit ACE must be configured in an ACL or all traffic is blocked.
For the network in the figure, applying either ACL 1 or ACL 2 to the S0/0/0 interface of R1 in the outbound direction will have the same effect.
Notes: 7.3 – Troubleshoot ACLs
7.3.1 – Processing Packets with ACLs
7.3.1.1 - The Implicit Deny Any

## Slide 48: Processing Packet with ACLs The Order of ACEs in an ACL
Notes: 7.3 – Troubleshoot ACLs
7.3.1 – Processing Packets with ACLs
7.3.1.2 - The Order of ACEs in an ACL

## Slide 49: Processing Packet with ACLs The Order of ACEs in an ACL (cont.)
Notes: 7.3 – Troubleshoot ACLs
7.3.1 – Processing Packets with ACLs
7.3.1.2 - The Order of ACEs in an ACL

## Slide 50: Processing Packet with ACLs Cisco IOS Reorders Standard ACLs
Notice that the statements are listed in a different order than they were entered.
Notes: 7.3 – Troubleshoot ACLs
7.3.1 – Processing Packets with ACLs
7.3.1.3 - Cisco IOS Reorders Standard ACLs

## Slide 51: Processing Packet with ACLs Cisco IOS Reorders Standard ACLs (cont.)
The order in which the standard ACEs are listed is the sequence used by the IOS to process the list.
Notes: 7.3 – Troubleshoot ACLs
7.3.1 – Processing Packets with ACLs
7.3.1.3 - Cisco IOS Reorders Standard ACLs (cont.)

## Slide 52: Processing Packet with ACLs Routing Processes and ACLs
As a frame enters an interface, the router checks to see whether the destination Layer 2 address matches its interface Layer 2 address, or whether the frame is a broadcast frame.
If the frame address is accepted, the frame information is stripped off and the router checks for an ACL on the inbound interface.
If an ACL exists, the packet is tested against the statements in the list.
If the packet matches a statement, the packet is either permitted or denied.
If the packet is accepted, it is then checked against routing table entries to determine the destination interface.
If a routing table entry exists for the destination, the packet is then switched to the outgoing interface, otherwise the packet is dropped.
Next, the router checks whether the outgoing interface has an ACL. If an ACL exists, the packet is tested against the statements in the list. If the packet matches a statement, it is either permitted or denied.
If there is no ACL or the packet is permitted, the packet is encapsulated in the new Layer 2 protocol and forwarded out the interface to the next device.
Notes: 7.3 – Troubleshoot ACLs
7.3.1 – Processing Packets with ACLs
7.3.1 - Routing Processes and ACLs

## Slide 53: Common Standard IPv4 ACL Errors Troubleshooting Standard IPv4 ACLs – Example 1
Notes: 7.3 – Troubleshoot ACLs
7.3.2 – Common Standard IPv4 ACL Errors
7.3.2.1 - Troubleshooting Standard IPv4 ACLs – Example 1

## Slide 54: Common Standard IPv4 ACL Errors Troubleshooting Standard IPv4 ACLs – Example 1 (cont.)
Notes: 7.3 – Troubleshoot ACLs
7.3.2 – Common Standard IPv4 ACL Errors
7.3.2.1 - Troubleshooting Standard IPv4 ACLs – Example 1 (cont.)

## Slide 55: Common Standard IPv4 ACL Errors Troubleshooting Standard IPv4 ACLs – Example 2
Security Policy: The 192.168.11.0/24 network should not be able to access the 192.168.10.0/24 network.
Notes: 7.3 – Troubleshoot ACLs
7.3.2 – Common Standard IPv4 ACL Errors
7.3.2.2 - Troubleshooting Standard IPv4 ACLs – Example 2

## Slide 56: Common Standard IPv4 ACL Errors Troubleshooting Standard IPv4 ACLs – Example 2 (cont.)
ACL 20 was applied to the wrong interface and in the wrong direction. All traffic from the 192.168.11.0/24 is denied inbound access through the G0/1 interface.
Notes: 7.3 – Troubleshoot ACLs
7.3.2 – Common Standard IPv4 ACL Errors
7.3.2.2 - Troubleshooting Standard IPv4 ACLs – Example 2 (cont.)

## Slide 57: Common Standard IPv4 ACL Errors Troubleshooting Standard IPv4 ACLs – Example 2 (cont.)
Notes: 7.3 – Troubleshoot ACLs
7.3.2 – Common Standard IPv4 ACL Errors
7.3.2.2 - Troubleshooting Standard IPv4 ACLs – Example 2 (cont.)

## Slide 58: Common Standard IPv4 ACL Errors Troubleshooting Standard IPv4 ACLs – Example 3
Problem
Security Policy: Only PC1 is allowed SSH remote access to R1.
Notes: 7.3 – Troubleshoot ACLs
7.3.2 – Common Standard IPv4 ACL Errors
7.3.2.3 - Troubleshooting Standard IPv4 ACLs – Example 3

## Slide 59: Common Standard IPv4 ACL Errors Troubleshooting Standard IPv4 ACLs – Example 3 (cont.)
Solution!
Security Policy: Only PC1 is allowed SSH remote access to R1.
Notes: 7.3 – Troubleshoot ACLs
7.3.2 – Common Standard IPv4 ACL Errors
7.3.2.3 - Troubleshooting Standard IPv4 ACLs – Example 3 (cont.)

## Slide 60: 7.4 Summary
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 7: Access Control Lists

## Slide 61: Chapter Summary Summary
Explain how ACLs filter traffic.
Explain how ACLs use wildcard masks.
Explain how to create ACLs.
Explain how to place ACLs.
Configure standard IPv4 ACLs to filter traffic to meet networking requirements.
Use sequence numbers to edit existing standard IPv4 ACLs.
Configure a standard ACL to secure vty access.
Explain how a router processes packets when an ACL is applied.
Troubleshoot common standard IPv4 ACL errors using CLI commands.
Notes: 7.4 - Summary

## Slide 62: Section 7.1 Terms and Commands
Access list (ACL)
Packet filtering
Access control entries (ACEs)
Standard ACLs
Extended ACLs
Inbound ACLs
Outbound ACLs
Wildcard masking
Wildcard mask bit 0
Wildcard mask bit 1
access-list access-list-number permit ip_address wildcard_mask
host
any
Notes: Terms and Commands

## Slide 63: Section 7.2 Terms and Commands
access-list access-list-number { deny | permit | remark }source [ source-wildcard ][ log ]
show access-lists
no access-list access-list-number
ip access-group {access-list-number | access-list-name} { in | out }
ip access-list standard name
clear access-list counters
access-class access-list-number { in |out }
Notes: New Terms and Commands