## Slide 1: Chapter 6: VLANs
Instructor Materials
CCNA Routing and Switching
Routing and Switching Essentials v6.0
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 6: VLANs

## Slide 2: Instructor Materials – Chapter 6 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 12
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3: Chapter 6: VLANs
Routing and Switching Essentials v6.0 Planning Guide
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 6: VLANs

## Slide 4: Chapter 6: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
6.0.1.2 | Class Activity | Vacation Station | Optional
6.1.1.5 | Packet Tracer | Who Hears the Broadcast? | Recommended
6.1.2.6 | Interactive Activity | Predict Switch Behavior | Recommended
6.1.2.7 | Packet Tracer | Investigating a VLAN Implementation | Recommended
6.2.1.2 | Syntax Checker | Creating a VLAN | -
6.2.1.3 | Syntax Checker | Assign Ports to VLANS | -
6.2.1.4 | Syntax Checker | Changing VLAN Port Membership | -
6.2.1.6 | Syntax Checker | Verifying VLAN Information | -
6.2.1.7 | Packet Tracer | Configuring VLANs | Recommended
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 6: Activities (Cont.)
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
6.2.2.3 | Syntax Checker | Verifying Trunk Configuration | -
6.2.2.4 | Packet Tracer | Configuring Trunks | Recommended
6.2.2.5 | Lab | Configuring VLANs and Trunking | Recommended
6.2.3.7 | Packet Tracer | Troubleshooting a VLAN Implementation – Scenario 1 | Recommended
6.2.3.8 | Packet Tracer | Troubleshooting a VLAN Implementation – Scenario 2 | Recommended
6.2.3.9 | Lab | Troubleshooting VLAN Configurations | Optional
6.3.1.4 | Activity | Identify the Types of Inter-VLAN Routing | Recommended
6.3.2.4 | Lab | Configuring Per-Interface Inter-VLAN Routing | Recommended
6.3.3.4 | Syntax Checker | Configuring Router-on-a-Stick Inter-VLAN Routing | -
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5

## Slide 6: Chapter 6: Activities (Cont.)
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
6.3.3.6 | Packet Tracer | Configuring Router-on-a-Stick Inter-VLAN Routing | Recommended
6.3.3.7 | Lab | Configuring 801.2Q Trunk-Based Inter-VLAN Routing | Optional
6.3.3.8 | Packet Tracer | Inter-VLAN Routing Challenge | Optional
6.4.1.1 | Class Activity | The Inside Track | Optional
6.4.1.2 | Packet Tracer | Skills Integration Challenge | Recommended
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 6

## Slide 7: Chapter 6: Assessment
Students should complete Chapter 6, “Assessment” after completing Chapter 6.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 7

## Slide 8: Chapter 6: Best Practices
Prior to teaching Chapter 6, the instructor should:
Complete Chapter 6, “Assessment.”
The objectives of this chapter are:
  Explain how VLANs segment broadcast domains in a small to medium-sized business network.
    Explain the purpose of VLANs in a switched network.
    Explain how a switch forwards frames based on VLAN configuration in a multi-switch environment.
  Implement VLANs to segment a small to medium-sized business network.
    Configure a switch port to be assigned to a VLAN based on requirements.
    Configure a trunk port on a LAN switch.
    Troubleshoot VLAN and trunk configurations in a switched network.
  Configure routing between VLANs in a small to medium-sized business network.
    Describe the two options for configuring Inter-VLAN routing.
    Configure legacy Inter-VLAN Routing.
    Configure Router-on-a-Stick Inter-VLAN Routing.
Notes: 8

## Slide 9: Chapter 6: Best Practices (Cont.)
In Section 6.1, students should complete Chapter 6, “Assessment” after completing Chapter 6. Quizzes, labs, and Packet Tracers. Other activities can be used to informally assess student progress.
In Section 6.2, Once students complete the troubleshooting labs, create additional challenges or have one team of students create problems on another team’s setup. Ensure that all changes and all solutions are documented.
In Section 6.3, once students complete the legacy inter-VLAN routing lab and the router-on-a-stick inter-VLAN routing labs, ask them to present the advantages and disadvantages of each method.
Notes: 9

## Slide 10: Chapter 6: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at: https://www.netacad.com/group/communities/community-home
Best practices from around the world for teaching CCNA Routing and Switching. https://www.netacad.com/group/communities/ccna
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Students can enroll in Introduction to Packet Tracer (self-paced).
Notes: 10

## Slide 12: Chapter 6: VLANs
CCNA Routing and Switching
Routing and Switching Essentials v6.0
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 6: VLANs

## Slide 13: Chapter 6 - Sections & Objectives
6.1 VLAN Segmentation
  Explain the purpose of VLANs in a switched network.
  Explain how a switch forwards frames based on VLAN configuration in a multi-switch environment.
6.2 VLAN Implementations
  Configure a switch port to be assigned to a VLAN based on requirements.
  Configure a trunk port on a LAN switch.
  Troubleshoot VLAN and trunk configurations in a switched network.
6.3 Inter-VLAN Routing Using Routers
  Describe the two options for configuring Inter-VLAN routing.
  Configure legacy Inter-VLAN Routing.
  Configure Router-on-a-Stick Inter-VLAN Routing
Notes: 13
Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 6: VLANs

## Slide 14: 6.1 VLAN Segmentation
Notes: 6 - VLANs
6.1 – VLAN Segmentation

## Slide 15: Overview of VLANs VLAN Definitions
VLANs can segment LAN devices without regard for the physical location of the user or device.
  In the figure, IT users on the first, second, and third floors are all on the same LAN segment. The same is true for HR and Sales users.
A VLAN is a logical partition of a Layer 2 network.
  Multiple partitions can be created and multiple VLANs can co-exist.
  The partitioning of the Layer 2 network takes place inside a Layer 2 device, usually via a switch.
  Each VLAN is a broadcast domain that can span multiple physical LAN segments.
  Hosts on the same VLAN are unaware of the VLAN’s existence.
VLANs are mutually isolated and packets can only pass between VLANs via a router.
Notes: 6.1 – VLAN Segmentation
6.1.1 – Overview of VLANs
6.1.1.1 – VLAN Definitions

## Slide 16: Overview of VLANs Benefits of VLANs
Notes: 6.1 – VLAN Segmentation
6.1.1 – Overview of VLANs
6.1.1.2 – Benefits of VLANs

## Slide 17: Overview of VLANs Types of VLANs
Common types of VLANs:
  Default VLAN – Also known as VLAN 1. All switch ports are members of VLAN 1 by default.
  Data VLAN – Data VLANs are commonly created for specific groups of users or devices. They carry user generated traffic.
  Native VLAN – This is the VLAN that carries all untagged traffic. This is traffic that does not originate from a VLAN port (e.g., STP BPDU traffic exchanged between STP enabled switches). The native VLAN is VLAN 1 by default.
  Management VLAN – This is a VLAN that is created to carry network management traffic including SSH, SNMP, Syslog, and more. VLAN 1 is the default VLAN used for network management.
Default VLAN Assignment
Initially, all switch ports are members of VLAN 1.
Notes: 6.1 – VLAN Segmentation
6.1.1 – Overview of VLANs
6.1.1.3 – Types of VLANs

## Slide 18: Overview of VLANs Voice VLANs
To support time-sensitive voice traffic, Cisco switches support a voice VLAN that requires:
  Assured bandwidth
  Delay of less than 150 ms across the network to ensure voice quality
  Transmission priority over other types of network traffic
  Ability to be routed around congested areas on the network.
The voice VLAN feature enables access ports to carry user and IP voice traffic.
  In the figure, the S3 F0/18 interface has been configured to tag student traffic on VLAN 20 and voice traffic on VLAN 150.
Notes: 6.1 – VLAN Segmentation
6.1.1 – Overview of VLANs
6.1.1.4 – Voice VLANs

## Slide 19: Overview of VLANs Packet Tracer – Who Hears the Broadcast?
Notes: 6.1 – VLAN Segmentation
6.1.1 – Overview of VLANs
6.1.1.5 – Packet Tracer – Who Hears the Broadcast?

## Slide 20: VLANs in a Multi-Switched Environment VLAN Trunks
A VLAN trunk is a point-to-point link that carries more than one VLAN.
  Usually established between switches to support intra VLAN communication.
  A VLAN trunk or trunk ports are not associated to any VLANs.
Cisco IOS supports IEEE 802.1q, a popular VLAN trunk protocol.
The links between switches S1 and S2, and S1 and S3 are configured to transmit traffic coming from VLANs 10, 20, 30, and 99 across the network.
Notes: 6.1 – VLAN Segmentation
6.1.2 – VLANs in a Multi-Switched Environment
6.1.2.1 – VLAN Trunks

## Slide 21: VLANs in a Multi-Switched Environment Controlling Broadcast Domains with VLANs
If a switch port receives a broadcast frame, it forwards it out all ports except the originating port.
  Eventually the entire network receives the broadcast because the network is one broadcast domain.
VLANs can be used to limit the reach of broadcast frames because each VLAN is a broadcast domain.
  VLANs help control the reach of broadcast frames and their impact in the network.
In the figure, PC1 on VLAN 10 sends a broadcast frame.
  Trunk links between S2 - S1 and S1 - S3 propagate the broadcast to other devices in VLAN 10.
  Only devices in the same VLAN receive the broadcast therefore, PC4 would receive the broadcast.
Notes: 6.1 – VLAN Segmentation
6.1.2 – VLANs in a Multi-Switched Environment
6.1.2.2 - Controlling Broadcast Domains with VLANs

## Slide 22: VLANs in a Multi-Switched Environment Tagging Ethernet Frames for VLAN Identification
Before a frame is forwarded across a trunk link, it must be tagged with its VLAN information.
  Frame tagging is the process of adding a VLAN identification header to the frame.
  It is used to properly transmit multiple VLAN frames through a trunk link.
IEEE 802.1Q is a vey popular VLAN trunking protocol that defines the structure of the tagging header added to the frame.
  Switches add VLAN tagging information after the Source MAC address field.
  The fields in the 802.1Q VLAN tag includes VLAN ID (VID).
  Trunk links add the tag information before sending the frame and then remove the tags before forwarding frames through non-trunk ports.
Notes: 6.1 – VLAN Segmentation
6.1.2 – VLANs in a Multi-Switched Environment
6.1.2.3 - Tagging Ethernet Frames for VLAN Identification

## Slide 23: VLANs in a Multi-Switched Environment Native VLANs and 802.1Q Tagging
Control traffic sent on the native VLAN should not be tagged.
Frames received untagged, remain untagged and are placed in the native VLAN when forwarded.
If there are no ports associated to the native VLAN and no other trunk links, an untagged frame is dropped.
When configuring a switch port on a Cisco switch, configure devices so that they do not send tagged frames on the native VLAN.
In Cisco switches, the native VLAN is VLAN 1, by default.
Notes: 6.1 – VLAN Segmentation
6.1.2 – VLANs in a Multi-Switched Environment
6.1.2.4 - Native VLANs and 802.1Q Tagging

## Slide 24: VLANs in a Multi-Switched Environment Voice VLAN Tagging
An access port connecting a Cisco IP phone can be configured to use two separate VLANs:
  A VLAN for voice traffic
  A VLAN for data traffic from a device attached to the phone.
The link between the switch and the IP phone behaves like a trunk to carry traffic from both VLANs.
Cisco IP Phone contains an integrated three-port 10/100 switch dedicated to these devices:
  Port 1 connects to the switch or other VoIP device.
  Port 2 is an internal 10/100 interface that carries the IP phone traffic.
  Port 3 (access port) connects to a PC or other device.
Notes: 6.1 – VLAN Segmentation
6.1.2 – VLANs in a Multi-Switched Environment
6.1.2.5 - Voice VLAN Tagging

## Slide 25: VLANs in a Multi-Switched Environment Packet Tracer – Investigating a VLAN Implementation
Notes: 6.1 – VLAN Segmentation
6.1.2 – VLANs in a Multi-Switched Environment
6.1.2.7 – Packet Tracer – Investigating a VLAN Implementation

## Slide 26: 6.2 VLAN Implementation
Notes: 6 - VLANs
6.2 – VLAN Implementation

## Slide 27: VLAN Assignment VLAN Ranges on Catalyst Switches
Cisco Catalyst 2960 and 3560 Series switches support over 4,000 VLANs.
VLANs are split into two categories:
  Normal range VLANs
    VLAN numbers from 1 to 1,005
    Configurations stored in the vlan.dat (in the flash memory)
    IDs 1002 through 1005 are reserved for legacy Token Ring and Fiber Distributed Data Interface (FDDI) VLANs, automatically created and cannot be removed.
  Extended Range VLANs
    VLAN numbers from 1,006 to 4,096
    Configurations stored in the running configuration (NVRAM)
    VLAN Trunking Protocol (VTP) does not learn extended VLANs
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.1 - VLAN Ranges on Catalyst Switches

## Slide 28: VLAN Assignment Creating a VLAN
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.2 – Creating a VLAN

## Slide 29: VLAN Assignment Assigning Ports to VLANs
Example 1
Example 2
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.3 – Assigning Ports to VLANs

## Slide 30: VLAN Assignment Changing VLAN Port Membership
Remove VLAN Assignment
Even though interface F0/18 was previously assigned to VLAN 20, it reset to the default VLAN1.
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.4 - Changing VLAN Port Membership

## Slide 31: VLAN Assignment Deleting VLANs
Use the no vlan vlan-id global configuration mode command to remove VLAN.
To delete the entire vlan.dat file, use the delete flash:vlan.dat privileged EXEC mode command.
  delete vlan.dat can be used if the vlan.dat file has not been moved from its default location.
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.5 – Deleting VLANs

## Slide 32: VLAN Assignment Verifying VLAN Information
VLAN configurations can be validated using the Cisco IOS show vlan and show interfaces command options.
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.6 - Verifying VLAN Information

## Slide 33: VLAN Assignment Packet Tracer – Configuring VLANs
Notes: 6.2 – VLAN Implementations
6.2.1 – VLAN Assignment
6.2.1.7 – Packet Tracer – Configuring VLANs

## Slide 34: VLAN Trunks Configuring IEEE 802.1q Trunk Links
Native VLAN
VLAN 99
172.17.99.0/24
Notes: 6.2 – VLAN Implementations
6.2.2 – VLAN Trunks
6.2.2.1 - Configuring IEEE 802.1q Trunk Links

## Slide 35: VLAN Trunks Resetting the Trunk to Default State
F0/1 is configured as an access port which removes the trunk feature.
Notes: 6.2 – VLAN Implementations
6.2.2 – VLAN Trunks
6.2.2.2 - Resetting the Trunk to Default State

## Slide 36: VLAN Trunks Verifying Trunk Configuration
Notes: 6.2 – VLAN Implementations
6.2.2 – VLAN Trunk
6.2.2.3 - Verifying Trunk Configuration

## Slide 37: VLAN Trunks Packet Tracer – Configuring Trunks
Notes: 6.2 – VLAN Implementations
6.2.2 – VLAN Trunks
6.2.2.4 - Packet Tracer – Configuring Trunks

## Slide 38: VLAN Trunks Lab – Configuring VLANs and Trunks
Notes: 6.2 – VLAN Implementations
6.2.2 – VLAN Trunks
6.2.2.5 – Lab – Configuring VLANs and Trunks

## Slide 39: Troubleshoot VLANs and Trunks IP Addressing Issues with VLANs
Common practice to associate a VLAN with an IP network.
  Different IP networks must communicate through a router.
  All devices within a VLAN must be part of the same IP network to communicate.
In the figure, PC1 cannot communicate to the server because it has a wrong IP address configured.
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.1 - IP Addressing Issues with VLANs

## Slide 40: Troubleshoot VLANs and Trunks Missing VLANs
If all the IP address mismatches have been solved, but the device still cannot connect, check if the VLAN exists in the switch.
If the VLAN to which the port belongs is deleted, the port becomes inactive and is unable to communicate with the rest of the network.
  It is not functional until the missing VLAN is created or the VLAN is removed from the port.
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.2 - Missing VLANs

## Slide 41: Troubleshoot VLANs and Trunks Introduction to Troubleshooting Trunks
  In this example, the Native VLAN should be VLAN 99 however, the output of the command identifies VLAN 2 as the Native VLAN.
  To solve this problem, configure the same native VLAN on both sides.
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.3 - Introduction to Troubleshooting Trunks

## Slide 42: Troubleshoot VLANs and Trunks Common Problems with Trunks
Trunking issues are usually associated with incorrect configurations.
The most common type of trunk configuration errors are:
When a trunk problem is suspected, it is recommended to troubleshoot in the order shown above.
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.4 - Common Problems with Trunks

## Slide 43: Troubleshoot VLANs and Trunks Incorrect Port Mode
In this example, PC4 cannot reach the Web server.
  The trunk links on S1 and S3 are verified and reveal that the S3 trunk port has been configured as an access port.
  To resolve the issue, the S3 F03 port is configured as a trunk link.
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.5 - Incorrect Port Mode

## Slide 44: Troubleshoot VLANs and Trunks Incorrect VLAN List
In this example, PC5 cannot reach the Student Email server.
  The output of the switchport trunk allowed vlan command reveals S1 is not allowing VLAN 20.
  To resolve the issue, the S1 F0/1 port is configured to allow VLANs 10, 20, and 99.
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.6 - Incorrect VLAN List

## Slide 45: Troubleshoot VLANs and Trunks Packet Tracer - Troubleshooting a VLAN Implementation - Scenario 1
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.7 - Packet Tracer - Troubleshooting a VLAN Implementation - Scenario 1

## Slide 46: Troubleshoot VLANs and Trunks Packet Tracer - Troubleshooting a VLAN Implementation - Scenario 2
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.8 - Packet Tracer - Troubleshooting a VLAN Implementation - Scenario 2

## Slide 47: Troubleshoot VLANs and Trunks Lab - Troubleshooting VLAN Configurations
Notes: 6.2 – VLAN Implementations
6.2.3 – Troubleshoot VLANs and Trunks
6.2.3.9 – Lab - Troubleshooting VLAN Configurations

## Slide 48: 6.3 Inter-VLAN Routing Using Routers
Notes: 6 - VLANs
6.3 – Inter-VLAN Routing Using Routers

## Slide 49: Inter-VLAN Routing Operation What is Inter-VLAN Routing?
Layer 2 switches cannot forward traffic between VLANs without the assistance of a router.
Inter-VLAN routing is a process for forwarding network traffic from one VLAN to another, using a router.
There are three options for inter-VLAN routing:
  Legacy inter-VLAN routing
  Router-on-a-Stick
  Layer 3 switching using SVIs
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.1 – Inter-VLAN Routing Operation
6.3.1.1 - What is Inter-VLAN Routing?

## Slide 50: Inter-VLAN Routing Operation Legacy Inter-VLAN Routing
In the past:
  Router interfaces were used to route between VLANs.
  Each VLAN was connected to a different physical router interface.
  Packets would arrive on the router through one interface, be routed and leave through another.
  Because the router interfaces were connected to VLANs and had IP addresses from that specific VLAN, routing between VLANs was achieved.
  Large networks with large number of VLANs required many router interfaces.
In this example, the router was configured with two separate physical interfaces to interact with the different VLANs and perform the routing.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.1 – Inter-VLAN Routing Operation
6.3.1.2 - Legacy Inter-VLAN Routing

## Slide 51: Inter-VLAN Routing Operation Router-on-a-Stick Inter-VLAN Routing
The router-on-a-stick approach uses only one of the router’s physical interface.
  One of the router’s physical interfaces is configured as a 802.1Q trunk port so it can understand VLAN tags.
  Logical subinterfaces are created; one subinterface per VLAN.
  Each subinterface is configured with an IP address from the VLAN it represents.
  VLAN members (hosts) are configured to use the subinterface address as a default gateway.
In this example, the R1 interface is configured as a trunk link and connects to the trunk F0/4 port on S1.
Router accepts VLAN-tagged traffic on the trunk interface
Router internally routes between the VLANs using subinterfaces.
Router then forwards the routed traffic as VLAN-tagged for the destination VLAN out the trunk link.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.1 – Inter-VLAN Routing Operation
6.3.1.3 - Router-on-a-Stick Inter-VLAN Routing

## Slide 52: Configure Legacy Inter-VLAN Routing Configure Legacy Inter-VLAN Routing: Preparation
Legacy inter-VLAN routing requires routers to have multiple physical interfaces.
Each one of the router’s physical interfaces is connected to a unique VLAN.
Each interface is also configured with an IP address for the subnet associated with the particular VLAN.
Network devices use the router as a gateway to access the devices connected to the other VLANs.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.2 – Configure Legacy Inter-VLAN Routing
6.3.2.1 - Configure Legacy Inter-VLAN Routing: Preparation

## Slide 53: Configure Legacy Inter-VLAN Routing Configure Legacy Inter-VLAN Routing: Switch Configuration
Configure the VLANs on the switch and then assign the ports to their respective VLANs.
In this example, the S1 ports are configured as follows:
  Ports F0/4 and F0/11 of S1 are on VLAN 10
  Ports F0/5 and F0/16 ports are on VLAN 30.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.2 – Configure Legacy Inter-VLAN Routing
6.3.2.2 - Configure Legacy Inter-VLAN Routing: Switch Configuration

## Slide 54: Configure Legacy Inter-VLAN Routing Configure Legacy Inter-VLAN Routing: Router Interface Configuration
Next configure the router interfaces.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.2 – Configure Legacy Inter-VLAN Routing
6.3.2.3 - Configure Legacy Inter-VLAN Routing: Router Interface Configuration

## Slide 55: Configure Legacy Inter-VLAN Routing Lab – Configuring Per-Interface Inter-VLAN Routing
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.2 – Configure Legacy Inter-VLAN Routing
6.3.2.4 – Lab – Configuring Per-Interface Inter-VLAN Routing

## Slide 56: Configure Router-on-a-Stick Inter-VLAN Routing Configure Router-on-a Stick: Preparation
An alternative to legacy inter-VLAN routing is to use VLAN trunking and subinterfaces.
VLAN trunking allows a single physical router interface to route traffic for multiple VLANs.
The physical interface of the router must be connected to a trunk link on the adjacent switch.
On the router, subinterfaces are created for each unique VLAN.
Each subinterface is assigned an IP address specific to its subnet or VLAN and is also configured to tag frames for that VLAN.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.3 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.1 - Configure Router-on-a Stick: Preparation

## Slide 57: Configure Router-on-a-Stick Inter-VLAN Routing Configure Router-on-a Stick: Switch Configuration
To enable inter-VLAN routing using router-on-a stick, start by enabling trunking on the switch port that is connected to the router.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.3 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.2 - Configure Router-on-a Stick: Switch Configuration

## Slide 58: Configure Router-on-a-Stick Inter-VLAN Routing Configure Router-on-a Stick: Router Subinterface Configuration
The router-on-a-stick method requires subinterfaces to be configured for each routable VLAN.
  The subinterfaces must be configured to support VLANs using the encapsulation dot1Q VLAN-ID interface configuration command.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.3 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.3 - Configure Router-on-a Stick: Router Subinterface Configuration

## Slide 59: Configure Router-on-a-Stick Inter-VLAN Routing Configure Router-on-a Stick: Verifying Subinterfaces
By default, Cisco routers are configured to route traffic between local subinterfaces.
  As a result, routing does not specifically need to be enabled.
Use the show vlan and show ip route commands to verify the subinterface configurations.
The show vlan command displays information about the Cisco IOS VLAN subinterfaces.
The show ip route command displays the routing table containing the networks associated with outgoing subinterfaces.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.3 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.4 - Configure Router-on-a Stick: Verifying Subinterfaces

## Slide 60: Configure Router-on-a-Stick Inter-VLAN Routing Configure Router-on-a Stick: Verifying Routing
Remote VLAN device connectivity can be tested using the ping command.
  The command sends an ICMP echo request and when a host receives an ICMP echo request, it responds with an ICMP echo reply.
Tracert is a useful utility for confirming the routed path taken between two devices.
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.3 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.5 - Configure Router-on-a Stick: Verifying Routing

## Slide 61: Configure Router-on-a-Stick Inter-VLAN Routing Packet Tracer - Configuring Router-on-a-Stick Inter-VLAN Routing
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.3 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.6 -Packet Tracer - Configuring Router-on-a-Stick Inter-VLAN Routing

## Slide 62: Configure Router-on-a-Stick Inter-VLAN Routing Lab - Configuring 801.2Q Trunk-Based Inter-VLAN Routing
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.3 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.7 -Lab - Configuring 801.2Q Trunk-Based Inter-VLAN Routing

## Slide 63: Configure Router-on-a-Stick Inter-VLAN Routing Packet Tracer - Inter-VLAN Routing Challenge
Notes: 6.3 – Inter-VLAN Routing Using Routers
6.3.3 – Configure Router-on-a-Stick Inter-VLAN Routing
6.3.3.8 -Packet Tracer - Inter-VLAN Routing Challenge

## Slide 64: 6.4 Chapter Summary
Notes: 6 - VLANs
6.4 – Summary

## Slide 65: Conclusion Packet Tracer - Skills Integration Challenge
Notes: 6.4 – Summary
6.4.1 – Conclusion
6.4.1.2 – Packet Tracer - Skills Integration Challenge

## Slide 66: Conclusion Chapter 6: VLANs
Explain how VLANs segment broadcast domains in a small to medium-sized business network.
Implement VLANs to segment a small to medium-sized business network..
Configure routing between VLANs in a small to medium-sized business network.
Notes: 6.4 – Summary
6.4.1 – Conclusion
6.4.1.3 – Chapter 6: VLANs

## Slide 67: Section 6.1 New Terms and Commands
VLAN Logical broadcast domain Data VLAN Default VLAN Native VLAN Management VLAN show vlan brief Voice VLAN VLAN Trunk VLAN Segmentation IEEE 802.1Q VLAN Tagging Canonical Format Identifier (CFI) | User Priority VLAN ID Type show interfaces int switchport
Notes: New Terms and Commands

## Slide 68: Section 6.2 New Terms and Commands
Normal Range VLANs Extended Range VLANs vlan vlan-id name vlan-name switchport mode access switchport access vlan vlan-id interface range no switchport access vlan vlan-id no vlan vlan-id delete flash:vlan.dat delete vlan.dat | show vlan show interfaces show vlan summary show interfaces vlan vlan_id switchport mode trunk switchport trunk allowed vlan vlan_list switchport trunk native vlan vlan_id no switchport trunk allowed vlan no switchport trunk native vlan show interfaces switchport | no switchport access vlan vlan_id show interfaces trunk show interfaces int_id trunk
Notes: New Terms and Commands

## Slide 69: Section 6.3 New Terms and Commands
Legacy Inter-VLAN Routing Router-on-a-Stick Inter-VLAN Routing interface interface_id.subinterface_id encapsulation dot1q vlan_id IEEE 802.1Q | 
Notes: New Terms and Commands