## Slide 2: Chapter 2: Static Routing
Routing and Switching Essentials 6.0 Planning Guide
Notes: Cisco Networking Academy Program
Routing & Switching Essentials v6.0
Chapter 2: Static Routing

## Slide 3: Chapter 2 - Sections & Objectives
2.1 Static Routing Advantages
2.2 Configure Static and Default Routes
2.3 Troubleshoot Static and Default Routes
Notes: 3
Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 2: Static Routing

## Slide 4: 2.1 Implement Static Routes
Notes: 2 - Static Routing
2.1 – Implement Static Routes

## Slide 5: Reach Remote Networks
A router learns about remote networks in two ways:
  Manually entered into the route table using static routes
      Static routes are not automatically updated and must be reconfigured when topology changes
  Dynamically (Automatically) learned using a routing protocol
Notes: 2.1 – Implement Static Routes
2.1.1 – Static Routing
2.1.1.1 – Reach Remote Networks

## Slide 6: Static and Default Routes

## Slide 7: Dynamic Routing

## Slide 8: Why Use Static Routing?
Dynamic versus Static Routing
Notes: 2.1 – Implement Static Routes
2.1.1 – Static Routing
2.1.1.2 – Why Use Static Routing?

## Slide 9: When to Use Static Routes
Three uses for static routes:
Smaller networks that are not expected to grow
Routing to and from stub networks
  Stub network accessed by a single route and has one neighbor
  172.16.3.0 is a stub network
A single default route to represent a path to any network not found in the routing table
  Use default route on R1 to point to R2 for all other networks
Stub Networks and Stub Routers
Notes: 2.1 – Implement Static Routes
2.1.1 – Static Routing
2.1.1.3 – When to Use Static Routes

## Slide 10: Static Route Applications
Use Static Routes To:
Connect to a specific network
Connect a stub router
Summarize routing table entries which reduces size of routing advertisements
Create a backup route in case a primary route link fails
Notes: 2.1 – Implement Static Routes
2.1.2 – Types of Static Routes
2.1.2.1 – Static Route Applications

## Slide 11: Standard Static Route
R2 configured with a static route to reach the stub network 172.16.3.0/24
Notes: 2.1 – Implement Static Routes
2.1.2 – Types of Static Routes
2.1.2.2 – Standard Static Route

## Slide 12: Default Static Route
Default route matches all packets and is used when a packet does not match a specific route in the routing table
Can be dynamically learned or statically configured
Default Static route uses 0.0.0.0/0 as the destination IPv4 address
Creates a Gateway of Last Resort
Common use is when connecting a company’s edge router to the ISP network
Router has only one router to which it is connected
Notes: 2.1 – Implement Static Routes
2.1.2 – Types of Static Routes
2.1.2.3 – Default Static Route

## Slide 13: Summary Static Route
Multiple static routes can be summarized into a single network address
  Destination networks must be contiguous
  Multiple static routes must use the same exit interface or next hop
  In figure, four networks is summarized into one summary static route
Notes: 2.1 – Implement Static Routes
2.1.2 – Types of Static Routes
2.1.2.4 – Summary Static Route

## Slide 14: Floating Static Route
Static routes that are used to provide a backup path
Used when primary route is not available
Configured with a higher administrative distance (trustworthiness) than the primary route
Example: EIGRP administrative distance equals 90. A floating static route with an AD of 91 or higher would serve as backup route and will be used if EIGRP route goes down.
Floating Static Route
Notes: 2.1 – Implement Static Routes
2.1.2 – Types of Static Routes
2.1.2.5 – Floating Static Route

## Slide 15: 2.2 Configure Static and Default Routes
Notes: 2 - Static Routing
2.2 – Configure Static and Default Routes

## Slide 16: ip route Command
Notes: 2.2 – Configure Static and Default Routes
2.2.1 – Configure IPv4 Static Routes
2.2.1.1 –ip route Command

## Slide 17: Next-Hop Options
In this example, each router only has entries for directly connected network
Notes: 2.2 – Configure Static and Default Routes
2.2.1 – Configure IPv4 Static Routes
2.2.1.2 – Next-Hop Options

## Slide 20: Configure IPv4 Static Routes Next-Hop Options (Cont.)
R1 does not have an entry in its routing table for the R3 LAN network
In a static route next-hop can be identified by
  Next-hop IP address
  Router exit interface
  Next-hop IP address and exit interface
Notes: 2.2 – Configure Static and Default Routes
2.2.1 – Configure IPv4 Static Routes
2.2.1.2 – Next-Hop Options

## Slide 22: Configure IPv4 Static Routes Configure a Next-Hop Static Route
In this example, only the next-hop IP address is specified
Before packet is forwarded the router must determine the exit interface to use (route resolvability)
Notes: 2.2 – Configure Static and Default Routes
2.2.1 – Configure IPv4 Static Routes
2.2.1.3 – Configure a Next-Hop Static Route

## Slide 23: Configure a Next-Hop Static Route (Cont.)
In example, when a packet is destined for 192.168.2.0/24 network, R1:
  Looks for match (#1) and needs to forward packets to 172.16.2.2
  R1 must determine how to reach 172.16.2.2 first
  Searches a second time for 172.16.2.0/24 (#2) and matches to exit interface s0/0/0
  Takes two routing table lookups, process referred to as recursive lookup
  If the exit interface is “down” or “administratively down” then the static route configured with next-hop will not be installed in routing table
Notes: 2.2 – Configure Static and Default Routes
2.2.1 – Configure IPv4 Static Routes
2.2.1.3 – Configure a Next-Hop Static Route

## Slide 24: Configure a Directly Connected Static Route
Use the exit interface to specify next-hop so no other lookups are required
Administrative distance of static route is 1
Notes: 2.2 – Configure Static and Default Routes
2.2.1 – Configure IPv4 Static Routes
2.2.1.4 – Configure a Directly Connected Static Route

## Slide 26: Configure a Directly Connected Static Route (Cont.)
Cisco Express Forwarding (CEF)
  default behavior on IOS 12.0 or later
  provides optimized lookup
  uses a Forwarding Information Base (FIB) which is a copy of the routing table and an adjacency table that includes Layer 2 addresses
  no recursive lookup needed for next-hop IP address lookups
Notes: 2.2 – Configure Static and Default Routes
2.2.1 – Configure IPv4 Static Routes
2.2.1.4 – Configure a Directly Connected Static Route

## Slide 27: Configure a Fully Specified Static Route
Both the exit interface and the next-hop IP address are specified
When exit interface is an Ethernet network, fully specified static route is used
Note: With CEF, a next-hop address could be used instead
Notes: 2.2 – Configure Static and Default Routes
2.2.1 – Configure IPv4 Static Routes
2.2.1.5 – Configure a Fully Specified Static Route

## Slide 30: Default Static Route
  Default static routes are commonly used when connecting:
  An edge router to a service provider network
  A stub router (a router with only one upstream neighbor router)
  Default route is used when no other routes in the routing table match the destination IP
Notes: 2.2 – Configure Static and Default Routes
2.2.2 – Configure IPv4 Default Routes
2.2.2.1 – Default Static Route

## Slide 32: Configure a Default Static Route
Any packets not matching route entries are forwarded to 172.16.2.2
Notes: 2.2 – Configure Static and Default Routes
2.2.2 – Configure IPv4 Default Routes
2.2.2.2 – Configure a Default Static Route

## Slide 33: Verify a Default Static Route
show ip route static displays just the static routes
  S indicates static route
  candidate default route indicated by *
  /0 mask in route entry indicates none of the bits are required to match
Notes: 2.2 – Configure Static and Default Routes
2.2.2 – Configure IPv4 Default Routes
2.2.2.3 – Verify a Default Static Route

## Slide 34: Packet Tracer – Configuring IPv4 Static and Default Routes
Notes: 2.2 – Configure Static and Default Routes
2.2.2 – Configure IPv4 Default Routes
2.2.2.4 – Packet Tracer – Configuring IPv4 Static and Default Routes

## Slide 35: Lab – Configuring IPv4 Static and Default Routes
Notes: 2.2 – Configure Static and Default Routes
2.2.2 – Configure IPv4 Default Routes
2.2.2.5 – Lab– Configuring IPv4 Static and Default Routes

## Slide 36: The ipv6 route Command
Notes: 2.2 – Configure Static and Default Routes
2.2.3 – Configure IPv6 Static Routes
2.2.3.1 – The ipv6 route Command

## Slide 37: The ipv6 route Command (Cont.)
ipv6 unicast-routing enables the router to forward IPv6 packets
Notes: 2.2 – Configure Static and Default Routes
2.2.3 – Configure IPv6 Static Routes
2.2.3.1 – The ipv6 route Command

## Slide 38: Next-Hop Options
Each router only knows about directly connected networks
  R1 can ping R2 (ipv6 2001:DB8:ACAD:4::2) but cannot ping R3 (ipv6 2001:DB8:ACAD:3::2)
Notes: 2.2 – Configure Static and Default Routes
2.2.3 – Configure IPv6 Static Routes
2.2.3.2 – Next-Hop Options

## Slide 41: Configure IPv6 Static Routes Next-Hop Options (Cont.)
Next hop can be identified by an IPv6 address, exit interface, or both.
Destination is specified by one of three route types:
  Next-hop static IPv6 route - Only the next-hop IPv6 address is specified
  Directly connected static IPv6 route - Only the router exit interface is specified
  Fully specified static IPv6 route - The next-hop IPv6 address and exit interface are specified
Notes: 2.2 – Configure Static and Default Routes
2.2.3 – Configure IPv6 Static Routes
2.2.3.2 – Next—Hop Options

## Slide 42: Configure IPv6 Static Routes Configure a Next Hop Static IPv6 Route
Three next-hop static routes are configured on R1
As with IPv4, must resolve the route to determine the exit interface to use to forward the packet
The IPv6 address matches the route for the directly connected network 2001:DB8:ACAD:4::/64 with the exit interface Serial 0/0/0.
Notes: 2.2 – Configure Static and Default Routes
2.2.3 – Configure IPv6 Static Routes
2.2.3.3 – Configure a Next Hop Static IPv6 Route

## Slide 43: Configure IPv6 Static Routes Configure a Directly Connected Static IPv6 Route
Alternative to next hop is to specify the exit interface
Packet destined for 2001:DB8:ACAD:3::/64 network, forwarded out Serial 0/0/0 – no other lookups needed
Notes: 2.2 – Configure Static and Default Routes
2.2.3 – Configure IPv6 Static Routes
2.2.3.4 – Configure a Directly Connected Static IPv6 Route

## Slide 44: Configure IPv6 Static Routes Configure a Fully Specified Static IPv6 Route
Fully specified static route must be used if IPv6 link-local address is used as next-hop
Notes: 2.2 – Configure Static and Default Routes
2.2.3 – Configure IPv6 Static Routes
2.2.3.5 – Configure a Fully Specified Static IPv6 Route

## Slide 45: Configure IPv6 Static Routes Verify IPv6 Static Routes
Notes: 2.2 – Configure Static and Default Routes
2.2.3 – Configure IPv6 Static Routes
2.2.3.6 – Verify IPv6 Static Routes

## Slide 46: Configure IPv6 Default Routes Default Static IPv6 Route
Default static route matches all packets not specified in routing table
Notes: 2.2 – Configure Static and Default Routes
2.2.4 – Configure IPv6 Default Routes
2.2.4.1 – Default Static IPv6 Route

## Slide 47: Configure IPv6 Default Routes Configure a Default Static IPv6 Route
R1 is a stub router because it is only connected to R2
More efficient to configure a default static IPv6 route in this topology
Notes: 2.2 – Configure Static and Default Routes
2.2.4 – Configure IPv6 Default Routes
2.2.4.2 – Configure a Default Static IPv6 Route

## Slide 48: Configure IPv6 Default Routes Verify a Default Static Route
::/0 mask indicates that none of the bits are required to match
If a more specific match does not exist, the default static IPv6 route matches all packets.
Notes: 2.2 – Configure Static and Default Routes
2.2.4 – Configure IPv6 Default Routes
2.2.4.3 – Verify a Default Static Route

## Slide 49: Configure IPv6 Default Routes Packet Tracer – Configuring IPv6 Static and Default Routes
Notes: 2.2 – Configure Static and Default Routes
2.2.4 – Configure IPv6 Default Routes
2.2.4.4 – Packet Tracer – Configuring IPv6 Static and Default Routes

## Slide 50: Configure IPv6 Default Routes Lab – Configuring IPv6 Static and Default Routes
Notes: 2.2 – Configure Static and Default Routes
2.2.4 – Configure IPv6 Default Routes
2.2.4.5 – Lab – Configuring IPv6 Static and Default Routes

## Slide 51: Configure Floating Static Routes Floating Static Routes
Floating static routes have an administrative distance greater than the dynamic routing protocol or other static route
Used as backup routes
Administrative distance of common routing protocols
  EIGRP = 90
  IGRP = 100
  OSPF = 110
  IS-IS = 115
  RIP = 120
By default, AD of static route = 1
Static route AD can be increased to make route less desirable until preferred route is lost
Notes: 2.2 – Configure Static and Default Routes
2.2.5 – Configure Floating Static Routes
2.2.5.1 – Floating Static Routes

## Slide 52: Configure Floating Static Routes Configure a Floating Static Route
Preferred router from R1 is to R2 (AD = 1)
Notes: 2.2 – Configure Static and Default Routes
2.2.5 – Configure Floating Static Routes
2.2.5.2 – Configure an IPv4 Floating Static Route

## Slide 53: Configure Floating Static Routes Test the IPv4 Floating Static Route
Notes: 2.2 – Configure Static and Default Routes
2.2.5 – Configure Floating Static Routes
2.2.5.3 – Test the IPv4 Floating Static Route

## Slide 54: Configure Floating Static Routes Test the IPv4 Floating Static Route (Cont.)
Notes: 2.2 – Configure Static and Default Routes
2.2.5 – Configure Floating Static Routes
2.2.5.3 – Test the IPv4 Floating Static Route

## Slide 55: Configure Floating Static Routes Configure an IPv6 Floating Static Route
Similar to IPv4 floating static routes
Notes: 2.2 – Configure Static and Default Routes
2.2.5 – Configure Floating Static Routes
2.2.5.4 –Configure an IPv6 Floating Static Route

## Slide 56: Configure Floating Static Routes Packet Tracer - Configuring Floating Static Routes
Notes: 2.2 – Configure Static and Default Routes
2.2.5 – Configure Floating Static Routes
2.2.5.5 –Packet Tracer - Configuring Floating Static Routes

## Slide 57: Configure Static Host Routes Automatically Installed Host Routes
Host route is an IPv4 address with a 32-bit mask or IPv6 address with a 128-bit mask.
Automatically installed when IP address is configured
Configured as a static host route
Allows more efficiency for packets directed to the router
Local route marked with “L” (introduced in IOS 15)
Notes: 2.2 – Configure Static and Default Routes
2.2.6 – Configure Static Host Routes
2.2.6.1 – Automatically Installed Host Routes

## Slide 58: Configure Static Host Routes Configure IPv4 and IPv6 Static Host Routes
Notes: 2.2 – Configure Static and Default Routes
2.2.6 – Configure Static Host Routes
2.2.6.2 – Configure IPv4 and IPv6 Static Host Routes

## Slide 59: 2.3 Troubleshoot Static and Default Routes
Notes: 2 - Static Routing
2.3 – Troubleshoot Static and Default Routes

## Slide 60: Packet Processing with Static Routes Static Routes and Packet Forwarding
PC1 sending packet to PC3 - Packet arrives on G0/0
R1 has no specific route to 192.168.2.0 so uses default route
R1 encapsulates packet in new frame
Frame forwarded out S0/0/0
Notes: 2.3 – Troubleshoot Static and Default Routes
2.3.1 – Packet Processing with Static Routes
2.3.1.1 – Static Routes and Packet Forwarding

## Slide 61: Packet Processing with Static Routes Static Routes and Packet Forwarding (Cont.)
Packet arrives on S0/0/0 interface on R2
R2 de-encapsulates the frame and looks for a route to the destination
R2 has a static route to 192.168.2.0/24 out the Serial 0/0/1 interface
R2 encapsulates the packet in a new frame and forwards out S0/0/1
Notes: 2.3 – Troubleshoot Static and Default Routes
2.3.1 – Packet Processing with Static Routes
2.3.1.1 – Static Routes and Packet Forwarding

## Slide 62: Packet Processing with Static Routes Static Routes and Packet Forwarding (Cont.)
R3 de-encapsulates the frame and sees a connected route to 192.168.2.0/24 out G0/0
R3 looks up the ARP table entry for 192.168.2.10 to find the Layer 2 MAC address for PC3 (ARP used if needed for PC3 MAC)
R3 encapsulates the packet in a new frame with the MAC address of the G0/0 interface as the source Layer 2 address and the MAC address of PC3 as the destination MAC address
Frame is forwarded out of G0/0 interface and packet arrives on the NIC interface of PC3
Notes: 2.3 – Troubleshoot Static and Default Routes
2.3.1 – Packet Processing with Static Routes
2.3.1.1 – Static Routes and Packet Forwarding

## Slide 63: Troubleshoot IPv4 Static and Default Route Configuration Troubleshoot a Missing Route
Common IOS troubleshooting commands include:
  ping
  traceroute
  show ip route
  show ip interface brief
  show cdp neighbors detail
Notes: 2.3 – Troubleshoot Static and Default Routes
2.3.2 – Troubleshoot IPv4 Static and Default Route Configuration
2.3.2.1 – Troubleshoot a Missing Route

## Slide 64: Troubleshoot IPv4 Static and Default Route Configuration Troubleshoot a Missing Route (Cont.)
Notes: 2.3 – Troubleshoot Static and Default Routes
2.3.2 – Troubleshoot IPv4 Static and Default Route Configuration
2.3.2.1 – Troubleshoot a Missing Route

## Slide 65: Troubleshoot IPv4 Static and Default Route Configuration Solve a Connectivity Problem
A traceroute reveals that R2 forwards the traceroute back to R1. R1 returns it to R2
Notes: 2.3 – Troubleshoot Static and Default Routes
2.3.2 – Troubleshoot IPv4 Static and Default Route Configuration
2.3.2.2 – Solve a Connectivity Problem

## Slide 66: Troubleshoot IPv4 Static and Default Route Configuration Solve a Connectivity Problem (Cont.)
Static route to 192.168.2.0/24 has been configured using the next-hop address 172.16.2.1.
Incorrect route is removed and the correct route is then entered
Notes: 2.3 – Troubleshoot Static and Default Routes
2.3.2 – Troubleshoot IPv4 Static and Default Route Configuration
2.3.2.2 – Solve a Connectivity Problem

## Slide 67: Troubleshoot IPv4 Static and Default Route Configuration Packet Tracer – Troubleshooting Static Routes
Notes: 2.3 – Troubleshoot Static and Default Routes
2.3.2 – Troubleshoot IPv4 Static and Default Route Configuration
2.3.2.3 – Packet Tracer – Troubleshooting Static Routes

## Slide 68: Troubleshoot IPv4 Static and Default Route Configuration Lab – Troubleshooting Static Routes
Notes: 2.3 – Troubleshoot Static and Default Routes
2.3.2 – Troubleshoot IPv4 Static and Default Route Configuration
2.3.2.4 – Lab – Troubleshooting Static Routes

## Slide 69: 2.4 Chapter Summary
Notes: 2 - Static Routing
2.4 – Summary

## Slide 70: Conclusion Chapter 2: Static Routing
Explain how static routes are implemented in a small to medium-sized business network.
Configure static routes to enable connectivity in a small to medium-sized business network.
Troubleshoot static and default route configurations.
Notes: 2.4 – Summary
2.4.1 – Conclusion
2.4.1.2 – Chapter 2: Static Routing

## Slide 71: Section 2.1 New Terms and Commands
stub network stub router Standard static route | Summary static route Floating static route exit interface
Notes: New Terms and Commands

## Slide 72: Section 2.2 New Terms and Commands
next-hop IP address next-hop static route directly connected static route fully specified static route | recursive lookup link-local address host route local host route
Notes: New Terms and Commands