## Slide 1: Chapter 5: Switch Configuration
Instructor Materials
CCNA Routing and Switching
Routing and Switching Essentials v6.0
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 5: Switch Configuration

## Slide 2: Chapter 5 - Sections & Objectives SMB
5.1 Basic Switch Configuration
5.2 Basic Device Configuration
    Configure the management virtual interface on a switch.
    Configure the port security feature to restrict network access.
Notes: 2
Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 5: Switch Configuration

## Slide 3: 5.1 Configure a Switch with Initial Settings
Notes: 5 – Switch Configuration
5.1 – Configure a Switch with Initial Settings

## Slide 4: Switch Boot Sequence
  Power-on self-test (POST), a program stored in ROM, executes and checks hardware like CPU and RAM.
  The boot loader, also stored in ROM, runs and initializes parts within the CPU, initializes the flash file system, and then locates and loads an IOS image.
    The IOS image can be defined within the BOOT environment variable.
    If the variable is not set, the switch scours through the flash file system searching for an executable image file, loading it into RAM, and launching it if found.
    If an executable image file is not found, the switch shows the prompt switch: where a few commands are allowed in order to provide access to operating system files found in flash memory and files used to load or reload an operating system.
  If an IOS operating system loads, the switch interfaces are initialized and any commands stored in the startup-config file load.
The startup-config file is stored in NVRAM.
Notes: 5.1 – Basic Switch Configuration
5.1.1 – Configure a Switch with Initial Settings
5.1.1.1 – Switch Boot Sequence

## Slide 5: Switch Boot Sequence (Cont.)
Notes: 5.1 – Basic Switch Configuration
5.1.1 – Configure a Switch with Initial Settings
5.1.1.1 – Switch Boot Sequence

## Slide 6: Recovering From a System Crash
The boot loader prompt can be accessed through a console connection to the switch:
  1. Cable the PC to the switch console port.
  2. Configure the terminal emulation software on the PC.
  3. Unplug the switch power cord.
  4. Reconnect the power cord and at the same time or within 15 seconds, press and hold the Mode button on the front of the switch until the System LED turns an amber color briefly and then turns a solid green.
The boot loader command prompt is switch: (instead of Switch>).
  The commands available through the boot loader command prompt are limited.
  Use the help command to display the available commands.
Notes: 5.1 – Basic Switch Configuration
5.1.1 – Configure a Switch with Initial Settings
5.1.1.2 – Recovering From a System Crash

## Slide 7: Switch LED Indicators
System LED shows if the switch has power applied.
Port LED states:
  Off – no link or shut down
  Green – link is present
  Blinking green – data activity
  Alternating green and amber – link fault
  Amber – port is not sending data; common for first 30 seconds of connectivity or activation
  Blinking amber – port is blocking to prevent a switch loop
Notes: 5.1 – Basic Switch Configuration
5.1.1 – Configure a Switch with Initial Settings
5.1.1.3 – Switch LED Indicators

## Slide 8: Preparing for Basic Switch Management
To configure a switch for remote access, the switch must be configured with an
IP address, subnet mask, and default gateway.
One particular switch virtual interface (SVI) is used to manage the switch:
  A switch IP address is assigned to an SVI.
  By default the management SVI is controlled and configured through VLAN 1.
  The management SVI is commonly called the management VLAN.
For security reasons, it is best practice to use a VLAN other than VLAN 1 for the management VLAN.
Remember that the switch console port is on the back of the switch.
Notes: 5.1 – Basic Switch Configuration
5.1.1 – Configure a Switch with Initial Settings
5.1.1.4 – Preparing for Basic Switch Management

## Slide 9: Switching Process: Learn
Examining the Source MAC Address
Switches examine all incoming frames for new source MAC address information to learn.
If the source MAC address is unknown, it is added to the table along with the port number.
If the source MAC address does exist, the switch updates the refresh timer for that entry.
By default, most Ethernet switches keep an entry in the table for 5 minutes.

## Slide 10: Switching Process: Forward
Examining the Destination MAC Address
If the destination MAC address is a broadcast or a multicast, the frame is also flooded out all ports except the incoming port.
If the destination MAC address is a unicast address, the switch will look for a match in its MAC address table.
If the destination MAC address is in the table, it will forward the frame out the specified port.
If the destination MAC address is not in the table (i.e., an unknown unicast) the switch will forward the frame out all ports except the incoming port.

## Slide 11: Configuring Basic Switch Management Access with IPv4
exit
Important Concept
The default gateway is the router address and is used by the switch to communicate with other networks.
Notes: 5.1 – Basic Switch Configuration
5.1.1 – Configure a Switch with Initial Settings
5.1.1.5 – Configuring Basic Switch Management Access with IPv4

## Slide 12: Basic Switch Configuration
Notes: 5.1 – Basic Switch Configuration
5.1.1 – Configure a Switch with Initial Settings
5.1.1.6 – Lab - Basic Switch Configuration

## Slide 13: Duplex Communication
Gigabit Ethernet and 10Gb Ethernet NICs require full-duplex connections to operate.
Bidirectional communication
Unidirectional communication
Obvody pro detekci kolize jsou vypnuty
Notes: 5.1 – Basic Switch Configuration
5.1.2 – Configure Switch Ports
5.1.2.1 – Duplex Communication

## Slide 14: Configure Switch Ports at the Physical Layer
Some switches have the default setting of auto for both duplex and speed.
Mismatched duplex and/or speed settings can cause connectivity issues.
Always check duplex and speed settings using the show interface interface_id command.
All fiber ports operate at one speed and are always full-duplex.
Notes: 5.1 – Basic Switch Configuration
5.1.2 – Configure Switch Ports
5.1.2.2 – Configure Switch Ports at the Physical Layer

## Slide 15: Auto-MDIX
Some switches have the automatic medium-dependent interface crossover (auto-MDIX) feature that allows an interface to detect the required cable connection type (straight-through or crossover) and configure the connection appropriately.
Notes: 5.1 – Basic Switch Configuration
5.1.2 – Configure Switch Ports
5.1.2.3 – Auto-MDIX

## Slide 16: Auto-MDIX (Cont.)
Use the show controllers Ethernet-controller command to verify auto-MDIX settings.
Notes: 5.1 – Basic Switch Configuration
5.1.2 – Configure Switch Ports
5.1.2.3 – Auto-MDIX (Cont.)

## Slide 17: Verifying Switch Port Configuration
Notes: 5.1 – Basic Switch Configuration
5.1.2 – Configure Switch Ports
5.1.2.4– Verifying Switch Port Configuration

## Slide 18: Verifying Switch Port Configuration (Cont.)
Notes: 5.1 – Basic Switch Configuration
5.1.2 – Configure Switch Ports
5.1.2.4– Verifying Switch Port Configuration (Cont.)

## Slide 19: Verifying Switch Port Configuration (Cont.)
Layer 1 OK
Layer 2 OK
Notes: 5.1 – Basic Switch Configuration
5.1.2 – Configure Switch Ports
5.1.2.4– Verifying Switch Port Configuration (Cont.)

## Slide 20: Network Access Layer Issues
Use the show interfaces command to detect common media issues.
The first parameter refers to Layer 1, the physical layer, and indicates if the interface is receiving a carrier detect signal.
The second parameter (protocol status) refers to the data link layer and indicates whether the data link layer protocol has been configured correctly and keepalives are being received.
Notes: 5.1 – Basic Switch Configuration
5.1.2 – Configure Switch Ports
5.1.2.5 – Network Access Layer Issues

## Slide 21: Network Access Layer Issues (Cont.)
Notes: 5.1 – Basic Switch Configuration
5.1.2 – Configure Switch Ports
5.1.2.5 – Network Access Layer Issues (Cont.)

## Slide 23: Late collision
Pozdní kolize jsou problémem, protože jakmile NIC zmešká skutečnost, že došlo ke kolizi, zotavení a opakovaný přenos jsou ponechány na horních vrstvách a doba zotavení drasticky vzroste. Zatímco síťová karta obvykle obnoví a znovu vysílá rámec za 2 –3 ms, u horních vrstev trvá obvykle 10x až 100x déle.

## Slide 24: Troubleshooting Network Access Layer Issues
Notes: 5.1 – Basic Switch Configuration
5.1.2 – Configure Switch Ports
5.1.2.6– Troubleshooting Network Access Layer Issues

## Slide 25: 5.2 Switch Security
Notes: 5 - Switch Configuration
5.2 – Switch Security

## Slide 26: SSH Operation
Secure Shell (SSH)
  An alternative protocol to Telnet. Telnet uses unsecure plaintext of the username and password as well as the data transmitted.
  SSH is more secure because it provides an encrypted management connection.
Wireshark Capture of Telnet
Wireshark Capture of SSH
Notes: 5.2 – Switch Security
5.2.1 – Secure Remote Access
5.2.1.1 – SSH Operation

## Slide 27: SSH Operation (Cont.)
A switch must have an IOS version (k9 at the end of the IOS file name) that includes cryptographic capabilities in order to configure and use SSH.
  Use the show version command to see the IOS version.
Notes: 5.2 – Switch Security
5.2.1 – Secure Remote Access
5.2.1.1 – SSH Operation (Cont.)

## Slide 28: Configuring SSH
Verify SSH support.
Configure the IP domain name.
Generate RSA key pairs.
Configure user authentication.
Configure the vty lines.
Enable SSH version 2.
Commonly forgotten command that is used in key generation
Default is to accept both Telnet and SSH (transport input all)
The login local command forces the use of the local database for username/ password.
Notes: 5.2 – Switch Security
5.2.1 – Secure Remote Access
5.2.1.2 – Configuring SSH

## Slide 29: Verifying SSH
On the PC, connect to the switch using SSH.
Switch IP address
Packet Tracer: ssh –l 172.17.99.11
Notes: 5.2 – Switch Security
5.2.1 – Secure Remote Access
5.2.1.3 – Verifying SSH

## Slide 30: Verifying SSH
On the PC, connect to the switch using SSH.
Switch IP address
The PC is using SSH to communicate and issue commands on the switch.
Notes: 5.2 – Switch Security
5.2.1 – Secure Remote Access
5.2.1.3 – Verifying SSH

## Slide 31: Packet Tracer – Configuring SSH
Notes: 5.2 – Switch Security
5.2.1 – Secure Remote Access
5.2.1.4 – Packet Tracer – Configuring SSH

## Slide 32: Secure Unused Ports
The interface range command can be used to apply a configuration to several switch ports at one time.
Notes: 5.2 – Switch Security
5.2.2 – Switch Port Security
5.2.2.1 – Secure Unused Ports

## Slide 33: Port Security: Operation
Port security limits the number of valid MAC addresses allowed to transmit data through a switch port.
  If a port has port security enabled and an unknown MAC address sends data, the switch presents a security violation.
  Default number of secure MAC addresses allowed is 1.
Methods use to configure MAC addresses within port security:
  Static secure MAC addresses – manually configure
  switchport port-security mac-address mac-address
  Dynamic secure MAC addresses – dynamically learned and removed if the switch restarts
  Sticky secure MAC addresses – dynamically learned and added to the running configuration (which can later be saved to the startup-config to permanently retain the MAC addresses)
  switchport port-security mac-address sticky mac-address
  Note: Disabling sticky learning converts sticky MAC addresses to dynamic secure addresses and removes them from the running-config.
Notes: 5.2 – Switch Security
5.2.2 – Switch Port Security
5.2.2.2 – Port Security: Operation

## Slide 34: Port Security: Violation Modes
Protect – data from unknown source MAC addresses are dropped; a security notification IS NOT presented by the switch
Restrict - data from unknown source MAC addresses are dropped; a security notification IS presented by the switch and the violation counter increments.
Shutdown – (default mode) interface becomes error-disabled and port LED turns off. The violation counter increments. Issues the shutdown and then the no shutdown command on the interface to bring it out of the error-disabled state.
Notes: 5.2 – Switch Security
5.2.2 – Switch Port Security
5.2.2.3 – Port Security: Violation Modes

## Slide 35: Port Security example: Configuring
Notes: 5.2 – Switch Security
5.2.2 – Switch Port Security
5.2.2.4 – Port Security: Configuring

## Slide 36: Port Security: Configuring (Cont.)
Before configuring port-security features, place the port in access mode and use the switchport port-security interface configuration command to enable port security on an interface.
Most common configuration error is to forget this command!
Notes: 5.2 – Switch Security
5.2.2 – Switch Port Security
5.2.2.4 – Port Security: Configuring (Cont.)

## Slide 37: Port Security: Configuring (Cont.)
Most common configuration error is to forget this command!
Notes: 5.2 – Switch Security
5.2.2 – Switch Port Security
5.2.2.4 – Port Security: Configuring (Cont.)

## Slide 38: Port Security: Verifying
Use the show port-security interface command to verify the maximum number of MAC addresses allowed on a particular port and how many of those addresses were learned dynamically using sticky.
Dynamic
Notes: 5.2 – Switch Security
5.2.2 – Switch Port Security
5.2.2.5 – Port Security: Verifying

## Slide 39: Port Security: Verifying
Use the show port-security interface command to verify the maximum number of MAC addresses
Sticky
Notes: 5.2 – Switch Security
5.2.2 – Switch Port Security
5.2.2.5 – Port Security: Verifying

## Slide 40: Port Security: Verifying (Cont.)
Use the show running-config command to see learned MAC addresses added to the configuration.
Notes: 5.2 – Switch Security
5.2.2 – Switch Port Security
5.2.2.5 – Port Security: Verifying (Cont.)

## Slide 41: Port Security: Verifying (Cont.)
The show port-security address command shows how MAC addresses were learned on a particular port.
Notes: 5.2 – Switch Security
5.2.2 – Switch Port Security
5.2.2.5 – Port Security: Verifying (Cont.)

## Slide 42: Ports in Error Disabled State
Switch console messages display when a port security violation occurs. Notice the port link status changes to down.
Notes: 5.2 – Switch Security
5.2.2 – Switch Port Security
5.2.2.6 – Ports in Error Disabled State

## Slide 43: Ports in Error Disabled State (Cont.)
Check the port status and the port security settings.
Notes: 5.2 – Switch Security
5.2.2 – Switch Port Security
5.2.2.6 – Ports in Error Disabled State (Cont.)

## Slide 44: Ports in Error Disabled State (Cont.)
Do not re-enable a port until the security threat is investigated and eliminated.
Notice that you must first shut the port down and then issue the no shutdown command in order to use the particular port again after a security violation has occurred.
Notes: 5.2 – Switch Security
5.2.2 – Switch Port Security
5.2.2.6 – Ports in Error Disabled State (Cont.)

## Slide 45: Hrátky s časem

## Slide 46: Typická konfigurace

## Slide 47: Jiný typický příklad

## Slide 48: Packet Tracer – Configuring Switch Port Security
Notes: 5.2 – Switch Security
5.2.2 – Switch Port Security
5.2.2.7 – Packet Tracer – Configuring Switch Port Security

## Slide 49: Packet Tracer – Troubleshooting Switch Port Security
Notes: 5.2 – Switch Security
5.2.2 – Switch Port Security
5.2.2.8 – Packet Tracer – Troubleshooting Switch Port Security

## Slide 50: Packet Tracer – Configuring Switch Security Features
Notes: 5.2 – Switch Security
5.2.2 – Switch Port Security
5.2.2.9 – Lab – Configuring Switch Security Features

## Slide 51: 5.3 Chapter Summary
Notes: 5 - Switch Configuration
5.3 – Summary

## Slide 52: Packet Tracer - Skills Integration Challenge
Notes: 5.3 – Summary
5.3.1 – Conclusion
5.3.1.2 – Packet Tracer - Skills Integration Challenge

## Slide 53: Security best practices:
  Disable ports that do not have a device connected to them using the shutdown command.
  Avoid using VLAN 1 because it is commonly attacked.
  Use port security to keep private devices from being attached to a network in place of a corporate wired device.
Notes: 53

## Slide 54: Nutné k zapamatování
  config t interface vlan 99 ip address 172.17.99.11 255.255.255.0 no shutdown ip default-gateway 172.16.99.1 (address on the router that is on the same 172.17.99.0 network) vlan 99 name Management exit

## Slide 55: Používejte příkazy show
  show interfaces interface_id or show ip interface brief
  show ip interface interface_id
  show running-config
  show flash
  show version
  show mac-address-table
Notes: 55

## Slide 56: ? is a KEY to IOS. Promts
  Switch> (User EXEC mode that is shown when a switch first boots)
  Switch# (Privileged EXEC mode that is shown after someone types enable)
  switch: (Boot loader mode shown when a switch does not have, or cannot find, an operating system)

## Slide 57: sh boot
Notes: 5.3 – Summary
5.3.1 – Conclusion
5.3.1.3 – Switch Configuration

## Slide 58: New Terms and Commands
POST Boot loader boot system command show boot command switch: prompt Mode button System LED Port LED SVI VLAN Management VLAN interface vlan command vlan command name command | Full-duplex Half-duplex Port speed duplex command speed command mdix command show interfaces command SSH configuration ip domain-name command crypto key generate rsa command transport input local command username secret command ip ssh version 2 command | login local command show ip ssh command Unused ports Port security switchport mode access command switchport port-security command switchport port-security maximum command switchport port-security mac-address sticky command show port-security interface command show port-security address command
Notes: Chapter 5 - New Terms and Commands