## Slide 1: PV198 – One-chip Controllers GPIO – LED & Button

## Slide 2: Content
What is GPIO
What is it used for
How does it work
  Switch debouncing
Application
  Output – LED using SDK example
  Input – Button using Config Tools

## Slide 3: What is GPIO
GPIO – General Purpose Input Output
Direct control of pins of the MCU
Basic interaction with external world
Can be programmed as Input or Output
Has only 2 states (logic 0, logic 1)

## Slide 4: Content
What is GPIO
What is it used for
How does it work
  Switch debouncing
Application
  Output – LED using SDK example
  Input – Button using Config Tools

## Slide 5: What is it used for
Anything that works with 2 states – on/off
LED
Buttons
Sensors
And used by more sophisticated peripherals

## Slide 6: Content
What is GPIO
What is it used for
How does it work
  Switch debouncing
Application
  Output – LED using SDK example
  Input – Button using Config Tools

## Slide 7: How buttons on the board work
Connects pit to ground (logic 0) or to voltage (logic 1)

## Slide 8: How does it work – Switch debouncing
Bouncing
  Looks like button is pressed multiple times
  Cause by mechanical contact of the switch

## Slide 9: How doeas it work – Switch debouncing
Bouncing
  Looks like button is pressed multiple times
  Cause by mechanical contact of the switch
Solution
  HW debounce(add capacitor)
  SW debounce(wait few miliseconds)

## Slide 10: Content
What is GPIO
What is it used for
How does it work
  Switch debouncing
Application
  Output – LED using SDK example
  Input – Button using Config Tools

## Slide 11: Application
Steps required to create an application:
Initialize( MCUXpresso Configuration Tools help here)
  Pin
  Clocks
  Peripherals
Write application code

## Slide 12: Application
Write everything from scratch
❌Error-prone , time demanding, tedious
USE SDK example
  ✔️Works out-of-box
  ❌More difficult to modify
USE Config Tools
  ✔️Easy to use and modify

## Slide 13: Content
What is GPIO
What is it used for
How does it work
  Switch debouncing
Application
  Output – LED using SDK example
  Input – Button using Config Tools

## Slide 14: Application – LED using SDK example
Import SDK example “gpio_led_output”
Select import SDK examples(s)…

## Slide 15: Application – LED using SDK example
In the SDK wizard unfold the K6x, select the MK66FN2… and click on the board image

## Slide 16: Application – LED using SDK example
Unfold driver_examples -> gpio
Select “gpio_led_output” example
Click Finish

## Slide 17: Application – LED using SDK example
Go through code together in detail
  Pins, clocks are already configured
  GPIO_PinInit
  GPIO_PortToggle

## Slide 18: Content
What is GPIO
What is it used for
How does it work
  Switch debouncing
Application
  Output – LED using SDK example
  Input – Button using Config Tools

## Slide 19: Application – Button using Config Tools
Goal:
Press SW2 button to print text into console

## Slide 20: Application – Button using Config Tools
Create new project
Open Config Tools

## Slide 21: Application – Button using Config Tools
You should see Pin tool now:

## Slide 22: Application – Initialization
How configuration tools can help us:
Modify settings easily
Visual representation of a configuration
Great for custom boards (our board already has a lot of useful DEFINEs, which is not a case when new board is created)

## Slide 23: Application – Button using Config Tools
Pins tool contains predefined configurations
Open dialog with functional groups by clicking on the icon

## Slide 25: Application – Button using Config Tools
Dialog with predefined functional group appears
Set checkbox at the bottom of the dialog for functional group: “BOARD_InitButtonsPins” to call initialization code for the group in default initialization function

## Slide 26
Prefix used
in generated code

## Slide 27: Application – Button using Config Tools
Code preview is updated
Initialization function now calls 1 more function

## Slide 29: Application – Button using Config Tools
Select “BOARD_InitBUTTONsPins” functional group from a combo-box

## Slide 30
GPIO signal is routed to “PTD11”

## Slide 31
User-friendly
Label – specific for our board
Identifier used in generated code
Identifier used in generated code
Prefix used in generated code
User friendly Label – specific for our board

## Slide 32: Application – Button using Config Tools
Your project needs to be updated by newly generated code now – this action is done automatically
Whenever generated code does not match the code is your project, it is displayed by changed color of the icon in the toolbar

## Slide 33: Application – Button using Config Tools
Update Project Files dialog should appear
You can view changes to each file by clicking on the “change” text in the “Status” column
Press “OK” to update your project

## Slide 34: Application – Button using Config Tools
Clocks tool – preconfigured, you can view clock settings
Peripherals tool – no need for now

## Slide 35: Application – Button using Config Tools
Write application code
  Read current state of the GPIO(button)
  Detect button press
    Print text into console

## Slide 36: Application – Button using Config Tools
When you press the button, text is printed more than once
Why?
How to resolve this issue?

## Slide 37: Work Progress
Write an applications that toggles GREEN LED when SW3 button is pressed
Fix the issue with button press being registered more than once
Make LED change color every time it is turned on (there are 3 LEDs on the board: Red, Green, Blue)

## Slide 38: Homework
Write an applications that reacts to both buttons
SW3 turns on/off selected color
SW2 changes selected color (R -> G -> B -> R …)
At start all colors are turned off, and RED is selected
All colors
are off
Red
turned on
Red
stays on
Green
Turned on
Green
Turned off
SW3
SW3
SW3
SW2

## Slide 39: Homework - git
Git Branch- “Week_02”
Git tag – “Submission_02_x”